## Slide 1: GPSC Technical Exchange
Josh Nimetz
USGS| National Geospatial Technical Operations Center
Virtual Web Conference
March 14, 2023

## Slide 2
Topics for discussion
Numerous pending LBS revisions
  Lidar Base Specification Revision Status | U.S. Geological Survey (usgs.gov)
Vector Tile Structure and DEM creation
ASPRS Positional Accuracy Standards update
  VVA check points
  Check point accuracy
Access to TEM materials – slides, recordings, etc.
  https://rockyweb.usgs.gov/outgoing/3DEP_TEM/
GPSCTechnicalInquiries@usgs.gov

## Slide 3
Vector Tile Structure and DEM Creation
GPSCTechnicalInquiries@usgs.gov
Please follow latest pending LBS update
  https://www.usgs.gov/ngp-standards-and-specifications/tile-scheme-generation-and-crs
In addition, please be mindful of orthogonal tile geometry so rasters are created properly
  Imprecise tile coordinates lead to offset pixels within interior of raster data set
Stair-stepped pixels along tile edges clipped to irregular (non-orthogonal) boundaries are okay and expected
  Please interpolate your DEMs beyond irregular boundaries and clip back!
Interior vector tile example, sub-pixel gaps were identifiable in interior of data set
!

## Slide 4
Review/Comment period extend through April 30, 2023
  Please review and comment!
  https://docs.google.com/forms/d/e/1FAIpQLSfvq-jNTQDb9gvizr1H9BVOa_kFNLT1AaglJSrP4pUkK8uPpw/viewform
Current Topics Being Deliberated Within USGS and ASPRS
  VVA check point quantity and surveying methodology
  Check point accuracy
GPSCTechnicalInquiries@usgs.gov
ASPRS Positional Accuracy Standards Update

## Slide 5
VVA Check Point Quantity and Surveying Methodology
  Removal of pass/fail threshold for VVA assessment
  Proposed change calls for equivalent number of NVA and VVA check points with a lower limit/minimum of 30 check points
  Do we need more VVA points?
  Do we need VVA points?
  Survey addendum calls for use of classical surveying with a properly calibrated total station in GPS/GNSS obscured environment
GPSCTechnicalInquiries@usgs.gov
ASPRS Positional Accuracy Standards Update

## Slide 6
Check Point Accuracy
  Check points have error and the objective is to include this error in overall product accuracy assessment
ASPRS Positional Accuracy Standards Update

## Slide 7
Check Point Accuracy
  Check points (and control points) must be 2 times better than…or ½ product RMSEz
  So, how do we know the positional accuracy of a check point?
  With RTK observations, real-time coordinate quality indicators reveal precision, but not accuracy
  One proposed approach – store observables in data logger memory and post-process vectors to active control stations to confirm elevation agrees within ½ product RMSEz
ASPRS Positional Accuracy Standards Update

## Slide 8
Thank you!