## Slide 1: Dive into USGS Hydrography
Cynthia Ritmiller
National Map Liaison

## Slide 2
Mission: Provide National topographic information to advance science, support government, enlighten citizens, and enable decision making.
USGS National Geospatial Program
Notes: Within USGS I’m part of the USGS National Geospatial Program(NGP).
NGP provides a foundation of digital geospatial data representing the topography, natural landscape, and manmade environment of the United States.
Here are some of the components of the NGP.
The National Map is the authoritative source for Hydrography, Elevation and Names.

## Slide 3
The 3D National Topography Model
Progression required to produce a fully integrated and continuous topographic model to meet the Nation’s critical applications
3DEP Baseline
3DHP
Next gen 3DEP
3DNTM
Complete the nationwide 3D Elevation Program (3DEP) baseline
Use the 3DEP baseline to derive the 3D Hydrography Program (3DHP)
Implement the next generation of 3DEP to multiply value and improve applications
Research and develop a 3D data model to fully integrate 3DEP, 3DHP, and other data
100% of the Nation has 3DEP baseline data available or in progress
Launched in FY24
First full year in FY27 (funding dependent)
Early development stage
Notes: The 3DNTM includes 3 components:
Starting with an initial 3DEP baseline nationwide coverage,
the 3D Hydrography Program, or 3DHP can be derived.
With the 3DHP in work, the next generation of the 3D Elevation Program can begin to be collected. This is really targeting areas where we have data older data.
The Next Gen 3DEP will also integrate inland bathymetry.
Finally, with the future being integrated elevation and hydrography data, these datasets can be further integrated with other data from The National Map.
_________________________________________________________________________________________________________________________________________
The 3D National Topography Model, or 3DNTM, is designed to deliver the terrestrial component of the 3D Nation vision by integrating national elevation and hydrography datasets to model the Nation’s topography in 3D.
3DNTM is an initiative that includes 3 components.
The first is the 3D Hydrography Program, The second component is the next generation of the 3D Elevation Program which is being designed with all new quality levels and refresh cycles and will integrate inland bathymetry with terrestrial elevation data. Because we plan to continue to incorporate new technology and approaches over time, we will assess the next gen 3DEP program design on a regular cycle of 3-5 years. This new strategy will allow for continual improvement in the program.
The third component is a vision for a future integrated 3D model. We are beginning research and development to more fully integrate 3DHP and the next gen 3DEP and to integrate other data from The National Map in a 3D data model.
3DNTM is based on extensive requirements and benefits documentation to maximize its return on investment to a broad range of business uses.
It will provide foundational data to critical initiatives including FEMA Risk Rating 2.0, the National Water Model, the Clean Water Act, and the National Landslides Preparedness Act.
3DNTM will provide universal discovery and sharing of water information as the geospatial foundation for the Internet of Water.
With multiple new vintages of data coverage and increased accuracy, the 3DNTM will enable new and emerging applications.
To set the stage for this presentation on the 3D Hydrography Program, I’m going to first talk about the 3D National Topography Model. 3DNTM is designed to deliver the terrestrial component of the 3D Nation vision by integrating national elevation and hydrography datasets to model the Nation’s topography in 3D.
3DNTM is an initiative that includes 3 components.
Thefirst is the 3D Hydrography Program, or 3DHP
·3DHP is an application of 3DEP that derives hydrography data from lidar and Alaska IfSAR
·Ensuring integration of the two datasets for the first time since they were originally surveyed for the USGS topographic map series.
·Enhancements include plans to provide new connections to groundwater, wetlands, and engineered hydrography; and improve water-related sharing by implementing the 3DHP infostructure as the underpinning of the Internet of Water.
The second component is the next generation of the 3D Elevation Program.
·Next gen isisbeing designed with all new quality levels and refresh cycles and will integrate inland bathymetry with terrestrial elevation data.
·Because we plan to continue to incorporate new technology and approaches over time, we will assess the next gen 3DEP program design on a regular cycle of 3-5 years.
·This new strategy will allow for continual improvement in the program.
The third component is a vision for a future integrated 3D model. We are beginning research and development to more fully integrate 3DHP and the next gen 3DEP and to integrate other data from The National Map in a 3D data model.

## Slide 4
New Seamless 1-meter Digital Elevation Model
USGS lidar coverage in 2,252 individual projects
S1M over Rolla, MO
Notes: Since its inception, 3DEP projects have been seamless within projects, but not between projects.
One of the exciting NEW things we are doing to assist in creating 3DHP is creating a seamless 1 meter DEM product. The workflow is fully developed, and data production began in 2025. A few watersheds have been published and production is ramping up to publish additional watersheds that are priorities for producing new 3D hydrography data.
The S1M is a foundational element of the 3D National Topo Model (3DNTM)
3DEP 1-meter resolution seamless DEM (S1M) can be used to derive 3DHP to create surface water features and watersheds
The S1M is a foundational element of the 3D National Topo Model (3DNTM)
Vertically and horizontally aligns and integrates 3DHP hydrography data and 3DEP elevation data
Applications require consistent data across large watersheds
  Flood modeling, storm surge analysis, fire models, and many other landscape-scale applications
Addresses National Geospatial Advisory Committee recommendation to develop a seamless 1-meter DEM for derivation of hydrography from elevation data
Produced for 10 km by 10 km tiles that intersect with the watershed boundary of a given project
Requires merging of 2201+ independently collected projects
_________________________________________________________________________________________
3DEP is developing a new 1m seamless DEM product that will support the 3D Hydrography Program and many other applications.
All seamless data creation had been done at the 1/3rd Arc Second (10m) or 1 Arc Second (30m) level.
Long version: The 3D National Topography Model updates and integrates USGS elevation and hydrography data to model the Nation in 3D. A key element of the 3DNTM is a new 3DEP product line, where we are building a 1-meter spatial resolution DEM that will be seamless across the nation. Currently, our DEM data holdings are a patchwork of projects in different coordinate systems that don’t always align perfectly at the borders. The new seamless DEMs are aligned in a single coordinate system and spatial resolution and will be used as the foundational baseline data by the 3D Hydrography Program for deriving updated hydrography data. Also, the new hydrography data will be aligned both vertically and horizontally with the high-resolution elevation data, which means that the new 3DHP data is more detailed and more accurate than the existing NHD. We are producing it one watershed at a time, prioritizing areas where the 3D Hydrography Program plans to produce new hydrography data next.

## Slide 5
New Seamless 1-meter Digital Elevation Model
10km by 10km
tile
Watershed boundary (HU10)
Seamless 1m DEM for the Dry Fork HU10 watershed in Missouri
Seamless 1m DEM availability as of August 2026
Notes: Initial tiles of S1M now available!
May include topobathymetric data for inland and coastal water bodies in the future, where data are available
Currently optimizing the production capability and beginning production for CONUS
Seamless 1m Product https://www.usgs.gov/3d-elevation-program/new-product-3d-elevation-program-seamless-1-meter-digital-elevation-model-s1m
  https://index.nationalmap.gov/arcgis/rest/services/USGS_Seamless1m_Index/MapServer

## Slide 6
Hydrography data on The National Map
National Hydrography Dataset (NHD)
Watershed Boundary Dataset (WBD)
3D Hydrography Program (3DHP)
Static versions of NHD, WBD, and NHDPlus HR are available and can be found: https://www.usgs.gov/national-hydrography/access-national-hydrography-products
NHDPlus High Resolution (NHDPlus HR)
Notes: Let’s look at what is the Hydrography Data is part included of The National Map.
(Click) The NHD was the first national surface water dataset. It is a powerful database that contains a flow network allowing for modeling and tracing water downstream or upstream. The majority of the NHD originally digitized from the 7.5 min topo maps. The NHD has 1:24,0000-scale or greater, with
(Click) The WBD established a drainage boundary framework. Made up of many hydrologic units (HU’s) the WBD became the containers for the NHD data.
(Click) NHDPlus HR was USGS’ first attempt at elevation derived hydrography. Using the NHD, WBD, as well as the 3DEP elevation data to derive the NHDPlus HR. NHDPlus HR provided additional features including hundreds attributes known as the NHDPlus VAA’s, catchments, as well as associated rasters. These additional features provided a more user-friendly dataset for network navigation and analysis.
The NHD and the WBD leveraged local knowledge and updates through a stewardship program with participants from 41 states and Washington, D.C. The updates to the data are not uniform. Only some areas have been updated. The national consistency of data quality has decreased over time. And NHD surface water features don’t align well with highly accurate 3DEP data.
(Click) In 2022, USGS began rebuilding a national water dataset the 3DHP.
The NHD, WBD, and NHDPlus HR are now considered legacy datasets and static versions can be found on our website.
Moving forward USGS is focused on building 3DHP

## Slide 7
Flow Direction
Flow Navigation
Reachcodes
Measures
National Hydrography Dataset (NHD)
Notes: First, we have the National Hydrography Datatset or NHD.
The National Hydrography Dataset (known as the NHD) is more than just blue lines on the map.
The NHD was the first national surface water dataset including features such as rivers, streams, canals, lakes, ponds, and streamgages
It is a powerful database that contains a flow network allowing for modeling and tracing water downstream or upstream.
The NHD has 1:24,0000-scale or greater, with the majority of the NHD originally digitized from the 7.5 min topo maps.
The NHD is a multi-resolution dataset because it is built from a variety of data sources, including EPA, Forest Service, and NHD partners.
Here are some of the NHD's attributes:
including flow direction, flow navigation, reachcodes, and measures.
Maintaining and improving the NHD was a challenge utilizing local knowledge through a network of state-organized stewards.
While this worked in most areas, this did not provide a nationally consistent dataset or was updated on a regular basis.

## Slide 8: Watershed Boundary Dataset (WBD)
Seamless baseline drainage area dataset for the Nation
Boundaries defined by hydrographic and topographic criteria with no regard for administrative boundaries
Delineated in a nested multi-level, hierarchical drainage system.
Each level assigned a progressive 2-digit Hydrologic Unit (HU) code which describes where the unit is in the country and the “level” of the unit
Complete for the US to HU12
Notes: Next is the Watershed Boundary Dataset (WBD)
- Watershed Boundaries are determined solely upon science-based hydrologic principles, not favoring any administrative boundaries or special projects, nor particular program or agency.
- The intent of defining Hydrologic Units (HU) for the Watershed Boundary Dataset is to establish a base-line drainage boundary framework, accounting for all land and surface areas.
- Hydrologic units are given a Hydrologic Unit Code which describes where the unit is in the country and the extent of that unit.
The WBD can be thought of as containers for the hydrologic features.
- The images on the right show the various HU levels from the HU2 to the HU12.

## Slide 9: NHDPlus High Resolution (NHDPlus HR)
NHD
WBD
3DEP
Plus, additional tables…
Notes: NHDPlus Hi Res was the one of the first phases of moving toward the integration of hydro and elevation data.
NHDPlus Hi Res, was derivated using the NHD, WBD and 3DEP datasets.
NHDPlus HR provided additional features including hundreds attributes known as the NHDPlus VAA’s, catchments, as well as associated rasters. These additional features provided a more user-friendly dataset for network navigation and analysis.

## Slide 10: NHDPlus HR Rasters
cat.tif
elev_cm.tif
fac.tif
catseed.tif
fdr.tif
filldepth.tif
swnet.tif
fdroverland.tif
shdrelief.jpg
hydrodem.tif
Notes: The raster data includes raster catchment files, source elevation data(elev_cm.tif), shaded relief, flow direction grids and flow accumulation rasters.
While these are raster files ie pixels you can see how some of them quickly start to look like a stream network.

## Slide 11
Derive from and align with 3DEP elevation
Follow 3DEP Best Practices for governance and acquisition
Data and systems built for hydrologic applications
Better accounting of the hydrologic cycle with connections to water-related information
Interoperability with non-hydrographic data
3DHP Program Goals
Replace older, inconsistent hydrography with higher accuracy data
Notes: Building on decades of previous hydrography concepts, the 3DHP is being established to completely refresh the Nation’s hydrography data and improve discovery and sharing of water-related data.
New hydrography will be standardized to align vertically, horizontally and temporally with 3DEP data.
Transitioning the hydrography program to 3DHP, allowed us to simplify the data and resources required to maintain a nationwide hydrography dataset.
Estimations to create 3DHP are about $685M over 9 years.

## Slide 12: The 3DHP Data Lifecycle
Notes: Let’s briefly walk through the steps of the 3DHP data lifecycle.
Once a 3DHP project is planned, the data will be aquired through the USGS Geospatioal G P S C or Co-op project
Validation will occur using our standand process and specifications.
Once the data has passed our validation checks, it will be distributed through The National Map and cloud services.
Once planned, a 3DHP can be acquired. Once USGS receives the data validation checks will be performed to ensure it meet our standards.
Once published, the data can be access by any users.

## Slide 13
3DHP Map Service
3dhp.nationalmap.gov/
Notes: We can see the 3DHP still contains point, line and polygon features but is much simpler than NHD or NHDPlus HR was.
The is also a drainage area feature class which will be similar to WBD.

## Slide 14
Notes: Website and adding service to map

## Slide 15
Notes: Loading service. This is real time

## Slide 16
Notes: Elevation match and NHD differences

## Slide 17
Notes: Ref Mainstem

## Slide 18: Flow Network Derivatives
Identify, sequence and measure
Hydro Sequence
Terminal Path
Path Length
Arbolate Sum
Network Flags
Start Flag
Terminal Flag
Divergence
Return Divergence
Hierarchy of flowlines
Stream Level
Level Path
Stream Order
Stream Calculator
usgs.gov/3d-hydrography-program/3dhp-flow-network-derivatives
Notes: Released nationally July 2026!!!!
The flow network in 3DHP data is what gives it its analytic power.
Flow Network Derivatives (FNDs) boost this power by pre-calculating several network characteristics to make network analysis faster and easier.
FNDs are recomputed nationally with each quarterly data release. While many FNDs will not change between releases, any could change.

## Slide 19
Notes: Pathlength in KM

## Slide 20
Probabilities of Stream Permanence
Notes: Stream Permanence estimates probabilities of detecting at least x days of zero streamflow, where x equals 1, 3, 7, and 30 days, for river locations across the contiguous United States.
Right now the

## Slide 21
69 out of 160
(43.1 percent) streamgages have at least 30 days of zero flow for Hydrologic Unit 15.
Notes: Here we can look at region 15.

## Slide 22
Notes: Here are the partnerships we have in FY26
Totally 162K

## Slide 23: 3DNTM Data Collaboration Announcement (DCA)
Notes: The Data collaboration Announcement or DCA allows non-federal entities funding opportunities to collect Hydrography or Elevation or in some cases both.
Here you can see the four key steps to navigate the 3DNTM DCA.
I’m always available to answer questions about the DCA or provide project cost estimates.

## Slide 24
Cynthia Ritmiller
critmiller@usgs.gov
303-202-4550
Notes: National Map Liaisons communicate and connect on national topographic mapping activities, especially elevation and hydrography topographic mapping data.
Part of the project planning can be including me to get a project cost estimate or see if there are other interested parties for your area of interest. Feel free to reach out with any questions.