## Slide 1: Modernizing watercourse mapping through the 3D Hydrography Program & 3DNTM DCA
Elaine Guidero
USGS National Geospatial Program
eguidero@usgs.gov
National Map Liaison to ID, MT, ND, SD, NE
Troy Blandford
Montana State Library
tblandford@mt.gov
GIS Analyst & Water Information Lead
August 21, 2025

## Slide 2: Watercourses, hydrography, stream or surface water mapping…call it what you’d like
We’re talking about the “blue” lines and polygons on a map
Mapping Montana’s rivers, streams, canals, lakes and other waterbodies

## Slide 3
High-accuracy elevation data (LiDAR) informs stream mapping
Topography and water shape each other
Water flows downhill > Align hydrography with elevation data

## Slide 4
To the Pacific Ocean
To the Atlantic Ocean
To Hudson Bay (Arctic Ocean)

## Slide 5: Montana Spatial Data Infrastructure
Hydro & Water Information
Addressing
15 MSDI Layers Total

## Slide 7
Hydrologic Position Index for mapping canals and ditches

## Slide 8: Why 3DHP? Don’t we have NHD already?
Inconsistency
Would take 20+ years to refresh MT NHD
Digitizing hydro from aerial imagery leads to chasing years (tendency to compare to the most current)
Those darn trees
Notes: Picture on right shows misalignment between NHD and lidar-derived DEM

## Slide 9: National Hydrography Dataset (left) Elevation-derived hydrography (right)
Example from Indiana

## Slide 10: NHD & EDH comparison - Montana
Swamp Creek in the Lower Noxon Reservoir HU-10, Sanders County, MT

## Slide 11: 3DHP benefits for Montana
Aligns with 3DEP lidar & integrates with future 3DHP
  Most MT lidar is less than 5 years old; the time is now
Montana state standard: “one Montana hydrography dataset”
  Detailed, standardized hydrography & catchments
Existing high-res hydrography will validate 3DHP
Maintenance, coordination, metadata, attribution, dissemination, and training & outreach will be supported at the state level by MSL; at the federal level by USGS
  Available through The National Map and the Montana State Library as a web service, downloadable data, and web map(s)
Notes: 3DHP will align with 3DEP and so likely won’t match existing data exactly but USGS can use it to verify that 3DHP doesn’t omit any features that have been mapped.
Project-level metadata will be part of all 3DHP data, with feature-level metadata for specific feature updates

## Slide 14
3D Hydrography Program
overview

## Slide 15: A new era for surface water mapping
1966
2022
3DHP is the first complete remapping of the Nation’s hydrography since the original USGS 24K topographic mapping program 1947–1992
Notes: To address the issues caused by the separation in development between elevation and hydrography data, has embarked on an effort to greatly improve the level of detail, consistency, and spatial accuracy of the Nation’s surface-water mapping and bring it into alignment with 3DEP elevation data.
3DHP is new data, we have a new database, web services, and data model.
This is in response to the need for water data that are accurate, precise, and consistent. Elevation-derived hydrography data that goes into 3DHP follows a formal specification, much like 3DEP does.
This is a big shift from the qualitative judgments that permeated the NHD, such as visual assessments of what just “looks right,” and individual steward-based decisions about capture conditions and feature density.

## Slide 16: Program goals
Replace older & inconsistent data
Meet higher accuracy standards
Align vertically, horizontally, and temporally with 3DEP
Increase data density
Create and follow best practices & data governance
Notes: 3DHP data has vertical, horizontal, and temporal alignment with 3DEP elevation.
We are modernizing the approach to mapping, delivering, and maintaining these critical datasets.
3DHP builds on decades of work that went into the NHD and WBD, but represent a fundamental transformation in how national hydrography data will be acquired and maintained.
The program is moving toward a set of best practices based on 3DEP best practices. WHAT DOES THIS MEAN?
More consistent data governance practices also will be employed WHAT DOES THIS MEAN?
The overall goal is to ensure that uniform, high quality data exists across the Nation

## Slide 17: Going beyond NHD
Specifically breaching features are included in 3DHP, and yes that means culverts
More canals & ditches will be included
x, y, and z alignment with elevation
Breaching features
Horizontal
Alignment
Z-values on every vertex
that matches the DEM
Notes: One of the key benefits that we anticipate 3DHP would bring for you is an improvement in flood prediction modeling. Data that is reflective of the current landscape can result in an improved representation of flood routing through a given network.
Floodplain managers have an important role to play in this data development with their expansive local knowledge of features that are often missed, such as culverts and other flow obstructions. An important topic that I did not cover today is how feedback from local stakeholders helps to make this effort stronger.
ELAINE consider additional details for slide about canals/more detail on culverts

## Slide 18: Old data model
Tools
NHD Update
WBD Update
NHD Utilities (6 tools)
HEM
HydroAdd
Geoconflation
Generalization
NHDPlus HR Build
Notes: If you are familiar with the previous hydrography datasets, the NHD, NHDPlus, and NHDPlus HR, the graphics representing their data models may have a familiar look.

## Slide 19: New data model
Radically simplified: crosswalked 107 Ftypes to
  7 flowline types (line)
  11 hydrolocation types (point)
  4 waterbody types (poly)
Still includes GNIS ID, Reachcode Start, Reachcode End for reference back to NHD
Catchments are foundational & will be used to make nested HUs
Notes: We anticipate that 95% of the features from the NHD, WBD, and NHDPlus will be represented in the 3DHP dataset. It’s not like the streams and rivers or lakes and ponds that were in those datasets disappeared; their position on the landscape will now be more accurately represented.
Reachcode Start & End are only on Hydrolocation Points
3DHP only has data that is strictly hydrologic in nature.
Those other 5% of features are either cartographic features like swimming pools and rocks, which are now gone, and some feature types (and their features) are also gone – playa and ice mass will be removed
3D Hydrography Program 3DHP_all 2023 Service | U.S. Geological Survey

## Slide 20: New attributes
id3dhp identifies an individual segment or flowline
mainstemID identifies entire river
entire length from headwater to confluence or outlet
Connects to the Internet of Water/Geoconnex
usgs.gov/3DHP/HydroProductSpecs
Notes: Reachcodes were converted to mainstem IDs

## Slide 21: 3DHP & Internet of Water
Federated sharing and discovery of stream network info
3DHP underlying data for the Internet of Water
Tools to reference data to the stream network
Tools to search and discover other data
Notes: One of the biggest technology shifts that has occurred since the initial days of NHD development is that there is not only a vast abundance of water-related data, but the majority of this data is available in a discoverable way – no longer buried in a static report table or only described in a journal article or government report.
The Internet of Water serves as a mechanism for water-related data to be made discoverable and accessible, regardless of collecting agency and data maturity.
Before the Internet of Water there was no systematic nationwide way to organize, search & discover water data.
3DHP forms the geospatial underpinning of this service. IoW will include tools to reference data…

## Slide 22: Geoconnex Explorer https://explorer.geoconnex.us/

## Slide 23: Geoconnex Explorer https://explorer.geoconnex.us/

## Slide 24: GeoConnex Explorer demo
https://www.usgs.gov/media/videos/july-22-2025-usgs-hydrography-community-call

## Slide 25: New derivatives table
flownetworkderivatives (table): relates flowlines to catchments and attributes that support network navigation and flow analysis
usgs.gov/3DHP/HydroProductSpecs

## Slide 26: 3DHP web service
REST WMS (and soon an Esri Feature Server) service
All data, whether NHD or 3DHP, provide National coverage
https://support.esri.com/en-us/knowledge-base/faq-what-is-the-difference-between-a-map-service-featur-000027304
Notes: The 3DHP_All Service is the 3DHP dataset published as a WMS service. It’s live right now, this replaces NHD and NHD+HR services. The current version of this service still includes NHD Geometry that was loaded at the end of fall 2023, and will be replaced by elevation-derived hydrography over time as projects are published and data become available.
The feature service is an Esri service, not OGC. You can download and visualize data from WFS. Basically it’s a map service with web features enabled.

## Slide 28
Partnerships for 3DHP

## Slide 29: What is the DCA?
How non-federal entities partner with USGS and other Federal agencies to acquire 3DHP
Open to Federal agencies, State and local governments, Tribes, regional consortia, academic institutions and the private sector
Applicants build coalitions to fund 50% or more of costs
3DHP funds cover remaining costs – up to 50% but this is not a guarantee
Notes: In October, we launched the 3DNTM Data Collaboration Announcement, also known as the “DCA”. This replaces our previous partnership vehicle (known as the Broad Agency Announcement) and will be our collaboration program for both 3DEP and 3DHP.
Project information and application materials are all available through USGS DCA website.
Collaboration applicants are encouraged to build funding coalitions that will fund at least 50% of project costs.
3DHP funding will cover the remaining costs. By law USGS cannot contribute more than 50% to a cost share, that’s our ceiling.

## Slide 30: FY26 3DNTM Data Collaboration Announcement
www.usgs.gov/3DNTM/DCA

## Slide 31: Project evaluation considerations
Project evaluation considerations
No existing 3DHP-quality EDH currently exists in the project area
Presence of published 3DEP data in the project area
Overlap with Federal areas of interest
Multi-state stakeholder funding where projects cross state boundaries (3DHP)
Cost realism
Level of matching funds offered
Maturity of the applicant’s project submission
Technical approach and past performance as applicable

## Slide 32: Potential partners
City governments
County governments
Conservation districts
Task forces
Montana DNRC
Montana DEQ
Conservation- or water-focused groups
Private sector groups/companies

## Slide 33: Here’s what you need NOW
Know how much money is available
  Do not spend money now
Watersheds you’re interested in
  Montana HUs and 3DHP Planning Map
Montana State Library will help with application
Applications due Sept 13

## Slide 34
Tentative timeline for first round FY26 DCA
Now: Identify priority area of interest: one to several HU-10s or one HU-8.
Now: Coordinate and identify funding partners, with a goal of at least 50% cost in total contributions from Montana partners. Partners sign a good-faith commitment.
By September 12, 2025: Montana State Library submits application to the first round FY26 USGS 3DHP Data Collaboration Announcement (DCA)
December 2025 to early January 2026: Acceptance Letter from USGS for first round submissions. Funding agreement(s) and task order development. Partners need to be ready to review and sign paperwork. Partner funds need to be available.
Throughout 2026 and into 2027: 3DHP data development by private contractors and data validation by the USGS. Regular status updates provided to partners.
Late 2027–2028: Final data delivery to the Montana State Library and other partners.
* Timeline depends on available USGS funding (amount and cycle).
Notes: 3DHP is built on data collaboration and funding partnerships.
The USGS (for the nation) and the Montana State Library (for the state) will lead the way but local, state, tribal, and federal funding is needed—it’s going to take a partnership of many organizations to make 3DHP happen for Montana.
DCA remains open (open all year)

## Slide 35: Step 2. Select project management
GPSC adds 6% overhead to project cost
Data from all projects must adhere to USGS specs in effect at the time of award
    www.usgs.gov/3DHP/HydroProductSpecs
USGS is responsible for the final inspection & validation of all data
Data will be shared publicly via The National Map
Who Manages the Project | Approach | Agreement Type | Funds Flow | Anticipated Percent of DCA Selections
USGS | USGS Geospatial Products and Services Contracts | Reimbursable Agreement | Partner  USGS | 80%
Partner | Partner Contract | Cooperative Agreement | USGS  Partner | 20%
Notes: The second step in the process of navigating the 3DNTM DCA is to determine who will manage the data acquisition project with the selection of a contract mechanism.
DCA applicants can apply to use the USGS Geospatial Products and Services Contracts to acquire data, or they can apply for a financial assistance agreement and manage data acquisition through a contract the partner directly oversees.
We recommend using the USGS GPSC especially with multiple partners on a project, because then USGS manages the project and the contract. With a coop agreement, somebody – one of you - has to step up and be the project coordinator. While there is a USGS coordinator (me) we’d still need someone else from the partnership who manages the contract.
With a GPSC setup, partners provide the funding to the USGS, then the USGS takes care of securing a vendor, developing the task order, project management, and final delivery. Performance expectations, timeline, and deliverables are all set and managed by the USGS. There will be paperwork initially to get the funding agreement in place between the partner and USGS (this is probably the heaviest lift for the partner) and to review the scope of work. There is a one to two hour kickoff meeting, then it is largely hands-off for the partners. The USGS typically send monthly status updates and may occasionally send a few questions/emails.

## Slide 36: Step 4. Submit forms and GIS files
www.usgs.gov/3DNTM/DCA
Both GPSC- and partner-managed project submissions will need to email required materials
Notes: Once all the required materials are assembled, project submissions for both GPSC and partner-managed or financial assistance projects can be sent to the emails listed here for consideration.
Directions for what to include in the subject line of your email will be available on the DCA portal.
It is important to let the programs know which program the project submission pertains to – 3DEP or 3DHP.
Initial project submissions must be submitted before the deadline that will be posted on the DCA portal. Project submissions received after the deadline will be considered for review after the initial project selection until no remaining FY25 funds are available for obligation.

## Slide 37: FY25 3DNTM DCA timeline
FY24
FY26
August
DCA
Open
Due September
DCA Decisions
DCA Selection Notifications
Partner Agreement(s)
DCA Released
(based on funding availability)
DCA Submissions
All agreements must be in place 60 days prior to desired project start
Agreement Deadline for all GPSC Projects
All FY25 Projects Awarded
Work can begin when project is officially awarded
Summer
Fall
Winter
Spring
Summer
Fall
FY25
SOW Development
Deadlines are approximate
DCA
Open
Decisions
FY26 DCA Released
FY26 DCA Submissions
Mid July
Manages
Project via GPSC
USGS
Manages
Project via own contract
Early May
Mid June
USGS Deadlines for Financial Assistance Agreements
Late March
Partner
> $500K
> $3M
< $500K
Notes: This slide illustrates the DCA timeline, the tracks each data acquisition option takes and some rough deadlines that are important to each.
Typically the DCA opens in August, first round submissions are due in September for a December decision deadline. Projects are awarded, task orders are completed, etc. throughout the next several months.
I’d like to point out that the DCA is open all year. As long as all the funds have not been committed, any incoming project submission has a chance to be awarded after that first-round submission deadline. Gallatin partners can still put together a DCA if you want to speed things up.
Depending on the size of the project, it probably takes about two years to complete a 3DHP project. We haven’t had enough projects yet to give a really accurate answer.

## Slide 38
More info

## Slide 39
NSGIC 3DHP FTN YouTube playlist
https://www.youtube.com/@NSGICOfficial
https://3dhp-for-the-nation-nsgic.hub.arcgis.com/
NSGIC 3DHP For the Nation Hub
USGS Hydrography Community Call
https://www.usgs.gov/3d-hydrography-program/hydrography-community-calls

## Slide 40
www.usgs.gov/3DNTM/DCA
Elaine Guidero
eguidero@usgs.gov
Bitterroot Forest, MT
Troy Blandford
tblandford@mt.gov

## Slide 41
Additional 3DHP technical info

## Slide 42: Geomorphic indicators
Primary derivatives
  Geomorphon valleys and depressions
  D-infinity flow models
  Plan Curvature
Additional layers
  D8 flow paths
  Low slope areas
  Sinks
  Contours
  Profiles
elevation derivatives developed from the source DEM that identify the most likely paths of water to flow or pool on the landscape
Notes: Contractors will utilize 1m DEMs that are derived from 3DEP-collected lidar (or IFSAR in Alaska).
While flow direction and flow accumulation models have long been used to interpret hydrography, they will now be one of the many indicators used to evaluate the landscape. With the higher resolution DEMs, we’re able to use more powerful means for landscape interpretation, such as geomorphic indicators. These methods allow for the ability to not just evaluate where stream channels and ditches are found, but also aid in determining where non-channelized features, such drainageways and indefinite surfaces, are located.

## Slide 43: EDH Acquisition Spec
Governs how EDH is derived from lidar, delineated, and attributed
Includes the formerly separate READ rules
2024 rev. A2

## Slide 44: FType crosswalk
stream/river
canal/ditch
drainageway
Drainageway
Canal
connector: indefinite surface
Surface Connector
artificial path
Waterbody Connector
connector: culvert
Elevation Breaching Connector
connector
Hydro Unenforced Connector
connector: non-nhd dataset
underground conduit
pipeline
connector: terrain breach
Channel line
**(future change)
EDH Lines
EDH Lines
3DHP Lines
3DHP Lines
Notes: Note that this not a crosswalk from NHD to 3DHP, although some of these terms are the same. This is EDH to 3DHP.
There’s a difference here between EDH and 3DHP - EDH is what the contractor makes, and 3DHP is our value-added, validated version.

## Slide 45: FType crosswalk
canal/ditch
Canal
lake/pond
Lake
reservoir
sink/rise
Sink
stream/river
River
Not in 3DHP
ice mass
playa
sea/ocean
dam/weir
Ocean or Great Lake
Waterbody Outlet
EDH Polygons
3DHP Polygons
EDH Points
3DHP Points
EDH Polygons
Notes: Here are the additional schema changes for polygons, points and even two features in EDH that are not within 3DHP.

## Slide 46: EDH vs 3DHP
EDH
  Raw data
  Derived from 1m DEMs (5m in AK)
  No 3DHP-specific attributes (MainstemID, GNIS names, stream order)
  Done by contractors
Ingestion & QA
  Conversion to 3DHP schema
  Attributes added
  Flow network information added
  Catchments generated
  Done by USGS
3DHP
  Validated & accepted by USGS
  Seamless with existing 3DHP
  Links to Internet of Water
  Allows addressing of local data & old NHD data through HydroAdd3D tool (coming soon

## Slide 47: 3DHP data interoperability
Connection to groundwater
Support Internet of Water
Align with National Wetlands Inventory
Enhance inclusion of engineered hydrologic systems
Greater compatibility with other data such as surficial geology, soils, landcover, transportation networks, and other infrastructure
Better accounting of water cycle and other connections
Notes: Additionally, one of the goals for 3DHP is to align vertically, horizontally, and temporally with elevation data from 3DEP. While working to achieve this goal, we are also communicating with other agencies who are the authoritative agents for related datasets, like the Fish and Wildlife Service for the National Wetlands Inventory and Army Corps for the National Inventory of Dams, to ensure adoption of a new data model that is consistent with the requirements for their programs. Already, we are seeing data alignments for features who meet the data acquisition requirements for both 3DHP and NWI.

## Slide 48: Governance
3DHP Working Group
BLM
EPA
FEMA
FPAC (NRCS)
FWS
NOAA-NWS
NPS
NRCS
NSGIC
USACE
USBR
USFS
USGS
Improve the currency and accuracy of National hydrography mapping
Maximize available funding to support national and agency-specific goals
Part of future 3DNTM joint governance for 3D Nation
Notes: At the Federal level, there is a 3DHP Working Group that is comprised of the membership you see here. Each of these agencies are invested in ensuring that data produced through 3DHP is relevant and accurately mapped. Together, we share our priorities not only in geographic coverage area but also across mission goals for our respective agencies.
12 member agencies working to move forward together with common purpose

## Slide 49: Data lifecycle
Planning
Federal, state, tribal, local or private entities partner on an area of interest
USGS and/or partners plan the project & award a task order
Acquisition
Contractors acquire and process data
Validation
USGS validates data & produces standard 3DHP products
Access
Users access analysis-ready data through web services or download
Publication
USGS publishes 3DHP data on The National Map
Over $ 1B in annual benefits to the Nation if hydrography data needs are met (HRBS, 2016)