Survey of LIDAR Ground Control and Checkpoints for the Denver Area USGS AOI.

SURVEY REPORT

Field Measurement by:	Steven A. Wood

For:		Sanborn Mapping

Field Measurement Date;	May 28 thru June 05, 2020

PROJECT LOCATION MAP

We were provided proposed locations selected to obtain LIDAR GCP gps truthing NVA and VVA x,y,z locations, GCP, and 2020_GCP locations for survey control for the Denver Area AOIs. The schematic is as below.  As we completed the measurements the locations were adjusted as necessary based on our ability to access each and the SV conditions at each.

Project Kick off and Control Staging

Survey crews arrived on site May 27, 2020.  Two additional crews were added to the survey team over the ensuing days. Each day following they set out to measure GCP locations and the process was a combination of using the using a fully static gps measured network tied to the local NGS CORS station and temporary bases throughout the AOI and working mostly within the confines of public access areas or where and when we had access to private property. The weather was favorable for the most part during the survey.  Initial field work was completed on the evening of June 05, 2020.

LOCATION METHODS, MEASUREMENTS AND EQUIPMENT

The equipment configuration for this project consists of industry standard gps surveying equipment.  The gps equipment used was a combination of Topcon dual frequency(L1/L2) receivers.  The Topcon receivers are the Hiper GD, Hiper Plus and HIPER SR models. Topcon Tools gps processing software was used to post process all observed gps data. Each gps observation was logged for site id, receiver type, height of antenna, start time and date.  Length of vector, time of day, SV configuration and site obstructions determined the length of observation at each site. Data was downloaded to the PC after each day’s sessions.  Initial processing was performed to verify we had good vector solutions between sites.

There are NGS CORS station located in or within close proximity to the AOI. A secondary CORs type base from Leica Smartnet RTN was also used.

The coordinate datum is as described below:

Horizontal and Vertical Control:

Data shall be referenced to NAD83(2011) Colorado State Plane Central (FIPS 0502) and Colorado State Plane North (FIPS 0501) in US Foot units, and NAVD88 orthometric heights in US Foot units based on GEOID 18  model from National Geodetic Survey.

The Topcon Tools processing software reports on static observations the horizontal and vertical precision of every vector measured and summarizes the standard deviation in x, y and z position for each individual control point.

Three field crews were utilized to obtain the GCP data.  Typically a base station was running and the crews performed with a rover tying the primary vector back to the base.  When multiple bases were running simultaneously the rover vector could be processed to both bases, and therefore the network triangle strength was heightened significantly with all the redundant data.

The Topcon Tools processing software summarizes the observed vectors, the raw vector horizontal and vertical RMSE components and the corresponding Residual in northing easting and elevation.  Upon final adjustment each point in the network has its corresponding RMSE standard deviation in all 3 directions.  We included all points in each daily report.

The points were preselected in the office and grouped into 3 categories. GCP for control check calibration points, NVA for non vegetation area points and VVA for vegetation area points.

The survey used several NGS CORS and Leica Smartnet CORS type base stations for the control datum origin monuments. They are summarized in the listing herein. All of them fit together great with one major exception.  NGS CORS station ZDV1 located near north central Denver data sheet has its published values per NGS.  The horizontal position fits with all the other CORS in the area BUT the vertical values published does not fit by 1.3 feet

A small network in the coords listing is included in the coordinate summary.  In the network we held NGS points and Leica Smartnet points and tried checking into ZDV1 and also another NGS CORS station in Fort Collins.  ZDV1 does not fit vertically yet COFC in Fort Collins does.

Consequently NGS CORS ZDV1 was not used in final adjustment of our gps survey.

The full Topcon Adjust Report is included herewith in one composite spreadsheet containing each days worth of gps observations. This spreadsheet is included separately from this report.

A composite coordinate summary spreadsheet is also included herewith to facilitate data retrieval and formatting for the all control and LIDAR QC processing.

We took pictures of the survey points and they are labeled by their unique GCP number and then a post script designation such as _1,  _2 or _3 on some PID points

Final documents were completed and are as shown in the composite summary spreadsheet attached separately. It lists all survey points on CO SPCS Central Zone and on CO SPCS North.

## COORDINATE SUMMARY

| Denver Area USGS LIDAR QC Swood | 6/21/2020 |  |
| --- | --- | --- |
| NGS and Smartnet LEICA CORS Network Discrepancy |  |
| CO SPCS Central Zone, NAD83, 2011, NAVD88, Geoid 18, USFoot |  |
| Name | Grid Northing (USft) | Grid Easting (USft) | Elevation (USft) |  |
| ZDV1 | 1857590.331 | 3104167.501 | 5114.218 | NGS CORS |
| P041 | 1770881.433 | 3085725.381 | 5728.278 | NGS CORS |
| CODN | 1726484.795 | 3233651.836 | 5433.529 | Leica CORS |
| ARVA | 1717707.416 | 3115821.463 | 5393.687 | Leica CORS |
| COFC | 2005515.310 | 3094330.634 | 5285.932 | NGS CORS |
| CO SPCS North Zone, NAD83, 2011, NAVD88, Geoid 18, USFoot |  |
| Name | Grid Northing (USft) | Grid Easting (USft) | Elevation (USft) |  |
| ZDV1 | 1311294.229 | 3104150.987 | 5114.218 | NGS CORS |
| P041 | 1224593.760 | 3085718.945 | 5728.278 | NGS CORS |
| CODN | 1180222.174 | 3233644.327 | 5433.529 | Leica CORS |
| ARVA | 1171425.282 | 3115818.687 | 5393.687 | Leica CORS |
| COFC | 1459184.257 | 3094302.182 | 5285.932 | NGS CORS |
| CO SPCS Central Zone, NAD83, 2011, NAVD88, Geoid 18, USFoot |  |
| LIDAR QC Points Central Zone CO SPCS |  |  |
| Name | Grid Northing (USft) | Grid Easting (USft) | Elevation (USft) |  |
| ARVA | 1717707.416 | 3115821.463 | 5393.687 | Leica CORS |
| Base89 | 1936495.173 | 2966981.767 | 8524.724 |  |
| COBK | 1618281.584 | 2845519.498 | 9279.283 | Leica CORS |
| COCC | 1570995.184 | 3178187.574 | 6132.761 | Leica CORS |
| CODN | 1726484.795 | 3233651.836 | 5433.529 | Leica CORS |
| COFC | 2005515.284 | 3094330.640 | 5286.040 | NGS CORS |
| COGW | 1647693.251 | 3172752.186 | 5718.178 | Leica CORS |
| COWI | 1759086.460 | 2919743.169 | 8844.098 | Leica CORS |
| CTMC | 1687841.270 | 3086394.060 | 6022.264 | Leica CORS |
| GCP001 | 2077977.093 | 2977334.145 | 8275.460 |  |
| GCP002 | 2043054.237 | 2969286.138 | 7297.961 |  |
| GCP002X | 2043061.895 | 2969541.259 | 7292.199 |  |
| GCP003 | 2048077.021 | 2937171.799 | 7726.856 |  |
| GCP004 | 1936565.943 | 2967028.163 | 8529.676 |  |
| GCP005 | 1939620.929 | 2934896.868 | 12092.804 |  |
| GCP006 | 1860638.301 | 2992480.541 | 8523.461 |  |
| GCP007 | 1837019.633 | 2998009.726 | 8565.036 |  |
| GCP008 | 1805840.649 | 2995422.878 | 9290.013 |  |
| GCP009 | 1774901.566 | 2997196.737 | 8231.691 |  |
| GCP010 | 1728007.431 | 2994236.992 | 8905.167 |  |
| GCP011 | 1695162.704 | 2997640.718 | 7502.686 |  |
| GCP012 | 1701745.339 | 2955324.968 | 8283.249 |  |
| GCP013 | 1703148.849 | 2932278.031 | 9122.107 |  |
| GCP013X | 1703160.897 | 2932235.347 | 9124.085 |  |
| GCP014 | 1707710.873 | 2917761.262 | 9650.808 |  |
| GCP015 | 1715657.327 | 2922119.344 | 11311.621 |  |
| GCP016 | 1745891.569 | 2927946.456 | 9208.770 |  |
| GCP017R | 1752376.276 | 2930817.726 | 9987.467 |  |
| GCP018 | 1769248.275 | 2912307.934 | 8571.443 |  |
| GCP019 | 1786646.513 | 2900986.108 | 8365.492 |  |
| GCP020 | 1810034.426 | 2811253.667 | 7600.602 |  |
| GCP021 | 1806112.364 | 2772669.158 | 7372.986 |  |
| GCP022 | 1723688.431 | 2802774.042 | 8061.337 |  |
| GCP023 | 1672221.164 | 2877019.844 | 11148.688 |  |
| GCP024 | 1678190.997 | 2936475.139 | 9118.988 |  |
| GCP025 | 1663953.142 | 2972995.108 | 10677.358 |  |
| GCP026 | 1656885.524 | 3051820.036 | 7025.254 |  |
| GCP027 | 1595053.468 | 3029124.707 | 8447.944 |  |
| GCP028 | 1609861.895 | 3130155.946 | 5612.582 |  |
| GCP029A | 1499794.068 | 3162764.749 | 6862.802 |  |
| GCP030 | 1508816.856 | 3226796.752 | 6829.522 |  |
| GCP031 | 1568125.060 | 3210954.507 | 6142.088 |  |
| GCP032 | 1627807.923 | 3196104.526 | 5793.880 |  |
| GCP033 | 1632309.399 | 3235659.538 | 6159.138 |  |
| GCP034 | 1658599.235 | 3258180.486 | 5985.874 |  |
| GCP035 | 1696473.147 | 3300047.355 | 5517.125 |  |
| GCP036 | 1791559.431 | 3335539.063 | 4945.046 |  |
| GCP036B | 1771244.177 | 3336022.346 | 4999.151 |  |
| GCP037 | 1790881.089 | 3277732.341 | 5069.518 |  |
| GCP038 | 1790344.003 | 3240765.806 | 5137.603 |  |
| GCP038B | 1790443.554 | 3240836.371 | 5134.648 |  |
| GCP039 | 1748363.634 | 3257334.500 | 5327.655 |  |
| GCP040 | 1726121.824 | 3204232.535 | 5321.152 |  |
| GCP041 | 1785412.380 | 3189902.951 | 4973.876 |  |
| GCP042 | 1821968.510 | 3159527.708 | 5040.686 |  |
| GCP044 | 1863779.932 | 3111270.777 | 5071.749 |  |
| GCP044A | 1867396.337 | 3147526.824 | 4967.966 |  |
| GCP045 | 1870039.819 | 3065564.695 | 5323.472 |  |
| GCP046 | 1851401.270 | 3033959.332 | 6761.810 |  |
| GCP047 | 1811861.640 | 3062638.755 | 5519.646 |  |
| GCP048 | 1740448.720 | 3072837.675 | 6245.114 |  |
| GCP049 | 1821958.268 | 3090113.120 | 5124.368 |  |
| GCP050R | 1687172.262 | 3085515.024 | 5991.441 |  |
| GCP051 | 1629678.316 | 3142849.358 | 5581.181 |  |
| GCP052 | 1631342.329 | 3176463.426 | 5859.856 |  |
| GCP053 | 1657622.308 | 3215508.269 | 5804.844 |  |
| GCP054 | 1711341.697 | 3169738.889 | 5238.966 |  |
| GCP055 | 1758392.584 | 3144757.998 | 5372.707 |  |
| GCP056R | 1836290.674 | 2993912.192 | 8669.528 |  |
| GCP057R | 1763386.499 | 2928799.713 | 9477.212 |  |
| NVA001 | 2077947.074 | 2977353.164 | 8273.911 |  |
| NVA002 | 2081558.302 | 2957561.493 | 8943.443 |  |
| NVA003 | 2043130.234 | 2969317.355 | 7300.262 |  |
| NVA004 | 2043938.847 | 2952175.092 | 7593.037 |  |
| NVA005 | 2047837.677 | 2937309.470 | 7722.440 |  |
| NVA006 | 1936571.413 | 2966895.762 | 8532.645 |  |
| NVA007 | 1932639.181 | 2956785.613 | 9390.821 |  |
| NVA008 | 1933285.801 | 2941115.370 | 11729.320 |  |
| NVA009 | 1939576.345 | 2934952.744 | 12094.706 |  |
| NVA010 | 1879271.040 | 2990036.291 | 8634.983 |  |
| NVA010X | 1879281.183 | 2990081.343 | 8637.710 |  |
| NVA011 | 1860723.616 | 2992294.032 | 8533.662 |  |
| NVA012 | 1850036.869 | 3010780.479 | 8146.217 |  |
| NVA013 | 1837040.073 | 2998000.736 | 8564.789 |  |
| NVA014 | 1816700.696 | 2999206.382 | 9269.737 |  |
| NVA015 | 1818345.307 | 2990466.560 | 10062.069 |  |
| NVA016 | 1805790.401 | 2995453.315 | 9291.741 |  |
| NVA017R | 1836220.905 | 2994140.950 | 8660.334 |  |
| NVA018 | 1795636.882 | 2997420.071 | 9037.761 |  |
| NVA019 | 1788272.400 | 3000546.556 | 8511.977 |  |
| NVA020 | 1774837.420 | 2997293.549 | 8233.750 |  |
| NVA021 | 1757437.113 | 2999992.885 | 8434.307 |  |
| NVA022 | 1742511.607 | 3010277.049 | 8999.743 |  |
| NVA023 | 1726294.439 | 3025291.307 | 8307.090 |  |
| NVA024 | 1728065.522 | 2994223.538 | 8908.083 |  |
| NVA025 | 1692919.278 | 3032448.847 | 6831.607 |  |
| NVA026 | 1684271.161 | 3051414.860 | 7662.193 |  |
| NVA027 | 1703540.431 | 2971355.618 | 7948.181 |  |
| NVA028 | 1701425.441 | 2954927.988 | 8269.381 |  |
| NVA029 | 1702872.428 | 2938097.859 | 8785.672 |  |
| NVA030R | 1706198.457 | 2909354.143 | 10027.923 |  |
| NVA031 | 1715614.228 | 2922112.581 | 11310.128 |  |
| NVA032 | 1726464.521 | 2927289.661 | 9761.964 |  |
| NVA033 | 1745664.785 | 2928493.862 | 9207.902 |  |
| NVA034R | 1752089.988 | 2931166.276 | 10005.712 |  |
| NVA035 | 1763022.000 | 2919234.019 | 8712.512 |  |
| NVA036 | 1769202.188 | 2912297.799 | 8573.356 |  |
| NVA037R | 1763323.516 | 2928733.056 | 9478.490 |  |
| NVA037R2 | 1763338.980 | 2928707.415 | 9477.799 |  |
| NVA038 | 1786790.161 | 2901371.942 | 8335.066 |  |
| NVA039 | 1792722.099 | 2881982.867 | 8600.890 |  |
| NVA040 | 1809857.559 | 2810774.494 | 7585.038 |  |
| NVA042 | 1806090.703 | 2772676.246 | 7373.752 |  |
| NVA043 | 1757210.651 | 2769482.522 | 7840.229 |  |
| NVA044 | 1736721.573 | 2792822.267 | 7996.108 |  |
| NVA045 | 1723583.389 | 2803222.660 | 8065.959 |  |
| NVA046 | 1667413.532 | 2865317.762 | 10292.519 |  |
| NVA047 | 1672183.214 | 2877035.646 | 11147.458 |  |
| NVA048 | 1678195.852 | 2934288.084 | 9149.801 |  |
| NVA049 | 1686160.986 | 2945041.524 | 8487.143 |  |
| NVA050 | 1695157.041 | 2999942.974 | 7485.750 |  |
| NVA051 | 1663889.035 | 2973020.117 | 10681.356 |  |
| NVA052 | 1667397.539 | 2971239.455 | 10474.531 |  |
| NVA053 | 1673459.962 | 2994498.532 | 10683.216 |  |
| NVA054 | 1670455.176 | 3015640.645 | 9198.665 |  |
| NVA055 | 1673520.134 | 3038011.356 | 7749.424 |  |
| NVA056 | 1656962.203 | 3051905.662 | 7019.156 |  |
| NVA057 | 1595166.741 | 3029150.095 | 8446.129 |  |
| NVA058 | 1625981.211 | 3070589.384 | 7921.059 |  |
| NVA059 | 1649787.435 | 3089838.277 | 6087.653 |  |
| NVA060 | 1629782.725 | 3130213.693 | 5408.715 |  |
| NVA061 | 1609889.097 | 3130182.913 | 5612.507 |  |
| NVA062 | 1584471.712 | 3152175.683 | 5833.960 |  |
| NVA063 | 1512929.544 | 3153891.803 | 6443.566 |  |
| NVA064 | 1499788.380 | 3162707.464 | 6861.676 |  |
| NVA065 | 1513767.364 | 3175584.764 | 6618.639 |  |
| NVA066 | 1508764.904 | 3226800.902 | 6830.588 |  |
| NVA067 | 1551459.898 | 3216745.321 | 6615.068 |  |
| NVA068 | 1568124.113 | 3210902.774 | 6140.667 |  |
| NVA069 | 1627541.235 | 3196267.705 | 5786.679 |  |
| NVA070 | 1632321.286 | 3236335.431 | 6173.999 |  |
| NVA071 | 1632214.613 | 3250282.947 | 5952.881 |  |
| NVA072 | 1658599.845 | 3258118.838 | 5985.916 |  |
| NVA073 | 1697439.687 | 3252689.872 | 5528.374 |  |
| NVA074 | 1696563.046 | 3300047.259 | 5516.284 |  |
| NVA075 | 1753788.021 | 3315238.314 | 5178.984 |  |
| NVA076 | 1748392.718 | 3258581.726 | 5336.627 |  |
| NVA077 | 1791569.591 | 3335591.220 | 4943.534 |  |
| NVA078 | 1790905.016 | 3278457.153 | 5060.114 |  |
| NVA079 | 1789897.325 | 3240809.290 | 5142.636 |  |
| NVA080 | 1785414.330 | 3210200.631 | 5102.306 |  |
| NVA081 | 1811562.110 | 3229946.529 | 4940.925 |  |
| NVA082 | 1811433.749 | 3210825.397 | 5142.962 |  |
| NVA083 | 1811143.369 | 3193300.725 | 4933.116 |  |
| NVA084 | 1821430.533 | 3177007.528 | 4946.423 |  |
| NVA085 | 1822016.537 | 3159536.208 | 5040.694 |  |
| NVA086 | 1863764.531 | 3168791.629 | 4793.592 |  |
| NVA087 | 1867396.588 | 3147551.804 | 4967.953 |  |
| NVA088 | 1864343.096 | 3124376.136 | 4994.121 |  |
| NVA089 | 1884705.670 | 3116309.555 | 5128.213 |  |
| NVA090 | 1863822.942 | 3111279.332 | 5071.908 |  |
| NVA091 | 1863338.178 | 3083984.755 | 5183.907 |  |
| NVA092 | 1870008.442 | 3065527.410 | 5322.103 |  |
| NVA093 | 1887250.381 | 3040828.453 | 6777.769 |  |
| NVA094 | 1851362.038 | 3033959.903 | 6760.459 |  |
| NVA095 | 1850075.248 | 3065156.163 | 5639.562 |  |
| NVA096 | 1836146.225 | 3061185.687 | 5559.893 |  |
| NVA097 | 1811895.186 | 3062761.071 | 5516.752 |  |
| NVA098 | 1794920.201 | 3049402.148 | 5771.547 |  |
| NVA099 | 1759227.548 | 3094727.753 | 5654.191 |  |
| NVA100 | 1795526.165 | 3111082.286 | 5248.345 |  |
| NVA100X | 1795477.485 | 3110995.451 | 5249.801 |  |
| NVA101 | 1839478.223 | 3101229.706 | 5032.710 |  |
| NVA102 | 1821193.423 | 3134992.922 | 5004.847 |  |
| NVA103 | 1782465.214 | 3132896.196 | 5347.532 |  |
| NVA104 | 1770268.614 | 3106011.213 | 5336.157 |  |
| NVA105 | 1739778.709 | 3116907.893 | 5432.246 |  |
| NVA106 | 1690319.776 | 3125474.711 | 5320.613 |  |
| NVA106X | 1690023.792 | 3125019.783 | 5332.380 |  |
| NVA107 | 1687087.564 | 3085357.234 | 5993.590 |  |
| NVA108 | 1663600.318 | 3109724.539 | 5514.584 |  |
| NVA109 | 1663448.599 | 3164847.279 | 5569.765 |  |
| NVA110 | 1631277.502 | 3176546.183 | 5860.856 |  |
| NVA111 | 1646230.600 | 3222092.738 | 6030.494 |  |
| NVA112 | 1696806.312 | 3221195.043 | 5510.991 |  |
| NVA113 | 1707180.399 | 3193509.535 | 5381.232 |  |
| NVA114 | 1711368.632 | 3169781.061 | 5239.600 |  |
| NVA115 | 1737360.427 | 3173142.024 | 5133.376 |  |
| NVA116 | 1756427.394 | 3188505.677 | 5087.794 |  |
| NVA117 | 1758092.579 | 3183145.895 | 5063.951 |  |
| NVA118 | 1758072.588 | 3161571.257 | 5221.680 |  |
| NVA119 | 1768313.462 | 3151603.710 | 5229.181 |  |
| NVA120 | 1758455.623 | 3144777.915 | 5372.140 |  |
| P041 | 1770881.433 | 3085725.381 | 5728.278 | NGS CORS |
| TMGO | 1836949.511 | 3074751.795 | 5543.897 | NGS CORS |
| VVA001 | 2077924.139 | 2977322.222 | 8273.685 |  |
| VVA002 | 2081533.905 | 2957618.277 | 8941.294 |  |
| VVA003 | 2043146.025 | 2969388.558 | 7300.994 |  |
| VVA004 | 2047857.318 | 2937355.416 | 7721.875 |  |
| VVA005 | 1936502.373 | 2966958.753 | 8525.991 |  |
| VVA006 | 1879395.556 | 2990047.670 | 8646.606 |  |
| VVA007 | 1860702.680 | 2992548.599 | 8530.479 |  |
| VVA008 | 1849981.517 | 3010785.252 | 8155.379 |  |
| VVA009 | 1837049.659 | 2997954.714 | 8566.099 |  |
| VVA010 | 1818433.616 | 2990438.581 | 10063.273 |  |
| VVA011 | 1795641.842 | 2997480.787 | 9044.567 |  |
| VVA012 | 1785830.588 | 3002368.331 | 8285.236 |  |
| VVA013 | 1774959.615 | 2997967.281 | 8208.278 |  |
| VVA014 | 1757407.326 | 3000012.171 | 8442.397 |  |
| VVA015 | 1742550.288 | 3010293.485 | 9005.288 |  |
| VVA016 | 1726341.428 | 3025296.332 | 8305.832 |  |
| VVA017 | 1727989.634 | 2994176.184 | 8903.497 |  |
| VVA018 | 1692909.200 | 3032479.533 | 6830.503 |  |
| VVA019 | 1684300.659 | 3051457.820 | 7659.176 |  |
| VVA020R | 1695257.529 | 2997748.550 | 7500.625 |  |
| VVA021 | 1703538.479 | 2971396.623 | 7947.785 |  |
| VVA022 | 1701638.677 | 2954872.777 | 8296.801 |  |
| VVA023R | 1706278.518 | 2909413.246 | 10036.107 |  |
| VVA024 | 1726437.571 | 2927231.343 | 9764.010 |  |
| VVA025 | 1745721.305 | 2928506.998 | 9210.149 |  |
| VVA026 | 1763115.787 | 2919235.772 | 8710.815 |  |
| VVA027 | 1769160.532 | 2912323.341 | 8575.375 |  |
| VVA028R | 1763379.090 | 2928739.024 | 9476.855 |  |
| VVA029 | 1786897.309 | 2901367.043 | 8335.371 |  |
| VVA030 | 1812876.385 | 2792057.724 | 7422.103 |  |
| VVA031 | 1723830.304 | 2802343.907 | 8054.108 |  |
| VVA032 | 1678204.773 | 2934128.517 | 9154.412 |  |
| VVA033 | 1686198.041 | 2945077.001 | 8485.558 |  |
| VVA034 | 1663906.911 | 2972977.672 | 10680.879 |  |
| VVA034X | 1752134.694 | 2931111.963 | 10002.804 |  |
| VVA035 | 1670523.202 | 3015654.951 | 9196.775 |  |
| VVA036 | 1673511.862 | 3037982.998 | 7751.660 |  |
| VVA037 | 1656975.379 | 3051956.123 | 7018.927 |  |
| VVA038 | 1595081.675 | 3029225.779 | 8444.050 |  |
| VVA039 | 1649723.753 | 3089899.504 | 6090.927 |  |
| VVA040 | 1629745.145 | 3130197.456 | 5409.771 |  |
| VVA041 | 1609861.495 | 3130130.239 | 5612.744 |  |
| VVA042 | 1584442.769 | 3152161.422 | 5832.590 |  |
| VVA043 | 1512963.707 | 3153861.208 | 6442.823 |  |
| VVA044A | 1499762.781 | 3162639.940 | 6862.207 |  |
| VVA045 | 1513792.023 | 3175610.686 | 6617.822 |  |
| VVA046 | 1508693.460 | 3226731.717 | 6828.742 |  |
| VVA047 | 1551584.219 | 3216737.053 | 6613.318 |  |
| VVA048 | 1568137.979 | 3210540.355 | 6126.717 |  |
| VVA049 | 1627962.710 | 3195861.796 | 5805.719 |  |
| VVA050 | 1646226.130 | 3222058.931 | 6032.845 |  |
| VVA051 | 1632180.857 | 3250310.634 | 5952.366 |  |
| VVA052 | 1696807.048 | 3221134.575 | 5509.100 |  |
| VVA053 | 1697411.244 | 3252715.984 | 5528.776 |  |
| VVA054 | 1696676.340 | 3300225.446 | 5517.764 |  |
| VVA055 | 1788952.038 | 3240820.649 | 5154.415 |  |
| VVA056 | 1785345.516 | 3210243.643 | 5102.648 |  |
| VVA057 | 1811210.641 | 3193328.436 | 4932.061 |  |
| VVA058 | 1821612.985 | 3177059.458 | 4945.172 |  |
| VVA059 | 1821993.654 | 3159357.668 | 5039.500 |  |
| VVA060 | 1821221.871 | 3135037.690 | 5005.062 |  |
| VVA061 | 1839449.901 | 3101259.955 | 5033.229 |  |
| VVA062 | 1863891.928 | 3168719.671 | 4792.716 |  |
| VVA063 | 1867393.013 | 3147480.714 | 4970.465 |  |
| VVA064R | 1863724.517 | 3123375.303 | 5016.369 |  |
| VVA065 | 1863823.635 | 3111220.228 | 5072.582 |  |
| VVA066 | 1884644.714 | 3116283.438 | 5127.588 |  |
| VVA067 | 1863375.720 | 3083982.193 | 5182.728 |  |
| VVA068 | 1870061.320 | 3065541.787 | 5324.566 |  |
| VVA069 | 1887195.697 | 3040821.576 | 6775.351 |  |
| VVA070 | 1849990.228 | 3065132.586 | 5643.896 |  |
| VVA071 | 1841992.144 | 3060835.125 | 5651.935 |  |
| VVA072 | 1811799.343 | 3062611.929 | 5520.632 |  |
| VVA073 | 1794849.058 | 3049485.056 | 5764.370 |  |
| VVA074 | 1759196.214 | 3094768.472 | 5655.105 |  |
| VVA075 | 1795406.258 | 3111067.933 | 5252.108 |  |
| VVA075X | 1795503.722 | 3110977.675 | 5248.684 |  |
| VVA076 | 1770260.445 | 3105965.519 | 5337.418 |  |
| VVA077 | 1782370.334 | 3132960.631 | 5357.957 |  |
| VVA078 | 1767886.110 | 3151658.929 | 5233.302 |  |
| VVA078X | 1768134.068 | 3151569.605 | 5229.405 |  |
| VVA079 | 1758010.808 | 3161516.566 | 5220.589 |  |
| VVA080 | 1757846.928 | 3183185.836 | 5061.574 |  |
| VVA081 | 1756539.107 | 3188505.755 | 5089.141 |  |
| VVA082 | 1737138.086 | 3172864.228 | 5131.666 |  |
| VVA083 | 1711325.657 | 3169785.995 | 5239.947 |  |
| VVA084 | 1707140.328 | 3193540.006 | 5380.945 |  |
| VVA085 | 1690413.052 | 3125562.591 | 5317.520 |  |
| VVA085X | 1690037.120 | 3125232.415 | 5331.470 |  |
| VVA086 | 1686998.761 | 3085305.644 | 6010.471 |  |
| VVA087 | 1663557.462 | 3109732.495 | 5515.629 |  |
| VVA088 | 1663353.046 | 3164731.604 | 5575.484 |  |
| VVA089 | 1631334.302 | 3176528.732 | 5862.477 |  |
| VVA090 | 1631800.618 | 3168050.268 | 5765.033 |  |
| VVA091 | 1625981.703 | 3070663.148 | 7912.077 |  |
| VVA092 | 1703513.283 | 2931297.205 | 9182.451 |  |
| ZDV1 | 1857590.292 | 3104167.534 | 5114.215 | NGS CORS |
| CO SPCS North Zone, NAD83, 2011, NAVD88, Geoid 18, USFoot |  |
| LIDAR QC Points North Zone CO SPCS |  |  |
| Name | Grid Northing (USft) | Grid Easting (USft) | Elevation (USft) |  |
| ARVA | 1171425.282 | 3115818.687 | 5393.687 | NGS CORS |
| Base89 | 1390178.846 | 2966989.520 | 8524.724 |  |
| COBK | 1072002.074 | 2845508.484 | 9279.283 | Leica CORS |
| COCC | 1024714.983 | 3178208.332 | 6132.761 | Leica CORS |
| CODN | 1180222.174 | 3233644.327 | 5433.529 | Leica CORS |
| COFC | 1459184.231 | 3094302.188 | 5286.040 | NGS CORS |
| COGW | 1101418.293 | 3172759.650 | 5718.178 | Leica CORS |
| COWI | 1212799.169 | 2919748.284 | 8844.098 | Leica CORS |
| CTMC | 1141556.568 | 3086394.460 | 6022.264 | NGS CORS |
| GCP001 | 1531617.565 | 2977342.578 | 8275.460 |  |
| GCP002 | 1496707.318 | 2969296.523 | 7297.961 |  |
| GCP002X | 1496714.965 | 2969551.558 | 7292.199 |  |
| GCP003 | 1501729.850 | 2937193.348 | 7726.856 |  |
| GCP004 | 1390249.598 | 2967035.907 | 8529.676 |  |
| GCP005 | 1393305.386 | 2934912.351 | 12092.804 |  |
| GCP006 | 1314336.506 | 2992481.756 | 8523.461 |  |
| GCP007 | 1290721.358 | 2998010.002 | 8565.036 |  |
| GCP008 | 1259546.241 | 2995423.376 | 9290.013 |  |
| GCP009 | 1228610.055 | 2997196.958 | 8231.691 |  |
| GCP010 | 1181718.579 | 2994237.187 | 8905.167 |  |
| GCP011 | 1148874.437 | 2997640.723 | 7502.686 |  |
| GCP012 | 1155457.988 | 2955325.358 | 8283.249 |  |
| GCP013 | 1156862.727 | 2932278.712 | 9122.107 |  |
| GCP013X | 1156874.778 | 2932236.030 | 9124.085 |  |
| GCP014 | 1161425.740 | 2917762.447 | 9650.808 |  |
| GCP015 | 1169371.715 | 2922121.061 | 11311.621 |  |
| GCP016 | 1199604.434 | 2927950.135 | 9208.770 |  |
| GCP017R | 1206088.596 | 2930821.690 | 9987.467 |  |
| GCP018 | 1222960.887 | 2912314.379 | 8571.443 |  |
| GCP019 | 1240358.719 | 2900995.040 | 8365.492 |  |
| GCP020 | 1263756.692 | 2811274.912 | 7600.602 |  |
| GCP021 | 1259842.789 | 2772693.864 | 7372.986 |  |
| GCP022 | 1177418.363 | 2802779.870 | 8061.337 |  |
| GCP023 | 1125939.939 | 2877017.428 | 11148.688 |  |
| GCP024 | 1131904.562 | 2936474.259 | 9118.988 |  |
| GCP025 | 1117664.830 | 2972994.366 | 10677.358 |  |
| GCP026 | 1110597.930 | 3051821.811 | 7025.254 |  |
| GCP027 | 1048761.049 | 3029127.425 | 8447.944 |  |
| GCP028 | 1063578.441 | 3130166.267 | 5612.582 |  |
| GCP029A | 953500.627 | 3162794.746 | 6862.802 |  |
| GCP030 | 962536.913 | 3226836.637 | 6829.522 |  |
| GCP031 | 1021850.600 | 3210979.677 | 6142.088 |  |
| GCP032 | 1081536.027 | 3196116.740 | 5793.880 |  |
| GCP033 | 1086045.941 | 3235673.225 | 6159.138 |  |
| GCP034 | 1112342.314 | 3258189.006 | 5985.874 |  |
| GCP035 | 1150228.021 | 3300046.414 | 5517.125 |  |
| GCP036 | 1245320.623 | 3335507.420 | 4945.046 |  |
| GCP036B | 1225007.215 | 3335997.222 | 4999.151 |  |
| GCP037 | 1244625.292 | 3277706.270 | 5069.518 |  |
| GCP038 | 1244079.037 | 3240743.301 | 5137.603 |  |
| GCP038B | 1244178.595 | 3240813.837 | 5134.648 |  |
| GCP039 | 1202105.678 | 3257320.844 | 5327.655 |  |
| GCP040 | 1179853.032 | 3204226.027 | 5321.152 |  |
| GCP041 | 1239137.326 | 3189886.076 | 4973.876 |  |
| GCP042 | 1275684.468 | 3159507.909 | 5040.686 |  |
| GCP044 | 1317483.569 | 3111252.473 | 5071.749 |  |
| GCP044A | 1321103.900 | 3147502.051 | 4967.966 |  |
| GCP045 | 1323738.508 | 3065553.511 | 5323.472 |  |
| GCP046 | 1305101.454 | 3033954.149 | 6761.810 |  |
| GCP047 | 1265568.438 | 3062631.582 | 5519.646 |  |
| GCP048 | 1194161.903 | 3072834.336 | 6245.114 |  |
| GCP049 | 1275665.883 | 3090101.928 | 5124.368 |  |
| GCP050R | 1140887.484 | 3085515.475 | 5991.441 |  |
| GCP051 | 1083397.907 | 3142857.984 | 5581.181 |  |
| GCP052 | 1085067.150 | 3176473.812 | 5859.856 |  |
| GCP053 | 1111355.680 | 3215515.555 | 5804.844 |  |
| GCP054 | 1165067.078 | 3169735.874 | 5238.966 |  |
| GCP055 | 1212112.309 | 3144748.882 | 5372.707 |  |
| GCP056R | 1289992.516 | 2993913.033 | 8669.528 |  |
| GCP057R | 1217098.266 | 2928804.546 | 9477.212 |  |
| NVA001 | 1531587.557 | 2977361.590 | 8273.911 |  |
| NVA002 | 1535198.061 | 2957577.430 | 8943.443 |  |
| NVA003 | 1496783.289 | 2969327.731 | 7300.262 |  |
| NVA004 | 1497592.282 | 2952191.303 | 7593.037 |  |
| NVA005 | 1501490.581 | 2937330.957 | 7722.440 |  |
| NVA006 | 1390255.070 | 2966903.538 | 8532.645 |  |
| NVA007 | 1386324.127 | 2956795.599 | 9390.821 |  |
| NVA008 | 1386971.372 | 2941129.014 | 11729.320 |  |
| NVA009 | 1393260.809 | 2934968.210 | 12094.706 |  |
| NVA010 | 1332966.087 | 2990038.079 | 8634.983 |  |
| NVA010X | 1332976.228 | 2990083.124 | 8637.710 |  |
| NVA011 | 1314421.807 | 2992295.278 | 8533.662 |  |
| NVA012 | 1303736.760 | 3010778.848 | 8146.217 |  |
| NVA013 | 1290741.795 | 2998001.014 | 8564.789 |  |
| NVA014 | 1270405.041 | 2999206.477 | 9269.737 |  |
| NVA015 | 1272049.498 | 2990467.712 | 10062.069 |  |
| NVA016 | 1259495.998 | 2995453.810 | 9291.741 |  |
| NVA017R | 1289922.756 | 2994141.759 | 8660.334 |  |
| NVA018 | 1249343.526 | 2997420.326 | 9037.761 |  |
| NVA019 | 1241979.744 | 3000546.506 | 8511.977 |  |
| NVA020 | 1228545.915 | 2997293.763 | 8233.750 |  |
| NVA021 | 1211146.831 | 2999992.886 | 8434.307 |  |
| NVA022 | 1196222.197 | 3010276.557 | 8999.743 |  |
| NVA023 | 1180005.935 | 3025290.490 | 8307.090 |  |
| NVA024 | 1181776.669 | 2994223.734 | 8908.083 |  |
| NVA025 | 1146631.516 | 3032448.838 | 6831.607 |  |
| NVA026 | 1137984.126 | 3051415.273 | 7662.193 |  |
| NVA027 | 1157252.500 | 2971355.918 | 7948.181 |  |
| NVA028 | 1155138.110 | 2954928.368 | 8269.381 |  |
| NVA029 | 1156585.947 | 2938098.465 | 8785.672 |  |
| NVA030R | 1159914.041 | 2909355.317 | 10027.923 |  |
| NVA031 | 1169328.617 | 2922114.294 | 11310.128 |  |
| NVA032 | 1180178.241 | 2927292.018 | 9761.964 |  |
| NVA033 | 1199377.625 | 2928497.498 | 9207.902 |  |
| NVA034R | 1205802.301 | 2931170.201 | 10005.712 |  |
| NVA035 | 1216734.490 | 2919239.472 | 8712.512 |  |
| NVA036 | 1222914.804 | 2912304.240 | 8573.356 |  |
| NVA037R | 1217035.292 | 2928737.889 | 9478.490 |  |
| NVA037R2 | 1217050.756 | 2928712.251 | 9477.799 |  |
| NVA038 | 1240502.318 | 2901380.853 | 8335.066 |  |
| NVA039 | 1246435.724 | 2881994.201 | 8600.890 |  |
| NVA040 | 1263579.932 | 2810795.760 | 7585.038 |  |
| NVA042 | 1259821.129 | 2772700.948 | 7373.752 |  |
| NVA043 | 1210945.911 | 2769496.732 | 7840.229 |  |
| NVA044 | 1190452.977 | 2792830.975 | 7996.108 |  |
| NVA045 | 1177313.240 | 2803228.455 | 8065.959 |  |
| NVA046 | 1121133.644 | 2865314.494 | 10292.519 |  |
| NVA047 | 1125901.986 | 2877033.226 | 11147.458 |  |
| NVA048 | 1131909.553 | 2934287.174 | 9149.801 |  |
| NVA049 | 1139874.145 | 2945041.182 | 8487.143 |  |
| NVA050 | 1148868.771 | 2999942.975 | 7485.750 |  |
| NVA051 | 1117600.720 | 2973019.374 | 10681.356 |  |
| NVA052 | 1121109.363 | 2971238.760 | 10474.531 |  |
| NVA053 | 1127171.534 | 2994498.431 | 10683.216 |  |
| NVA054 | 1124166.790 | 3015640.977 | 9198.665 |  |
| NVA055 | 1127232.384 | 3038012.052 | 7749.424 |  |
| NVA056 | 1110674.616 | 3051907.436 | 7019.156 |  |
| NVA057 | 1048874.333 | 3029152.813 | 8446.129 |  |
| NVA058 | 1079693.198 | 3070593.889 | 7921.059 |  |
| NVA059 | 1103502.150 | 3089841.968 | 6087.653 |  |
| NVA060 | 1083500.673 | 3130221.540 | 5408.715 |  |
| NVA061 | 1063605.648 | 3130193.234 | 5612.507 |  |
| NVA062 | 1038188.898 | 3152191.446 | 5833.960 |  |
| NVA063 | 966637.109 | 3153918.239 | 6443.566 |  |
| NVA064 | 953494.930 | 3162737.451 | 6861.676 |  |
| NVA065 | 967478.474 | 3175614.794 | 6618.639 |  |
| NVA066 | 962484.952 | 3226840.799 | 6830.588 |  |
| NVA067 | 1005184.489 | 3216774.629 | 6615.068 |  |
| NVA068 | 1021849.643 | 3210927.938 | 6140.667 |  |
| NVA069 | 1081269.352 | 3196279.979 | 5786.679 |  |
| NVA070 | 1086057.981 | 3236349.156 | 6173.999 |  |
| NVA071 | 1085954.547 | 3250297.518 | 5952.881 |  |
| NVA072 | 1112342.909 | 3258127.355 | 5985.916 |  |
| NVA073 | 1151182.013 | 3252688.805 | 5528.374 |  |
| NVA074 | 1150317.919 | 3300046.292 | 5516.284 |  |
| NVA075 | 1207545.691 | 3315220.006 | 5178.984 |  |
| NVA076 | 1202135.069 | 3258567.997 | 5336.627 |  |
| NVA077 | 1245330.799 | 3335559.569 | 4943.534 |  |
| NVA078 | 1244649.411 | 3278431.009 | 5060.114 |  |
| NVA079 | 1243632.411 | 3240786.885 | 5142.636 |  |
| NVA080 | 1239143.181 | 3210181.962 | 5102.306 |  |
| NVA081 | 1265292.508 | 3229920.333 | 4940.925 |  |
| NVA082 | 1265160.104 | 3210801.394 | 5142.962 |  |
| NVA083 | 1264866.347 | 3193278.763 | 4933.116 |  |
| NVA084 | 1275149.391 | 3176985.658 | 4946.423 |  |
| NVA085 | 1275732.491 | 3159516.401 | 5040.694 |  |
| NVA086 | 1317475.941 | 3168763.883 | 4793.592 |  |
| NVA087 | 1321104.154 | 3147527.026 | 4967.953 |  |
| NVA088 | 1318048.130 | 3124355.611 | 4994.121 |  |
| NVA089 | 1338406.210 | 3116288.075 | 5128.213 |  |
| NVA090 | 1317526.573 | 3111261.023 | 5071.908 |  |
| NVA091 | 1317039.317 | 3083970.973 | 5183.907 |  |
| NVA092 | 1323707.135 | 3065516.234 | 5322.103 |  |
| NVA093 | 1340944.722 | 3040820.810 | 6777.769 |  |
| NVA094 | 1305062.228 | 3033954.721 | 6760.459 |  |
| NVA095 | 1303777.124 | 3065146.303 | 5639.562 |  |
| NVA096 | 1289849.873 | 3061177.249 | 5559.893 |  |
| NVA097 | 1265601.988 | 3062753.882 | 5516.752 |  |
| NVA098 | 1248628.087 | 3049397.296 | 5771.547 |  |
| NVA099 | 1212941.464 | 3094721.705 | 5654.191 |  |
| NVA100 | 1249238.753 | 3111071.319 | 5248.345 |  |
| NVA100X | 1249190.070 | 3110984.497 | 5249.801 |  |
| NVA101 | 1293184.541 | 3101215.425 | 5032.710 |  |
| NVA102 | 1274905.998 | 3134976.263 | 5004.847 |  |
| NVA103 | 1236181.568 | 3132884.749 | 5347.532 |  |
| NVA104 | 1223982.857 | 3106003.320 | 5336.157 |  |
| NVA105 | 1193495.937 | 3116902.615 | 5432.246 |  |
| NVA106 | 1144039.050 | 3125475.001 | 5320.613 |  |
| NVA106X | 1143743.011 | 3125020.107 | 5332.380 |  |
| NVA107 | 1140802.773 | 3085357.691 | 5993.590 |  |
| NVA108 | 1117317.410 | 3109727.598 | 5514.584 |  |
| NVA109 | 1117172.932 | 3164851.914 | 5569.765 |  |
| NVA110 | 1085002.334 | 3176556.586 | 5860.856 |  |
| NVA111 | 1099964.897 | 3222102.672 | 6030.494 |  |
| NVA112 | 1150541.486 | 3221194.224 | 5510.991 |  |
| NVA113 | 1160909.985 | 3193506.880 | 5381.232 |  |
| NVA114 | 1165094.019 | 3169778.041 | 5239.600 |  |
| NVA115 | 1191085.590 | 3173134.626 | 5133.376 |  |
| NVA116 | 1210154.245 | 3188494.178 | 5087.794 |  |
| NVA117 | 1211818.371 | 3183134.427 | 5063.951 |  |
| NVA118 | 1211794.808 | 3161561.136 | 5221.680 |  |
| NVA119 | 1222033.493 | 3151592.718 | 5229.181 |  |
| NVA120 | 1212175.347 | 3144768.788 | 5372.140 |  |
| P041 | 1224593.760 | 3085718.945 | 5728.278 | NGS CORS |
| TMGO | 1290653.936 | 3074741.430 | 5543.897 | NGS CORS |
| VVA001 | 1531564.630 | 2977330.659 | 8273.685 |  |
| VVA002 | 1535173.672 | 2957634.192 | 8941.294 |  |
| VVA003 | 1496799.072 | 2969398.911 | 7300.994 |  |
| VVA004 | 1501510.212 | 2937376.888 | 7721.875 |  |
| VVA005 | 1390186.045 | 2966966.511 | 8525.991 |  |
| VVA006 | 1333090.581 | 2990049.458 | 8646.606 |  |
| VVA007 | 1314400.873 | 2992549.803 | 8530.479 |  |
| VVA008 | 1303681.417 | 3010783.621 | 8155.379 |  |
| VVA009 | 1290751.380 | 2997954.998 | 8566.099 |  |
| VVA010 | 1272137.796 | 2990439.737 | 10063.273 |  |
| VVA011 | 1249348.486 | 2997481.036 | 9044.567 |  |
| VVA012 | 1239538.156 | 3002368.120 | 8285.236 |  |
| VVA013 | 1228668.098 | 2997967.442 | 8208.278 |  |
| VVA014 | 1211117.047 | 3000012.170 | 8442.397 |  |
| VVA015 | 1196260.876 | 3010292.992 | 9005.288 |  |
| VVA016 | 1180052.922 | 3025295.514 | 8305.832 |  |
| VVA017 | 1181700.783 | 2994176.382 | 8903.497 |  |
| VVA018 | 1146621.438 | 3032479.525 | 6830.503 |  |
| VVA019 | 1138013.627 | 3051458.232 | 7659.176 |  |
| VVA020R | 1148969.261 | 2997748.555 | 7500.625 |  |
| VVA021 | 1157250.547 | 2971396.922 | 7947.785 |  |
| VVA022 | 1155351.347 | 2954873.167 | 8296.801 |  |
| VVA023R | 1159994.096 | 2909414.427 | 10036.107 |  |
| VVA024 | 1180151.296 | 2927233.700 | 9764.010 |  |
| VVA025 | 1199434.140 | 2928510.637 | 9210.149 |  |
| VVA026 | 1216828.271 | 2919241.232 | 8710.815 |  |
| VVA027 | 1222873.150 | 2912329.777 | 8575.375 |  |
| VVA028R | 1217090.862 | 2928743.861 | 9476.855 |  |
| VVA029 | 1240609.457 | 2901375.964 | 8335.371 |  |
| VVA030 | 1266601.994 | 2792081.688 | 7422.103 |  |
| VVA031 | 1177560.313 | 2802349.774 | 8054.108 |  |
| VVA032 | 1131918.484 | 2934127.605 | 9154.412 |  |
| VVA033 | 1139911.199 | 2945076.662 | 8485.558 |  |
| VVA034 | 1117618.598 | 2972976.928 | 10680.879 |  |
| VVA034X | 1205847.008 | 2931115.894 | 10002.804 |  |
| VVA035 | 1124234.818 | 3015655.282 | 9196.775 |  |
| VVA036 | 1127224.111 | 3037983.694 | 7751.660 |  |
| VVA037 | 1110687.794 | 3051957.898 | 7018.927 |  |
| VVA038 | 1048789.261 | 3029228.506 | 8444.050 |  |
| VVA039 | 1103438.471 | 3089903.202 | 6090.927 |  |
| VVA040 | 1083463.088 | 3130205.307 | 5409.771 |  |
| VVA041 | 1063578.038 | 3130140.559 | 5612.744 |  |
| VVA042 | 1038159.950 | 3152177.188 | 5832.590 |  |
| VVA043 | 966671.274 | 3153887.633 | 6442.823 |  |
| VVA044A | 953469.315 | 3162669.919 | 6862.207 |  |
| VVA045 | 967503.142 | 3175640.716 | 6617.822 |  |
| VVA046 | 962413.480 | 3226771.617 | 6828.742 |  |
| VVA047 | 1005308.825 | 3216766.335 | 6613.318 |  |
| VVA048 | 1021863.438 | 3210565.473 | 6126.717 |  |
| VVA049 | 1081690.778 | 3195873.966 | 5805.719 |  |
| VVA050 | 1099960.419 | 3222068.865 | 6032.845 |  |
| VVA051 | 1085920.795 | 3250325.214 | 5952.366 |  |
| VVA052 | 1150542.209 | 3221133.755 | 5509.100 |  |
| VVA053 | 1151153.576 | 3252714.924 | 5528.776 |  |
| VVA054 | 1150431.264 | 3300224.446 | 5517.764 |  |
| VVA055 | 1242687.213 | 3240798.461 | 5154.415 |  |
| VVA056 | 1239074.382 | 3210224.984 | 5102.648 |  |
| VVA057 | 1264933.617 | 3193306.459 | 4932.061 |  |
| VVA058 | 1275331.830 | 3177037.550 | 4945.172 |  |
| VVA059 | 1275709.584 | 3159337.886 | 5039.500 |  |
| VVA060 | 1274934.447 | 3135021.022 | 5005.062 |  |
| VVA061 | 1293156.225 | 3101245.672 | 5033.229 |  |
| VVA062 | 1317603.305 | 3168691.916 | 4792.716 |  |
| VVA063 | 1321100.570 | 3147455.948 | 4970.465 |  |
| VVA064R | 1317429.533 | 3123355.017 | 5016.369 |  |
| VVA065 | 1317527.259 | 3111201.928 | 5072.582 |  |
| VVA066 | 1338345.263 | 3116261.969 | 5127.588 |  |
| VVA067 | 1317076.853 | 3083968.408 | 5182.728 |  |
| VVA068 | 1323760.004 | 3065530.605 | 5324.566 |  |
| VVA069 | 1340890.048 | 3040813.936 | 6775.351 |  |
| VVA070 | 1303692.116 | 3065122.735 | 5643.896 |  |
| VVA071 | 1295694.950 | 3060826.393 | 5651.935 |  |
| VVA072 | 1265506.147 | 3062604.763 | 5520.632 |  |
| VVA073 | 1248556.955 | 3049480.199 | 5764.370 |  |
| VVA074 | 1212910.136 | 3094762.423 | 5655.105 |  |
| VVA075 | 1249118.857 | 3111056.980 | 5252.108 |  |
| VVA075X | 1249216.301 | 3110966.719 | 5248.684 |  |
| VVA076 | 1223974.684 | 3105957.631 | 5337.418 |  |
| VVA077 | 1236086.704 | 3132949.190 | 5357.957 |  |
| VVA078 | 1221606.180 | 3151647.996 | 5233.302 |  |
| VVA078X | 1221854.107 | 3151558.642 | 5229.405 |  |
| VVA079 | 1211733.023 | 3161506.458 | 5220.589 |  |
| VVA080 | 1211572.742 | 3183174.409 | 5061.574 |  |
| VVA081 | 1210265.951 | 3188494.235 | 5089.141 |  |
| VVA082 | 1190863.213 | 3172856.880 | 5131.666 |  |
| VVA083 | 1165051.046 | 3169782.982 | 5239.947 |  |
| VVA084 | 1160869.919 | 3193537.357 | 5380.945 |  |
| VVA085 | 1144132.337 | 3125562.870 | 5317.520 |  |
| VVA085X | 1143756.364 | 3125232.738 | 5331.470 |  |
| VVA086 | 1140713.965 | 3085306.108 | 6010.471 |  |
| VVA087 | 1117274.554 | 3109735.559 | 5515.629 |  |
| VVA088 | 1117077.357 | 3164736.251 | 5575.484 |  |
| VVA089 | 1085059.134 | 3176539.124 | 5862.477 |  |
| VVA090 | 1085524.081 | 3168060.083 | 5765.033 |  |
| VVA091 | 1079693.695 | 3070667.658 | 7912.077 |  |
| VVA092 | 1157227.222 | 2931297.919 | 9182.451 |  |
| ZDV1 | 1311294.190 | 3104151.020 | 5114.215 | NGS CORS |

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.8

Starting Datasheet Retrieval...

1        National Geodetic Survey,   Retrieval Date = JUNE 20, 2020

DM5962 ***********************************************************************

DM5962  CORS        -  This is a GPS Continuously Operating Reference Station.

DM5962  DESIGNATION -  CDOT GOLDEN CORS ARP

DM5962  CORS_ID     -  CTMC

DM5962  PID         -  DM5962

DM5962  STATE/COUNTY-  CO/JEFFERSON

DM5962  COUNTRY     -  US

DM5962  USGS QUAD   -  MORRISON (2019)

DM5962

DM5962                         *CURRENT SURVEY CONTROL

DM5962  ______________________________________________________________________

DM5962* NAD 83(2011) POSITION- 39 43 17.49312(N) 105 11 34.33565(W)   ADJUSTED

DM5962* NAD 83(2011) ELLIP HT-  1819.842 (meters)        (06/??/19)   ADJUSTED

DM5962* NAD 83(2011) EPOCH   -  2010.00

DM5962  ______________________________________________________________________

DM5962  GEOID HEIGHT    -        -15.748 (meters)                     GEOID18

DM5962  NAD 83(2011) X  - -1,287,787.771 (meters)                     COMP

DM5962  NAD 83(2011) Y  - -4,742,178.369 (meters)                     COMP

DM5962  NAD 83(2011) Z  -  4,055,414.617 (meters)                     COMP

DM5962

DM5962  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

DM5962  Standards:

DM5962         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

DM5962            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

DM5962  -------------------------------------------------------------------

DM5962  NETWORK    0.17   0.41           0.06   0.07   0.21      0.23305400

DM5962  -------------------------------------------------------------------

DM5962

DM5962

DM5962.The coordinates were established by GPS observations

DM5962.and adjusted by the National Geodetic Survey in June 2019.

DM5962

DM5962.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DM5962.been affixed to the stable North American Tectonic Plate.

DM5962

DM5962.The coordinates are valid at the epoch date displayed above

DM5962.which is a decimal equivalence of Year/Month/Day.

DM5962

DM5962.Due to the release of the International GNSS Service (IGS) 2014

DM5962.realization of the International Terrestrial Reference Frame of 2014

DM5962.(ITRF2014), NGS reprocessed all NOAA CORS Network and some IGS stations

DM5962.using data collected between 1/1/1996 and 1/30/2017. The resulting ITRF2014

DM5962.epoch 2010.00 coordinates, referred to as Multi-Year CORS Solution 2

DM5962.(MYCS2), were transformed to NAD 83 (2011/PA11/MA11) maintaining the

DM5962.currently published epoch of 2010.00.

DM5962

DM5962.Additional information on MYCS2 is available at

DM5962.https://geodesy.noaa.gov/CORS/coords.shtml

DM5962

DM5962.Significant digits in the geoid height do not necessarily reflect accuracy.

DM5962.GEOID18 height accuracy estimate available here.

DM5962

DM5962.The PID for the CORS L1 Phase Center is DM5963.

DM5962

DM5962.Click photographs - Photos may exist for this station.

DM5962

DM5962.The XYZ, and position/ellipsoidal ht. are equivalent.

DM5962

DM5962.The ellipsoidal height was determined by GPS observations

DM5962.and is referenced to NAD 83.

DM5962

DM5962. The following values were computed from the NAD 83(2011) position.

DM5962

DM5962;                    North         East     Units Scale Factor Converg.

DM5962;SPC CO C     -   514,455.048   940,734.790   MT  0.99999449   +0 11 37.3

DM5962;SPC CO C     - 1,687,841.27  3,086,394.06   sFT  0.99999449   +0 11 37.3

DM5962;UTM  13      - 4,396,867.838   483,469.900   MT  0.99960336   -0 07 23.7

DM5962

DM5962!             -  Elev Factor  x  Scale Factor =   Combined Factor

DM5962!SPC CO C     -   0.99971458  x   0.99999449  =   0.99970907

DM5962!UTM  13      -   0.99971458  x   0.99960336  =   0.99931805

DM5962

DM5962_U.S. NATIONAL GRID SPATIAL ADDRESS: 13SDD8346996867(NAD 83)

DM5962

DM5962                          SUPERSEDED SURVEY CONTROL

DM5962

DM5962  NAD 83(2011)-  39 43 17.49315(N)    105 11 34.33560(W) AD(2010.00) c

DM5962  ELLIP H (08/??/11) 1819.836  (m)                       GP(2010.00) c c

DM5962  NAD 83(CORS)-  39 43 17.49312(N)    105 11 34.33640(W) AD(2002.00) c

DM5962  ELLIP H (03/??/11) 1819.837  (m)                       GP(2002.00) c c

DM5962

DM5962.Superseded values are not recommended for survey control.

DM5962

DM5962.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DM5962.See file dsdata.pdf to determine how the superseded data were derived.

DM5962

DM5962_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DM5962

DM5962                          STATION DESCRIPTION

DM5962

DM5962'DESCRIBED BY NATIONAL GEODETIC SURVEY 2019

DM5962'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DM5962'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DM5962'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DM5962'   ftp://cors.ngs.noaa.gov/cors/README.txt

DM5962'   ftp://cors.ngs.noaa.gov/cors/coord/coord_14

DM5962'   ftp://cors.ngs.noaa.gov/cors/station_log

DM5962'   https://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:02

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.8

Starting Datasheet Retrieval...

1        National Geodetic Survey,   Retrieval Date = JUNE 20, 2020

DF9219 ***********************************************************************

DF9219  CORS        -  This is a GPS Continuously Operating Reference Station.

DF9219  DESIGNATION -  DENVER WAAS 1 CORS ARP

DF9219  CORS_ID     -  ZDV1

DF9219  PID         -  DF9219

DF9219  STATE/COUNTY-  CO/BOULDER

DF9219  COUNTRY     -  US

DF9219  USGS QUAD   -  HYGIENE (2019)

DF9219

DF9219                         *CURRENT SURVEY CONTROL

DF9219  ______________________________________________________________________

DF9219* NAD 83(2011) POSITION- 40 11 14.27201(N) 105 07 37.95983(W)   ADJUSTED

DF9219* NAD 83(2011) ELLIP HT-  1541.784 (meters)        (06/??/19)   ADJUSTED

DF9219* NAD 83(2011) EPOCH   -  2010.00

DF9219  ______________________________________________________________________

DF9219  GEOID HEIGHT    -        -16.642 (meters)                     GEOID18

DF9219  NAD 83(2011) X  - -1,273,627.707 (meters)                     COMP

DF9219  NAD 83(2011) Y  - -4,711,376.566 (meters)                     COMP

DF9219  NAD 83(2011) Z  -  4,094,889.922 (meters)                     COMP

DF9219

DF9219  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

DF9219  Standards:

DF9219         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

DF9219            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

DF9219  -------------------------------------------------------------------

DF9219  NETWORK    0.18   0.45           0.07   0.08   0.23      0.19623100

DF9219  -------------------------------------------------------------------

DF9219

DF9219

DF9219.The coordinates were established by GPS observations

DF9219.and adjusted by the National Geodetic Survey in June 2019.

DF9219

DF9219.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DF9219.been affixed to the stable North American Tectonic Plate.

DF9219

DF9219.The coordinates are valid at the epoch date displayed above

DF9219.which is a decimal equivalence of Year/Month/Day.

DF9219

DF9219.Due to the release of the International GNSS Service (IGS) 2014

DF9219.realization of the International Terrestrial Reference Frame of 2014

DF9219.(ITRF2014), NGS reprocessed all NOAA CORS Network and some IGS stations

DF9219.using data collected between 1/1/1996 and 1/30/2017. The resulting ITRF2014

DF9219.epoch 2010.00 coordinates, referred to as Multi-Year CORS Solution 2

DF9219.(MYCS2), were transformed to NAD 83 (2011/PA11/MA11) maintaining the

DF9219.currently published epoch of 2010.00.

DF9219

DF9219.Additional information on MYCS2 is available at

DF9219.https://geodesy.noaa.gov/CORS/coords.shtml

DF9219

DF9219.Significant digits in the geoid height do not necessarily reflect accuracy.

DF9219.GEOID18 height accuracy estimate available here.

DF9219

DF9219.The PID for the CORS L1 Phase Center is DI6103.

DF9219

DF9219.Click photographs - Photos may exist for this station.

DF9219

DF9219.The XYZ, and position/ellipsoidal ht. are equivalent.

DF9219

DF9219.The ellipsoidal height was determined by GPS observations

DF9219.and is referenced to NAD 83.

DF9219

DF9219. The following values were computed from the NAD 83(2011) position.

DF9219

DF9219;                    North         East     Units Scale Factor Converg.

DF9219;SPC CO N     -   399,683.267   946,147.123   MT  0.99995746   +0 14 27.1

DF9219;SPC CO N     - 1,311,294.19  3,104,151.02   sFT  0.99995746   +0 14 27.1

DF9219;UTM  13      - 4,448,553.535   489,171.026   MT  0.99960144   -0 04 55.5

DF9219

DF9219!             -  Elev Factor  x  Scale Factor =   Combined Factor

DF9219!SPC CO N     -   0.99975819  x   0.99995746  =   0.99971566

DF9219!UTM  13      -   0.99975819  x   0.99960144  =   0.99935973

DF9219

DF9219_U.S. NATIONAL GRID SPATIAL ADDRESS: 13TDE8917148553(NAD 83)

DF9219

DF9219                          SUPERSEDED SURVEY CONTROL

DF9219

DF9219  ELLIP H (06/27/12) 1541.773  (m)                       GP(2010.00) 0 0

DF9219  NAD 83(2011)-  40 11 14.27248(N)    105 07 37.95969(W) AD(2010.00) c

DF9219  NAD 83(2011)-  40 11 14.27200(N)    105 07 37.95976(W) AD(2010.00) c

DF9219  ELLIP H (08/??/11) 1541.784  (m)                       GP(2010.00) c c

DF9219  ELLIP H (02/10/07) 1541.783  (m)                       GP(2002.00)

DF9219  NAD 83(2007)-  40 11 14.27224(N)    105 07 37.96036(W) AD(2002.00) c

DF9219  NAD 83(CORS)-  40 11 14.27224(N)    105 07 37.96036(W) AD(2002.00) c

DF9219  ELLIP H (12/??/03) 1541.783  (m)                       GP(2002.00) c c

DF9219

DF9219.Superseded values are not recommended for survey control.

DF9219

DF9219.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DF9219.See file dsdata.pdf to determine how the superseded data were derived.

DF9219

DF9219_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DF9219

DF9219                          STATION DESCRIPTION

DF9219

DF9219'DESCRIBED BY NATIONAL GEODETIC SURVEY 2019

DF9219'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DF9219'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DF9219'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DF9219'   ftp://cors.ngs.noaa.gov/cors/README.txt

DF9219'   ftp://cors.ngs.noaa.gov/cors/coord/coord_14

DF9219'   ftp://cors.ngs.noaa.gov/cors/station_log

DF9219'   https://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:02

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.8

Starting Datasheet Retrieval...

1        National Geodetic Survey,   Retrieval Date = JUNE 20, 2020

DG7429 ***********************************************************************

DG7429  CORS        -  This is a GPS Continuously Operating Reference Station.

DG7429  DESIGNATION -  MARSHALL FIELD CORS ARP

DG7429  CORS_ID     -  P041

DG7429  PID         -  DG7429

DG7429  STATE/COUNTY-  CO/BOULDER

DG7429  COUNTRY     -  US

DG7429  USGS QUAD   -  LOUISVILLE (2019)

DG7429

DG7429                         *CURRENT SURVEY CONTROL

DG7429  ______________________________________________________________________

DG7429* NAD 83(2011) POSITION- 39 56 58.15001(N) 105 11 39.31658(W)   ADJUSTED

DG7429* NAD 83(2011) ELLIP HT-  1729.724 (meters)        (06/??/19)   ADJUSTED

DG7429* NAD 83(2011) EPOCH   -  2010.00

DG7429  ______________________________________________________________________

DG7429  GEOID HEIGHT    -        -16.258 (meters)                     GEOID18

DG7429  NAD 83(2011) X  - -1,283,633.475 (meters)                     COMP

DG7429  NAD 83(2011) Y  - -4,726,429.207 (meters)                     COMP

DG7429  NAD 83(2011) Z  -  4,074,798.095 (meters)                     COMP

DG7429

DG7429  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

DG7429  Standards:

DG7429         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

DG7429            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

DG7429  -------------------------------------------------------------------

DG7429  NETWORK    0.14   0.34           0.05   0.06   0.17      0.26471700

DG7429  -------------------------------------------------------------------

DG7429

DG7429

DG7429.The coordinates were established by GPS observations

DG7429.and adjusted by the National Geodetic Survey in June 2019.

DG7429

DG7429.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DG7429.been affixed to the stable North American Tectonic Plate.

DG7429

DG7429.The coordinates are valid at the epoch date displayed above

DG7429.which is a decimal equivalence of Year/Month/Day.

DG7429

DG7429.Due to the release of the International GNSS Service (IGS) 2014

DG7429.realization of the International Terrestrial Reference Frame of 2014

DG7429.(ITRF2014), NGS reprocessed all NOAA CORS Network and some IGS stations

DG7429.using data collected between 1/1/1996 and 1/30/2017. The resulting ITRF2014

DG7429.epoch 2010.00 coordinates, referred to as Multi-Year CORS Solution 2

DG7429.(MYCS2), were transformed to NAD 83 (2011/PA11/MA11) maintaining the

DG7429.currently published epoch of 2010.00.

DG7429

DG7429.Additional information on MYCS2 is available at

DG7429.https://geodesy.noaa.gov/CORS/coords.shtml

DG7429

DG7429.Significant digits in the geoid height do not necessarily reflect accuracy.

DG7429.GEOID18 height accuracy estimate available here.

DG7429

DG7429.The PID for the CORS L1 Phase Center is DP7042.

DG7429

DG7429.Click photographs - Photos may exist for this station.

DG7429

DG7429.The XYZ, and position/ellipsoidal ht. are equivalent.

DG7429

DG7429.The ellipsoidal height was determined by GPS observations

DG7429.and is referenced to NAD 83.

DG7429

DG7429. The following values were computed from the NAD 83(2011) position.

DG7429

DG7429;                    North         East     Units Scale Factor Converg.

DG7429;SPC CO N     -   373,256.925   940,529.016   MT  0.99997059   +0 11 51.2

DG7429;SPC CO N     - 1,224,593.76  3,085,718.95   sFT  0.99997059   +0 11 51.2

DG7429;UTM  13      - 4,422,168.758   483,406.268   MT  0.99960339   -0 07 29.0

DG7429

DG7429!             -  Elev Factor  x  Scale Factor =   Combined Factor

DG7429!SPC CO N     -   0.99972872  x   0.99997059  =   0.99969931

DG7429!UTM  13      -   0.99972872  x   0.99960339  =   0.99933221

DG7429

DG7429_U.S. NATIONAL GRID SPATIAL ADDRESS: 13SDE8340622168(NAD 83)

DG7429

DG7429                          SUPERSEDED SURVEY CONTROL

DG7429

DG7429  ELLIP H (06/27/12) 1729.679  (m)                       GP(2010.00) 0 0

DG7429  NAD 83(2011)-  39 56 58.15008(N)    105 11 39.31661(W) AD(2010.00) c

DG7429  NAD 83(2011)-  39 56 58.15018(N)    105 11 39.31657(W) AD(2010.00) c

DG7429  ELLIP H (08/??/11) 1729.713  (m)                       GP(2010.00) c c

DG7429  NAD 83(CORS)-  39 56 58.15000(N)    105 11 39.31685(W) AD(2002.00) c

DG7429  ELLIP H (10/??/04) 1729.708  (m)                       GP(2002.00) c c

DG7429

DG7429.Superseded values are not recommended for survey control.

DG7429

DG7429.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DG7429.See file dsdata.pdf to determine how the superseded data were derived.

DG7429

DG7429_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DG7429

DG7429                          STATION DESCRIPTION

DG7429

DG7429'DESCRIBED BY NATIONAL GEODETIC SURVEY 2019

DG7429'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DG7429'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DG7429'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DG7429'   ftp://cors.ngs.noaa.gov/cors/README.txt

DG7429'   ftp://cors.ngs.noaa.gov/cors/coord/coord_14

DG7429'   ftp://cors.ngs.noaa.gov/cors/station_log

DG7429'   https://geodesy.noaa.gov/CORS

1        National Geodetic Survey,   Retrieval Date = JUNE 20, 2020

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.8

Starting Datasheet Retrieval...

1        National Geodetic Survey,   Retrieval Date = JUNE 20, 2020

AF9516 ***********************************************************************

AF9516  HT_MOD      -  This is a Height Modernization Survey Station.

AF9516  CORS        -  This is a GPS Continuously Operating Reference Station.

AF9516  DESIGNATION -  TABLE MOUNTAIN CORS ARP

AF9516  CORS_ID     -  TMGO

AF9516  PID         -  AF9516

AF9516  STATE/COUNTY-  CO/BOULDER

AF9516  COUNTRY     -  US

AF9516  USGS QUAD   -  HYGIENE (2019)

AF9516

AF9516                         *CURRENT SURVEY CONTROL

AF9516  ______________________________________________________________________

AF9516* NAD 83(2011) POSITION- 40 07 51.34537(N) 105 13 57.71669(W)   ADJUSTED

AF9516* NAD 83(2011) ELLIP HT-  1673.858 (meters)        (06/??/19)   ADJUSTED

AF9516* NAD 83(2011) EPOCH   -  2010.00

AF9516* NAVD 88 ORTHO HEIGHT -  1689.78  (meters)     5543.9   (feet) GPS OBS

AF9516  ______________________________________________________________________

AF9516  NAVD 88 orthometric height was determined with geoid model    GEOID99

AF9516  GEOID HEIGHT    -        -15.862 (meters)                     GEOID99

AF9516  GEOID HEIGHT    -        -15.925 (meters)                     GEOID18

AF9516  NAD 83(2011) X  - -1,283,387.066 (meters)                     COMP

AF9516  NAD 83(2011) Y  - -4,713,016.775 (meters)                     COMP

AF9516  NAD 83(2011) Z  -  4,090,190.386 (meters)                     COMP

AF9516

AF9516  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

AF9516  Standards:

AF9516         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

AF9516            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

AF9516  -------------------------------------------------------------------

AF9516  NETWORK    0.17   0.48           0.07   0.07   0.24      0.12649200

AF9516  -------------------------------------------------------------------

AF9516

AF9516

AF9516.The coordinates were established by GPS observations

AF9516.and adjusted by the National Geodetic Survey in June 2019.

AF9516

AF9516.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

AF9516.been affixed to the stable North American Tectonic Plate.

AF9516

AF9516.The coordinates are valid at the epoch date displayed above

AF9516.which is a decimal equivalence of Year/Month/Day.

AF9516

AF9516.Due to the release of the International GNSS Service (IGS) 2014

AF9516.realization of the International Terrestrial Reference Frame of 2014

AF9516.(ITRF2014), NGS reprocessed all NOAA CORS Network and some IGS stations

AF9516.using data collected between 1/1/1996 and 1/30/2017. The resulting ITRF2014

AF9516.epoch 2010.00 coordinates, referred to as Multi-Year CORS Solution 2

AF9516.(MYCS2), were transformed to NAD 83 (2011/PA11/MA11) maintaining the

AF9516.currently published epoch of 2010.00.

AF9516

AF9516.Additional information on MYCS2 is available at

AF9516.https://geodesy.noaa.gov/CORS/coords.shtml

AF9516

AF9516.The orthometric height was determined by GPS observations and a

AF9516.high-resolution geoid model using precise GPS observation and

AF9516.processing techniques.

AF9516

AF9516.Significant digits in the geoid height do not necessarily reflect accuracy.

AF9516.GEOID18 height accuracy estimate available here.

AF9516

AF9516.The PID for the CORS L1 Phase Center is DH5957.

AF9516

AF9516.Click photographs - Photos may exist for this station.

AF9516

AF9516.The XYZ, and position/ellipsoidal ht. are equivalent.

AF9516

AF9516.The ellipsoidal height was determined by GPS observations

AF9516.and is referenced to NAD 83.

AF9516

AF9516. The following values were computed from the NAD 83(2011) position.

AF9516

AF9516;                    North         East     Units Scale Factor Converg.

AF9516;SPC CO N     -   393,392.107   937,183.062   MT  0.99995902   +0 10 21.8

AF9516;SPC CO N     - 1,290,653.94  3,074,741.43   sFT  0.99995902   +0 10 21.8

AF9516;UTM  13      - 4,442,315.200   480,174.856   MT  0.99960484   -0 08 59.9

AF9516

AF9516!             -  Elev Factor  x  Scale Factor =   Combined Factor

AF9516!SPC CO N     -   0.99973748  x   0.99995902  =   0.99969651

AF9516!UTM  13      -   0.99973748  x   0.99960484  =   0.99934242

AF9516

AF9516_U.S. NATIONAL GRID SPATIAL ADDRESS: 13TDE8017442315(NAD 83)

AF9516

AF9516                          SUPERSEDED SURVEY CONTROL

AF9516

AF9516  ELLIP H (06/27/12) 1673.830  (m)                       GP(2010.00) 0 0

AF9516  NAD 83(2011)-  40 07 51.34521(N)    105 13 57.71682(W) AD(2010.00) c

AF9516  NAD 83(2011)-  40 07 51.34543(N)    105 13 57.71653(W) AD(2010.00) c

AF9516  ELLIP H (08/??/11) 1673.853  (m)                       GP(2010.00) c c

AF9516  ELLIP H (02/10/07) 1673.858  (m)                       GP(2002.00)

AF9516  NAD 83(2007)-  40 07 51.34512(N)    105 13 57.71720(W) AD(2002.00) c

AF9516  NAD 83(CORS)-  40 07 51.34512(N)    105 13 57.71720(W) AD(2002.00) c

AF9516  ELLIP H (03/??/02) 1673.858  (m)                       GP(2002.00) c c

AF9516  NAD 83(CORS)-  40 07 51.34493(N)    105 13 57.71724(W) AD(1997.00) c

AF9516  ELLIP H (04/??/96) 1673.871  (m)                       GP(1997.00) c c

AF9516  NAD 83(CORS)-  40 07 51.34493(N)    105 13 57.71724(W) AD(1996.00) c

AF9516  ELLIP H (04/??/96) 1673.871  (m)                       GP(1996.00) c c

AF9516  NAVD 88 (01/06/00) 1689.79   (m)  UNKNOWN model used   GPS OBS

AF9516

AF9516.Superseded values are not recommended for survey control.

AF9516

AF9516.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

AF9516.See file dsdata.pdf to determine how the superseded data were derived.

AF9516

AF9516_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

AF9516

AF9516                          STATION DESCRIPTION

AF9516

AF9516'DESCRIBED BY NATIONAL GEODETIC SURVEY 2019

AF9516'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

AF9516'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

AF9516'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

AF9516'   ftp://cors.ngs.noaa.gov/cors/README.txt

AF9516'   ftp://cors.ngs.noaa.gov/cors/coord/coord_14

AF9516'   ftp://cors.ngs.noaa.gov/cors/station_log

AF9516'   https://geodesy.noaa.gov/CORS

*** retrieval complete.

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.8

Starting Datasheet Retrieval...

1        National Geodetic Survey,   Retrieval Date = JUNE 20, 2020

DL2742 ***********************************************************************

DL2742  CORS        -  This is a GPS Continuously Operating Reference Station.

DL2742  DESIGNATION -  FORT COLLINS CORS ARP

DL2742  CORS_ID     -  COFC

DL2742  PID         -  DL2742

DL2742  STATE/COUNTY-  CO/LARIMER

DL2742  COUNTRY     -  US

DL2742  USGS QUAD   -  HORSETOOTH RESERVOIR (2019)

DL2742

DL2742                         *CURRENT SURVEY CONTROL

DL2742  ______________________________________________________________________

DL2742* NAD 83(2011) POSITION- 40 35 36.10799(N) 105 09 37.56860(W)   ADJUSTED

DL2742* NAD 83(2011) ELLIP HT-  1595.986 (meters)        (06/??/19)   ADJUSTED

DL2742* NAD 83(2011) EPOCH   -  2010.00

DL2742  ______________________________________________________________________

DL2742  GEOID HEIGHT    -        -15.203 (meters)                     GEOID18

DL2742  NAD 83(2011) X  - -1,268,727.233 (meters)                     COMP

DL2742  NAD 83(2011) Y  - -4,682,468.860 (meters)                     COMP

DL2742  NAD 83(2011) Z  -  4,129,276.430 (meters)                     COMP

DL2742

DL2742  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

DL2742  Standards:

DL2742         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

DL2742            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

DL2742  -------------------------------------------------------------------

DL2742  NETWORK    0.16   0.39           0.06   0.07   0.20      0.23408900

DL2742  -------------------------------------------------------------------

DL2742

DL2742

DL2742.The coordinates were established by GPS observations

DL2742.and adjusted by the National Geodetic Survey in June 2019.

DL2742

DL2742.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DL2742.been affixed to the stable North American Tectonic Plate.

DL2742

DL2742.The coordinates are valid at the epoch date displayed above

DL2742.which is a decimal equivalence of Year/Month/Day.

DL2742

DL2742.Due to the release of the International GNSS Service (IGS) 2014

DL2742.realization of the International Terrestrial Reference Frame of 2014

DL2742.(ITRF2014), NGS reprocessed all NOAA CORS Network and some IGS stations

DL2742.using data collected between 1/1/1996 and 1/30/2017. The resulting ITRF2014

DL2742.epoch 2010.00 coordinates, referred to as Multi-Year CORS Solution 2

DL2742.(MYCS2), were transformed to NAD 83 (2011/PA11/MA11) maintaining the

DL2742.currently published epoch of 2010.00.

DL2742

DL2742.Additional information on MYCS2 is available at

DL2742.https://geodesy.noaa.gov/CORS/coords.shtml

DL2742

DL2742.Significant digits in the geoid height do not necessarily reflect accuracy.

DL2742.GEOID18 height accuracy estimate available here.

DL2742

DL2742.The PID for the CORS L1 Phase Center is DL2743.

DL2742

DL2742.Click photographs - Photos may exist for this station.

DL2742

DL2742.The XYZ, and position/ellipsoidal ht. are equivalent.

DL2742

DL2742.The ellipsoidal height was determined by GPS observations

DL2742.and is referenced to NAD 83.

DL2742

DL2742. The following values were computed from the NAD 83(2011) position.

DL2742

DL2742;                    North         East     Units Scale Factor Converg.

DL2742;SPC CO N     -   444,760.243   943,145.193   MT  0.99997469   +0 13 09.9

DL2742;SPC CO N     - 1,459,184.23  3,094,302.19   sFT  0.99997469   +0 13 09.9

DL2742;UTM  13      - 4,493,630.498   486,424.524   MT  0.99960227   -0 06 15.8

DL2742

DL2742!             -  Elev Factor  x  Scale Factor =   Combined Factor

DL2742!SPC CO N     -   0.99974970  x   0.99997469  =   0.99972440

DL2742!UTM  13      -   0.99974970  x   0.99960227  =   0.99935207

DL2742

DL2742_U.S. NATIONAL GRID SPATIAL ADDRESS: 13TDE8642493630(NAD 83)

DL2742

DL2742                          SUPERSEDED SURVEY CONTROL

DL2742

DL2742  NAD 83(2011)-  40 35 36.10801(N)    105 09 37.56853(W) AD(2010.00) c

DL2742  ELLIP H (08/??/11) 1595.981  (m)                       GP(2010.00) c c

DL2742  NAD 83(CORS)-  40 35 36.10790(N)    105 09 37.56921(W) AD(2002.00) c

DL2742  ELLIP H (05/??/09) 1595.974  (m)                       GP(2002.00) c c

DL2742

DL2742.Superseded values are not recommended for survey control.

DL2742

DL2742.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DL2742.See file dsdata.pdf to determine how the superseded data were derived.

DL2742

DL2742_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DL2742

DL2742                          STATION DESCRIPTION

DL2742

DL2742'DESCRIBED BY NATIONAL GEODETIC SURVEY 2019

DL2742'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DL2742'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DL2742'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DL2742'   ftp://cors.ngs.noaa.gov/cors/README.txt

DL2742'   ftp://cors.ngs.noaa.gov/cors/coord/coord_14

DL2742'   ftp://cors.ngs.noaa.gov/cors/station_log

DL2742'   https://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:01

PROJECT SURVEYOR	Steven A. Wood