The following document Kansas 2013 Update Delivery June 19, 2014 is an explanation, in response to, some of the Calls made in the USGS LiDAR Quality Assessment Report for KS_Area1-Eastern_2013.

USGS LiDAR Quality Assessment Report, page 12, under Vertical Accuracy Results:  in response to the question “****Short grass is used for FVA testing.”  Yes, the FVA was run on Land Cover Category: Low Grass resulting in an FVA of 0.113m.  Land Cover Categories have also been addressed; updated Separated Report, Shapes and Accuracy Reports, and Project Metadata have been provided in the updated delivery

USGS LiDAR Quality Assessment Report, pages 17 through 19 questioned the appearance of an anomalous error throughout the eastern section of the Kansas 2013 data set. In the UTM15 geodatabase a shape has been added with the description of Kansas_2012_Data_Limit.   In order to provide full tile DEMs between Kansas 2013 and Kansas 2012 project areas, Kansas 2012 data was included.  The inclusion of Kansas 2012 data introduced a visible seam between the two data sets due to seasonal changes, differences between missions, and sensors. The only way to alleviate the appearance of the anomalous error would be by the removal of the Kansas 2012 data, and by providing partial tiles along the eastern boundary of Kansas 2013.

USGS LiDAR Quality Assessment Report, page 21, pertains to “****Water issue beneath bridge.”   Re-work of a river section ended with marginal success.  An updated Bare Earth Surface DEM has been included in the update delivery.

Shape file, USGS calls; Breakline 2 is represented as a box culvert in the Bare Earth DEM. IMG with no breaklines.