GPSC3 TO 140G0218F0164-NJ_South_Jersey_Lidar_2018_B18

Southern New Jersey USGS LIDAR QC Ground Control Point

LIDAR SURVEY REPORT

Field Measurement by:	Steven A. Wood

For:		Sanborn Mapping

Field Measurement Date;	November 2018

PROJECT LOCATION MAP

Locations were selected to obtain LIDAR GCP gps truthing NVA and VVA x,y,z locations for the Southern New Jersey AOIs. The schematic is as below.  As we completed the measurements the locations were adjusted as necessary based on our ability to access each and the SV conditions at each.

Project Kick off and Control Staging

Crews arrived on site in Southern New Jersey greater AOI area on November 06, 2018. Each day they set out to measure and the process was a combination of using the using a fully static gps measured network tied to the local NGS CORS station and always working within the confines of public access areas or where and when we had access to private property. The weather was favorable for the most part.  Initial field work was completed by days end on November 15, 2018.

LOCATION METHODS, MEASUREMENTS AND EQUIPMENT

The equipment configuration for this project consists of industry standard gps surveying equipment.  The gps equipment used was a combination of Topcon dual frequency(L1/L2) receivers.  The Topcon receivers are the Hiper GD and Hiper Plus type. Topcon Tools gps processing software was used to post process all observed gps data. Each gps observation was logged for site id, receiver type, height of antenna, start time and date.  Length of vector, time of day, SV configuration and site obstructions determined the length of observation at each site. Data was downloaded to the PC after each day’s sessions.  Initial processing was performed to verify we had good vector solutions between sites.

The data for the LIDAR ground truthing locations was collected using full static collection procedures and post processed.  There is more than one NGS CORS station located in or within close proximity to the AOI.

The coordinate datum is as described below:

Coordinate system: New Jersey State Plane Coordinate System

Horizontal Datum: NAD83 Epoch 2011

Vertical Datum: NAVD88, Geoid 12B   Map Units: US Foot

The Topcon Tools processing software reports on static observations the horizontal and vertical precision of every vector measured and summarizes the standard deviation in x, y and z position for each individual control point. For purposes of this report we included all points measured.  We have several supplemental additional GCPs that were measured as base stations in VVA areas and serve as additional quality control check points.

Two field crews were utilized to obtain the GCP data.  Typically a base station was running and the crews performed with a rover tying the primary vector back to the base.  When multiple bases were running simultaneously the rover vector could be processed to both bases, and therefore the network triangle strength was heightened significantly with all the redundant data.

The Topcon Tools processing software summarizes the observed vectors, the raw vector horizontal and vertical RMSE components and the corresponding Residual in northing easting and elevation.  Upon final adjustment each point in the network has its corresponding RMSE standard deviation in all 3 directions.  We included all points in each daily report.

The points were preselected in the office and grouped into 3 categories. GCP for control calibration points, NVA for non vegetation area points and VVA for vegetation area points.

The coordinate datum was based upon the NGS CORS stations NJCM, NJOC and NJGC. These control locations were supplemented by the 3rd party CORS stations from KEYNETGPS a private Trimble network that covers lots of the Eastern seaboard area.  They have their own CORS base stations running and are like other Trimble sites whereby you can generate base station data at Virtual CORS type locations to supplement your post processing calculations. Additionally we sat several of our own static collection base station receivers to keep our vector lengths and thereby our measurements to a reasonable time frame.

Daily downloads of the CORS data were incorporated into the Topcon Tools adjustment.

The full Topcon Adjust Report is included herewith in one composite spreadsheet containing each days worth of gps observations. This spreadsheet is included separately from this report.

A composite coordinate summary spreadsheet is also included herewith to facilitate data retrieval and formatting for the LIDAR QC processing.

We took several pictures of the quality control points and they are labeled by their unique GCP number and then a post script designation like “A’ or “B” or “Z” for the first picture at a point, the second picture at a point typically at about 90 degrees to the first and then a zoom of the point measured in case it was a photo identifiable type point and could be more clearly defined.

The author is aware that two points have different types of photos designated.  NVA20 and NVA36 experienced camera malfunctions that were not noticed until we demobilized from the site.  In these two instances we created a Google “top” view of the area as one picture and then a second zoom taken from similar locations to help identify the paint stripe points located.

Final documents were completed and are as contained herewith.

Final Adjusted Coordinates

| Name | Grid Northing (USft) | Grid Easting (USft) | Elevation (USft) |  | Control |
| --- | --- | --- | --- | --- | --- |
| Base93 | 303333.426 | 545037.503 | 29.678 |  | None |
| Base94 | 51837.949 | 366364.650 | 14.305 |  | None |
| Base95 | 198250.642 | 434371.527 | 14.193 |  | None |
| Base96 | 235734.731 | 373077.605 | 100.197 |  | None |
| Base97 | 195795.456 | 332031.633 | 80.657 |  | None |
| Base98 | 253085.333 | 284724.120 | 123.323 |  | None |
| Base99 | 228615.312 | 267532.516 | 115.844 |  | None |
| GCP001R | 455070.936 | 483058.167 | 105.483 |  | None |
| GCP002 | 478497.508 | 554077.059 | 124.907 |  | None |
| GCP003 | 464535.094 | 601441.823 | 32.388 |  | None |
| GCP004 | 405352.912 | 528456.714 | 143.429 |  | None |
| GCP004 | 405352.909 | 528456.743 | 143.440 |  | None |
| GCP005 | 416356.312 | 578612.500 | 55.661 |  | None |
| GCP006 | 449800.247 | 618214.759 | 1.616 |  | None |
| GCP007 | 338830.469 | 602561.802 | 6.147 |  | None |
| GCP008 | 337381.979 | 543399.155 | 138.542 |  | None |
| GCP009 | 280631.631 | 535209.069 | 14.913 |  | None |
| GCP010 | 268422.523 | 565837.385 | 3.755 |  | None |
| GCP011 | 328812.828 | 218081.984 | 4.722 |  | None |
| GCP012 | 226947.860 | 286331.996 | 88.907 |  | None |
| GCP013 | 267926.901 | 219324.875 | 4.031 |  | None |
| GCP014 | 276464.508 | 300828.247 | 120.989 |  | None |
| GCP015 | 186549.742 | 294256.339 | 46.035 |  | None |
| GCP016 | 296919.933 | 255621.147 | 54.829 |  | None |
| GCP017 | 240115.171 | 353020.535 | 95.994 |  | None |
| GCP018 | 294672.888 | 412903.427 | 84.560 |  | None |
| GCP019 | 238487.061 | 502486.448 | 43.466 |  | None |
| GCP020 | 156113.337 | 355466.735 | 20.507 |  | None |
| GCP021 | 200172.594 | 517750.252 | 7.016 |  | None |
| GCP022 | 52001.509 | 365833.291 | 13.655 |  | None |
| GCP023 | 167375.816 | 419926.415 | 10.298 |  | None |
| GCP023QC | 167375.902 | 419926.431 | 10.323 |  | None |
| GCP024 | 107320.383 | 413721.350 | 13.377 |  | None |
| GCP025 | 218609.588 | 451157.550 | 61.638 |  | None |
| GCP026 | 245215.727 | 227933.108 | 15.177 |  | None |
| GCP027 | 203328.934 | 348812.946 | 54.220 |  | None |
| GCP028 | 95359.194 | 430257.368 | 7.600 |  | None |
| GCP029 | 261449.597 | 426009.062 | 82.969 |  | None |
| JJW1 | 404428.523 | 492603.726 | 136.572 |  | Both |
| NJBL | 338746.525 | 602480.204 | 25.322 |  | None |
| NJCM | 97501.720 | 406170.630 | 32.251 |  | Both |
| NJGC | 345869.380 | 317946.480 | 95.239 |  | Both |
| NJOC | 407864.510 | 578046.080 | 81.498 |  | Both |
| NJOC | 407864.478 | 578046.090 | 81.517 |  | None |
| NJOC | 407864.375 | 578046.057 | 81.577 |  | None |
| NVA001R | 455093.757 | 483114.426 | 106.246 |  | None |
| NVA002 | 478898.668 | 554336.209 | 133.131 |  | None |
| NVA003R | 464614.325 | 600685.014 | 30.031 |  | None |
| NVA004 | 405495.987 | 528488.681 | 140.198 |  | None |
| NVA005 | 416330.873 | 579205.146 | 58.459 |  | None |
| NVA006 | 450213.080 | 618967.495 | 3.348 |  | None |
| NVA007 | 338624.357 | 602108.332 | 3.991 |  | None |
| NVA008 | 337079.248 | 542971.027 | 127.823 |  | None |
| NVA009 | 280227.071 | 535318.736 | 18.354 |  | None |
| NVA010 | 268030.161 | 565771.532 | 2.916 |  | None |
| NVA011 | 329225.814 | 217931.271 | 6.431 |  | None |
| NVA012 | 226619.334 | 286093.673 | 78.454 |  | None |
| NVA013 | 268230.407 | 218986.815 | 1.627 |  | None |
| NVA014 | 276488.298 | 301056.863 | 121.236 |  | None |
| NVA015R | 185028.590 | 293804.118 | 28.955 |  | None |
| NVA016 | 297018.061 | 256008.074 | 55.337 |  | None |
| NVA017 | 239799.078 | 352973.438 | 98.250 |  | None |
| NVA018 | 294409.140 | 413085.368 | 81.800 |  | None |
| NVA019 | 238473.922 | 502981.997 | 39.636 |  | None |
| NVA020 | 156934.993 | 355421.079 | 20.221 |  | None |
| NVA021 | 200455.309 | 517350.722 | 7.732 |  | None |
| NVA022 | 51794.497 | 366365.671 | 13.702 |  | None |
| NVA023 | 167353.103 | 420651.053 | 9.886 |  | None |
| NVA024 | 107600.639 | 413148.440 | 15.659 |  | None |
| NVA025 | 218095.301 | 451162.808 | 63.611 |  | None |
| NVA026 | 244753.460 | 228358.832 | 13.718 |  | None |
| NVA027 | 203267.359 | 348574.426 | 53.594 |  | None |
| NVA028 | 95037.745 | 430018.867 | 7.986 |  | None |
| NVA029 | 261021.726 | 425561.801 | 84.191 |  | None |
| NVA030 | 472520.578 | 519298.733 | 155.302 |  | None |
| NVA031 | 430891.713 | 548944.949 | 62.042 |  | None |
| NVA032 | 451857.234 | 579248.232 | 61.672 |  | None |
| NVA033R | 388328.459 | 588044.818 | 19.664 |  | None |
| NVA034 | 450895.926 | 532004.305 | 108.715 |  | None |
| NVA035R | 427329.922 | 512995.786 | 173.122 |  | None |
| NVA036 | 267943.999 | 528730.924 | 5.784 |  | None |
| NVA037 | 307548.647 | 555969.900 | 26.380 |  | None |
| NVA038 | 362570.292 | 576399.617 | 10.865 |  | None |
| NVA039A | 390845.759 | 609502.771 | 3.359 |  | None |
| NVA040 | 319407.676 | 528526.891 | 83.853 |  | None |
| NVA041 | 371197.032 | 525508.572 | 146.377 |  | None |
| NVA042 | 296893.048 | 205301.960 | 7.839 |  | None |
| NVA043 | 265008.000 | 246911.001 | 32.272 |  | None |
| NVA044R | 314819.346 | 240133.169 | 38.929 |  | None |
| NVA045 | 279137.996 | 229202.299 | 21.914 |  | None |
| NVA046 | 253224.136 | 284486.729 | 125.400 |  | None |
| NVA047 | 182032.011 | 345197.952 | 17.178 |  | None |
| NVA047QC | 182031.985 | 345197.859 | 17.236 |  | None |
| NVA048 | 255204.116 | 365974.456 | 114.829 |  | None |
| NVA049 | 220930.972 | 391260.721 | 97.565 |  | None |
| NVA050 | 159169.521 | 390031.774 | 45.260 |  | None |
| NVA051 | 145481.748 | 404492.622 | 35.213 |  | None |
| NVA052 | 177955.077 | 464562.643 | 7.873 |  | None |
| NVA053 | 286093.977 | 286416.726 | 134.503 |  | None |
| NVA054R | 387013.735 | 542134.152 | 86.033 |  | None |
| NVA055 | 78465.925 | 378185.874 | 15.087 |  | None |
| NVA056 | 246647.296 | 463917.624 | 65.448 |  | None |
| NVA057 | 276595.122 | 462124.389 | 21.853 |  | None |
| NVA058 | 410170.419 | 558819.398 | 40.798 |  | None |
| NVA059 | 216572.811 | 418797.910 | 50.514 |  | None |
| NVA060 | 249197.560 | 317471.457 | 95.861 |  | None |
| NVA061 | 198386.712 | 400302.648 | 80.329 |  | None |
| NVA062 | 226953.165 | 253936.111 | 102.424 |  | None |
| NVA063 | 152767.653 | 459784.091 | 6.108 |  | None |
| NVA064 | 195508.419 | 456597.980 | 49.552 |  | None |
| NVA065 | 219430.436 | 317264.800 | 63.454 |  | None |
| NVA066 | 50896.759 | 397415.648 | 8.652 |  | None |
| NVA067 | 90232.842 | 401394.901 | 12.556 |  | None |
| NVA068 | 141911.996 | 439448.945 | 16.977 |  | None |
| NVA069 | 203153.458 | 486081.595 | 29.735 |  | None |
| NVA070 | 268501.692 | 273713.491 | 126.432 |  | None |
| NVA071 | 169242.665 | 303868.545 | 9.566 |  | None |
| NVA072 | 235435.820 | 339217.674 | 91.007 |  | None |
| NVA073R | 126746.723 | 426682.454 | 18.704 |  | None |
| NVA074 | 218686.886 | 348922.077 | 66.766 |  | None |
| NVA075 | 229183.445 | 426083.257 | 18.628 |  | None |
| NVA076 | 236704.592 | 397976.966 | 98.845 |  | None |
| NVA077 | 214261.327 | 282154.935 | 57.452 |  | None |
| NVA078 | 214214.802 | 528996.869 | 7.082 |  | None |
| NVA079 | 259242.090 | 344176.469 | 106.569 |  | None |
| QualInnBaseEast | 440421.741 | 469863.589 | 123.183 |  | None |
| QualInnBaseQC | 440421.736 | 469863.630 | 123.191 |  | None |
| QualInnNorth | 440591.924 | 469731.828 | 121.309 |  | None |
| QualInnNorth | 440591.924 | 469731.828 | 121.309 |  | Both |
| QualInnSW | 440121.624 | 469692.782 | 115.918 |  | None |
| V016 | 308135.346 | 555840.315 | 112.685 |  | None |
| V018 | 440102.500 | 469572.329 | 139.704 |  | None |
| V019 | 456384.198 | 483032.150 | 139.570 |  | None |
| V020 | 472485.578 | 519463.782 | 172.251 |  | None |
| V022 | 478822.351 | 554553.441 | 172.315 |  | None |
| V025 | 450849.731 | 532158.262 | 139.789 |  | None |
| V026 | 427149.996 | 513133.256 | 172.781 |  | None |
| V027 | 430645.928 | 548917.273 | 140.510 |  | None |
| V028 | 451880.357 | 579184.533 | 140.684 |  | None |
| V029 | 464922.424 | 602058.215 | 140.919 |  | None |
| V030 | 450026.842 | 618838.110 | 141.246 |  | None |
| V033 | 405515.403 | 528726.620 | 140.537 |  | None |
| V036 | 410333.307 | 558929.740 | 140.948 |  | None |
| V037 | 416160.644 | 578530.855 | 141.304 |  | None |
| V038 | 386718.957 | 542002.979 | 140.886 |  | None |
| V043 | 388167.918 | 587979.329 | 141.345 |  | None |
| V053 | 361818.266 | 575987.988 | 141.388 |  | None |
| V056 | 390788.531 | 609398.400 | 141.693 |  | None |
| V058 | 362325.460 | 576376.352 | 141.388 |  | None |
| V060 | 297037.584 | 205064.455 | 141.871 |  | None |
| V072 | 405211.873 | 528727.060 | 222.549 |  | None |
| V074 | 405716.619 | 527947.595 | 206.357 |  | None |
| V075 | 280268.652 | 535170.355 | 142.818 |  | None |
| VVA001 | 456389.481 | 482902.979 | 96.388 |  | None |
| VVA002 | 478864.746 | 554413.689 | 133.760 |  | None |
| VVA003 | 464947.623 | 601901.779 | 41.864 |  | None |
| VVA004 | 405533.966 | 528643.836 | 136.111 |  | None |
| VVA004 | 405533.966 | 528643.862 | 136.121 |  | None |
| VVA005 | 416501.598 | 578630.568 | 57.029 |  | None |
| VVA006 | 450007.328 | 618726.889 | 3.163 |  | None |
| VVA007 | 338478.936 | 601812.450 | 4.857 |  | None |
| VVA008 | 339706.035 | 542057.714 | 140.649 |  | None |
| VVA009 | 280681.685 | 535194.910 | 14.373 |  | None |
| VVA010 | 267654.025 | 565585.685 | 3.119 |  | None |
| VVA011 | 331999.727 | 219231.114 | 6.683 |  | None |
| VVA012 | 225512.496 | 285948.552 | 60.901 |  | None |
| VVA013 | 269168.456 | 217630.842 | -1.113 |  | None |
| VVA014 | 274849.101 | 300070.803 | 128.361 |  | None |
| VVA015 | 185425.851 | 294685.464 | 32.710 |  | None |
| VVA016 | 296798.158 | 256464.832 | 63.644 |  | None |
| VVA017 | 240169.016 | 352863.659 | 96.200 |  | None |
| VVA018 | 296871.568 | 412705.332 | 87.249 |  | None |
| VVA019 | 241092.740 | 504491.951 | 35.535 |  | None |
| VVA020 | 156185.632 | 355359.852 | 20.473 |  | None |
| VVA021 | 200554.167 | 517140.783 | 8.135 |  | None |
| VVA022 | 51997.963 | 366378.895 | 16.104 |  | None |
| VVA023 | 168123.560 | 418692.585 | 18.360 |  | None |
| VVA024 | 108309.828 | 413061.674 | 18.250 |  | None |
| VVA025 | 218482.323 | 451165.811 | 62.252 |  | None |
| VVA026 | 245411.158 | 228056.848 | 8.021 |  | None |
| VVA027 | 204738.693 | 350652.894 | 43.167 |  | None |
| VVA028 | 95940.310 | 428602.249 | 5.634 |  | None |
| VVA029 | 260880.298 | 425898.663 | 82.325 |  | None |
| VVA030 | 448712.116 | 531024.408 | 102.866 |  | None |
| VVA031 | 451615.016 | 579382.655 | 44.265 |  | None |
| VVA032R | 371128.281 | 525200.070 | 151.559 |  | None |
| VVA033R | 362007.873 | 575821.594 | 7.681 |  | None |
| VVA034 | 390716.857 | 609473.064 | 3.199 |  | None |
| VVA035 | 410409.001 | 558787.276 | 39.934 |  | None |
| VVA036 | 307340.310 | 555552.188 | 26.543 |  | None |
| VVA037 | 267723.946 | 528433.741 | 6.241 |  | None |
| VVA038 | 317853.983 | 528696.937 | 85.453 |  | None |
| VVA039 | 216894.373 | 419114.802 | 55.245 |  | None |
| VVA040 | 245544.750 | 465880.344 | 57.534 |  | None |
| VVA041 | 77857.201 | 376683.963 | 9.955 |  | None |
| VVA042 | 177866.480 | 464797.858 | 7.243 |  | None |
| VVA043 | 265199.565 | 246539.106 | 29.178 |  | None |
| VVA044R | 153926.693 | 459691.367 | 3.882 |  | None |
| VVA045 | 145816.188 | 404066.493 | 36.213 |  | None |
| VVA046 | 249261.239 | 315921.297 | 86.728 |  | None |
| VVA047 | 182126.896 | 345168.188 | 17.287 |  | None |
| VVA048 | 219829.443 | 316849.661 | 77.156 |  | None |
| VVA049 | 198457.242 | 400333.939 | 79.488 |  | None |
| VVA050 | 277386.501 | 462126.653 | 20.604 |  | None |
| VVA051 | 222448.250 | 393430.694 | 91.199 |  | None |
| VVA052 | 195783.131 | 456742.278 | 51.272 |  | None |
| VVA053 | 255572.798 | 365964.409 | 116.875 |  | None |
| VVA054 | 251949.160 | 283187.094 | 124.646 |  | None |
| VVA055R | 227103.336 | 253722.614 | 93.117 |  | None |
| VVA056 | 297082.155 | 205282.280 | 7.951 |  | None |
| VVA057 | 268938.656 | 269559.453 | 135.615 |  | None |
| VVA058 | 159231.336 | 389859.665 | 46.210 |  | None |
| VVA059 | 214544.239 | 529187.289 | 4.836 |  | None |
| VVA060 | 203006.465 | 487980.824 | 4.401 |  | None |
| VVA061 | 471318.523 | 517920.450 | 153.691 |  | None |

Point Classification Descriptions

| Name | Class Description |
| --- | --- |
| Base93 | Base grass |
| Base94 | Base grass |
| Base95 | Base grass |
| Base96 | Base Cor SW |
| Base97 | Base |
| Base98 | Base |
| Base99 | Base |
| GCP001R | Paint Stripe |
| GCP002 | Tip of Arrow |
| GCP003 | Paint stripe |
| GCP004 | Paint stripe |
| GCP004 | Cor Paint lines |
| GCP005 | Cor of paint lines |
| GCP006 | Paint stripe |
| GCP007 | Cor of paint stripe |
| GCP008 | Asphalt |
| GCP009 | Paint Stripe |
| GCP010 | Cor of paint stripe |
| GCP011 | Concrete Area |
| GCP012 | Paint Stripe |
| GCP013 | Paint Stripe |
| GCP014 | Paint Stripe |
| GCP015 | Paint Stripe |
| GCP016 | Paint Stripe |
| GCP017 | Paint Stripe |
| GCP018 | Paint Stripe |
| GCP019 | Paint Stripe |
| GCP020 | Paint Stripe |
| GCP021 | Cor SW |
| GCP022 | Paint Stripe |
| GCP023 | Paint Stripe |
| GCP023QC | GCP023QC |
| GCP024 | Paint Stripe |
| GCP025 | Paint Stripe |
| GCP026 | Paint Stripe |
| GCP027 | Cor SW |
| GCP028 | Paint Stripe |
| GCP029 | Paint Stripe |
| JJW1 | 3rd Party CORS |
| NJBL | 3rd Party CORS |
| NJCM | CORS |
| NJGC | CORS |
| NJOC | CORS |
| NJOC | CORS |
| NJOC | CORS |
| NVA001R | Cor SW |
| NVA002 | Tip of Arrow |
| NVA003R | Cor of paint lines |
| NVA004 | CL Paint line intersects |
| NVA005 | Paint stripe |
| NVA006 | Paint stripe |
| NVA007 | CL Manhole |
| NVA008 | Paint Stripe |
| NVA009 | Paint Stripe |
| NVA010 | Paint Stripe |
| NVA011 | Cor SW |
| NVA012 | Paint Stripe |
| NVA013 | Paint Stripe |
| NVA014 | Cor SW |
| NVA015R | Cor SW |
| NVA016 | Paint Stripe |
| NVA017 | Paint Stripe |
| NVA018 | Paint Stripe |
| NVA019 | Cor stop bar |
| NVA020 | Paint Stripe |
| NVA021 | Cor SW |
| NVA022 | Paint Stripe |
| NVA023 | Paint Stripe |
| NVA024 | Paint Stripe |
| NVA025 | Cor of Paint stripe |
| NVA026 | Cor SW |
| NVA027 | Paint Stripe |
| NVA028 | Paint Stripe |
| NVA029 | Paint Stripe |
| NVA030 | Sidewalk and drive |
| NVA031 | Paint stripe |
| NVA032 | Paint stripe |
| NVA033R | Cor stop bar |
| NVA034 | CL Paint line intersects |
| NVA035R | Tip of Arrow |
| NVA036 | Paint Stripe |
| NVA037 | Paint Stripe |
| NVA038 | Paint stripe |
| NVA039A | Cor of stop bar |
| NVA040 | Gravel |
| NVA041 | Gravel |
| NVA042 | Paint Stripe |
| NVA043 | Paint Stripe |
| NVA044R | Cor stop bar |
| NVA045 | Paint Stripe |
| NVA046 | Gravel |
| NVA047 | Paint Stripe |
| NVA047QC | NVA047QC |
| NVA048 | Paint Stripe |
| NVA049 | Cor of Asphalt |
| NVA050 | Paint Stripe |
| NVA051 | Paint Stripe |
| NVA052 | Paint Stripe |
| NVA053 | Paint Stripe |
| NVA054R | CL Paint line intersects |
| NVA055 | Paint Stripe |
| NVA056 | Paint Stripe |
| NVA057 | Paint Stripe |
| NVA058 | Cor of paint lines |
| NVA059 | Cor of SW |
| NVA060 | Cor SW |
| NVA061 | Gravel |
| NVA062 | Paint Stripe |
| NVA063 | Paint Stripe |
| NVA064 | Paint Stripe |
| NVA065 | Paint Stripe |
| NVA066 | Cor of stop bar |
| NVA067 | Paint Stripe |
| NVA068 | Cor SW |
| NVA069 | Paint Stripe |
| NVA070 | Paint Stripe |
| NVA071 | Paint Stripe |
| NVA072 | Paint Stripe |
| NVA073R | Cor of metal plate |
| NVA074 | Cor SW |
| NVA075 | Paint Stripe |
| NVA076 | Paint Stripe |
| NVA077 | Paint Stripe |
| NVA078 | Paint Stripe |
| NVA079 | Paint Stripe |
| QualInnBaseEast | Paint stripe |
| QualInnBaseQC | Paint stripe |
| QualInnNorth | Paint stripe |
| QualInnNorth | Paint Stripe |
| QualInnSW | Paint stripe |
| V016 | Virtual CORS |
| V018 | Virtual CORS |
| V019 | Virtual CORS |
| V020 | Virtual CORS |
| V022 | Virtual CORS |
| V025 | Virtual CORS |
| V026 | Virtual CORS |
| V027 | Virtual CORS |
| V028 | Virtual CORS |
| V029 | Virtual CORS |
| V030 | Virtual CORS |
| V033 | Virtual CORS |
| V036 | Virtual CORS |
| V037 | Virtual CORS |
| V038 | Virtual CORS |
| V043 | Virtual CORS |
| V053 | Virtual CORS |
| V056 | Virtual CORS |
| V058 | Virtual CORS |
| V060 | Virtual Base |
| V072 | Virtual CORS |
| V074 | Virtual CORS |
| V075 | Virtual CORS |
| VVA001 | Trees |
| VVA002 | Grass |
| VVA003 | Brush |
| VVA004 | Grass |
| VVA004 | Grass |
| VVA005 | Grass |
| VVA006 | Grass |
| VVA007 | Grass |
| VVA008 | Grass |
| VVA009 | Grass |
| VVA010 | Grass |
| VVA011 | Trees |
| VVA012 | Grass |
| VVA013 | Grass |
| VVA014 | Grass |
| VVA015 | Grass |
| VVA016 | Grass |
| VVA017 | Grass |
| VVA018 | Tall grass |
| VVA019 | Grass |
| VVA020 | Grass |
| VVA021 | Grass |
| VVA022 | Grass |
| VVA023 | Grass |
| VVA024 | Grass |
| VVA025 | Grass |
| VVA026 | Grass |
| VVA027 | Grass |
| VVA028 | Grass |
| VVA029 | Grass |
| VVA030 | Grass |
| VVA031 | Grass |
| VVA032R | Tall Grass |
| VVA033R | Tall Grass |
| VVA034 | Brush |
| VVA035 | Grass |
| VVA036 | Tall Grass |
| VVA037 | Tall grass |
| VVA038 | Tall Grass |
| VVA039 | Grass |
| VVA040 | Grass |
| VVA041 | Grass |
| VVA042 | Tall Grass |
| VVA043 | Grass |
| VVA044R | Shrub |
| VVA045 | Grass |
| VVA046 | Tall Grass |
| VVA047 | Tall Grass |
| VVA048 | Shrub |
| VVA049 | Grass |
| VVA050 | Grass |
| VVA051 | Tall Grass |
| VVA052 | Grass |
| VVA053 | Grass |
| VVA054 | Tall Grass |
| VVA055R | Grass |
| VVA056 | Trees |
| VVA057 | Grass |
| VVA058 | Grass |
| VVA059 | Grass |
| VVA060 | Grass |
| VVA061 | Trees |

Point RMSE Standard Deviations

| Name | Std Dev n (USft) | Std Dev e (USft) | Std Dev u (USft) | Std Dev Hz (USft) | Geoid Separation (USft) |
| --- | --- | --- | --- | --- | --- |
| Base93 | 0.028 | 0.024 | 0.069 | 0.037 | -109.162 |
| Base94 | 0.016 | 0.009 | 0.046 | 0.018 | -116.226 |
| Base95 | 0.014 | 0.011 | 0.030 | 0.018 | -111.926 |
| Base96 | 0.019 | 0.013 | 0.034 | 0.022 | -110.898 |
| Base97 | 0.019 | 0.014 | 0.033 | 0.023 | -111.357 |
| Base98 | 0.016 | 0.010 | 0.035 | 0.019 | -110.386 |
| Base99 | 0.036 | 0.026 | 0.073 | 0.045 | -110.726 |
| GCP001R | 0.009 | 0.005 | 0.024 | 0.011 | -106.559 |
| GCP002 | 0.029 | 0.020 | 0.068 | 0.035 | -106.723 |
| GCP003 | 0.009 | 0.008 | 0.020 | 0.012 | -108.096 |
| GCP004 | 0.011 | 0.008 | 0.029 | 0.013 | -107.720 |
| GCP004 | 0.022 | 0.014 | 0.055 | 0.026 | -107.720 |
| GCP005 | 0.007 | 0.006 | 0.016 | 0.009 | -108.289 |
| GCP006 | 0.011 | 0.009 | 0.022 | 0.014 | -108.435 |
| GCP007 | 0.017 | 0.011 | 0.040 | 0.020 | -109.314 |
| GCP008 | 0.058 | 0.025 | 0.070 | 0.063 | -108.383 |
| GCP009 | 0.028 | 0.024 | 0.069 | 0.037 | -109.783 |
| GCP010 | 0.033 | 0.023 | 0.064 | 0.040 | -110.857 |
| GCP011 | 0.025 | 0.017 | 0.061 | 0.030 | -108.390 |
| GCP012 | 0.037 | 0.027 | 0.074 | 0.045 | -110.725 |
| GCP013 | 0.032 | 0.027 | 0.056 | 0.042 | -110.001 |
| GCP014 | 0.028 | 0.019 | 0.067 | 0.033 | -110.002 |
| GCP015 | 0.029 | 0.021 | 0.050 | 0.035 | -111.452 |
| GCP016 | 0.019 | 0.016 | 0.045 | 0.025 | -109.456 |
| GCP017 | 0.023 | 0.014 | 0.036 | 0.027 | -110.791 |
| GCP018 | 0.026 | 0.019 | 0.054 | 0.032 | -109.550 |
| GCP019 | 0.035 | 0.022 | 0.077 | 0.042 | -110.906 |
| GCP020 | 0.022 | 0.017 | 0.043 | 0.028 | -112.865 |
| GCP021 | 0.033 | 0.022 | 0.079 | 0.039 | -112.727 |
| GCP022 | 0.017 | 0.010 | 0.048 | 0.020 | -116.218 |
| GCP023 | 0.018 | 0.013 | 0.037 | 0.022 | -112.888 |
| GCP023QC | 0.016 | 0.012 | 0.034 | 0.020 | -112.888 |
| GCP024 | 0.004 | 0.003 | 0.008 | 0.005 | -115.040 |
| GCP025 | 0.024 | 0.018 | 0.053 | 0.030 | -111.335 |
| GCP026 | 0.032 | 0.023 | 0.085 | 0.040 | -110.539 |
| GCP027 | 0.020 | 0.015 | 0.038 | 0.026 | -111.297 |
| GCP028 | 0.007 | 0.005 | 0.016 | 0.009 | -115.587 |
| GCP029 | 0.026 | 0.018 | 0.051 | 0.031 | -110.375 |
| JJW1 | 0.000 | 0.000 | 0.000 | 0.000 | -107.326 |
| NJBL | 0.007 | 0.006 | 0.016 | 0.009 | -109.314 |
| NJCM | 0.000 | 0.000 | 0.000 | 0.000 | -115.299 |
| NJGC | 0.000 | 0.000 | 0.000 | 0.000 | -108.343 |
| NJOC | 0.000 | 0.000 | 0.000 | 0.000 | -108.348 |
| NJOC | 0.005 | 0.004 | 0.011 | 0.006 | -108.348 |
| NJOC | 0.023 | 0.022 | 0.060 | 0.032 | -108.348 |
| NVA001R | 0.009 | 0.005 | 0.023 | 0.010 | -106.559 |
| NVA002 | 0.029 | 0.020 | 0.067 | 0.035 | -106.719 |
| NVA003R | 0.011 | 0.009 | 0.024 | 0.014 | -108.082 |
| NVA004 | 0.331 | 0.161 | 0.115 | 0.368 | -107.719 |
| NVA005 | 0.006 | 0.005 | 0.015 | 0.008 | -108.295 |
| NVA006 | 0.009 | 0.008 | 0.019 | 0.012 | -108.436 |
| NVA007 | 0.017 | 0.011 | 0.040 | 0.020 | -109.312 |
| NVA008 | 0.028 | 0.015 | 0.041 | 0.032 | -108.383 |
| NVA009 | 0.028 | 0.024 | 0.069 | 0.037 | -109.800 |
| NVA010 | 0.034 | 0.024 | 0.067 | 0.041 | -110.871 |
| NVA011 | 0.025 | 0.018 | 0.061 | 0.031 | -108.379 |
| NVA012 | 0.038 | 0.028 | 0.079 | 0.048 | -110.729 |
| NVA013 | 0.032 | 0.027 | 0.059 | 0.042 | -109.991 |
| NVA014 | 0.029 | 0.019 | 0.064 | 0.034 | -110.002 |
| NVA015R | 0.028 | 0.020 | 0.050 | 0.034 | -111.496 |
| NVA016 | 0.029 | 0.020 | 0.060 | 0.036 | -109.455 |
| NVA017 | 0.024 | 0.014 | 0.038 | 0.028 | -110.795 |
| NVA018 | 0.027 | 0.020 | 0.057 | 0.034 | -109.556 |
| NVA019 | 0.036 | 0.023 | 0.078 | 0.042 | -110.911 |
| NVA020 | 0.022 | 0.016 | 0.039 | 0.027 | -112.834 |
| NVA021 | 0.033 | 0.022 | 0.079 | 0.039 | -112.710 |
| NVA022 | 0.017 | 0.009 | 0.048 | 0.019 | -116.227 |
| NVA023 | 0.017 | 0.013 | 0.039 | 0.021 | -112.895 |
| NVA024 | 0.004 | 0.003 | 0.009 | 0.005 | -115.025 |
| NVA025 | 0.024 | 0.018 | 0.054 | 0.030 | -111.348 |
| NVA026 | 0.033 | 0.023 | 0.085 | 0.040 | -110.548 |
| NVA027 | 0.020 | 0.016 | 0.040 | 0.026 | -111.296 |
| NVA028 | 0.007 | 0.005 | 0.016 | 0.009 | -115.595 |
| NVA029 | 0.026 | 0.018 | 0.051 | 0.031 | -110.388 |
| NVA030 | 0.020 | 0.019 | 0.047 | 0.027 | -106.416 |
| NVA031 | 0.020 | 0.017 | 0.040 | 0.027 | -107.681 |
| NVA032 | 0.012 | 0.010 | 0.024 | 0.016 | -107.875 |
| NVA033R | 0.038 | 0.026 | 0.074 | 0.046 | -108.543 |
| NVA034 | 0.008 | 0.009 | 0.018 | 0.012 | -106.961 |
| NVA035R | 0.019 | 0.011 | 0.054 | 0.022 | -107.147 |
| NVA036 | 0.029 | 0.025 | 0.071 | 0.038 | -110.153 |
| NVA037 | 0.019 | 0.014 | 0.040 | 0.024 | -109.234 |
| NVA038 | 0.017 | 0.015 | 0.032 | 0.022 | -108.583 |
| NVA039A | 0.035 | 0.021 | 0.062 | 0.041 | -108.678 |
| NVA040 | 0.020 | 0.014 | 0.037 | 0.025 | -108.565 |
| NVA041 | 0.019 | 0.016 | 0.039 | 0.025 | -108.002 |
| NVA042 | 0.032 | 0.027 | 0.064 | 0.042 | -109.048 |
| NVA043 | 0.020 | 0.017 | 0.045 | 0.026 | -110.198 |
| NVA044R | 0.028 | 0.034 | 0.103 | 0.044 | -108.950 |
| NVA045 | 0.018 | 0.016 | 0.043 | 0.024 | -109.784 |
| NVA046 | 0.018 | 0.011 | 0.036 | 0.021 | -110.384 |
| NVA047 | 0.020 | 0.015 | 0.036 | 0.025 | -111.847 |
| NVA047QC | 0.020 | 0.015 | 0.036 | 0.025 | -111.847 |
| NVA048 | 0.023 | 0.016 | 0.047 | 0.028 | -110.574 |
| NVA049 | 0.030 | 0.021 | 0.059 | 0.036 | -111.194 |
| NVA050 | 0.020 | 0.016 | 0.044 | 0.025 | -112.945 |
| NVA051 | 0.014 | 0.013 | 0.033 | 0.019 | -113.545 |
| NVA052 | 0.022 | 0.020 | 0.049 | 0.030 | -112.899 |
| NVA053 | 0.021 | 0.013 | 0.048 | 0.024 | -109.746 |
| NVA054R | 0.010 | 0.008 | 0.025 | 0.013 | -108.071 |
| NVA055 | 0.015 | 0.011 | 0.037 | 0.018 | -115.647 |
| NVA056 | 0.036 | 0.025 | 0.064 | 0.043 | -110.595 |
| NVA057 | 0.023 | 0.016 | 0.047 | 0.028 | -109.822 |
| NVA058 | 0.009 | 0.006 | 0.023 | 0.011 | -108.117 |
| NVA059 | 0.022 | 0.015 | 0.038 | 0.027 | -111.393 |
| NVA060 | 0.028 | 0.019 | 0.092 | 0.034 | -110.550 |
| NVA061 | 0.019 | 0.016 | 0.049 | 0.025 | -111.731 |
| NVA062 | 0.036 | 0.027 | 0.073 | 0.045 | -110.775 |
| NVA063 | 0.017 | 0.015 | 0.039 | 0.022 | -113.830 |
| NVA064 | 0.017 | 0.013 | 0.035 | 0.021 | -112.114 |
| NVA065 | 0.026 | 0.018 | 0.044 | 0.032 | -110.889 |
| NVA066 | 0.019 | 0.013 | 0.035 | 0.023 | -116.489 |
| NVA067 | 0.006 | 0.005 | 0.013 | 0.008 | -115.478 |
| NVA068 | 0.018 | 0.012 | 0.038 | 0.022 | -114.007 |
| NVA069 | 0.042 | 0.028 | 0.096 | 0.050 | -112.131 |
| NVA070 | 0.017 | 0.011 | 0.037 | 0.020 | -110.120 |
| NVA071 | 0.026 | 0.018 | 0.045 | 0.032 | -112.042 |
| NVA072 | 0.023 | 0.015 | 0.044 | 0.028 | -110.810 |
| NVA073R | 0.021 | 0.014 | 0.058 | 0.026 | -114.451 |
| NVA074 | 0.024 | 0.018 | 0.047 | 0.030 | -111.039 |
| NVA075 | 0.024 | 0.017 | 0.045 | 0.029 | -111.140 |
| NVA076 | 0.025 | 0.017 | 0.052 | 0.030 | -110.945 |
| NVA077 | 0.040 | 0.029 | 0.080 | 0.049 | -110.895 |
| NVA078 | 0.039 | 0.026 | 0.087 | 0.047 | -112.313 |
| NVA079 | 0.020 | 0.014 | 0.047 | 0.024 | -110.491 |
| QualInnBaseEast | 0.014 | 0.014 | 0.038 | 0.019 | -106.667 |
| QualInnBaseQC | 0.011 | 0.007 | 0.020 | 0.013 | -106.667 |
| QualInnNorth | 0.008 | 0.005 | 0.014 | 0.010 | -106.666 |
| QualInnNorth | 0.000 | 0.000 | 0.000 | 0.000 | -106.666 |
| QualInnSW | 0.008 | 0.005 | 0.014 | 0.010 | -106.669 |
| V016 | 0.018 | 0.013 | 0.037 | 0.022 | -109.214 |
| V018 | 0.008 | 0.005 | 0.014 | 0.009 | -106.669 |
| V019 | 0.008 | 0.007 | 0.019 | 0.010 | -106.553 |
| V020 | 0.010 | 0.006 | 0.018 | 0.011 | -106.417 |
| V022 | 0.010 | 0.006 | 0.020 | 0.012 | -106.725 |
| V025 | 0.006 | 0.007 | 0.015 | 0.009 | -106.964 |
| V026 | 0.006 | 0.006 | 0.015 | 0.009 | -107.153 |
| V027 | 0.006 | 0.006 | 0.014 | 0.009 | -107.686 |
| V028 | 0.007 | 0.006 | 0.015 | 0.009 | -107.874 |
| V029 | 0.007 | 0.007 | 0.017 | 0.010 | -108.101 |
| V030 | 0.007 | 0.007 | 0.017 | 0.010 | -108.436 |
| V033 | 0.006 | 0.005 | 0.013 | 0.008 | -107.722 |
| V036 | 0.006 | 0.005 | 0.014 | 0.008 | -108.117 |
| V037 | 0.006 | 0.005 | 0.015 | 0.008 | -108.290 |
| V038 | 0.006 | 0.006 | 0.014 | 0.008 | -108.072 |
| V043 | 0.007 | 0.006 | 0.016 | 0.009 | -108.544 |
| V053 | 0.007 | 0.006 | 0.017 | 0.010 | -108.584 |
| V056 | 0.007 | 0.006 | 0.016 | 0.009 | -108.678 |
| V058 | 0.007 | 0.006 | 0.017 | 0.010 | -108.585 |
| V060 | 0.028 | 0.025 | 0.054 | 0.038 | -109.041 |
| V072 | 0.008 | 0.007 | 0.017 | 0.010 | -107.725 |
| V074 | 0.008 | 0.006 | 0.017 | 0.010 | -107.708 |
| V075 | 0.028 | 0.024 | 0.068 | 0.037 | -109.796 |
| VVA001 | 0.012 | 0.008 | 0.028 | 0.014 | -106.554 |
| VVA002 | 0.029 | 0.019 | 0.067 | 0.034 | -106.722 |
| VVA003 | 0.010 | 0.008 | 0.022 | 0.013 | -108.098 |
| VVA004 | 0.009 | 0.007 | 0.026 | 0.011 | -107.720 |
| VVA004 | 0.023 | 0.015 | 0.058 | 0.027 | -107.720 |
| VVA005 | 0.007 | 0.006 | 0.017 | 0.010 | -108.288 |
| VVA006 | 0.009 | 0.008 | 0.018 | 0.012 | -108.436 |
| VVA007 | 0.016 | 0.010 | 0.039 | 0.019 | -109.311 |
| VVA008 | 0.026 | 0.014 | 0.037 | 0.029 | -108.342 |
| VVA009 | 0.028 | 0.024 | 0.068 | 0.037 | -109.781 |
| VVA010 | 0.032 | 0.023 | 0.063 | 0.039 | -110.882 |
| VVA011 | 0.025 | 0.018 | 0.062 | 0.031 | -108.337 |
| VVA012 | 0.040 | 0.029 | 0.081 | 0.049 | -110.744 |
| VVA013 | 0.031 | 0.027 | 0.055 | 0.041 | -109.954 |
| VVA014 | 0.021 | 0.016 | 0.048 | 0.027 | -110.033 |
| VVA015 | 0.024 | 0.018 | 0.043 | 0.030 | -111.486 |
| VVA016 | 0.018 | 0.015 | 0.043 | 0.024 | -109.461 |
| VVA017 | 0.022 | 0.014 | 0.035 | 0.026 | -110.790 |
| VVA018 | 0.026 | 0.019 | 0.053 | 0.032 | -109.500 |
| VVA019 | 0.033 | 0.021 | 0.075 | 0.040 | -110.826 |
| VVA020 | 0.020 | 0.014 | 0.035 | 0.025 | -112.862 |
| VVA021 | 0.032 | 0.021 | 0.078 | 0.039 | -112.703 |
| VVA022 | 0.017 | 0.009 | 0.048 | 0.019 | -116.221 |
| VVA023 | 0.014 | 0.011 | 0.032 | 0.017 | -112.852 |
| VVA024 | 0.004 | 0.003 | 0.008 | 0.005 | -115.000 |
| VVA025 | 0.023 | 0.017 | 0.052 | 0.029 | -111.338 |
| VVA026 | 0.033 | 0.023 | 0.086 | 0.040 | -110.536 |
| VVA027 | 0.020 | 0.015 | 0.037 | 0.025 | -111.280 |
| VVA028 | 0.007 | 0.005 | 0.015 | 0.008 | -115.555 |
| VVA029 | 0.025 | 0.018 | 0.050 | 0.031 | -110.391 |
| VVA030 | 0.007 | 0.007 | 0.016 | 0.010 | -106.992 |
| VVA031 | 0.011 | 0.010 | 0.023 | 0.015 | -107.882 |
| VVA032R | 0.020 | 0.017 | 0.041 | 0.026 | -108.000 |
| VVA033R | 0.021 | 0.018 | 0.044 | 0.028 | -108.581 |
| VVA034 | 0.035 | 0.021 | 0.063 | 0.041 | -108.679 |
| VVA035 | 0.009 | 0.007 | 0.022 | 0.011 | -108.115 |
| VVA036 | 0.020 | 0.015 | 0.041 | 0.025 | -109.232 |
| VVA037 | 0.029 | 0.025 | 0.070 | 0.038 | -110.157 |
| VVA038 | 0.020 | 0.014 | 0.037 | 0.024 | -108.597 |
| VVA039 | 0.022 | 0.014 | 0.037 | 0.026 | -111.387 |
| VVA040 | 0.036 | 0.025 | 0.064 | 0.043 | -110.612 |
| VVA041 | 0.014 | 0.010 | 0.034 | 0.018 | -115.655 |
| VVA042 | 0.022 | 0.019 | 0.048 | 0.029 | -112.905 |
| VVA043 | 0.021 | 0.018 | 0.048 | 0.027 | -110.194 |
| VVA044R | 0.016 | 0.014 | 0.037 | 0.021 | -113.784 |
| VVA045 | 0.012 | 0.011 | 0.029 | 0.016 | -113.529 |
| VVA046 | 0.030 | 0.020 | 0.099 | 0.036 | -110.541 |
| VVA047 | 0.019 | 0.015 | 0.035 | 0.024 | -111.844 |
| VVA048 | 0.025 | 0.016 | 0.041 | 0.030 | -110.883 |
| VVA049 | 0.019 | 0.015 | 0.046 | 0.024 | -111.730 |
| VVA050 | 0.041 | 0.032 | 0.094 | 0.052 | -109.801 |
| VVA051 | 0.027 | 0.019 | 0.053 | 0.033 | -111.179 |
| VVA052 | 0.016 | 0.013 | 0.034 | 0.021 | -112.105 |
| VVA053 | 0.022 | 0.015 | 0.046 | 0.027 | -110.567 |
| VVA054 | 0.017 | 0.011 | 0.036 | 0.020 | -110.402 |
| VVA055R | 0.036 | 0.027 | 0.073 | 0.045 | -110.774 |
| VVA056 | 0.034 | 0.029 | 0.069 | 0.045 | -109.043 |
| VVA057 | 0.025 | 0.016 | 0.048 | 0.029 | -110.114 |
| VVA058 | 0.014 | 0.014 | 0.036 | 0.020 | -112.942 |
| VVA059 | 0.040 | 0.026 | 0.087 | 0.047 | -112.302 |
| VVA060 | 0.041 | 0.027 | 0.094 | 0.049 | -112.166 |
| VVA061 | 0.011 | 0.010 | 0.024 | 0.015 | -106.424 |

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.2

1        National Geodetic Survey,   Retrieval Date = NOVEMBER 12, 2018

DF8717 ***********************************************************************

DF8717  CORS        -  This is a GPS Continuously Operating Reference Station.

DF8717  DESIGNATION -  NJGC CORS ARP

DF8717  CORS_ID     -  NJGC

DF8717  PID         -  DF8717

DF8717  STATE/COUNTY-  NJ/GLOUCESTER

DF8717  COUNTRY     -  US

DF8717  USGS QUAD   -  RUNNEMEDE (1994)

DF8717

DF8717                         *CURRENT SURVEY CONTROL

DF8717  ______________________________________________________________________

DF8717* NAD 83(2011) POSITION- 39 46 52.79148(N) 075 07 11.25002(W)   ADJUSTED

DF8717* NAD 83(2011) ELLIP HT-    -3.994 (meters)        (08/??/11)   ADJUSTED

DF8717* NAD 83(2011) EPOCH   -  2010.00

DF8717* NAVD 88 ORTHO HEIGHT -    29.036 (meters)       95.26  (feet) ADJUSTED

DF8717  ______________________________________________________________________

DF8717  GEOID HEIGHT    -        -33.023 (meters)                     GEOID12B

DF8717  NAD 83(2011) X  -  1,260,440.053 (meters)                     COMP

DF8717  NAD 83(2011) Y  - -4,743,675.695 (meters)                     COMP

DF8717  NAD 83(2011) Z  -  4,059,354.199 (meters)                     COMP

DF8717  VERT ORDER      -  FIRST     CLASS II

DF8717

DF8717  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

DF8717  Standards:

DF8717         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

DF8717            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

DF8717  -------------------------------------------------------------------

DF8717  NETWORK    1.30   4.29           0.57   0.48   2.19      0.01712700

DF8717  -------------------------------------------------------------------

DF8717

DF8717

DF8717.The coordinates were established by GPS observations

DF8717.and adjusted by the National Geodetic Survey in August 2011.

DF8717

DF8717.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DF8717.been affixed to the stable North American Tectonic Plate.

DF8717

DF8717.The coordinates are valid at the epoch date displayed above

DF8717.which is a decimal equivalence of Year/Month/Day.

DF8717

DF8717.The orthometric height was determined by differential leveling and

DF8717.adjusted by the NATIONAL GEODETIC SURVEY

DF8717.in May 2012.

DF8717

DF8717.No vertical observational check was made to the station.

DF8717

DF8717.Significant digits in the geoid height do not necessarily reflect accuracy.

DF8717.GEOID12B height accuracy estimate available here.

DF8717

DF8717.The PID for the CORS L1 Phase Center is DO7544.

DF8717

DF8717.The XYZ, and position/ellipsoidal ht. are equivalent.

DF8717

DF8717.The ellipsoidal height was determined by GPS observations

DF8717.and is referenced to NAD 83.

DF8717

DF8717. The following values were computed from the NAD 83(2011) position.

DF8717

DF8717;                    North         East     Units Scale Factor Converg.

DF8717;SPC NJ       -   105,421.197    96,910.281   MT  0.99993469   -0 23 47.7

DF8717;SPC NJ       -   345,869.38    317,946.48   sFT  0.99993469   -0 23 47.7

DF8717;UTM  18      - 4,403,494.415   489,742.075   MT  0.99960130   -0 04 35.9

DF8717

DF8717!             -  Elev Factor  x  Scale Factor =   Combined Factor

DF8717!SPC NJ       -   1.00000063  x   0.99993469  =   0.99993532

DF8717!UTM  18      -   1.00000063  x   0.99960130  =   0.99960193

DF8717

DF8717_U.S. NATIONAL GRID SPATIAL ADDRESS: 18SVK8974203494(NAD 83)

DF8717

DF8717                          SUPERSEDED SURVEY CONTROL

DF8717

DF8717  ELLIP H (06/27/12)   -3.986  (m)                       GP(2010.00) 0 0

DF8717  NAD 83(2011)-  39 46 52.79162(N)    075 07 11.24999(W) AD(2010.00) c

DF8717  ELLIP H (02/10/07)   -3.984  (m)                       GP(2002.00)

DF8717  NAD 83(2007)-  39 46 52.79170(N)    075 07 11.25056(W) AD(2002.00) c

DF8717  NAD 83(CORS)-  39 46 52.79170(N)    075 07 11.25056(W) AD(2002.00) c

DF8717  ELLIP H (11/??/03)   -3.984  (m)                       GP(2002.00) c c

DF8717

DF8717.Superseded values are not recommended for survey control.

DF8717

DF8717.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DF8717.See file dsdata.pdf to determine how the superseded data were derived.

DF8717

DF8717_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DF8717

DF8717                          STATION DESCRIPTION

DF8717

DF8717'DESCRIBED BY NATIONAL GEODETIC SURVEY 2011

DF8717'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DF8717'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DF8717'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DF8717'   ftp://cors.ngs.noaa.gov/cors/README.txt

DF8717'   ftp://cors.ngs.noaa.gov/cors/coord/coord_08

DF8717'   ftp://cors.ngs.noaa.gov/cors/station_log

DF8717'   http://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:06

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.2

1        National Geodetic Survey,   Retrieval Date = NOVEMBER 12, 2018

DI1077 ***********************************************************************

DI1077  CORS        -  This is a GPS Continuously Operating Reference Station.

DI1077  DESIGNATION -  NJOC CORS ARP

DI1077  CORS_ID     -  NJOC

DI1077  PID         -  DI1077

DI1077  STATE/COUNTY-  NJ/OCEAN

DI1077  COUNTRY     -  US

DI1077  USGS QUAD   -  TOMS RIVER (1989)

DI1077

DI1077                         *CURRENT SURVEY CONTROL

DI1077  ______________________________________________________________________

DI1077* NAD 83(2011) POSITION- 39 57 10.02328(N) 074 11 36.59328(W)   ADJUSTED

DI1077* NAD 83(2011) ELLIP HT-    -8.184 (meters)        (08/??/11)   ADJUSTED

DI1077* NAD 83(2011) EPOCH   -  2010.00

DI1077* NAVD 88 ORTHO HEIGHT -    24.830 (meters)       81.46  (feet) ADJUSTED

DI1077  ______________________________________________________________________

DI1077  GEOID HEIGHT    -        -33.025 (meters)                     GEOID12B

DI1077  NAD 83(2011) X  -  1,333,637.621 (meters)                     COMP

DI1077  NAD 83(2011) Y  - -4,710,934.885 (meters)                     COMP

DI1077  NAD 83(2011) Z  -  4,073,962.892 (meters)                     COMP

DI1077  VERT ORDER      -  FIRST     CLASS II

DI1077

DI1077  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

DI1077  Standards:

DI1077         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

DI1077            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

DI1077  -------------------------------------------------------------------

DI1077  NETWORK    2.90   9.65           1.28   1.08   4.92      0.03411100

DI1077  -------------------------------------------------------------------

DI1077

DI1077

DI1077.The coordinates were established by GPS observations

DI1077.and adjusted by the National Geodetic Survey in August 2011.

DI1077

DI1077.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DI1077.been affixed to the stable North American Tectonic Plate.

DI1077

DI1077.The coordinates are valid at the epoch date displayed above

DI1077.which is a decimal equivalence of Year/Month/Day.

DI1077

DI1077.The orthometric height was determined by differential leveling and

DI1077.adjusted by the NATIONAL GEODETIC SURVEY

DI1077.in May 2012.

DI1077

DI1077.No vertical observational check was made to the station.

DI1077

DI1077.Significant digits in the geoid height do not necessarily reflect accuracy.

DI1077.GEOID12B height accuracy estimate available here.

DI1077

DI1077.The PID for the CORS L1 Phase Center is DO6882.

DI1077

DI1077.Photographs are available for this station.

DI1077

DI1077.The XYZ, and position/ellipsoidal ht. are equivalent.

DI1077

DI1077.The ellipsoidal height was determined by GPS observations

DI1077.and is referenced to NAD 83.

DI1077

DI1077. The following values were computed from the NAD 83(2011) position.

DI1077

DI1077;                    North         East     Units Scale Factor Converg.

DI1077;SPC NJ       -   124,317.352   176,188.798   MT  0.99990844   +0 11 48.6

DI1077;SPC NJ       -   407,864.51    578,046.08   sFT  0.99990844   +0 11 48.6

DI1077;UTM  18      - 4,422,828.117   568,890.553   MT  0.99965842   +0 31 04.5

DI1077

DI1077!             -  Elev Factor  x  Scale Factor =   Combined Factor

DI1077!SPC NJ       -   1.00000128  x   0.99990844  =   0.99990972

DI1077!UTM  18      -   1.00000128  x   0.99965842  =   0.99965970

DI1077

DI1077_U.S. NATIONAL GRID SPATIAL ADDRESS: 18SWK6889022828(NAD 83)

DI1077

DI1077                          SUPERSEDED SURVEY CONTROL

DI1077

DI1077  NAD 83(CORS)-  39 57 10.02338(N)    074 11 36.59353(W) AD(2002.00) c

DI1077  ELLIP H (08/??/06)   -8.169  (m)                       GP(2002.00) c c

DI1077

DI1077.Superseded values are not recommended for survey control.

DI1077

DI1077.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DI1077.See file dsdata.pdf to determine how the superseded data were derived.

DI1077

DI1077_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DI1077

DI1077                          STATION DESCRIPTION

DI1077

DI1077'DESCRIBED BY NATIONAL GEODETIC SURVEY 2011

DI1077'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DI1077'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DI1077'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DI1077'   ftp://cors.ngs.noaa.gov/cors/README.txt

DI1077'   ftp://cors.ngs.noaa.gov/cors/coord/coord_08

DI1077'   ftp://cors.ngs.noaa.gov/cors/station_log

DI1077'   http://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:05

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.2

1        National Geodetic Survey,   Retrieval Date = NOVEMBER 12, 2018

DK7749 ***********************************************************************

DK7749  CORS        -  This is a GPS Continuously Operating Reference Station.

DK7749  DESIGNATION -  NEPTUNE TOWNSHIP CORS ARP

DK7749  CORS_ID     -  NJNT

DK7749  PID         -  DK7749

DK7749  STATE/COUNTY-  NJ/MONMOUTH

DK7749  COUNTRY     -  US

DK7749  USGS QUAD   -  ASBURY PARK (1989)

DK7749

DK7749                         *CURRENT SURVEY CONTROL

DK7749  ______________________________________________________________________

DK7749* NAD 83(2011) POSITION- 40 12 33.61966(N) 074 02 11.58975(W)   ADJUSTED

DK7749* NAD 83(2011) ELLIP HT-   -15.522 (meters)        (08/??/11)   ADJUSTED

DK7749* NAD 83(2011) EPOCH   -  2010.00

DK7749* NAVD 88 ORTHO HEIGHT -    17.301 (meters)       56.76  (feet) ADJUSTED

DK7749  ______________________________________________________________________

DK7749  GEOID HEIGHT    -        -32.827 (meters)                     GEOID12B

DK7749  NAD 83(2011) X  -  1,341,490.883 (meters)                     COMP

DK7749  NAD 83(2011) Y  - -4,689,624.213 (meters)                     COMP

DK7749  NAD 83(2011) Z  -  4,095,754.366 (meters)                     COMP

DK7749  VERT ORDER      -  FIRST     CLASS II

DK7749

DK7749.Formal positional accuracy estimates are not available for this CORS

DK7749.because its coordinates were determined in part using modeled

DK7749.velocities. Approximate one-sigma accuracies for latitude, longitude,

DK7749.and ellipsoid height can be obtained from the short-term time series.

DK7749.Additional information regarding modeled velocities is available on

DK7749.the CORS Coordinates and Multi-Year CORS Solution FAQ web pages.

DK7749

DK7749.The coordinates were established by GPS observations

DK7749.and adjusted by the National Geodetic Survey in August 2011.

DK7749

DK7749.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DK7749.been affixed to the stable North American Tectonic Plate.

DK7749

DK7749.The coordinates are valid at the epoch date displayed above

DK7749.which is a decimal equivalence of Year/Month/Day.

DK7749

DK7749.The orthometric height was determined by differential leveling and

DK7749.adjusted by the NATIONAL GEODETIC SURVEY

DK7749.in May 2012.

DK7749

DK7749.No vertical observational check was made to the station.

DK7749

DK7749.Significant digits in the geoid height do not necessarily reflect accuracy.

DK7749.GEOID12B height accuracy estimate available here.

DK7749

DK7749.The PID for the CORS L1 Phase Center is DQ1143.

DK7749

DK7749.The XYZ, and position/ellipsoidal ht. are equivalent.

DK7749

DK7749.The ellipsoidal height was determined by GPS observations

DK7749.and is referenced to NAD 83.

DK7749

DK7749. The following values were computed from the NAD 83(2011) position.

DK7749

DK7749;                    North         East     Units Scale Factor Converg.

DK7749;SPC NJ       -   152,859.366   189,450.562   MT  0.99991915   +0 17 57.1

DK7749;SPC NJ       -   501,506.10    621,555.72   sFT  0.99991915   +0 17 57.1

DK7749;UTM  18      - 4,451,437.242   581,988.537   MT  0.99968275   +0 37 19.3

DK7749

DK7749!             -  Elev Factor  x  Scale Factor =   Combined Factor

DK7749!SPC NJ       -   1.00000244  x   0.99991915  =   0.99992158

DK7749!UTM  18      -   1.00000244  x   0.99968275  =   0.99968518

DK7749

DK7749_U.S. NATIONAL GRID SPATIAL ADDRESS: 18TWK8198851437(NAD 83)

DK7749

DK7749                          SUPERSEDED SURVEY CONTROL

DK7749

DK7749  NAD 83(CORS)-  40 12 33.62005(N)    074 02 11.59038(W) AD(2002.00) c

DK7749  ELLIP H (12/??/08)  -15.507  (m)                       GP(2002.00) c c

DK7749

DK7749.Superseded values are not recommended for survey control.

DK7749

DK7749.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DK7749.See file dsdata.pdf to determine how the superseded data were derived.

DK7749

DK7749_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DK7749

DK7749                          STATION DESCRIPTION

DK7749

DK7749'DESCRIBED BY NATIONAL GEODETIC SURVEY 2011

DK7749'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DK7749'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DK7749'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DK7749'   ftp://cors.ngs.noaa.gov/cors/README.txt

DK7749'   ftp://cors.ngs.noaa.gov/cors/coord/coord_08

DK7749'   ftp://cors.ngs.noaa.gov/cors/station_log

DK7749'   http://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:05

## The NGS Data Sheet

##### See file dsdata.pdf for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 8.12.5.2

1        National Geodetic Survey,   Retrieval Date = NOVEMBER 12, 2018

DI3828 ***********************************************************************

DI3828  CORS        -  This is a GPS Continuously Operating Reference Station.

DI3828  DESIGNATION -  MIDDLE TOWNSHIP CORS ARP

DI3828  CORS_ID     -  NJCM

DI3828  PID         -  DI3828

DI3828  STATE/COUNTY-  NJ/CAPE MAY

DI3828  COUNTRY     -  US

DI3828  USGS QUAD   -  STONE HARBOR (1972)

DI3828

DI3828                         *CURRENT SURVEY CONTROL

DI3828  ______________________________________________________________________

DI3828* NAD 83(2011) POSITION- 39 06 02.39693(N) 074 48 10.42433(W)   ADJUSTED

DI3828* NAD 83(2011) ELLIP HT-   -25.313 (meters)        (08/??/11)   ADJUSTED

DI3828* NAD 83(2011) EPOCH   -  2010.00

DI3828* NAVD 88 ORTHO HEIGHT -     9.846 (meters)       32.30  (feet) ADJUSTED

DI3828  ______________________________________________________________________

DI3828  GEOID HEIGHT    -        -35.143 (meters)                     GEOID12B

DI3828  NAD 83(2011) X  -  1,299,237.868 (meters)                     COMP

DI3828  NAD 83(2011) Y  - -4,782,945.132 (meters)                     COMP

DI3828  NAD 83(2011) Z  -  4,000,979.917 (meters)                     COMP

DI3828  VERT ORDER      -  FIRST     CLASS II

DI3828

DI3828  Network accuracy estimates per FGDC Geospatial Positioning Accuracy

DI3828  Standards:

DI3828         FGDC (95% conf, cm)     Standard deviation (cm)     CorrNE

DI3828            Horiz  Ellip           SD_N   SD_E   SD_h      (unitless)

DI3828  -------------------------------------------------------------------

DI3828  NETWORK    2.02   6.86           0.88   0.77   3.50     -0.02994800

DI3828  -------------------------------------------------------------------

DI3828

DI3828

DI3828.The coordinates were established by GPS observations

DI3828.and adjusted by the National Geodetic Survey in August 2011.

DI3828

DI3828.NAD 83(2011) refers to NAD 83 coordinates where the reference frame has

DI3828.been affixed to the stable North American Tectonic Plate.

DI3828

DI3828.The coordinates are valid at the epoch date displayed above

DI3828.which is a decimal equivalence of Year/Month/Day.

DI3828

DI3828.The orthometric height was determined by differential leveling and

DI3828.adjusted by the NATIONAL GEODETIC SURVEY

DI3828.in March 2014.

DI3828

DI3828.No vertical observational check was made to the station.

DI3828

DI3828.Significant digits in the geoid height do not necessarily reflect accuracy.

DI3828.GEOID12B height accuracy estimate available here.

DI3828

DI3828.The PID for the CORS L1 Phase Center is DO6883.

DI3828

DI3828.The XYZ, and position/ellipsoidal ht. are equivalent.

DI3828

DI3828.The ellipsoidal height was determined by GPS observations

DI3828.and is referenced to NAD 83.

DI3828

DI3828. The following values were computed from the NAD 83(2011) position.

DI3828

DI3828;                    North         East     Units Scale Factor Converg.

DI3828;SPC NJ       -    29,718.584   123,801.055   MT  0.99990845   -0 11 27.7

DI3828;SPC NJ       -    97,501.72    406,170.63   sFT  0.99990845   -0 11 27.7

DI3828;UTM  18      - 4,327,966.162   517,043.408   MT  0.99960358   +0 07 27.5

DI3828

DI3828!             -  Elev Factor  x  Scale Factor =   Combined Factor

DI3828!SPC NJ       -   1.00000397  x   0.99990845  =   0.99991242

DI3828!UTM  18      -   1.00000397  x   0.99960358  =   0.99960755

DI3828

DI3828_U.S. NATIONAL GRID SPATIAL ADDRESS: 18SWJ1704327966(NAD 83)

DI3828

DI3828                          SUPERSEDED SURVEY CONTROL

DI3828

DI3828  NAD 83(CORS)-  39 06 02.39710(N)    074 48 10.42446(W) AD(2002.00) c

DI3828  ELLIP H (03/??/07)  -25.289  (m)                       GP(2002.00) c c

DI3828

DI3828.Superseded values are not recommended for survey control.

DI3828

DI3828.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DI3828.See file dsdata.pdf to determine how the superseded data were derived.

DI3828

DI3828_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DI3828_MAGNETIC: N = NO MAGNETIC MATERIAL

DI3828

DI3828                          STATION DESCRIPTION

DI3828

DI3828'DESCRIBED BY NATIONAL GEODETIC SURVEY 2011

DI3828'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DI3828'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DI3828'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DI3828'   ftp://cors.ngs.noaa.gov/cors/README.txt

DI3828'   ftp://cors.ngs.noaa.gov/cors/coord/coord_08

DI3828'   ftp://cors.ngs.noaa.gov/cors/station_log

DI3828'   http://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:05

## The KEYNETGPS Data Sheet Info

PROJECT SURVEYOR	Steven A. Wood