Elevation QA Report

Project:       Contractor:

Data Delivery Date:   Date Data Reviewed:

Reviewer:    Total Square Miles Reviewed:

Elevation Type:     Format:       Grid Spacing:    Tile size:

Projection:       Zone:       Datum:         Units:

Licensing:           Metadata:

Materials Received:

Vertical Accuracy Test Performed:       Test Point Source:            RMSE:

Vertical Accuracy Test Notes:

QC Review Summary:

11-2-2010

LiDAR Quality Control (QC) Review Process

Preparation:

-Metadata reviewed to determine data projection, datum, format, etc.

-If ARRA contract, check for raw .LAS files, classified .LAS files, breaklines, blind control points,

and DEM in Image or Grid format

-Open data in Global Mapper

Vertical accuracy testing:

-If ARRA contract, use Vertical Accuracy Test Worksheet to perform RMSE on 20 blind point

positions provided by contractor

Inspection and Correction of data:

-Minimum and maximum elevations in dataset; correct if in error

-Appropriate hydro flattening as specified in V12 Lidar Specification (For ARRA/GPSC Data)

-Data void areas

-Data spikes

-Tile edge seam lines

-Non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Elevation errors - raised/lowered areas/tiles

-Other surface treatment anomalies

-Check DRGs for correct elevations and horizontal positioning (if test points not available)

-Create footprint (project boundary) shape file and establish square miles

During Inspection, identify data errors and create “error” file folder:

-Capture geo-referenced JPG or TIFF image(s) of identified errors

-Copy to Error file

During Inspection, level elevations and remove artifacts (these two steps not done for ARRA data):

-Level smoothing to remove non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Level data spikes where possible

Export image files and create project Elevation QC Review Report:

-Export ERDAS Imagine image files in native projection and resolution

-If ARRA, Copy Vertical Accuracy Test Worksheet into QC Report

-Place QC Review Process and Project Area Extent into QC Report

-If rejected, attach sample geo-referenced JPG or TIFF error images with an explanation of reason

-If rejected, restart QC process when replacement data is received

-Provide completed Elevation QC Review Report to Elevation Supervisor for final viewing

-Add QC Report, footprint, Imagine image(s), and Error file to original data file for final shipment to EROS

Baldwin Co. East AL Area Extent

Vertical Accuracy

| Baldwin Co. AL East-West- Vertical Accuracy Statistic Worksheet |  |  |  |
| --- | --- | --- | --- |
| elevations units in meters |  |  |  |
| A | D | E | F | G | H |  |
| Point | Point | z | z |  |  |  |
| number | description | Vendor Elev | NGTOC Elev | diff in z | (diff in z)2 | Comments |
| B101 | B101 | 1.355 | 1.322 | 0.033 | 0.001 |  |
| B102 | B102 | 5.689 | 5.624 | 0.065 | 0.004 |  |
| B103 | B103 | 19.822 | 19.786 | 0.036 | 0.001 |  |
| B104 | B104 | 14.042 | 14.04 | 0.002 | 0.000 |  |
| B105 | B105 | 1.851 | 1.964 | -0.113 | 0.013 |  |
| B201 | B201 | 12.917 | 12.428 | 0.489 | 0.239 |  |
| B202 | B202 | 20.79 | 20.73 | 0.060 | 0.004 |  |
| B203 | B203 | 9.783 | 9.803 | -0.020 | 0.000 |  |
| B204 | B204 | 23.311 | 23.369 | -0.058 | 0.003 |  |
| B205 | B205 | 22.356 | 22.41 | -0.054 | 0.003 |  |
| B206 | B206 | 25.102 | 25.021 | 0.081 | 0.007 |  |
| B207 | B207 | 1.13 | 1.027 | 0.103 | 0.011 |  |
| B208 | B208 | 15.603 | 15.568 | 0.035 | 0.001 |  |
| B209 | B209 | 27.88 | 27.927 | -0.047 | 0.002 |  |
| B210 | B210 | 3.961 | 3.995 | -0.034 | 0.001 |  |
| B211 | B211 | 22.755 | 22.715 | 0.040 | 0.002 |  |
| B212 | B212 | 11.827 | 11.862 | -0.035 | 0.001 |  |
| B213 | B213 | 25.704 | 25.67 | 0.034 | 0.001 |  |
| B214 | B214 | 22.613 | 22.59 | 0.023 | 0.001 |  |
| B215 | B215 | 57.755 | 57.734 | 0.021 | 0.000 |  |
| B216 | B216 | 38.235 | 38.175 | 0.060 | 0.004 |  |
| Outlier: a control point located in an area that does not reflect the true ground elevation, i.e. bridges, etc. | average | 0.000 |  |
|  | RMSEz | 0.013 | 1.3cm |
|  | NSSDA | 0.026 |  |

Errors-Baldwin East

30° 44' 3.4206" N, 87° 30' 56.8333" W.  There is an island in the middle of the river (outlined in red) that is confirmed with ancillary data. The outline of the island appears in the image, but shows as water.  In 3-D, the water is elevated at the island form.