Lidar Report

for

Alabama – Tennessee River

Contract Number: G10PC00026

Task Order:  G10PD00947

July 30, 2010

Table of Contents

Project Description	1

Flight Parameters	1

Dates Flown	3

Flight Line Layout	3

File Information	3

Projection / Datum	3

GPS Collection Parameters	4

Data Processing	4

QA/QC Analysis	5

Problems Encountered	7

List of Appendices  (Reference Included Files)

Appendix A: Survey Report	8

Appendix B: Logs	8

Appendix C: System Calibration Reports	8

Appendix D: Aeroplan Sensor Report	8

Appendix E: Trajectory Report (by flight date)	8

# Project Description

The purpose of this project is to provide professional surveying and mapping services for the creation of a high-resolution digital elevation model developed from LIDAR data for the Alabama – Tennessee River AOI.  The project area is shown in the graphic below.

All flights for the project were accomplished with customized single-engine Cessna 206s which provide an ideal, stable aerial base for Lidar acquisition.  This platform has relatively fast cruise speeds that are beneficial for project mobilization / demobilization while maintaining relatively slow stall speeds which can prove ideal for collection of a high-density, consistent data posting.

Photo Science utilized both of our Optec Gemini LiDAR scanners on this project to date.  Both systems are capable of collecting data at a maximum frequency of 167 kHz, which affords elevation data collection of up to 167,000 points per second.  The system utilizes a Multi-pulse in the Air option (MPIA).  This sensor is also equipped with the ability to measure up to 4 returns per outgoing pulse from the laser and these come in the form of 1st, 2nd, 3rd, and last returns.  The intensity of the first three returns is also captured during the aerial acquisition.

See appendix C for system calibration information

# Flight Parameters

Detailed project planning was performed for this project.  This planning was based on project specific requirements and the characteristics of the project site.   The basis of this planning included the required accuracies, type of development, amount and type of vegetation within the project area, the required data posting, and potential altitude restrictions for flights in the general area.  A brief summary of the aerial acquisition parameters for this project are shown in the table below:

Reference the Aeroplan sensor summary information included in Appendix D.

# Dates Flown

Collection occurred as weather permitted between the period of April 13th, 2010 through April 21st 9th, 2010, with an additional mission flown on May 7, 2010.  Eleven lifts were flown (April 13th, 14th, 15th, 20th, 21st, May 7th).

# Flight Line Layout

As depicted above, the area requires 115 Lines totaling 2,382 Kilometers (1,006 Flight Line miles).  The buffered area covers 214.52 square miles.

File Information

The 1500 x 1500 meter tiles are delivered as LAS, DEM, and Intensity Images.  The file naming schema is based on the lower left hand corner of each tile.  Naming convention is based on the National Grid for UTM Zone 16N.  The deliverable formats for the files are in the table below:

- LAS (518 – LAS Version 1.2 files)

- Hydro Flattened Raster DEM (518 – 2 Meter DEM files in ERDAS IMG format)

- Intensity Images (518 – GeoTIFF Images in TIF/TFW Format)

- Hydro Flattened Breaklines (1 – Arc Shapfile format)

- Raw Flight Line Source (148 – LAS Files in 10 folders)

# Projection / Datum

All data for this project were reduced to UTM (Zone 16), NAD83, Meters. All elevations were presented as orthometric heights using NAVD88 Meters.

There are several limiting factors to LiDAR data collection which include:

Weather: there can be no clouds, excess moisture (rain, fog or excessive humidity) between the sensor and the ground we are profiling. Additionally, high winds which if blowing perpendicular to the line of flight could provide for excessive crab resulting in “slivers” or “holidays” between flight lines as well as unsafe flight conditions such as wind shear or clear air turbulence.

Ground Conditions: Such as standing water from recent heavy rains, excessive “ponding” or “pooling” of water which will affect the accuracy of the LiDAR returns as will snow and Ice. This is especially apparent in ditches with high water and along roadways and fence lines with drifting snow.

Satellite Configuration: Typically one does not want to collect LiDAR during time of high PDOP, this is due to the GPS configuration providing accuracy less than desired. For this project there is to be no data collection during periods of PDOP above 3.5 or periods with less than 6 visible satellites.  To these ends, PDOP was checked each morning with a fresh almanac and newly updated satellite health status from the US Coast Guard Navigation Center website.

# GPS Collection Parameters

Collection parameters for this project included the following:

| Parameter | Value |
| --- | --- |
| Maximum PDOP | 3.5 |
| Minimum number of SVs | 6 |
| Ground collection epoch | 2 Hz (0.5 sec) |

# Data Processing

Optech software was used in the post-processing of the airborne GPS and inertial data that is critical to the positioning of the sensor during all flights.  This software suite includes Applanix’s PosPac and Waypoint’s GrafNav solutions.  PosPac provides the smoothed best estimate of trajectory (SBET) that is necessary for Optech’s post processor to develop the point cloud from the Lidar missions.  The point cloud is the mathematical three dimensional collection of all returns from all laser pulses as determined from the aerial mission.  At this point this data is ready for analysis, classification, and filtering to generate a bare earth surface model in which the above ground features are removed from the data set.

The point cloud was created using Optech’s Post Processor software.  GeoCue was used in the creation of some of the files needed in downstream processing, as well as in the tiling of the dataset into more manageable file sizes.  The TerraScan and TerraModeler software packages are then used for the automated data classification, manual cleanup, and bare earth generation from this data.  Project specific macros were used to classify the ground and to remove the side overlap between parallel flight lines.  All data was manually reviewed and any remaining artifacts removed using functionality provided by TerraScan and TerraModeler.  QT Modeler was used as a final check of the bare earth dataset.  GeoCue was then used to create the deliverable LAS 1.2 files for both the All Point Cloud Data and the Bare Earth.  In-house software was then used to perform final statistical analysis of the classes in the LAS files.

# QA/QC Analysis

A total of 20 points in three different land cover types (bare earth, tall grass, and urban) were established in the field for check points assessing the accuracy of the Lidar surface.  Two points in open areas over existing NGS benchmarks were established.  The table below lists the statistics of this analysis of the QC (blind points):

| Statistical Analysis |  | Coordinate System |
| --- | --- | --- |
| Average Dz | - |  | Horizontal Projection |
| Minimum Dz | 0 |  | NAD83 - UTM Zone 16N, Meters |
| Maximum Dz | 0 |  |  |
| RMSE | - |  | Vertical Datum |
| Standard Deviation | - |  | NAVD88 - Geoid09, Meters |
| Point | Easting | Northing | Known Z | LIDAR Z | Dz |
| BL01 | 416743.666 | 3602346.802 | 34.148 |  |  |
| BL02 | 410805.402 | 3610594.430 | 33.535 |  |  |
| BL03 | 400603.618 | 3607553.525 | 30.591 |  |  |
| BL04 | 395769.834 | 3617584.423 | 42.880 |  |  |
| BL05 | 400590.008 | 3628159.185 | 35.597 |  |  |
| BL05E | 400971.352 | 3628174.657 | 35.979 |  |  |
| BL06 | 391889.986 | 3636467.368 | 34.486 |  |  |
| BL07R | 388080.541 | 3642208.960 | 59.678 |  |  |
| BL08 | 391153.671 | 3649283.527 | 35.800 |  |  |
| BL09 | 388749.431 | 3653916.796 | 41.992 |  |  |
| BL10 | 385328.511 | 3661483.159 | 40.100 |  |  |
| BL11 | 380870.637 | 3677084.876 | 43.676 |  |  |
| BL12 | 377060.049 | 3687390.169 | 44.771 |  |  |
| BL13 | 362149.378 | 3709499.467 | 53.105 |  |  |
| BL14 | 370227.756 | 3709053.710 | 53.568 |  |  |
| BL15 | 373455.435 | 3712823.398 | 54.179 |  |  |
| BL16 | 356224.858 | 3710539.048 | 62.928 |  |  |
| BL17 | 360146.411 | 3723075.767 | 66.592 |  |  |
| BL18 | 360122.580 | 3740990.345 | 58.209 |  |  |
| BL19 | 360779.310 | 3762053.909 | 70.757 |  |  |
| BL20 | 371661.177 | 3776208.438 | 77.935 |  |  |
| BL21 | 368858.602 | 3793177.963 | 79.799 |  |  |

In addition to the quality control points collected, the following production field control was utilized for this project:

| Statistical Analysis |  | Coordinate System |
| --- | --- | --- |
| Average Dz | 0 |  | Horizontal Projection |
| Minimum Dz | -0.15 |  | NAD83 - UTM Zone 16N, Meters |
| Maximum Dz | 0.153 |  |  |
| RMSE | 0.062 |  | Vertical Datum |
| Standard Deviation | 0.063 |  | NAVD88 - Geoid09, Meters |
| Point | Easting | Northing | Known Z | LIDAR Z | Dz |
| AL01 | 417661.68 | 3602003.35 | 26.46 | 26.42 | -0.04 |
| AL01E | 417681.67 | 3601960.44 | 25.74 | 25.68 | -0.06 |
| AL02 | 411000.76 | 3610605.24 | 33.66 | 33.51 | -0.15 |
| AL03 | 400606.71 | 3607821.54 | 29.40 | 29.41 | 0.01 |
| AL04 | 396760.22 | 3616982.68 | 31.70 | 31.70 | 0.00 |
| AL05 | 400347.76 | 3628252.58 | 28.23 | 28.24 | 0.01 |
| AL06 | 391960.37 | 3636513.85 | 35.10 | 35.25 | 0.15 |
| AL07R | 387425.83 | 3642637.96 | 53.50 | 53.55 | 0.05 |
| AL08 | 391075.01 | 3649289.49 | 35.78 | 35.81 | 0.03 |
| AL09 | 388313.76 | 3654392.16 | 42.47 | 42.41 | -0.06 |
| AL10 | 384366.16 | 3660503.76 | 46.92 | 46.94 | 0.02 |
| AL11 | 379864.72 | 3677364.38 | 42.93 | 42.93 | 0.00 |
| AL12 | 378318.69 | 3680176.10 | 43.73 | 43.72 | -0.01 |
| AL13 | 369981.52 | 3695604.06 | 47.77 | 47.75 | -0.02 |
| AL14 | 361973.50 | 3709674.59 | 52.76 | 52.71 | -0.05 |
| AL15 | 370024.04 | 3707448.24 | 51.48 | 51.51 | 0.03 |
| AL16 | 373198.75 | 3713253.70 | 55.99 | 55.97 | -0.02 |
| AL17 | 355943.34 | 3710294.60 | 69.80 | 69.81 | 0.01 |
| AL18 | 360126.52 | 3723481.74 | 67.75 | 67.80 | 0.05 |
| AL19 | 360342.38 | 3740992.81 | 58.15 | 58.15 | 0.00 |
| AL20 | 361069.95 | 3762693.36 | 66.39 | 66.37 | -0.02 |
| AL21 | 371769.92 | 3776721.05 | 81.08 | 81.15 | 0.07 |
| AL22 | 369100.56 | 3793446.47 | 81.65 | 81.69 | 0.04 |
| Base99 | 393589.15 | 3633768.95 | 41.48 | 41.55 | 0.07 |
| CO0137 | 392581.70 | 3633566.44 | 35.49 | 35.36 | -0.13 |

# Problems Encountered

Problems encountered during this project were minimal.  There were a few times with winds outside what we consider an acceptable range.  There were also some times with less than acceptable GPS configuration in terms of high PDOP or less than 6 satellites available for tracking.  The crew checked the expected GPS configuration daily along with the weather and did not fly during less than ideal times.  No issues were documented in the LAS tile development phase of production.

Appendix

# Appendix A: Survey Report (Ref: AL_Tenn_River_ARRA_LIDAR_Survey_Report_G10PD00947 directory)

# Appendix B: Logs (Ref: AL_Tenn_River_ARRA_LIDAR_Flight_Logs_G10PD00947 Directory)

# Appendix C: System Calibration Reports (Ref: AL_Tenn_River_ARRA_LIDAR_System_Calibration_Report_G10PD00947 directory)

# Appendix D: Aeroplan Sensor Report (Ref: AL_Tenn_River_ARRA_LIDAR_Aeroplan_G10PD00947 directory)

# Appendix E: Trajectory Report by flight date (Ref: AL_Tenn_River_ARRA_LIDAR_Trajectory Report_G10PD000947 directory)