May 2012

Placer County California East Area around Lake Tahoe LIDAR QC Survey Control Report 2012

The scope of this project included control recovery and GPS surveying to establish x, y, & z positions of 30 plus locations divided into 3 unique ground cover classifications to be used as LIDAR imagery ground truthing quality control checking throughout the new project image area.

Locations were planned from office project limits layouts with some field adjustments. Control points classification points were located then measured by gps surveys for horizontal and vertical locations.  Recovered NGS high Order horizontal and vertical monuments were used to establish the horizontal and vertical datum used for this survey. Six existing federal government geodetic control stations were incorporated to our primary control network.  Surveyor positioned two secondary base stations to supplement the NGS control stations and to provide shorter vectors and a more dense overall network.  Control was planned to be at least Second Order horizontal and Third Order vertical.  The datum for this project was in NAD83 horizontal and NAVD88 vertical in meter units and the final adjusted data was reported in UTM North Zone 11 datum with orthometric elevations.

.

This project area is comprised of large unpopulated areas of National Forests and remote hills around the Northern and Western portions of Lake Tahoe.

gps measurements commenced on July 09, 2012 and were completed on July 12, 2012 which is Julian days 191 thru 194 in year 2012. All measurements were made in a static mode. Each site was occupied for several minutes and the base stations ran for several hours. Control point sites were located with two dual frequency receivers running as base stations and a second and third and fourth(sometimes)dual frequency receiver as rovers to the various new locations.

The equipment configuration for this project consists of industry standard gps and conventional surveying equipment.  The gps equipment used was a combination of Topcon dual frequency(L1/L2) receivers.  The Topcon receivers are the Hiper GD and Hiper Plus type. Topcon Tools gps processing software was used to post process all observed data.

Each observation was logged for site id, receiver type, height of antenna, start time and date.  Length of vector, time of day, SV configuration and site obstructions determined the length of observation at each site. Data was downloaded to the PC after each day’s sessions.  Initial processing was performed to verify we had good vector solutions between sites.

The horizontal and vertical datum for this survey was based on recovered high order NGS monuments NGS PID DH6444, AE9835, DH6446, KS0282, KS0285, and KS0325.

The Topcon Tools processing software reports the horizontal and vertical precision of every vector measured and summarizes the standard deviation in x, y and z position for each individual control point.

The final adjusted coordinate values are as listed herein.  gps software adjustment summaries are included for your future reference.  Photo references are attached in separate documents.

Steven A. Wood, L.S., C.P.,

Project Area Map

Land Cover Classifications

| NUMBER OF POINTS | LAND COVER CLASS | LAND COVER DESCRIPTION |
| --- | --- | --- |
| 10 | Class 1 | Bare Earth / Open Terrain |
| 10 | Class 3 | Tall Weeds and Crops |
| 10 | Class 5 | Forested and Fully Grown |

gps Observation  Survey Adjustments

Project Summary

Project name: PlacerEast07092012.ttp 
Surveyor: 
Comment: 
Linear unit: Meters 
Projection: UTMNorth-Zone_11 : 120W to 114W 
Geoid: g2009u05

Adjustment Summary

Adjustment type: Plane + Height, Minimal constraint 
Confidence level: 95 % 
Number of adjusted points: 80 
Number of plane control points: 1 
Number of used GPS vectors: 201 
Number of rejected GPS vectors by plane: 2 
A posteriori plane UWE: 1.205546 , Bounds: ( 0.9105396 , 1.089353 ) 
Number of height control points: 1 
Number of rejected GPS vectors by height: 8 
A posteriori height UWE: 1.13034 , Bounds: ( 0.8702528 , 1.129527 )

| Used GPS Observations |
| --- |
| Name | dN (m) | dE (m) | dHt (m) | Horz RMS (m) | Vert RMS (m) |
| 401ABase−401Base | 5.080 | 21.906 | -2.130 | 0.002 | 0.003 |
| 401ABase−401Base | 5.077 | 21.907 | -2.135 | 0.001 | 0.001 |
| 401ABase−401Base | 5.084 | 21.906 | -2.142 | 0.001 | 0.001 |
| 401ABase−401Base | 5.087 | 21.902 | -2.146 | 0.001 | 0.001 |
| 401ABase−402 | 12314.500 | 2918.710 | -208.678 | 0.008 | 0.014 |
| 401ABase−403 | -2411.196 | 581.542 | -20.128 | 0.003 | 0.007 |
| 401ABase−403A | -2412.124 | 561.374 | -19.091 | 0.003 | 0.009 |
| 401ABase−405 | -7570.695 | 4161.427 | -25.151 | 0.017 | 0.021 |
| 401ABase−406A_PID | -10158.133 | 5986.245 | -90.332 | 0.015 | 0.024 |
| 401ABase−406_PID | -10148.134 | 5992.776 | -90.398 | 0.016 | 0.025 |
| 401ABase−407 | -13736.656 | 1061.913 | 136.894 | 0.006 | 0.017 |
| 401ABase−407A | -13728.307 | 1001.556 | 138.645 | 0.018 | 0.037 |
| 401ABase−408 | 5602.465 | 14355.179 | 165.926 | 0.007 | 0.010 |
| 401ABase−408A_PID | 5610.857 | 14334.595 | 167.639 | 0.008 | 0.011 |
| 401ABase−409 | 3934.884 | 20337.536 | -67.336 | 0.009 | 0.015 |
| 401ABase−409A | 3951.158 | 20344.444 | -68.319 | 0.010 | 0.019 |
| 401ABase−409B_PID | 3965.404 | 20350.139 | -69.217 | 0.009 | 0.016 |
| 401ABase−409C | 3993.840 | 20385.523 | -71.509 | 0.030 | 0.054 |
| 401ABase−410 | -1365.675 | 11379.154 | -35.115 | 0.009 | 0.020 |
| 401ABase−410A | -1368.545 | 11394.663 | -36.074 | 0.006 | 0.014 |
| 401ABase−411 | -4575.047 | 5349.354 | -98.014 | 0.006 | 0.009 |
| 401ABase−411A | -4546.282 | 5326.799 | -96.753 | 0.006 | 0.009 |
| 401ABase−412E | -630.877 | 112.473 | -105.728 | 0.007 | 0.015 |
| 401ABase−412W | -630.712 | 108.268 | -105.690 | 0.006 | 0.015 |
| 401ABase−501A | 100.590 | 2809.652 | -133.423 | 0.015 | 0.016 |
| 401ABase−502 | 6285.615 | 2043.219 | -174.867 | 0.018 | 0.027 |
| 401ABase−502A | 6312.839 | 2052.566 | -175.409 | 0.010 | 0.015 |
| 401ABase−503 | 3576.122 | 829.663 | -0.716 | 0.006 | 0.012 |
| 401ABase−503A | 3560.158 | 839.366 | -1.838 | 0.006 | 0.012 |
| 401ABase−504 | -5195.798 | 7261.474 | -82.426 | 0.006 | 0.016 |
| 401ABase−504A | -5214.003 | 7261.222 | -81.901 | 0.008 | 0.023 |
| 401ABase−505 | -10502.744 | 3221.337 | -56.152 | 0.005 | 0.011 |
| 401ABase−505A | -10513.396 | 3204.044 | -56.036 | 0.006 | 0.013 |
| 401ABase−506 | -13276.594 | 5633.246 | -93.030 | 0.006 | 0.013 |
| 401ABase−506A | -13295.049 | 5652.105 | -93.676 | 0.006 | 0.012 |
| 401ABase−506B_PID | -13392.782 | 5715.112 | -95.443 | 0.008 | 0.016 |
| 401ABase−507 | 3288.422 | 17400.176 | -92.192 | 0.006 | 0.012 |
| 401ABase−507A | 3297.953 | 17414.722 | -91.746 | 0.006 | 0.012 |
| 401ABase−508 | 2097.590 | 13341.043 | -96.999 | 0.007 | 0.013 |
| 401ABase−508A | 2097.601 | 13320.957 | -96.972 | 0.007 | 0.014 |
| 401ABase−509A | -2930.779 | 3381.525 | -106.867 | 0.007 | 0.024 |
| 401ABase−509_DP3 | -2937.814 | 3388.899 | -106.750 | 0.011 | 0.032 |
| 401ABase−510 | -2269.876 | 9621.651 | -84.945 | 0.010 | 0.014 |
| 401ABase−510A | -2229.752 | 9621.955 | -81.839 | 0.006 | 0.010 |
| 401ABase−701 | 2062.739 | 2671.959 | -148.320 | 0.015 | 0.019 |
| 401ABase−701A | 2086.675 | 2665.990 | -148.388 | 0.008 | 0.010 |
| 401ABase−702 | 10150.523 | 3468.186 | -56.167 | 0.008 | 0.020 |
| 401ABase−702A | 10155.299 | 3492.785 | -54.457 | 0.021 | 0.042 |
| 401ABase−704 | -7904.951 | 6241.435 | -88.699 | 0.051 | 0.106 |
| 401ABase−704A | -7909.295 | 6248.475 | -88.857 | 0.012 | 0.024 |
| 401ABase−705 | -17732.174 | 4938.714 | 36.455 | 0.009 | 0.013 |
| 401ABase−705A | -17697.856 | 4891.834 | 38.461 | 0.013 | 0.021 |
| 401ABase−705B | -17722.987 | 4917.672 | 38.492 | 0.011 | 0.017 |
| 401ABase−706 | -16559.103 | 7746.681 | -29.441 | 0.018 | 0.039 |
| 401ABase−706A | -16573.461 | 7732.795 | -29.043 | 0.009 | 0.021 |
| 401ABase−707 | 4700.403 | 12332.215 | 267.410 | 0.012 | 0.024 |
| 401ABase−707A | 4688.129 | 12357.006 | 265.309 | 0.013 | 0.028 |
| 401ABase−708 | 2668.855 | 7558.884 | 399.619 | 0.009 | 0.012 |
| 401ABase−708A | 2666.662 | 7603.298 | 399.296 | 0.015 | 0.027 |
| 401ABase−709 | 1914.583 | 19600.220 | -52.193 | 0.007 | 0.016 |
| 401ABase−709A | 1900.346 | 19581.434 | -52.895 | 0.010 | 0.025 |
| 401ABase−710 | 4519.357 | 15700.420 | -39.261 | 0.055 | 0.104 |
| 401ABase−710A | 4534.142 | 15734.365 | -39.641 | 0.016 | 0.022 |
| 401ABase−710B_PID | 4588.365 | 15689.559 | -29.418 | 0.010 | 0.015 |
| 401ABase−711 | 9030.399 | 1562.139 | -67.708 | 0.005 | 0.009 |
| 401ABase−711A | 9000.646 | 1550.052 | -69.977 | 0.007 | 0.011 |
| 401ABase−711B | 9020.121 | 1571.784 | -69.228 | 0.007 | 0.014 |
| 401ABase−AE9835 | 189.311 | 2336.623 | -119.421 | 0.008 | 0.013 |
| 401ABase−AP1 | 12622.203 | 7908.945 | -198.747 | 0.006 | 0.011 |
| 401ABase−AP2_A | 12642.810 | 7754.730 | -198.550 | 0.005 | 0.010 |
| 401ABase−DH6444 | -7594.070 | 4176.548 | -25.803 | 0.008 | 0.013 |
| 401ABase−DH6444 | -7594.083 | 4176.542 | -25.794 | 0.013 | 0.017 |
| 401ABase−DH6446 | -1336.113 | 11403.348 | -30.756 | 0.007 | 0.017 |
| 401ABase−K0285os | -4367.970 | 7437.024 | -95.589 | 0.005 | 0.014 |
| 401ABase−KS0282 | -4322.556 | 7413.604 | -95.859 | 0.012 | 0.030 |
| 401ABase−KS0325 | 3282.643 | 17355.727 | -92.458 | 0.011 | 0.022 |
| 401Base−402 | 12309.417 | 2896.812 | -206.543 | 0.008 | 0.015 |
| 401Base−403 | -2416.273 | 559.645 | -17.965 | 0.008 | 0.022 |
| 401Base−403A | -2417.197 | 539.490 | -16.889 | 0.003 | 0.006 |
| 401Base−404A | -6341.559 | 1017.587 | 124.888 | 0.005 | 0.010 |
| 401Base−404_PID | -6328.051 | 1023.532 | 125.570 | 0.005 | 0.009 |
| 401Base−405 | -7575.799 | 4139.505 | -23.034 | 0.020 | 0.021 |
| 401Base−406A_PID | -10163.205 | 5964.340 | -88.227 | 0.013 | 0.022 |
| 401Base−406_PID | -10153.209 | 5970.877 | -88.273 | 0.016 | 0.024 |
| 401Base−407 | -13741.733 | 1040.008 | 139.010 | 0.006 | 0.015 |
| 401Base−407A | -13733.363 | 979.638 | 140.720 | 0.013 | 0.022 |
| 401Base−408 | 5597.403 | 14333.280 | 168.076 | 0.007 | 0.010 |
| 401Base−408A_PID | 5605.796 | 14312.698 | 169.795 | 0.008 | 0.010 |
| 401Base−409 | 3929.803 | 20315.621 | -65.207 | 0.008 | 0.017 |
| 401Base−409A | 3946.112 | 20322.531 | -66.291 | 0.009 | 0.016 |
| 401Base−409B_PID | 3960.322 | 20328.224 | -67.094 | 0.009 | 0.016 |
| 401Base−409C | 3988.776 | 20363.613 | -69.439 | 0.020 | 0.040 |
| 401Base−410 | -1370.748 | 11357.250 | -32.987 | 0.007 | 0.014 |
| 401Base−410A | -1373.616 | 11372.756 | -33.945 | 0.007 | 0.012 |
| 401Base−411 | -4580.133 | 5327.444 | -95.879 | 0.007 | 0.011 |
| 401Base−411A | -4551.389 | 5304.873 | -94.584 | 0.012 | 0.019 |
| 401Base−412E | -635.969 | 90.579 | -103.533 | 0.002 | 0.004 |
| 401Base−412W | -635.802 | 86.373 | -103.485 | 0.002 | 0.004 |
| 401Base−501 | 79.027 | 2778.707 | -130.737 | 0.011 | 0.016 |
| 401Base−501A | 95.486 | 2787.743 | -131.286 | 0.004 | 0.007 |
| 401Base−502 | 6280.527 | 2021.321 | -172.710 | 0.004 | 0.006 |
| 401Base−502A | 6307.750 | 2030.666 | -173.248 | 0.006 | 0.010 |
| 401Base−503 | 3571.065 | 807.754 | 1.367 | 0.023 | 0.047 |
| 401Base−503A | 3555.097 | 817.463 | 0.260 | 0.021 | 0.044 |
| 401Base−504 | -5200.876 | 7239.569 | -80.286 | 0.004 | 0.011 |
| 401Base−504A | -5219.081 | 7239.322 | -79.738 | 0.005 | 0.013 |
| 401Base−505 | -10507.809 | 3199.439 | -54.066 | 0.005 | 0.011 |
| 401Base−505A | -10518.458 | 3182.146 | -53.952 | 0.005 | 0.011 |
| 401Base−506 | -13281.668 | 5611.349 | -90.885 | 0.005 | 0.011 |
| 401Base−506A | -13300.124 | 5630.206 | -91.524 | 0.005 | 0.010 |
| 401Base−506B_PID | -13397.854 | 5693.213 | -93.300 | 0.008 | 0.016 |
| 401Base−507 | 3283.346 | 17378.270 | -90.058 | 0.006 | 0.012 |
| 401Base−507A | 3292.876 | 17392.817 | -89.607 | 0.006 | 0.013 |
| 401Base−508 | 2092.511 | 13319.134 | -94.852 | 0.010 | 0.018 |
| 401Base−508A | 2092.517 | 13299.050 | -94.816 | 0.008 | 0.015 |
| 401Base−509A | -2935.855 | 3359.633 | -104.614 | 0.003 | 0.007 |
| 401Base−509_DP3 | -2942.888 | 3367.007 | -104.505 | 0.004 | 0.008 |
| 401Base−510 | -2274.953 | 9599.739 | -82.823 | 0.007 | 0.010 |
| 401Base−510A | -2234.810 | 9600.029 | -79.732 | 0.008 | 0.012 |
| 401Base−701 | 2057.673 | 2650.058 | -146.174 | 0.015 | 0.017 |
| 401Base−701A | 2081.586 | 2644.086 | -146.249 | 0.010 | 0.013 |
| 401Base−702 | 10145.422 | 3446.291 | -54.000 | 0.008 | 0.020 |
| 401Base−702A | 10150.187 | 3470.884 | -52.274 | 0.016 | 0.037 |
| 401Base−703A | 8554.365 | 1591.566 | -73.586 | 0.011 | 0.019 |
| 401Base−704 | -7910.036 | 6219.529 | -86.568 | 0.022 | 0.043 |
| 401Base−704A | -7914.374 | 6226.570 | -86.704 | 0.010 | 0.021 |
| 401Base−705 | -17737.240 | 4916.802 | 38.575 | 0.008 | 0.012 |
| 401Base−705A | -17702.922 | 4869.926 | 40.583 | 0.014 | 0.023 |
| 401Base−705B | -17728.059 | 4895.769 | 40.625 | 0.008 | 0.014 |
| 401Base−706 | -16564.165 | 7724.769 | -27.335 | 0.015 | 0.034 |
| 401Base−707 | 4695.334 | 12310.310 | 269.499 | 0.012 | 0.024 |
| 401Base−707A | 4683.049 | 12335.104 | 267.428 | 0.009 | 0.019 |
| 401Base−708 | 2663.792 | 7536.985 | 401.767 | 0.004 | 0.008 |
| 401Base−708A | 2661.499 | 7581.392 | 401.357 | 0.010 | 0.020 |
| 401Base−709 | 1909.496 | 19578.315 | -50.062 | 0.008 | 0.017 |
| 401Base−709A | 1895.258 | 19559.520 | -50.781 | 0.008 | 0.019 |
| 401Base−710 | 4514.282 | 15678.521 | -37.150 | 0.016 | 0.023 |
| 401Base−710A | 4529.071 | 15712.463 | -37.493 | 0.014 | 0.018 |
| 401Base−710B_PID | 4583.305 | 15667.651 | -27.273 | 0.010 | 0.015 |
| 401Base−711 | 9025.311 | 1540.234 | -65.565 | 0.005 | 0.010 |
| 401Base−711A | 8995.565 | 1528.141 | -67.858 | 0.007 | 0.012 |
| 401Base−711B | 9015.038 | 1549.876 | -67.081 | 0.007 | 0.014 |
| 401Base−AE9835 | 184.226 | 2314.721 | -117.305 | 0.005 | 0.009 |
| 401Base−AP1 | 12617.121 | 7887.053 | -196.615 | 0.006 | 0.012 |
| 401Base−AP2_A | 12637.720 | 7732.837 | -196.404 | 0.006 | 0.011 |
| 401Base−AP2_B | 12629.627 | 7745.771 | -196.487 | 0.025 | 0.057 |
| 401Base−DH6444 | -7599.157 | 4154.637 | -23.666 | 0.010 | 0.016 |
| 401Base−DH6446 | -1341.185 | 11381.443 | -28.612 | 0.007 | 0.016 |
| 401Base−K0285os | -4373.057 | 7415.119 | -93.442 | 0.005 | 0.014 |
| 401Base−KS0282 | -4327.633 | 7391.720 | -93.669 | 0.012 | 0.028 |
| 401Base−KS0325 | 3277.568 | 17333.825 | -90.325 | 0.011 | 0.024 |
| 402−402A_PID | 4.434 | 11.980 | -0.524 | 0.003 | 0.005 |
| 403−403A | -0.926 | -20.163 | 1.050 | 0.005 | 0.014 |
| 404A−404_PID | 13.505 | 5.949 | 0.692 | 0.003 | 0.006 |
| 405−DH6444 | -23.383 | 15.110 | -0.639 | 0.009 | 0.010 |
| 406A_PID−406_PID | 10.023 | 6.531 | -0.084 | 0.014 | 0.020 |
| 407−407A | 8.367 | -60.364 | 1.684 | 0.009 | 0.017 |
| 408−408A_PID | 8.394 | -20.587 | 1.724 | 0.002 | 0.002 |
| 409−409A | 16.297 | 6.913 | -1.056 | 0.004 | 0.007 |
| 409−409B_PID | 30.518 | 12.599 | -1.874 | 0.002 | 0.003 |
| 409−409C | 58.951 | 47.977 | -4.207 | 0.003 | 0.005 |
| 409A−409B_PID | 14.219 | 5.686 | -0.817 | 0.004 | 0.007 |
| 409A−409C | 42.652 | 41.073 | -3.153 | 0.007 | 0.012 |
| 409B_PID−409C | 28.429 | 35.384 | -2.319 | 0.004 | 0.007 |
| 410−410A | -2.869 | 15.498 | -0.943 | 0.002 | 0.003 |
| 410−DH6446 | 29.560 | 24.189 | 4.389 | 0.002 | 0.005 |
| 410A−DH6446 | 32.427 | 8.688 | 5.342 | 0.003 | 0.007 |
| 411−411A | 28.763 | -22.559 | 1.258 | 0.002 | 0.003 |
| 412E−412W | 0.166 | -4.207 | 0.047 | 0.001 | 0.002 |
| 501−501A | 16.468 | 9.022 | -0.588 | 0.006 | 0.010 |
| 502−502A | 27.226 | 9.347 | -0.549 | 0.004 | 0.005 |
| 503−503A | -15.959 | 9.703 | -1.121 | 0.004 | 0.008 |
| 504−504A | -18.203 | -0.249 | 0.533 | 0.004 | 0.011 |
| 505−505A | -10.653 | -17.293 | 0.120 | 0.002 | 0.004 |
| 506−506A | -18.462 | 18.854 | -0.629 | 0.001 | 0.002 |
| 506−506B_PID | -116.189 | 81.866 | -2.406 | 0.002 | 0.003 |
| 506A−506B_PID | -97.730 | 63.012 | -1.766 | 0.001 | 0.002 |
| 507−507A | 9.528 | 14.548 | 0.450 | 0.001 | 0.002 |
| 507−KS0325 | -5.766 | -44.448 | -0.303 | 0.008 | 0.014 |
| 507A−KS0325 | -15.292 | -58.999 | -0.737 | 0.005 | 0.010 |
| 508−508A | 0.006 | -20.087 | 0.038 | 0.001 | 0.001 |
| 509A−509_DP3 | -7.035 | 7.374 | 0.113 | 0.001 | 0.002 |
| 510−510A | 40.130 | 0.296 | 3.101 | 0.012 | 0.018 |
| 702−702A | 4.782 | 24.596 | 1.744 | 0.007 | 0.012 |
| 703−703A | -26.358 | 2.887 | 0.604 | 0.007 | 0.023 |
| 704−704A | -4.345 | 7.038 | -0.144 | 0.008 | 0.014 |
| 705−705A | 34.310 | -46.876 | 2.004 | 0.007 | 0.010 |
| 705−705B | 9.172 | -21.038 | 2.084 | 0.007 | 0.012 |
| 705A−705B | -25.146 | 25.853 | 0.048 | 0.012 | 0.020 |
| 706−706A | -14.352 | -13.882 | 0.381 | 0.009 | 0.021 |
| 707−707A | -12.277 | 24.779 | -2.082 | 0.005 | 0.010 |
| 708−708A | -2.302 | 44.404 | -0.396 | 0.009 | 0.016 |
| 709−709A | -14.227 | -18.784 | -0.717 | 0.003 | 0.007 |
| 710−710A | 14.781 | 33.943 | -0.358 | 0.013 | 0.018 |
| 710−710B_PID | 69.011 | -10.868 | 9.835 | 0.009 | 0.013 |
| 710A−710B_PID | 54.231 | -44.805 | 10.183 | 0.010 | 0.013 |
| 711−711A | -29.748 | -12.090 | -2.280 | 0.008 | 0.012 |
| 711−711B | -10.276 | 9.645 | -1.526 | 0.003 | 0.005 |
| 711A−711B | 19.475 | 21.723 | 0.737 | 0.018 | 0.034 |
| AP1−AP2_A | 20.607 | -154.214 | 0.199 | 0.001 | 0.001 |
| AP1−AP2_B | 12.492 | -141.283 | 0.163 | 0.001 | 0.003 |
| GPS Observation Residuals |
| Name | dN (m) | dE (m) | dHt (m) | Horz RMS (m) | Vert RMS (m) |
| 401ABase−401Base | 5.080 | 21.906 | -2.130 | 0.002 | 0.003 |
| 401ABase−401Base | 5.077 | 21.907 | -2.135 | 0.001 | 0.001 |
| 401ABase−401Base | 5.084 | 21.906 | -2.142 | 0.001 | 0.001 |
| 401ABase−401Base | 5.087 | 21.902 | -2.146 | 0.001 | 0.001 |
| 401ABase−402 | 12314.500 | 2918.710 | -208.678 | 0.008 | 0.014 |
| 401ABase−403 | -2411.196 | 581.542 | -20.128 | 0.003 | 0.007 |
| 401ABase−403A | -2412.124 | 561.374 | -19.091 | 0.003 | 0.009 |
| 401ABase−405 | -7570.695 | 4161.427 | -25.151 | 0.017 | 0.021 |
| 401ABase−406A_PID | -10158.133 | 5986.245 | -90.332 | 0.015 | 0.024 |
| 401ABase−406_PID | -10148.134 | 5992.776 | -90.398 | 0.016 | 0.025 |
| 401ABase−407 | -13736.656 | 1061.913 | 136.894 | 0.006 | 0.017 |
| 401ABase−407A | -13728.307 | 1001.556 | 138.645 | 0.018 | 0.037 |
| 401ABase−408 | 5602.465 | 14355.179 | 165.926 | 0.007 | 0.010 |
| 401ABase−408A_PID | 5610.857 | 14334.595 | 167.639 | 0.008 | 0.011 |
| 401ABase−409 | 3934.884 | 20337.536 | -67.336 | 0.009 | 0.015 |
| 401ABase−409A | 3951.158 | 20344.444 | -68.319 | 0.010 | 0.019 |
| 401ABase−409B_PID | 3965.404 | 20350.139 | -69.217 | 0.009 | 0.016 |
| 401ABase−409C | 3993.840 | 20385.523 | -71.509 | 0.030 | 0.054 |
| 401ABase−410 | -1365.675 | 11379.154 | -35.115 | 0.009 | 0.020 |
| 401ABase−410A | -1368.545 | 11394.663 | -36.074 | 0.006 | 0.014 |
| 401ABase−411 | -4575.047 | 5349.354 | -98.014 | 0.006 | 0.009 |
| 401ABase−411A | -4546.282 | 5326.799 | -96.753 | 0.006 | 0.009 |
| 401ABase−412E | -630.877 | 112.473 | -105.728 | 0.007 | 0.015 |
| 401ABase−412W | -630.712 | 108.268 | -105.690 | 0.006 | 0.015 |
| 401ABase−501A | 100.590 | 2809.652 | -133.423 | 0.015 | 0.016 |
| 401ABase−502 | 6285.615 | 2043.219 | -174.867 | 0.018 | 0.027 |
| 401ABase−502A | 6312.839 | 2052.566 | -175.409 | 0.010 | 0.015 |
| 401ABase−503 | 3576.122 | 829.663 | -0.716 | 0.006 | 0.012 |
| 401ABase−503A | 3560.158 | 839.366 | -1.838 | 0.006 | 0.012 |
| 401ABase−504 | -5195.798 | 7261.474 | -82.426 | 0.006 | 0.016 |
| 401ABase−504A | -5214.003 | 7261.222 | -81.901 | 0.008 | 0.023 |
| 401ABase−505 | -10502.744 | 3221.337 | -56.152 | 0.005 | 0.011 |
| 401ABase−505A | -10513.396 | 3204.044 | -56.036 | 0.006 | 0.013 |
| 401ABase−506 | -13276.594 | 5633.246 | -93.030 | 0.006 | 0.013 |
| 401ABase−506A | -13295.049 | 5652.105 | -93.676 | 0.006 | 0.012 |
| 401ABase−506B_PID | -13392.782 | 5715.112 | -95.443 | 0.008 | 0.016 |
| 401ABase−507 | 3288.422 | 17400.176 | -92.192 | 0.006 | 0.012 |
| 401ABase−507A | 3297.953 | 17414.722 | -91.746 | 0.006 | 0.012 |
| 401ABase−508 | 2097.590 | 13341.043 | -96.999 | 0.007 | 0.013 |
| 401ABase−508A | 2097.601 | 13320.957 | -96.972 | 0.007 | 0.014 |
| 401ABase−509A | -2930.779 | 3381.525 | -106.867 | 0.007 | 0.024 |
| 401ABase−509_DP3 | -2937.814 | 3388.899 | -106.750 | 0.011 | 0.032 |
| 401ABase−510 | -2269.876 | 9621.651 | -84.945 | 0.010 | 0.014 |
| 401ABase−510A | -2229.752 | 9621.955 | -81.839 | 0.006 | 0.010 |
| 401ABase−701 | 2062.739 | 2671.959 | -148.320 | 0.015 | 0.019 |
| 401ABase−701A | 2086.675 | 2665.990 | -148.388 | 0.008 | 0.010 |
| 401ABase−702 | 10150.523 | 3468.186 | -56.167 | 0.008 | 0.020 |
| 401ABase−702A | 10155.299 | 3492.785 | -54.457 | 0.021 | 0.042 |
| 401ABase−704 | -7904.951 | 6241.435 | -88.699 | 0.051 | 0.106 |
| 401ABase−704A | -7909.295 | 6248.475 | -88.857 | 0.012 | 0.024 |
| 401ABase−705 | -17732.174 | 4938.714 | 36.455 | 0.009 | 0.013 |
| 401ABase−705A | -17697.856 | 4891.834 | 38.461 | 0.013 | 0.021 |
| 401ABase−705B | -17722.987 | 4917.672 | 38.492 | 0.011 | 0.017 |
| 401ABase−706 | -16559.103 | 7746.681 | -29.441 | 0.018 | 0.039 |
| 401ABase−706A | -16573.461 | 7732.795 | -29.043 | 0.009 | 0.021 |
| 401ABase−707 | 4700.403 | 12332.215 | 267.410 | 0.012 | 0.024 |
| 401ABase−707A | 4688.129 | 12357.006 | 265.309 | 0.013 | 0.028 |
| 401ABase−708 | 2668.855 | 7558.884 | 399.619 | 0.009 | 0.012 |
| 401ABase−708A | 2666.662 | 7603.298 | 399.296 | 0.015 | 0.027 |
| 401ABase−709 | 1914.583 | 19600.220 | -52.193 | 0.007 | 0.016 |
| 401ABase−709A | 1900.346 | 19581.434 | -52.895 | 0.010 | 0.025 |
| 401ABase−710 | 4519.357 | 15700.420 | -39.261 | 0.055 | 0.104 |
| 401ABase−710A | 4534.142 | 15734.365 | -39.641 | 0.016 | 0.022 |
| 401ABase−710B_PID | 4588.365 | 15689.559 | -29.418 | 0.010 | 0.015 |
| 401ABase−711 | 9030.399 | 1562.139 | -67.708 | 0.005 | 0.009 |
| 401ABase−711A | 9000.646 | 1550.052 | -69.977 | 0.007 | 0.011 |
| 401ABase−711B | 9020.121 | 1571.784 | -69.228 | 0.007 | 0.014 |
| 401ABase−AE9835 | 189.311 | 2336.623 | -119.421 | 0.008 | 0.013 |
| 401ABase−AP1 | 12622.203 | 7908.945 | -198.747 | 0.006 | 0.011 |
| 401ABase−AP2_A | 12642.810 | 7754.730 | -198.550 | 0.005 | 0.010 |
| 401ABase−DH6444 | -7594.070 | 4176.548 | -25.803 | 0.008 | 0.013 |
| 401ABase−DH6444 | -7594.083 | 4176.542 | -25.794 | 0.013 | 0.017 |
| 401ABase−DH6446 | -1336.113 | 11403.348 | -30.756 | 0.007 | 0.017 |
| 401ABase−K0285os | -4367.970 | 7437.024 | -95.589 | 0.005 | 0.014 |
| 401ABase−KS0282 | -4322.556 | 7413.604 | -95.859 | 0.012 | 0.030 |
| 401ABase−KS0325 | 3282.643 | 17355.727 | -92.458 | 0.011 | 0.022 |
| 401Base−402 | 12309.417 | 2896.812 | -206.543 | 0.008 | 0.015 |
| 401Base−402A_PID | 12313.817 | 2908.775 | -207.071 | 0.008 | 0.018 |
| 401Base−403 | -2416.273 | 559.645 | -17.965 | 0.008 | 0.022 |
| 401Base−403A | -2417.197 | 539.490 | -16.889 | 0.003 | 0.006 |
| 401Base−404A | -6341.559 | 1017.587 | 124.888 | 0.005 | 0.010 |
| 401Base−404_PID | -6328.051 | 1023.532 | 125.570 | 0.005 | 0.009 |
| 401Base−405 | -7575.799 | 4139.505 | -23.034 | 0.020 | 0.021 |
| 401Base−406A_PID | -10163.205 | 5964.340 | -88.227 | 0.013 | 0.022 |
| 401Base−406_PID | -10153.209 | 5970.877 | -88.273 | 0.016 | 0.024 |
| 401Base−407 | -13741.733 | 1040.008 | 139.010 | 0.006 | 0.015 |
| 401Base−407A | -13733.363 | 979.638 | 140.720 | 0.013 | 0.022 |
| 401Base−408 | 5597.403 | 14333.280 | 168.076 | 0.007 | 0.010 |
| 401Base−408A_PID | 5605.796 | 14312.698 | 169.795 | 0.008 | 0.010 |
| 401Base−409 | 3929.803 | 20315.621 | -65.207 | 0.008 | 0.017 |
| 401Base−409A | 3946.112 | 20322.531 | -66.291 | 0.009 | 0.016 |
| 401Base−409B_PID | 3960.322 | 20328.224 | -67.094 | 0.009 | 0.016 |
| 401Base−409C | 3988.776 | 20363.613 | -69.439 | 0.020 | 0.040 |
| 401Base−410 | -1370.748 | 11357.250 | -32.987 | 0.007 | 0.014 |
| 401Base−410A | -1373.616 | 11372.756 | -33.945 | 0.007 | 0.012 |
| 401Base−411 | -4580.133 | 5327.444 | -95.879 | 0.007 | 0.011 |
| 401Base−411A | -4551.389 | 5304.873 | -94.584 | 0.012 | 0.019 |
| 401Base−412E | -635.969 | 90.579 | -103.533 | 0.002 | 0.004 |
| 401Base−412W | -635.802 | 86.373 | -103.485 | 0.002 | 0.004 |
| 401Base−501 | 79.027 | 2778.707 | -130.737 | 0.011 | 0.016 |
| 401Base−501A | 95.486 | 2787.743 | -131.286 | 0.004 | 0.007 |
| 401Base−502 | 6280.527 | 2021.321 | -172.710 | 0.004 | 0.006 |
| 401Base−502A | 6307.750 | 2030.666 | -173.248 | 0.006 | 0.010 |
| 401Base−503 | 3571.065 | 807.754 | 1.367 | 0.023 | 0.047 |
| 401Base−503A | 3555.097 | 817.463 | 0.260 | 0.021 | 0.044 |
| 401Base−504 | -5200.876 | 7239.569 | -80.286 | 0.004 | 0.011 |
| 401Base−504A | -5219.081 | 7239.322 | -79.738 | 0.005 | 0.013 |
| 401Base−505 | -10507.809 | 3199.439 | -54.066 | 0.005 | 0.011 |
| 401Base−505A | -10518.458 | 3182.146 | -53.952 | 0.005 | 0.011 |
| 401Base−506 | -13281.668 | 5611.349 | -90.885 | 0.005 | 0.011 |
| 401Base−506A | -13300.124 | 5630.206 | -91.524 | 0.005 | 0.010 |
| 401Base−506B_PID | -13397.854 | 5693.213 | -93.300 | 0.008 | 0.016 |
| 401Base−507 | 3283.346 | 17378.270 | -90.058 | 0.006 | 0.012 |
| 401Base−507A | 3292.876 | 17392.817 | -89.607 | 0.006 | 0.013 |
| 401Base−508 | 2092.511 | 13319.134 | -94.852 | 0.010 | 0.018 |
| 401Base−508A | 2092.517 | 13299.050 | -94.816 | 0.008 | 0.015 |
| 401Base−509A | -2935.855 | 3359.633 | -104.614 | 0.003 | 0.007 |
| 401Base−509_DP3 | -2942.888 | 3367.007 | -104.505 | 0.004 | 0.008 |
| 401Base−510 | -2274.953 | 9599.739 | -82.823 | 0.007 | 0.010 |
| 401Base−510A | -2234.810 | 9600.029 | -79.732 | 0.008 | 0.012 |
| 401Base−701 | 2057.673 | 2650.058 | -146.174 | 0.015 | 0.017 |
| 401Base−701A | 2081.586 | 2644.086 | -146.249 | 0.010 | 0.013 |
| 401Base−702 | 10145.422 | 3446.291 | -54.000 | 0.008 | 0.020 |
| 401Base−702A | 10150.187 | 3470.884 | -52.274 | 0.016 | 0.037 |
| 401Base−703 | 8580.684 | 1588.673 | -73.857 | 0.016 | 0.041 |
| 401Base−703A | 8554.365 | 1591.566 | -73.586 | 0.011 | 0.019 |
| 401Base−704 | -7910.036 | 6219.529 | -86.568 | 0.022 | 0.043 |
| 401Base−704A | -7914.374 | 6226.570 | -86.704 | 0.010 | 0.021 |
| 401Base−705 | -17737.240 | 4916.802 | 38.575 | 0.008 | 0.012 |
| 401Base−705A | -17702.922 | 4869.926 | 40.583 | 0.014 | 0.023 |
| 401Base−705B | -17728.059 | 4895.769 | 40.625 | 0.008 | 0.014 |
| 401Base−706 | -16564.165 | 7724.769 | -27.335 | 0.015 | 0.034 |
| 401Base−707 | 4695.334 | 12310.310 | 269.499 | 0.012 | 0.024 |
| 401Base−707A | 4683.049 | 12335.104 | 267.428 | 0.009 | 0.019 |
| 401Base−708 | 2663.792 | 7536.985 | 401.767 | 0.004 | 0.008 |
| 401Base−708A | 2661.499 | 7581.392 | 401.357 | 0.010 | 0.020 |
| 401Base−709 | 1909.496 | 19578.315 | -50.062 | 0.008 | 0.017 |
| 401Base−709A | 1895.258 | 19559.520 | -50.781 | 0.008 | 0.019 |
| 401Base−710 | 4514.282 | 15678.521 | -37.150 | 0.016 | 0.023 |
| 401Base−710A | 4529.071 | 15712.463 | -37.493 | 0.014 | 0.018 |
| 401Base−710B_PID | 4583.305 | 15667.651 | -27.273 | 0.010 | 0.015 |
| 401Base−711 | 9025.311 | 1540.234 | -65.565 | 0.005 | 0.010 |
| 401Base−711A | 8995.565 | 1528.141 | -67.858 | 0.007 | 0.012 |
| 401Base−711B | 9015.038 | 1549.876 | -67.081 | 0.007 | 0.014 |
| 401Base−AE9835 | 184.226 | 2314.721 | -117.305 | 0.005 | 0.009 |
| 401Base−AP1 | 12617.121 | 7887.053 | -196.615 | 0.006 | 0.012 |
| 401Base−AP2_A | 12637.720 | 7732.837 | -196.404 | 0.006 | 0.011 |
| 401Base−AP2_B | 12629.627 | 7745.771 | -196.487 | 0.025 | 0.057 |
| 401Base−DH6444 | -7599.157 | 4154.637 | -23.666 | 0.010 | 0.016 |
| 401Base−DH6444 | -7599.179 | 4154.619 | -23.656 | 0.021 | 0.021 |
| 401Base−DH6446 | -1341.185 | 11381.443 | -28.612 | 0.007 | 0.016 |
| 401Base−K0285os | -4373.057 | 7415.119 | -93.442 | 0.005 | 0.014 |
| 401Base−KS0282 | -4327.633 | 7391.720 | -93.669 | 0.012 | 0.028 |
| 401Base−KS0325 | 3277.568 | 17333.825 | -90.325 | 0.011 | 0.024 |
| 402−402A_PID | 4.434 | 11.980 | -0.524 | 0.003 | 0.005 |
| 403−403A | -0.926 | -20.163 | 1.050 | 0.005 | 0.014 |
| 404A−404_PID | 13.505 | 5.949 | 0.692 | 0.003 | 0.006 |
| 405−DH6444 | -23.383 | 15.110 | -0.639 | 0.009 | 0.010 |
| 406A_PID−406_PID | 10.023 | 6.531 | -0.084 | 0.014 | 0.020 |
| 407−407A | 8.367 | -60.364 | 1.684 | 0.009 | 0.017 |
| 408−408A_PID | 8.394 | -20.587 | 1.724 | 0.002 | 0.002 |
| 409−409A | 16.297 | 6.913 | -1.056 | 0.004 | 0.007 |
| 409−409B_PID | 30.518 | 12.599 | -1.874 | 0.002 | 0.003 |
| 409−409C | 58.951 | 47.977 | -4.207 | 0.003 | 0.005 |
| 409A−409B_PID | 14.219 | 5.686 | -0.817 | 0.004 | 0.007 |
| 409A−409C | 42.652 | 41.073 | -3.153 | 0.007 | 0.012 |
| 409B_PID−409C | 28.429 | 35.384 | -2.319 | 0.004 | 0.007 |
| 410−410A | -2.869 | 15.498 | -0.943 | 0.002 | 0.003 |
| 410−DH6446 | 29.560 | 24.189 | 4.389 | 0.002 | 0.005 |
| 410A−DH6446 | 32.427 | 8.688 | 5.342 | 0.003 | 0.007 |
| 411−411A | 28.763 | -22.559 | 1.258 | 0.002 | 0.003 |
| 412E−412W | 0.166 | -4.207 | 0.047 | 0.001 | 0.002 |
| 501−501A | 16.468 | 9.022 | -0.588 | 0.006 | 0.010 |
| 502−502A | 27.226 | 9.347 | -0.549 | 0.004 | 0.005 |
| 503−503A | -15.959 | 9.703 | -1.121 | 0.004 | 0.008 |
| 504−504A | -18.203 | -0.249 | 0.533 | 0.004 | 0.011 |
| 505−505A | -10.653 | -17.293 | 0.120 | 0.002 | 0.004 |
| 506−506A | -18.462 | 18.854 | -0.629 | 0.001 | 0.002 |
| 506−506B_PID | -116.189 | 81.866 | -2.406 | 0.002 | 0.003 |
| 506A−506B_PID | -97.730 | 63.012 | -1.766 | 0.001 | 0.002 |
| 507−507A | 9.528 | 14.548 | 0.450 | 0.001 | 0.002 |
| 507−KS0325 | -5.766 | -44.448 | -0.303 | 0.008 | 0.014 |
| 507A−KS0325 | -15.292 | -58.999 | -0.737 | 0.005 | 0.010 |
| 508−508A | 0.006 | -20.087 | 0.038 | 0.001 | 0.001 |
| 509A−509_DP3 | -7.035 | 7.374 | 0.113 | 0.001 | 0.002 |
| 510−510A | 40.130 | 0.296 | 3.101 | 0.012 | 0.018 |
| 702−702A | 4.782 | 24.596 | 1.744 | 0.007 | 0.012 |
| 703−703A | -26.358 | 2.887 | 0.604 | 0.007 | 0.023 |
| 704−704A | -4.345 | 7.038 | -0.144 | 0.008 | 0.014 |
| 705−705A | 34.310 | -46.876 | 2.004 | 0.007 | 0.010 |
| 705−705B | 9.172 | -21.038 | 2.084 | 0.007 | 0.012 |
| 705A−705B | -25.146 | 25.853 | 0.048 | 0.012 | 0.020 |
| 706−706A | -14.352 | -13.882 | 0.381 | 0.009 | 0.021 |
| 707−707A | -12.277 | 24.779 | -2.082 | 0.005 | 0.010 |
| 708−708A | -2.302 | 44.404 | -0.396 | 0.009 | 0.016 |
| 709−709A | -14.227 | -18.784 | -0.717 | 0.003 | 0.007 |
| 710−710A | 14.781 | 33.943 | -0.358 | 0.013 | 0.018 |
| 710−710B_PID | 69.011 | -10.868 | 9.835 | 0.009 | 0.013 |
| 710A−710B_PID | 54.231 | -44.805 | 10.183 | 0.010 | 0.013 |
| 711−711A | -29.748 | -12.090 | -2.280 | 0.008 | 0.012 |
| 711−711B | -10.276 | 9.645 | -1.526 | 0.003 | 0.005 |
| 711A−711B | 19.475 | 21.723 | 0.737 | 0.018 | 0.034 |
| AP1−AP2_A | 20.607 | -154.214 | 0.199 | 0.001 | 0.001 |
| AP1−AP2_B | 12.492 | -141.283 | 0.163 | 0.001 | 0.003 |

| Control Points |
| --- |
| Name | Grid Northing (m) | Grid Easting (m) | Elevation (m) | Code |
| AE9835 | 4344524.474 | 223245.744 | 1877.054 |  |
| Adjusted Points |
| Name | Grid Northing (m) | Grid Easting (m) | Elevation (m) | Code |
| 401ABase | 4344335.166 | 220909.120 | 1996.459 |  |
| 401Base | 4344340.247 | 220931.024 | 1994.319 |  |
| 402 | 4356649.665 | 223827.833 | 1787.813 |  |
| 402A_PID | 4356654.099 | 223839.813 | 1787.289 |  |
| 403 | 4341923.971 | 221490.664 | 1976.363 |  |
| 403A | 4341923.047 | 221470.506 | 1977.430 |  |
| 404A | 4337998.689 | 221948.609 | 2119.276 |  |
| 404_PID | 4338012.195 | 221954.557 | 2119.967 |  |
| 405 | 4336764.475 | 225070.552 | 1971.453 |  |
| 406A_PID | 4334177.032 | 226895.366 | 1906.362 |  |
| 406_PID | 4334187.043 | 226901.899 | 1906.291 |  |
| 407 | 4330598.512 | 221971.032 | 2133.494 |  |
| 407A | 4330606.877 | 221910.667 | 2135.182 |  |
| 408 | 4349937.638 | 235264.304 | 2162.510 |  |
| 408A_PID | 4349946.033 | 235243.717 | 2164.232 |  |
| 409 | 4348270.050 | 241246.652 | 1929.303 |  |
| 409A | 4348286.348 | 241253.562 | 1928.245 |  |
| 409B_PID | 4348300.569 | 241259.250 | 1927.427 |  |
| 409C | 4348329.000 | 241294.631 | 1925.099 |  |
| 410 | 4342969.496 | 232288.279 | 1961.573 |  |
| 410A | 4342966.627 | 232303.778 | 1960.628 |  |
| 411 | 4339760.116 | 226258.472 | 1898.598 |  |
| 411A | 4339788.879 | 226235.913 | 1899.856 |  |
| 412E | 4343704.279 | 221021.602 | 1890.792 |  |
| 412W | 4343704.445 | 221017.396 | 1890.839 |  |
| 501 | 4344419.269 | 223709.738 | 1863.647 |  |
| 501A | 4344435.735 | 223718.766 | 1863.069 |  |
| 502 | 4350620.774 | 222952.343 | 1821.615 |  |
| 502A | 4350648.000 | 222961.690 | 1821.067 |  |
| 503 | 4347911.287 | 221738.783 | 1995.734 |  |
| 503A | 4347895.327 | 221748.486 | 1994.613 |  |
| 504 | 4339139.370 | 228170.593 | 1914.256 |  |
| 504A | 4339121.166 | 228170.345 | 1914.793 |  |
| 505 | 4333832.432 | 224130.460 | 1940.439 |  |
| 505A | 4333821.780 | 224113.168 | 1940.558 |  |
| 506 | 4331058.579 | 226542.371 | 1903.680 |  |
| 506A | 4331040.118 | 226561.226 | 1903.048 |  |
| 506B_PID | 4330942.389 | 226624.237 | 1901.281 |  |
| 507 | 4347623.590 | 238309.294 | 1904.455 |  |
| 507A | 4347633.118 | 238323.842 | 1904.904 |  |
| 508 | 4346432.758 | 234250.161 | 1899.646 |  |
| 508A | 4346432.764 | 234230.075 | 1899.684 |  |
| 509A | 4341404.391 | 224290.654 | 1889.782 |  |
| 509_DP3 | 4341397.356 | 224298.029 | 1889.896 |  |
| 510 | 4342065.292 | 230530.766 | 1911.735 |  |
| 510A | 4342105.422 | 230531.066 | 1914.837 |  |
| 701 | 4346397.912 | 223581.080 | 1848.167 |  |
| 701A | 4346421.838 | 223575.110 | 1848.095 |  |
| 702 | 4354485.678 | 224377.310 | 1940.333 |  |
| 702A | 4354490.457 | 224401.905 | 1942.074 |  |
| 703 | 4352920.970 | 222519.702 | 1920.129 |  |
| 703A | 4352894.612 | 222522.590 | 1920.733 |  |
| 704 | 4336430.216 | 227150.555 | 1907.982 |  |
| 704A | 4336425.871 | 227157.594 | 1907.838 |  |
| 705 | 4326603.005 | 225847.828 | 2033.124 |  |
| 705A | 4326637.317 | 225800.951 | 2035.132 |  |
| 705B | 4326612.180 | 225826.793 | 2035.188 |  |
| 706 | 4327776.067 | 228655.797 | 1967.343 |  |
| 706A | 4327761.710 | 228641.915 | 1967.734 |  |
| 707 | 4349035.574 | 233241.341 | 2263.963 |  |
| 707A | 4349023.297 | 233266.123 | 2261.881 |  |
| 708 | 4347004.037 | 228468.008 | 2396.181 |  |
| 708A | 4347001.739 | 228512.413 | 2395.782 |  |
| 709 | 4346249.742 | 240509.337 | 1944.498 |  |
| 709A | 4346235.513 | 240490.551 | 1943.782 |  |
| 710 | 4348854.531 | 236609.543 | 1957.341 |  |
| 710A | 4348869.312 | 236643.483 | 1956.986 |  |
| 710B_PID | 4348923.541 | 236598.676 | 1967.179 |  |
| 711 | 4353365.561 | 222471.258 | 1928.754 |  |
| 711A | 4353335.813 | 222459.169 | 1926.473 |  |
| 711B | 4353355.286 | 222480.902 | 1927.229 |  |
| AP1 | 4356957.366 | 228818.070 | 1797.801 |  |
| AP2_A | 4356977.973 | 228663.856 | 1798.000 |  |
| AP2_B | 4356969.858 | 228676.788 | 1797.963 |  |
| DH6444 | 4336741.093 | 225085.664 | 1970.814 |  |
| DH6446 | 4342999.055 | 232312.467 | 1965.963 |  |
| K0285os | 4339967.193 | 228346.144 | 1901.085 |  |
| KS0282 | 4340012.613 | 228322.735 | 1900.836 |  |
| KS0325 | 4347617.823 | 238264.845 | 1904.167 |  |

Final Control Summary

| Placer County East Lake Tahoe CA |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Swood | Jul-12 |  |  |  |  |  |
| UTM North Zone 11 |  |  |  |  |  |  |
| NAD83, NAVD88, Meters |  |  |  |  |  |
|  | LIDAR QC Classification Codes |  |  |  |  |
|  | Bare Earth/Open Terrain | 400s |  | OT |  |
|  | Tall Weeds and Crops | 500s |  | TW |  |
|  | Forested and Fuly Grown | 700s |  | F |  |
| Name | Grid Northing (m) | Grid Easting (m) | Elevation (m) |  | Control | Note |
| DH6444 | 4336741.093 | 225085.664 | 1970.814 |  | None | NGS PID |
| 401ABase | 4344335.166 | 220909.120 | 1996.459 |  | None | OT |
| 401Base | 4344340.247 | 220931.024 | 1994.319 |  | None | OT |
| 402 | 4356649.665 | 223827.833 | 1787.813 |  | None | OT |
| 403 | 4341923.971 | 221490.664 | 1976.363 |  | None | OT |
| 405 | 4336764.475 | 225070.552 | 1971.453 |  | None | OT |
| 407 | 4330598.512 | 221971.032 | 2133.494 |  | None | OT |
| 408 | 4349937.638 | 235264.304 | 2162.510 |  | None | OT |
| 409 | 4348270.050 | 241246.652 | 1929.303 |  | None | OT |
| 410 | 4342969.496 | 232288.279 | 1961.573 |  | None | OT |
| 411 | 4339760.116 | 226258.472 | 1898.598 |  | None | OT |
| 501 | 4344419.269 | 223709.738 | 1863.647 |  | None | TW |
| 502 | 4350620.774 | 222952.343 | 1821.615 |  | None | TW |
| 503 | 4347911.287 | 221738.783 | 1995.734 |  | None | TW |
| 504 | 4339139.370 | 228170.593 | 1914.256 |  | None | TW |
| 505 | 4333832.432 | 224130.460 | 1940.439 |  | None | TW |
| 506 | 4331058.579 | 226542.371 | 1903.680 |  | None | TW |
| 507 | 4347623.590 | 238309.294 | 1904.455 |  | None | TW |
| 508 | 4346432.758 | 234250.161 | 1899.646 |  | None | TW |
| 510 | 4342065.292 | 230530.766 | 1911.735 |  | None | TW |
| 701 | 4346397.912 | 223581.080 | 1848.167 |  | None | F |
| 702 | 4354485.678 | 224377.310 | 1940.333 |  | None | F |
| 703 | 4352920.970 | 222519.702 | 1920.129 |  | None | F |
| 704 | 4336430.216 | 227150.555 | 1907.982 |  | None | F |
| 705 | 4326603.005 | 225847.828 | 2033.124 |  | None | F |
| 706 | 4327776.067 | 228655.797 | 1967.343 |  | None | F |
| 707 | 4349035.574 | 233241.341 | 2263.963 |  | None | F |
| 708 | 4347004.037 | 228468.008 | 2396.181 |  | None | F |
| 709 | 4346249.742 | 240509.337 | 1944.498 |  | None | F |
| 710 | 4348854.531 | 236609.543 | 1957.341 |  | None | F |
| 711 | 4353365.561 | 222471.258 | 1928.754 |  | None | F |
| 402A_PID | 4356654.099 | 223839.813 | 1787.289 |  | None | OT |
| 403A | 4341923.047 | 221470.506 | 1977.430 |  | None | OT |
| 404_PID | 4338012.195 | 221954.557 | 2119.967 |  | None | OT |
| 404A | 4337998.689 | 221948.609 | 2119.276 |  | None | OT |
| 406_PID | 4334187.043 | 226901.899 | 1906.291 |  | None | OT |
| 406A_PID | 4334177.032 | 226895.366 | 1906.362 |  | None | OT |
| 407A | 4330606.877 | 221910.667 | 2135.182 |  | None | OT |
| 408A_PID | 4349946.033 | 235243.717 | 2164.232 |  | None | OT |
| 409A | 4348286.348 | 241253.562 | 1928.245 |  | None | OT |
| 409B_PID | 4348300.569 | 241259.250 | 1927.427 |  | None | OT |
| 409C | 4348329.000 | 241294.631 | 1925.099 |  | None | OT |
| 410A | 4342966.627 | 232303.778 | 1960.628 |  | None | OT |
| 411A | 4339788.879 | 226235.913 | 1899.856 |  | None | OT |
| 412E | 4343704.279 | 221021.602 | 1890.792 |  | None | OT |
| 412W | 4343704.445 | 221017.396 | 1890.839 |  | None | OT |
| 501A | 4344435.735 | 223718.766 | 1863.069 |  | None | TW |
| 502A | 4350648.000 | 222961.690 | 1821.067 |  | None | TW |
| 503A | 4347895.327 | 221748.486 | 1994.613 |  | None | TW |
| 504A | 4339121.166 | 228170.345 | 1914.793 |  | None | TW |
| 505A | 4333821.780 | 224113.168 | 1940.558 |  | None | TW |
| 506A | 4331040.118 | 226561.226 | 1903.048 |  | None | TW |
| 506B_PID | 4330942.389 | 226624.237 | 1901.281 |  | None | TW |
| 507A | 4347633.118 | 238323.842 | 1904.904 |  | None | TW |
| 508A | 4346432.764 | 234230.075 | 1899.684 |  | None | TW |
| 509_DP3 | 4341397.356 | 224298.029 | 1889.896 |  | None | TW |
| 509A | 4341404.391 | 224290.654 | 1889.782 |  | None | TW |
| 510A | 4342105.422 | 230531.066 | 1914.837 |  | None | TW |
| 701A | 4346421.838 | 223575.110 | 1848.095 |  | None | F |
| 702A | 4354490.457 | 224401.905 | 1942.074 |  | None | F |
| 703A | 4352894.612 | 222522.590 | 1920.733 |  | None | F |
| 704A | 4336425.871 | 227157.594 | 1907.838 |  | None | F |
| 705A | 4326637.317 | 225800.951 | 2035.132 |  | None | F |
| 705B | 4326612.180 | 225826.793 | 2035.188 |  | None | F |
| 706A | 4327761.710 | 228641.915 | 1967.734 |  | None | F |
| 707A | 4349023.297 | 233266.123 | 2261.881 |  | None | F |
| 708A | 4347001.739 | 228512.413 | 2395.782 |  | None | F |
| 709A | 4346235.513 | 240490.551 | 1943.782 |  | None | F |
| 710A | 4348869.312 | 236643.483 | 1956.986 |  | None | F |
| 710B_PID | 4348923.541 | 236598.676 | 1967.179 |  | None | F |
| 711A | 4353335.813 | 222459.169 | 1926.473 |  | None | F |
| 711B | 4353355.286 | 222480.902 | 1927.229 |  | None | F |
| AE9835 | 4344524.474 | 223245.744 | 1877.054 |  | Both | NGS PID |
| AP1 | 4356957.366 | 228818.070 | 1797.801 |  | None | ABGPS |
| AP2_A | 4356977.973 | 228663.856 | 1798.000 |  | None | Temp |
| AP2_B | 4356969.858 | 228676.788 | 1797.963 |  | None | Temp |
| DH6446 | 4342999.055 | 232312.467 | 1965.963 |  | None | NGS PID |
| K0285os | 4339967.193 | 228346.144 | 1901.085 |  | None | NGS PID |
| KS0282 | 4340012.613 | 228322.735 | 1900.836 |  | None | NGS PID |
| KS0325 | 4347617.823 | 238264.845 | 1904.167 |  | None | NGS PID |

| Name | Std Dev n (m) | Std Dev e (m) | Std Dev u (m) | Std Dev Hz (m) | Geoid Separation (m) |
| --- | --- | --- | --- | --- | --- |
| DH6444 | 0.006 | 0.005 | 0.012 | 0.008 |  | -23.671 |  |
| 401ABase | 0.004 | 0.003 | 0.009 | 0.005 |  | -23.515 |  |
| 401Base | 0.004 | 0.003 | 0.009 | 0.005 |  | -23.515 |  |
| 402 | 0.007 | 0.005 | 0.014 | 0.008 |  | -23.548 |  |
| 403 | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.540 |  |
| 405 | 0.010 | 0.006 | 0.014 | 0.012 |  | -23.671 |  |
| 407 | 0.006 | 0.005 | 0.015 | 0.007 |  | -23.666 |  |
| 408 | 0.006 | 0.004 | 0.010 | 0.007 |  | -23.638 |  |
| 409 | 0.005 | 0.004 | 0.012 | 0.007 |  | -23.710 |  |
| 410 | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.763 |  |
| 411 | 0.005 | 0.004 | 0.011 | 0.007 |  | -23.666 |  |
| 501 | 0.007 | 0.005 | 0.014 | 0.009 |  | -23.555 |  |
| 502 | 0.005 | 0.004 | 0.010 | 0.007 |  | -23.519 |  |
| 503 | 0.006 | 0.005 | 0.014 | 0.008 |  | -23.508 |  |
| 504 | 0.005 | 0.004 | 0.012 | 0.006 |  | -23.735 |  |
| 505 | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.678 |  |
| 506 | 0.005 | 0.004 | 0.010 | 0.006 |  | -23.769 |  |
| 507 | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.703 |  |
| 508 | 0.006 | 0.004 | 0.012 | 0.007 |  | -23.701 |  |
| 510 | 0.006 | 0.005 | 0.012 | 0.008 |  | -23.746 |  |
| 701 | 0.013 | 0.005 | 0.017 | 0.014 |  | -23.539 |  |
| 702 | 0.006 | 0.005 | 0.017 | 0.008 |  | -23.547 |  |
| 703 | 0.013 | 0.011 | 0.035 | 0.017 |  | -23.514 |  |
| 704 | 0.009 | 0.009 | 0.023 | 0.012 |  | -23.743 |  |
| 705 | 0.006 | 0.004 | 0.012 | 0.008 |  | -23.743 |  |
| 706 | 0.010 | 0.007 | 0.024 | 0.012 |  | -23.844 |  |
| 707 | 0.006 | 0.006 | 0.017 | 0.009 |  | -23.638 |  |
| 708 | 0.006 | 0.004 | 0.011 | 0.007 |  | -23.613 |  |
| 709 | 0.006 | 0.005 | 0.014 | 0.007 |  | -23.750 |  |
| 710 | 0.009 | 0.006 | 0.016 | 0.011 |  | -23.665 |  |
| 711 | 0.005 | 0.004 | 0.010 | 0.006 |  | -23.514 |  |
| 402A_PID | 0.007 | 0.006 | 0.016 | 0.009 |  | -23.549 |  |
| 403A | 0.005 | 0.003 | 0.010 | 0.006 |  | -23.540 |  |
| 404_PID | 0.006 | 0.004 | 0.012 | 0.007 |  | -23.588 |  |
| 404A | 0.006 | 0.004 | 0.012 | 0.007 |  | -23.588 |  |
| 406_PID | 0.011 | 0.006 | 0.019 | 0.012 |  | -23.761 |  |
| 406A_PID | 0.009 | 0.007 | 0.018 | 0.011 |  | -23.761 |  |
| 407A | 0.008 | 0.006 | 0.019 | 0.010 |  | -23.666 |  |
| 408A_PID | 0.006 | 0.004 | 0.010 | 0.007 |  | -23.637 |  |
| 409A | 0.006 | 0.004 | 0.012 | 0.007 |  | -23.709 |  |
| 409B_PID | 0.005 | 0.004 | 0.012 | 0.007 |  | -23.709 |  |
| 409C | 0.006 | 0.004 | 0.012 | 0.007 |  | -23.709 |  |
| 410A | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.764 |  |
| 411A | 0.006 | 0.004 | 0.011 | 0.007 |  | -23.665 |  |
| 412E | 0.004 | 0.003 | 0.009 | 0.005 |  | -23.520 |  |
| 412W | 0.004 | 0.003 | 0.009 | 0.005 |  | -23.520 |  |
| 501A | 0.006 | 0.004 | 0.011 | 0.007 |  | -23.555 |  |
| 502A | 0.006 | 0.004 | 0.011 | 0.007 |  | -23.519 |  |
| 503A | 0.006 | 0.005 | 0.014 | 0.008 |  | -23.508 |  |
| 504A | 0.005 | 0.004 | 0.013 | 0.007 |  | -23.736 |  |
| 505A | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.677 |  |
| 506A | 0.005 | 0.004 | 0.010 | 0.006 |  | -23.770 |  |
| 506B_PID | 0.005 | 0.004 | 0.010 | 0.006 |  | -23.773 |  |
| 507A | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.703 |  |
| 508A | 0.006 | 0.004 | 0.012 | 0.007 |  | -23.701 |  |
| 509_DP3 | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.594 |  |
| 509A | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.594 |  |
| 510A | 0.006 | 0.005 | 0.012 | 0.007 |  | -23.746 |  |
| 701A | 0.008 | 0.004 | 0.012 | 0.009 |  | -23.539 |  |
| 702A | 0.008 | 0.007 | 0.020 | 0.010 |  | -23.547 |  |
| 703A | 0.012 | 0.009 | 0.023 | 0.015 |  | -23.514 |  |
| 704A | 0.007 | 0.006 | 0.019 | 0.010 |  | -23.743 |  |
| 705A | 0.007 | 0.005 | 0.013 | 0.009 |  | -23.742 |  |
| 705B | 0.007 | 0.004 | 0.013 | 0.008 |  | -23.742 |  |
| 706A | 0.009 | 0.006 | 0.022 | 0.011 |  | -23.843 |  |
| 707A | 0.006 | 0.006 | 0.016 | 0.009 |  | -23.638 |  |
| 708A | 0.008 | 0.006 | 0.017 | 0.010 |  | -23.613 |  |
| 709A | 0.006 | 0.005 | 0.014 | 0.007 |  | -23.751 |  |
| 710A | 0.008 | 0.006 | 0.014 | 0.010 |  | -23.665 |  |
| 710B_PID | 0.007 | 0.005 | 0.013 | 0.009 |  | -23.663 |  |
| 711A | 0.006 | 0.004 | 0.012 | 0.007 |  | -23.514 |  |
| 711B | 0.005 | 0.004 | 0.011 | 0.007 |  | -23.514 |  |
| AE9835 | 0.000 | 0.000 | 0.000 | 0.000 |  | -23.546 |  |
| AP1 | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.606 |  |
| AP2_A | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.605 |  |
| AP2_B | 0.005 | 0.004 | 0.011 | 0.007 |  | -23.605 |  |
| DH6446 | 0.005 | 0.004 | 0.011 | 0.006 |  | -23.763 |  |
| K0285os | 0.005 | 0.004 | 0.014 | 0.007 |  | -23.726 |  |
| KS0282 | 0.010 | 0.006 | 0.025 | 0.012 |  | -23.725 |  |
| KS0325 | 0.006 | 0.004 | 0.013 | 0.008 |  | -23.703 |  |

Gps Observations Summary Part One

| Point Name | Original Name | Antenna Type | Antenna Height (USft) | Ant Height Method | Start Time |
| --- | --- | --- | --- | --- | --- |
| DH6444 | R0600710b_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 1:32 |
| 401Base | B0560709a_81KW | HiPer+ | 4.67 | Vertical | 7/9/2012 16:06 |
| 401ABase | B3610709a_ESQO | HiPer GD/GGD | 4.35 | Vertical | 7/9/2012 16:07 |
| AE9835 | B38730709q_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 16:31 |
| 501A | B38730709qa_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 16:50 |
| 701A | B38730709r_DO1S | HiPer+ | 4.23 | Vertical | 7/9/2012 17:14 |
| AP2_A | B38730709s_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 18:01 |
| AP2_B | B38730709sa_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 18:40 |
| 702A | B38730709t_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 19:22 |
| 402 | B38730709u_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 20:18 |
| 703A | B38730709v_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 21:12 |
| 502 | B38730709va_DO1S | HiPer+ | 4.34 | Vertical | 7/9/2012 21:43 |
| 503A | B38730709w_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 22:24 |
| 403A | B38730709x_DO1S | HiPer+ | 4.41 | Vertical | 7/9/2012 23:42 |
| KS0282 | B38730710a_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 0:28 |
| K0285os | B38730710aa_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 0:52 |
| 501 | R0600709q_1LHC | HiPer+ | 4.30 | Vertical | 7/9/2012 16:49 |
| 701 | R0600709r_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 17:12 |
| AP1 | R0600709s_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 18:09 |
| 702 | R0600709t_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 19:20 |
| 402A_PID | R0600709u_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 20:19 |
| 703 | R0600709v_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 21:10 |
| 502A | R0600709va_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 21:47 |
| 503 | R0600709w_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 22:21 |
| 403 | R0600709x_1LHC | HiPer+ | 4.41 | Vertical | 7/9/2012 23:41 |
| 706A | R0600710w_1LHC | HiPer+ | 4.31 | Vertical | 7/10/2012 22:54 |
| 401Base | B0560710a_81KW | HiPer+ | 4.54 | Vertical | 7/10/2012 14:06 |
| 506B_PID | B3610710a_ESQO | HiPer GD/GGD | 4.37 | Vertical | 7/10/2012 20:26 |
| 401ABase | B2850710b_1728 | HiPer GD/GGD | 4.41 | Vertical | 7/10/2012 14:15 |
| 705B | B3610710b_ESQO | HiPer GD/GGD | 3.70 | Vertical | 7/10/2012 21:28 |
| 504 | B38730710p_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 15:19 |
| 704 | B38730710q_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 16:03 |
| 404_PID | B38730710qa_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 16:45 |
| DH6444 | B38730710r_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 17:13 |
| 406_PID | B38730710ra_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 17:46 |
| 505A | B38730710s_DO1S | HiPer+ | 3.80 | Vertical | 7/10/2012 18:25 |
| 407A | B38730710t_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 19:11 |
| 506 | B38730710u_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 20:13 |
| 705A | B38730710v_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 21:15 |
| 706 | B38730710w_DO1S | HiPer+ | 4.41 | Vertical | 7/10/2012 22:52 |
| 504A | R0600710p_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 15:19 |
| 704A | R0600710q_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 16:05 |
| 404A | R0600710qa_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 16:46 |
| 405 | R0600710r_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 17:14 |
| 406A_PID | R0600710ra_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 17:47 |
| 505 | R0600710s_1LHC | HiPer+ | 4.10 | Vertical | 7/10/2012 18:24 |
| 407 | R0600710t_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 19:08 |
| 506A | R0600710u_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 20:15 |
| 705 | R0600710v_1LHC | HiPer+ | 4.41 | Vertical | 7/10/2012 21:13 |
| 510 | R0600712b_1LHC | HiPer+ | 4.41 | Vertical | 7/12/2012 1:30 |
| 401Base | B0560711a_81KW | HiPer+ | 4.48 | Vertical | 7/11/2012 14:36 |
| 401ABase | B2850711a_1728 | HiPer GD/GGD | 4.54 | Vertical | 7/11/2012 14:41 |
| 707A | B3610711a_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/11/2012 15:44 |
| 708 | B3610711b_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/11/2012 16:32 |
| 408A_PID | B3610711c_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/11/2012 17:17 |
| 507 | B3610711d_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/11/2012 18:06 |
| 409 | B3610711e_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/11/2012 20:01 |
| 710A | B3610711f_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/11/2012 21:14 |
| 410 | B3610712a_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/12/2012 0:28 |
| 411 | B3610712c_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/12/2012 2:13 |
| 707 | B38730711p_DO1S | HiPer+ | 4.41 | Vertical | 7/11/2012 15:41 |
| 708A | B38730711q_DO1S | HiPer+ | 4.41 | Vertical | 7/11/2012 16:35 |
| 408 | B38730711r_DO1S | HiPer+ | 4.41 | Vertical | 7/11/2012 17:16 |
| 507A | B38730711s_DO1S | HiPer+ | 4.37 | Vertical | 7/11/2012 18:07 |
| 709A | B38730711t_DO1S | HiPer+ | 4.41 | Vertical | 7/11/2012 19:04 |
| 409B_PID | B38730711u_DO1S | HiPer+ | 4.41 | Vertical | 7/11/2012 20:03 |
| 710 | B38730711v_DO1S | HiPer+ | 4.41 | Vertical | 7/11/2012 21:10 |
| 508A | B38730711w_DO1S | HiPer+ | 4.37 | Vertical | 7/11/2012 22:05 |
| 509_DP3 | B38730711x_DO1S | HiPer+ | 4.41 | Vertical | 7/11/2012 23:36 |
| DH6446 | B38730712a_DO1S | HiPer+ | 4.41 | Vertical | 7/12/2012 0:20 |
| 510A | B38730712b_DO1S | HiPer+ | 4.41 | Vertical | 7/12/2012 1:28 |
| 411A | B38730712c_DO1S | HiPer+ | 4.41 | Vertical | 7/12/2012 2:16 |
| 409C | R0590711u_UN0G | HiPer+ | 4.41 | Vertical | 7/11/2012 20:24 |
| KS0325 | R0600711s_1LHC | HiPer+ | 4.41 | Vertical | 7/11/2012 18:16 |
| 709 | R0600711t_1LHC | HiPer+ | 4.41 | Vertical | 7/11/2012 19:01 |
| 409A | R0600711u_1LHC | HiPer+ | 4.41 | Vertical | 7/11/2012 20:02 |
| 710B_PID | R0600711v_1LHC | HiPer+ | 4.32 | Vertical | 7/11/2012 21:19 |
| 508 | R0600711w_1LHC | HiPer+ | 4.41 | Vertical | 7/11/2012 22:03 |
| 509A | R0600711x_1LHC | HiPer+ | 4.31 | Vertical | 7/11/2012 23:38 |
| 410A | R0600712a_1LHC | HiPer+ | 4.41 | Vertical | 7/12/2012 0:32 |
| 412W | R0600712p_1LHC | HiPer+ | 4.41 | Vertical | 7/12/2012 15:00 |
| 401Base | B0560712a_81KW | HiPer+ | 4.64 | Vertical | 7/12/2012 13:07 |
| 401ABase | B2850712b_1728 | HiPer GD/GGD | 4.39 | Vertical | 7/12/2012 13:11 |
| 711A | B3610712d_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/12/2012 13:40 |
| 711B | B38730712n_DO1S | HiPer+ | 4.41 | Vertical | 7/12/2012 13:45 |
| 412E | B38730712p_DO1S | HiPer+ | 4.33 | Vertical | 7/12/2012 15:00 |
| 711 | R0600712n_1LHC | HiPer+ | 4.41 | Vertical | 7/12/2012 13:37 |

Gps Observations Summary Part Two

| Point Name | Original Name | Stop Time | Duration | Method | Receiver |
| --- | --- | --- | --- | --- | --- |
| DH6444 | R0600710b_1LHC | 7/10/2012 1:49 | 0:17:25 | Static | 8RJYCOT1LHC |
| 401Base | B0560709a_81KW | 7/10/2012 2:13 | 10:06:55 | Static | 8PZFI4M81KW |
| 401ABase | B3610709a_ESQO | 7/10/2012 2:16 | 10:08:10 | Static | 8PJPJX3ESQO |
| AE9835 | B38730709q_DO1S | 7/9/2012 16:42 | 0:10:35 | Static | 8RHDWKLDO1S |
| 501A | B38730709qa_DO1S | 7/9/2012 17:02 | 0:11:30 | Static | 8RHDWKLDO1S |
| 701A | B38730709r_DO1S | 7/9/2012 17:32 | 0:17:35 | Static | 8RHDWKLDO1S |
| AP2_A | B38730709s_DO1S | 7/9/2012 18:39 | 0:38:00 | Static | 8RHDWKLDO1S |
| AP2_B | B38730709sa_DO1S | 7/9/2012 18:47 | 0:06:55 | Static | 8RHDWKLDO1S |
| 702A | B38730709t_DO1S | 7/9/2012 19:43 | 0:21:30 | Static | 8RHDWKLDO1S |
| 402 | B38730709u_DO1S | 7/9/2012 20:48 | 0:30:10 | Static | 8RHDWKLDO1S |
| 703A | B38730709v_DO1S | 7/9/2012 21:30 | 0:17:25 | Static | 8RHDWKLDO1S |
| 502 | B38730709va_DO1S | 7/9/2012 22:03 | 0:19:25 | Static | 8RHDWKLDO1S |
| 503A | B38730709w_DO1S | 7/9/2012 22:39 | 0:14:35 | Static | 8RHDWKLDO1S |
| 403A | B38730709x_DO1S | 7/10/2012 0:02 | 0:20:25 | Static | 8RHDWKLDO1S |
| KS0282 | B38730710a_DO1S | 7/10/2012 0:45 | 0:17:05 | Static | 8RHDWKLDO1S |
| K0285os | B38730710aa_DO1S | 7/10/2012 1:08 | 0:16:15 | Static | 8RHDWKLDO1S |
| 501 | R0600709q_1LHC | 7/9/2012 17:02 | 0:13:25 | Static | 8RJYCOT1LHC |
| 701 | R0600709r_1LHC | 7/9/2012 17:32 | 0:19:40 | Static | 8RJYCOT1LHC |
| AP1 | R0600709s_1LHC | 7/9/2012 18:49 | 0:39:50 | Static | 8RJYCOT1LHC |
| 702 | R0600709t_1LHC | 7/9/2012 19:42 | 0:22:30 | Static | 8RJYCOT1LHC |
| 402A_PID | R0600709u_1LHC | 7/9/2012 20:45 | 0:26:20 | Static | 8RJYCOT1LHC |
| 703 | R0600709v_1LHC | 7/9/2012 21:30 | 0:20:00 | Static | 8RJYCOT1LHC |
| 502A | R0600709va_1LHC | 7/9/2012 22:02 | 0:15:30 | Static | 8RJYCOT1LHC |
| 503 | R0600709w_1LHC | 7/9/2012 22:39 | 0:18:05 | Static | 8RJYCOT1LHC |
| 403 | R0600709x_1LHC | 7/10/2012 0:03 | 0:22:10 | Static | 8RJYCOT1LHC |
| 706A | R0600710w_1LHC | 7/10/2012 23:40 | 0:45:55 | Static | 8RJYCOT1LHC |
| 401Base | B0560710a_81KW | 7/11/2012 0:21 | 10:15:15 | Static | 8PZFI4M81KW |
| 506B_PID | B3610710a_ESQO | 7/10/2012 20:49 | 0:23:10 | Static | 8PJPJX3ESQO |
| 401ABase | B2850710b_1728 | 7/11/2012 0:25 | 10:09:15 | Static | 8R0PSO61728 |
| 705B | B3610710b_ESQO | 7/10/2012 22:00 | 0:32:00 | Static | 8PJPJX3ESQO |
| 504 | B38730710p_DO1S | 7/10/2012 15:44 | 0:24:55 | Static | 8RHDWKLDO1S |
| 704 | B38730710q_DO1S | 7/10/2012 16:26 | 0:23:30 | Static | 8RHDWKLDO1S |
| 404_PID | B38730710qa_DO1S | 7/10/2012 17:03 | 0:18:05 | Static | 8RHDWKLDO1S |
| DH6444 | B38730710r_DO1S | 7/10/2012 17:24 | 0:11:30 | Static | 8RHDWKLDO1S |
| 406_PID | B38730710ra_DO1S | 7/10/2012 18:14 | 0:27:15 | Static | 8RHDWKLDO1S |
| 505A | B38730710s_DO1S | 7/10/2012 18:51 | 0:25:15 | Static | 8RHDWKLDO1S |
| 407A | B38730710t_DO1S | 7/10/2012 19:40 | 0:29:40 | Static | 8RHDWKLDO1S |
| 506 | B38730710u_DO1S | 7/10/2012 20:52 | 0:38:55 | Static | 8RHDWKLDO1S |
| 705A | B38730710v_DO1S | 7/10/2012 22:02 | 0:47:05 | Static | 8RHDWKLDO1S |
| 706 | B38730710w_DO1S | 7/10/2012 23:41 | 0:48:20 | Static | 8RHDWKLDO1S |
| 504A | R0600710p_1LHC | 7/10/2012 15:43 | 0:23:40 | Static | 8RJYCOT1LHC |
| 704A | R0600710q_1LHC | 7/10/2012 16:26 | 0:21:05 | Static | 8RJYCOT1LHC |
| 404A | R0600710qa_1LHC | 7/10/2012 17:02 | 0:15:55 | Static | 8RJYCOT1LHC |
| 405 | R0600710r_1LHC | 7/10/2012 17:23 | 0:09:10 | Static | 8RJYCOT1LHC |
| 406A_PID | R0600710ra_1LHC | 7/10/2012 18:13 | 0:26:05 | Static | 8RJYCOT1LHC |
| 505 | R0600710s_1LHC | 7/10/2012 18:51 | 0:27:30 | Static | 8RJYCOT1LHC |
| 407 | R0600710t_1LHC | 7/10/2012 19:42 | 0:33:15 | Static | 8RJYCOT1LHC |
| 506A | R0600710u_1LHC | 7/10/2012 20:51 | 0:36:25 | Static | 8RJYCOT1LHC |
| 705 | R0600710v_1LHC | 7/10/2012 22:04 | 0:50:15 | Static | 8RJYCOT1LHC |
| 510 | R0600712b_1LHC | 7/12/2012 1:52 | 0:22:05 | Static | 8RJYCOT1LHC |
| 401Base | B0560711a_81KW | 7/12/2012 2:47 | 12:11:05 | Static | 8PZFI4M81KW |
| 401ABase | B2850711a_1728 | 7/12/2012 2:50 | 12:08:50 | Static | 8R0PSO61728 |
| 707A | B3610711a_ESQO | 7/11/2012 16:11 | 0:27:45 | Static | 8PJPJX3ESQO |
| 708 | B3610711b_ESQO | 7/11/2012 16:56 | 0:24:40 | Static | 8PJPJX3ESQO |
| 408A_PID | B3610711c_ESQO | 7/11/2012 17:51 | 0:34:05 | Static | 8PJPJX3ESQO |
| 507 | B3610711d_ESQO | 7/11/2012 18:49 | 0:43:30 | Static | 8PJPJX3ESQO |
| 409 | B3610711e_ESQO | 7/11/2012 20:40 | 0:39:30 | Static | 8PJPJX3ESQO |
| 710A | B3610711f_ESQO | 7/11/2012 21:48 | 0:33:25 | Static | 8PJPJX3ESQO |
| 410 | B3610712a_ESQO | 7/12/2012 0:58 | 0:30:35 | Static | 8PJPJX3ESQO |
| 411 | B3610712c_ESQO | 7/12/2012 2:32 | 0:18:20 | Static | 8PJPJX3ESQO |
| 707 | B38730711p_DO1S | 7/11/2012 16:12 | 0:31:00 | Static | 8RHDWKLDO1S |
| 708A | B38730711q_DO1S | 7/11/2012 16:55 | 0:20:15 | Static | 8RHDWKLDO1S |
| 408 | B38730711r_DO1S | 7/11/2012 17:52 | 0:36:00 | Static | 8RHDWKLDO1S |
| 507A | B38730711s_DO1S | 7/11/2012 18:50 | 0:42:55 | Static | 8RHDWKLDO1S |
| 709A | B38730711t_DO1S | 7/11/2012 19:40 | 0:36:10 | Static | 8RHDWKLDO1S |
| 409B_PID | B38730711u_DO1S | 7/11/2012 20:39 | 0:35:50 | Static | 8RHDWKLDO1S |
| 710 | B38730711v_DO1S | 7/11/2012 21:47 | 0:36:25 | Static | 8RHDWKLDO1S |
| 508A | B38730711w_DO1S | 7/11/2012 22:30 | 0:24:45 | Static | 8RHDWKLDO1S |
| 509_DP3 | B38730711x_DO1S | 7/11/2012 23:54 | 0:17:50 | Static | 8RHDWKLDO1S |
| DH6446 | B38730712a_DO1S | 7/12/2012 0:55 | 0:35:00 | Static | 8RHDWKLDO1S |
| 510A | B38730712b_DO1S | 7/12/2012 1:53 | 0:24:45 | Static | 8RHDWKLDO1S |
| 411A | B38730712c_DO1S | 7/12/2012 2:33 | 0:17:40 | Static | 8RHDWKLDO1S |
| 409C | R0590711u_UN0G | 7/11/2012 20:37 | 0:13:00 | Static | 8QCP5IOUN0G |
| KS0325 | R0600711s_1LHC | 7/11/2012 18:48 | 0:32:05 | Static | 8RJYCOT1LHC |
| 709 | R0600711t_1LHC | 7/11/2012 19:40 | 0:38:50 | Static | 8RJYCOT1LHC |
| 409A | R0600711u_1LHC | 7/11/2012 20:40 | 0:38:05 | Static | 8RJYCOT1LHC |
| 710B_PID | R0600711v_1LHC | 7/11/2012 21:44 | 0:25:35 | Static | 8RJYCOT1LHC |
| 508 | R0600711w_1LHC | 7/11/2012 22:31 | 0:27:30 | Static | 8RJYCOT1LHC |
| 509A | R0600711x_1LHC | 7/11/2012 23:55 | 0:16:45 | Static | 8RJYCOT1LHC |
| 410A | R0600712a_1LHC | 7/12/2012 0:58 | 0:25:45 | Static | 8RJYCOT1LHC |
| 412W | R0600712p_1LHC | 7/12/2012 15:11 | 0:11:00 | Static | 8RJYCOT1LHC |
| 401Base | B0560712a_81KW | 7/12/2012 15:16 | 2:09:05 | Static | 8PZFI4M81KW |
| 401ABase | B2850712b_1728 | 7/12/2012 15:17 | 2:06:15 | Static | 8R0PSO61728 |
| 711A | B3610712d_ESQO | 7/12/2012 14:05 | 0:25:35 | Static | 8PJPJX3ESQO |
| 711B | B38730712n_DO1S | 7/12/2012 14:04 | 0:19:15 | Static | 8RHDWKLDO1S |
| 412E | B38730712p_DO1S | 7/12/2012 15:11 | 0:10:15 | Static | 8RHDWKLDO1S |
| 711 | R0600712n_1LHC | 7/12/2012 14:07 | 0:29:35 | Static | 8RJYCOT1LHC |

Placer County East Area CP Sketch

NGS DataSheets

DATABASE = NGSIDB , PROGRAM = datasheet95, VERSION = 7.89

1        National Geodetic Survey,   Retrieval Date = JULY  8, 2012

DH6444 ***********************************************************************

DH6444  DESIGNATION -  WARD CREEK

DH6444  PID         -  DH6444

DH6444  STATE/COUNTY-  CA/PLACER

DH6444  COUNTRY     -  US

DH6444  USGS QUAD   -  TAHOE CITY (1992)

DH6444

DH6444                         *CURRENT SURVEY CONTROL

DH6444  ______________________________________________________________________

DH6444* NAD 83(2011) POSITION- 39 08 11.33039(N) 120 10 50.22268(W)   ADJUSTED

DH6444* NAD 83(2011) ELLIP HT-  1947.084 (meters)        (06/27/12)   ADJUSTED

DH6444* NAD 83(2011) EPOCH   -  2010.00

DH6444* NAVD 88 ORTHO HEIGHT -  1970.8    (meters)    6466.    (feet) GPS OBS

DH6444  ______________________________________________________________________

DH6444  NAVD 88 orthometric height was determined with geoid model    GEOID03

DH6444  GEOID HEIGHT    -        -23.62  (meters)                     GEOID03

DH6444  GEOID HEIGHT    -        -23.73  (meters)                     GEOID12

DH6444  NAD 83(2011) X  - -2,491,159.924 (meters)                     COMP

DH6444  NAD 83(2011) Y  - -4,283,573.820 (meters)                     COMP

DH6444  NAD 83(2011) Z  -  4,005,309.635 (meters)                     COMP

DH6444  LAPLACE CORR    -         -7.26  (seconds)                    DEFLEC09

DH6444

DH6444  FGDC Geospatial Positioning Accuracy Standards (95% confidence, cm)

DH6444  Type                                         Horiz  Ellip  Dist(km)

DH6444  -------------------------------------------------------------------

DH6444  NETWORK                                       0.76   1.51

DH6444  -------------------------------------------------------------------

DH6444  MEDIAN LOCAL ACCURACY AND DIST (003 points)   0.78   1.25      8.00

DH6444  -------------------------------------------------------------------

DH6444  NOTE: Click here for information on individual local accuracy

DH6444  values and other accuracy information.

DH6444

DH6444

DH6444.The horizontal coordinates were established by GPS observations

DH6444.and adjusted by the National Geodetic Survey in June 2012.

DH6444

DH6444.NAD 83(2011) refers to NAD 83 coordinates where the reference

DH6444.frame has been affixed to the stable North American tectonic plate. See

DH6444.www.ngs.noaa.gov/web/surveys/NA2011 for more information.

DH6444

DH6444.The horizontal coordinates are valid at the epoch date displayed above

DH6444.which is a decimal equivalence of Year/Month/Day.

DH6444

DH6444.The orthometric height was determined by GPS observations and a

DH6444.high-resolution geoid model.

DH6444

DH6444.The X, Y, and Z were computed from the position and the ellipsoidal ht.

DH6444

DH6444.The Laplace correction was computed from DEFLEC09 derived deflections.

DH6444

DH6444.The ellipsoidal height was determined by GPS observations

DH6444.and is referenced to NAD 83.

DH6444

DH6444. The following values were computed from the NAD 83(2011) position.

DH6444

DH6444;                    North         East     Units Scale Factor Converg.

DH6444;SPC CA 2     -   664,731.810 2,157,279.477   MT  0.99991508   +1 08 49.4

DH6444;SPC CA 2     - 2,180,874.28  7,077,674.42   sFT  0.99991508   +1 08 49.4

DH6444;UTM  10      - 4,335,708.095   743,685.773   MT  1.00033125   +1 46 49.4

DH6444

DH6444!             -  Elev Factor  x  Scale Factor =   Combined Factor

DH6444!SPC CA 2     -   0.99969461  x   0.99991508  =   0.99960971

DH6444!UTM  10      -   0.99969461  x   1.00033125  =   1.00002576

DH6444

DH6444                          SUPERSEDED SURVEY CONTROL

DH6444

DH6444  NAD 83(2007)-  39 08 11.32918(N)    120 10 50.22215(W) AD(2007.00) 0

DH6444  ELLIP H (02/10/07) 1947.065  (m)                       GP(2007.00)

DH6444  NAD 83(1998)-  39 08 11.32892(N)    120 10 50.22115(W) AD(2004.69) B

DH6444  ELLIP H (09/28/05) 1947.094  (m)                       GP(2004.69) 4 1

DH6444

DH6444.Superseded values are not recommended for survey control.

DH6444

DH6444.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DH6444.See file dsdata.txt to determine how the superseded data were derived.

DH6444

DH6444_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SGJ4368535708(NAD 83)

DH6444

DH6444_MARKER: DD = SURVEY DISK

DH6444_SETTING: 15 = METAL ROD DRIVEN INTO GROUND. SEE TEXT FOR ADDITIONAL

DH6444+WITH SETTING: INFORMATION.

DH6444_STAMPING: WARD CREEK 2004

DH6444_MARK LOGO: CADT

DH6444_PROJECTION: PROJECTING 5 CENTIMETERS

DH6444_MAGNETIC: M = MARKER EQUIPPED WITH BAR MAGNET

DH6444_STABILITY: B = PROBABLY HOLD POSITION/ELEVATION WELL

DH6444_SATELLITE: THE SITE LOCATION WAS REPORTED AS SUITABLE FOR

DH6444+SATELLITE: SATELLITE OBSERVATIONS - July 28, 2004

DH6444_ROD/PIPE-DEPTH: 1.20 meters

DH6444_SLEEVE-DEPTH  : N/A meters

DH6444

DH6444  HISTORY     - Date     Condition        Report By

DH6444  HISTORY     - 20040728 MONUMENTED       CADT

DH6444

DH6444                          STATION DESCRIPTION

DH6444

DH6444'DESCRIBED BY CALTRANS 2004 (FTC)

DH6444'THE STATION IS LOCATED IN PLACER COUNTY NEAR SUNNYSIDE ON THE WEST

DH6444'SHORE OF LAKE  TAHOE, ABOUT 12.1 KM NORTHWEST OF MEEKS BAY, 8.7 KM

DH6444'SOUTHWEST OF DOLLAR POINT, AND 5.4  KM SOUTHWEST OF TAHOE CITY.

DH6444'

DH6444'TO REACH THE STATION FROM THE INTERSECTION OF STATE HIGHWAY 28 AND

DH6444'STATE HIGHWAY 89 IN  TAHOE CITY, PROCEED 3.88 KM SOUTHERLY ON STATE

DH6444'HIGHWAY 89 TO A SIDE ROAD RIGHT, PINELAND  DRIVE. TURN RIGHT AND

DH6444'PROCEED WESTERLY ON PINELAND DRIVE 710 M TO A FORK. BEAR LEFT AT  THE

DH6444'FORK, ON TWIN PEAKS DRIVE, AND CONTINUE WESTERLY 200 M TO A POINT AT

DH6444'WHICH TWIN  PEAKS DRIVE BECOMES WARD CREEK ROAD. CONTINUE ON WARD

DH6444'CREEK ROAD 1.52 KM TO A SMALL  GRAVEL PARKING AREA AND THE STATION ON

DH6444'THE LEFT.

DH6444'

DH6444'THE STATION IS A 3/4 IN ALUMINUM ALLOY ROD DRIVEN TO REFUSAL, WITH A

DH6444'CADT/CSRC ALUMINUM  SURVEY DISK AFFIXED, SET IN A 6 IN DIAMETER PVC

DH6444'WELL CASING WITH AN ALUMINUM ACCESS COVER.  THE STATION LIES 64.0 M

DH6444'SOUTHEAST OF A POWER POLE, 16.7 M NORTH-NORTHWEST OF THE  WESTERLY

DH6444'GATE POST OF A METAL FOREST SERVICE GATE, 15.1 M SOUTHWEST OF THE

DH6444'CENTERLINE  OF THE ROAD, 10.3 M SOUTHWEST OF POWER POLE NO. 1235, 1.0

DH6444'M NORTHEAST OF A METAL GUARD  POST, AND ABOUT 0.5 M LOWER THAN THE

DH6444'ROAD. THIS STATION WAS OCCUPIED AS PART OF A  CALTRANS NORTH REGION

DH6444'OFFICE OF SURVEYORS GPS HEIGHT MODERNIZATION PROJECT.

1        National Geodetic Survey,   Retrieval Date = JULY  8, 2012

DH6446 ***********************************************************************

DH6446  DESIGNATION -  DOLLAR

DH6446  PID         -  DH6446

DH6446  STATE/COUNTY-  CA/PLACER

DH6446  COUNTRY     -  US

DH6446  USGS QUAD   -  KINGS BEACH (1992)

DH6446

DH6446                         *CURRENT SURVEY CONTROL

DH6446  ______________________________________________________________________

DH6446* NAD 83(2011) POSITION- 39 11 42.14331(N) 120 05 58.54397(W)   ADJUSTED

DH6446* NAD 83(2011) ELLIP HT-  1942.179 (meters)        (06/27/12)   ADJUSTED

DH6446* NAD 83(2011) EPOCH   -  2010.00

DH6446* NAVD 88 ORTHO HEIGHT -  1966.0    (meters)    6450.    (feet) GPS OBS

DH6446  ______________________________________________________________________

DH6446  NAVD 88 orthometric height was determined with geoid model    GEOID03

DH6446  GEOID HEIGHT    -        -23.68  (meters)                     GEOID03

DH6446  GEOID HEIGHT    -        -23.84  (meters)                     GEOID12

DH6446  NAD 83(2011) X  - -2,483,038.371 (meters)                     COMP

DH6446  NAD 83(2011) Y  - -4,283,535.656 (meters)                     COMP

DH6446  NAD 83(2011) Z  -  4,010,348.568 (meters)                     COMP

DH6446  LAPLACE CORR    -         -4.46  (seconds)                    DEFLEC09

DH6446

DH6446  FGDC Geospatial Positioning Accuracy Standards (95% confidence, cm)

DH6446  Type                                         Horiz  Ellip  Dist(km)

DH6446  -------------------------------------------------------------------

DH6446  NETWORK                                       1.02   1.74

DH6446  -------------------------------------------------------------------

DH6446  MEDIAN LOCAL ACCURACY AND DIST (003 points)   0.95   1.45      9.19

DH6446  -------------------------------------------------------------------

DH6446  NOTE: Click here for information on individual local accuracy

DH6446  values and other accuracy information.

DH6446

DH6446

DH6446.The horizontal coordinates were established by GPS observations

DH6446.and adjusted by the National Geodetic Survey in June 2012.

DH6446

DH6446.NAD 83(2011) refers to NAD 83 coordinates where the reference

DH6446.frame has been affixed to the stable North American tectonic plate. See

DH6446.www.ngs.noaa.gov/web/surveys/NA2011 for more information.

DH6446

DH6446.The horizontal coordinates are valid at the epoch date displayed above

DH6446.which is a decimal equivalence of Year/Month/Day.

DH6446

DH6446.The orthometric height was determined by GPS observations and a

DH6446.high-resolution geoid model.

DH6446

DH6446.The X, Y, and Z were computed from the position and the ellipsoidal ht.

DH6446

DH6446.The Laplace correction was computed from DEFLEC09 derived deflections.

DH6446

DH6446.The ellipsoidal height was determined by GPS observations

DH6446.and is referenced to NAD 83.

DH6446

DH6446. The following values were computed from the NAD 83(2011) position.

DH6446

DH6446;                    North         East     Units Scale Factor Converg.

DH6446;SPC CA 2     -   671,374.341 2,164,146.616   MT  0.99991652   +1 11 53.3

DH6446;SPC CA 2     - 2,202,667.32  7,100,204.36   sFT  0.99991652   +1 11 53.3

DH6446;UTM  10      - 4,342,429.198   750,481.892   MT  1.00037260   +1 50 02.0

DH6446

DH6446!             -  Elev Factor  x  Scale Factor =   Combined Factor

DH6446!SPC CA 2     -   0.99969538  x   0.99991652  =   0.99961192

DH6446!UTM  10      -   0.99969538  x   1.00037260  =   1.00006787

DH6446

DH6446                          SUPERSEDED SURVEY CONTROL

DH6446

DH6446  NAD 83(2007)-  39 11 42.14235(N)    120 05 58.54371(W) AD(2007.00) 0

DH6446  ELLIP H (02/10/07) 1942.159  (m)                       GP(2007.00)

DH6446  NAD 83(1998)-  39 11 42.14196(N)    120 05 58.54248(W) AD(2004.69) B

DH6446  ELLIP H (09/28/05) 1942.187  (m)                       GP(2004.69) 4 1

DH6446

DH6446.Superseded values are not recommended for survey control.

DH6446

DH6446.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DH6446.See file dsdata.txt to determine how the superseded data were derived.

DH6446

DH6446_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SGJ5048142429(NAD 83)

DH6446

DH6446_MARKER: DD = SURVEY DISK

DH6446_SETTING: 15 = METAL ROD DRIVEN INTO GROUND. SEE TEXT FOR ADDITIONAL

DH6446+WITH SETTING: INFORMATION.

DH6446_STAMPING: DOLLAR 2004

DH6446_MARK LOGO: CADT

DH6446_PROJECTION: PROJECTING 15 CENTIMETERS

DH6446_MAGNETIC: M = MARKER EQUIPPED WITH BAR MAGNET

DH6446_STABILITY: B = PROBABLY HOLD POSITION/ELEVATION WELL

DH6446_SATELLITE: THE SITE LOCATION WAS REPORTED AS SUITABLE FOR

DH6446+SATELLITE: SATELLITE OBSERVATIONS - July 27, 2004

DH6446_ROD/PIPE-DEPTH: 1.50 meters

DH6446_SLEEVE-DEPTH  : N/A meters

DH6446

DH6446  HISTORY     - Date     Condition        Report By

DH6446  HISTORY     - 20040727 MONUMENTED       CADT

DH6446

DH6446                          STATION DESCRIPTION

DH6446

DH6446'DESCRIBED BY CALTRANS 2004 (FTC)

DH6446'THE STATION IS LOCATED IN PLACER COUNTY AT DOLLAR POINT, LAKE TAHOE,

DH6446'ABOUT 16.5 KM  SOUTHEAST OF TRUCKEE, 7.1 KM SOUTHWEST OF TAHOE VISTA,

DH6446'AND 4.2 KM EAST OF TAHOE CITY.

DH6446'

DH6446'TO REACH THE STATION FROM THE INTERSECTION OF STATE HIGHWAY 89 AND

DH6446'STATE HIGHWAY 28 IN  TAHOE CITY, PROCEED 5.20 KM EAST ON STATE HIGHWAY

DH6446'28 TO THE STATION ON THE RIGHT, ON THE  OUTSIDE OF A CURVE AT THE TOP

DH6446'OF A LARGE CUT BANK, AT HIGHWAY POST MILE 3.25.

DH6446'

DH6446'THE STATION IS A 3/4 IN ALUMINUM ALLOY ROD DRIVEN TO REFUSAL, WITH A

DH6446'CADT/CSRC ALUMINUM  SURVEY DISK AFFIXED, SET IN A 6 IN DIAMETER PVC

DH6446'WELL CASING WITH AN ALUMINUM ACCESS COVER.  THE STATION LIES 27.1 M

DH6446'SOUTHEAST OF THE CENTERLINE OF THE HIGHWAY, 14.8 M NORTHEAST OF A

DH6446'TWIN 0.40 M DBH JEFFREY PINE TREE, 11.7 M SOUTHWEST OF A 0.45 M DBH

DH6446'JEFFREY PINE, 5.8 M  SOUTHEAST OF A FOOT PATH ALONG THE TOP OF THE CUT

DH6446'BANK, 1.0 M SOUTHEAST OF A METAL  GUARD POST, AND ABOUT 9 M HIGHER

DH6446'THAN THE HIGHWAY. THIS STATION WAS OCCUPIED AS PART  OF A CALTRANS

DH6446'NORTH REGION OFFICE OF SURVEYORS GPS HEIGHT MODERNIZATION PROJECT.

1        National Geodetic Survey,   Retrieval Date = JULY  8, 2012

AE9835 ***********************************************************************

AE9835  DESIGNATION -  HPGN D CA 03 HQ

AE9835  PID         -  AE9835

AE9835  STATE/COUNTY-  CA/PLACER

AE9835  COUNTRY     -  US

AE9835  USGS QUAD   -  TAHOE CITY (1992)

AE9835

AE9835                         *CURRENT SURVEY CONTROL

AE9835  ______________________________________________________________________

AE9835* NAD 83(2011) POSITION- 39 12 21.33008(N) 120 12 18.19352(W)   ADJUSTED

AE9835* NAD 83(2011) ELLIP HT-  1853.465 (meters)        (06/27/12)   ADJUSTED

AE9835* NAD 83(2011) EPOCH   -  2010.00

AE9835* NAVD 88 ORTHO HEIGHT -  1877.0    (meters)    6158.    (feet) GPS OBS

AE9835  ______________________________________________________________________

AE9835  NAVD 88 orthometric height was determined with geoid model    GEOID03

AE9835  GEOID HEIGHT    -        -23.46  (meters)                     GEOID03

AE9835  GEOID HEIGHT    -        -23.59  (meters)                     GEOID12

AE9835  NAD 83(2011) X  - -2,490,499.442 (meters)                     COMP

AE9835  NAD 83(2011) Y  - -4,278,238.433 (meters)                     COMP

AE9835  NAD 83(2011) Z  -  4,011,229.267 (meters)                     COMP

AE9835  LAPLACE CORR    -         -1.32  (seconds)                    DEFLEC09

AE9835

AE9835  FGDC Geospatial Positioning Accuracy Standards (95% confidence, cm)

AE9835  Type                                         Horiz  Ellip  Dist(km)

AE9835  -------------------------------------------------------------------

AE9835  NETWORK                                       0.76   1.47

AE9835  -------------------------------------------------------------------

AE9835  MEDIAN LOCAL ACCURACY AND DIST (024 points)   0.87   1.70     38.13

AE9835  -------------------------------------------------------------------

AE9835  NOTE: Click here for information on individual local accuracy

AE9835  values and other accuracy information.

AE9835

AE9835

AE9835.The horizontal coordinates were established by GPS observations

AE9835.and adjusted by the National Geodetic Survey in June 2012.

AE9835

AE9835.NAD 83(2011) refers to NAD 83 coordinates where the reference

AE9835.frame has been affixed to the stable North American tectonic plate. See

AE9835.www.ngs.noaa.gov/web/surveys/NA2011 for more information.

AE9835

AE9835.The horizontal coordinates are valid at the epoch date displayed above

AE9835.which is a decimal equivalence of Year/Month/Day.

AE9835

AE9835.The orthometric height was determined by GPS observations and a

AE9835.high-resolution geoid model.

AE9835

AE9835.The X, Y, and Z were computed from the position and the ellipsoidal ht.

AE9835

AE9835.The Laplace correction was computed from DEFLEC09 derived deflections.

AE9835

AE9835.The ellipsoidal height was determined by GPS observations

AE9835.and is referenced to NAD 83.

AE9835

AE9835. The following values were computed from the NAD 83(2011) position.

AE9835

AE9835;                    North         East     Units Scale Factor Converg.

AE9835;SPC CA 2     -   672,397.277 2,155,015.063   MT  0.99991690   +1 07 54.0

AE9835;SPC CA 2     - 2,206,023.40  7,070,245.25   sFT  0.99991690   +1 07 54.0

AE9835;UTM  10      - 4,343,351.131   741,335.636   MT  1.00031720   +1 46 03.2

AE9835

AE9835!             -  Elev Factor  x  Scale Factor =   Combined Factor

AE9835!SPC CA 2     -   0.99970929  x   0.99991690  =   0.99962621

AE9835!UTM  10      -   0.99970929  x   1.00031720  =   1.00002640

AE9835

AE9835                          SUPERSEDED SURVEY CONTROL

AE9835

AE9835  NAD 83(2007)-  39 12 21.32904(N)    120 12 18.19303(W) AD(2007.00) 0

AE9835  ELLIP H (02/10/07) 1853.442  (m)                       GP(2007.00)

AE9835  NAD 83(1998)-  39 12 21.32865(N)    120 12 18.19206(W) AD(2004.69) B

AE9835  ELLIP H (09/28/05) 1853.473  (m)                       GP(2004.69) 4 1

AE9835  NAD 83(1992)-  39 12 21.32489(N)    120 12 18.18599(W) AD(1991.35) 1

AE9835  ELLIP H (05/26/98) 1853.512  (m)                       GP(1991.35) 4 2

AE9835

AE9835.Superseded values are not recommended for survey control.

AE9835

AE9835.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

AE9835.See file dsdata.txt to determine how the superseded data were derived.

AE9835

AE9835_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SGJ4133543351(NAD 83)

AE9835

AE9835_MARKER: DD = SURVEY DISK

AE9835_SETTING: 50 = ALUMINUM ALLOY ROD W/O SLEEVE (10 FT.+)

AE9835_STAMPING: CA-HPGN-DENSIFICATION STA. 03-HQ 1994

AE9835_MARK LOGO: CADT

AE9835_MAGNETIC: N = NO MAGNETIC MATERIAL

AE9835_STABILITY: B = PROBABLY HOLD POSITION/ELEVATION WELL

AE9835_SATELLITE: THE SITE LOCATION WAS REPORTED AS SUITABLE FOR

AE9835+SATELLITE: SATELLITE OBSERVATIONS - September 30, 2008

AE9835

AE9835  HISTORY     - Date     Condition        Report By

AE9835  HISTORY     - 1994     MONUMENTED       CADT

AE9835  HISTORY     - 20030821 GOOD             CADT

AE9835  HISTORY     - 20080930 GOOD             SPPC

AE9835

AE9835                          STATION DESCRIPTION

AE9835

AE9835'DESCRIBED BY CALTRANS 1994 (BES)

AE9835'THE STATION IS LOCATED IN SQUAW VALLEY ON THE NORTH SIDE OF SQUAW

AE9835'VALLEY ROAD, ABOUT 8 MI (12.9 KM) SOUTH OF TRUCKEE AND 4 MI (6.4 KM)

AE9835'NORTHWEST OF TAHOE CITY.  TO REACH THE STATION FROM THE JUNCTION OF

AE9835'INTERSTATE HIGHWAY 80 AND STATE HIGHWAY 89 (SOUTH) IN TRUCKEE, GO

AE9835'SOUTH ON HIGHWAY 89 FOR 0.5 MI (0.8 KM) TO THE NEVADA/PLACER COUNTY

AE9835'LINE.  CONTINUE SOUTH ON HIGHWAY 89 FOR 8.0 MI (12.9 KM) TO A SIDE

AE9835'ROAD RIGHT, SQUAW VALLEY ROAD.  TURN RIGHT AND GO WEST ON SQUAW VALLEY

AE9835'ROAD FOR 0.3 MI (0.5 KM) TO SQUAW VALLEY ACADEMY ON THE LEFT AND THE

AE9835'STATION ON THE RIGHT AT POST MILE 2.03.  THE STATION IS A SURVEY DISK

AE9835'ENCASED IN PVC PIPE WITH ACCESS COVER SET IN CONCRETE FLUSH WITH THE

AE9835'GROUND, 113 FT (34.4 M) WEST OF JOINT POLE NO 17-A5/CA-24, 98 FT (29.9

AE9835'M) EAST OF JOINT POLE NO J-50950, 53 FT (16.2 M) WEST-NORTHWEST OF A

AE9835'SIERRA PACIFIC POWER CO MANHOLE, 46.0 FT (14.0 M) NORTH OF THE

AE9835'CENTERLINE OF SQUAW VALLEY ROAD, 9.5 FT (2.9 M) SOUTH OF A PEELER CORE

AE9835'FENCE, 8.0 FT (2.4 M) SOUTH OF A CARSONITE WITNESS POST AND LEVEL WITH

AE9835'SQUAW VALLEY ROAD.  THE STATION WAS OCCUPIED AS PART OF A CALIFORNIA

AE9835'HPGN DENSIFICATION SURVEY.

AE9835

AE9835                          STATION RECOVERY (2003)

AE9835

AE9835'RECOVERY NOTE BY CALTRANS 2003 (DWM)

AE9835'THE STATION WAS RECOVERED AS DESCRIBED. THIS STATION WAS OCCUPIED AS

AE9835'PART OF A  CALTRANS NORTH REGION OFFICE OF SURVEYORS GPS HEIGHT

AE9835'MODERNIZATION PROJECT.

AE9835

AE9835                          STATION RECOVERY (2008)

AE9835

AE9835'RECOVERY NOTE BY SIERRA PACIFIC POWER COMPANY 2008 (LDL)

AE9835'RECOVERED IN GOOD CONDITION.

*** retrieval complete.

Elapsed Time = 00:00:04

64a94033-1196-4c22-bcdb-14018c710166

Y2:64a94033-1196-4c22-bcdb-14018c710166

KS0325 ***********************************************************************

KS0325  DESIGNATION -  H 181

KS0325  PID         -  KS0325

KS0325  STATE/COUNTY-  CA/PLACER

KS0325  COUNTRY     -  US

KS0325  USGS QUAD   -  KINGS BEACH (1992)

KS0325

KS0325                         *CURRENT SURVEY CONTROL

KS0325  ______________________________________________________________________

KS0325* NAD 83(2011) POSITION- 39 14 18.29036(N) 120 01 57.18735(W)   ADJUSTED

KS0325* NAD 83(2011) ELLIP HT-  1880.444 (meters)        (06/27/12)   ADJUSTED

KS0325* NAD 83(2011) EPOCH   -  2010.00

KS0325* NAVD 88 ORTHO HEIGHT -  1904.2    (meters)    6247.    (feet) GPS OBS

KS0325  ______________________________________________________________________

KS0325  NAVD 88 orthometric height was determined with geoid model    GEOID03

KS0325  GEOID HEIGHT    -        -23.66  (meters)                     GEOID03

KS0325  GEOID HEIGHT    -        -23.78  (meters)                     GEOID12

KS0325  NAD 83(2011) X  - -2,476,476.208 (meters)                     COMP

KS0325  NAD 83(2011) Y  - -4,283,760.204 (meters)                     COMP

KS0325  NAD 83(2011) Z  -  4,014,041.424 (meters)                     COMP

KS0325  LAPLACE CORR    -         -0.23  (seconds)                    DEFLEC09

KS0325

KS0325  FGDC Geospatial Positioning Accuracy Standards (95% confidence, cm)

KS0325  Type                                         Horiz  Ellip  Dist(km)

KS0325  -------------------------------------------------------------------

KS0325  NETWORK                                       1.04   1.84

KS0325  -------------------------------------------------------------------

KS0325  MEDIAN LOCAL ACCURACY AND DIST (021 points)   1.13   2.04     42.69

KS0325  -------------------------------------------------------------------

KS0325  NOTE: Click here for information on individual local accuracy

KS0325  values and other accuracy information.

KS0325

KS0325

KS0325.The horizontal coordinates were established by GPS observations

KS0325.and adjusted by the National Geodetic Survey in June 2012.

KS0325

KS0325.NAD 83(2011) refers to NAD 83 coordinates where the reference

KS0325.frame has been affixed to the stable North American tectonic plate. See

KS0325.www.ngs.noaa.gov/web/surveys/NA2011 for more information.

KS0325

KS0325.The horizontal coordinates are valid at the epoch date displayed above

KS0325.which is a decimal equivalence of Year/Month/Day.

KS0325

KS0325.The orthometric height was determined by GPS observations and a

KS0325.high-resolution geoid model.

KS0325

KS0325.The X, Y, and Z were computed from the position and the ellipsoidal ht.

KS0325

KS0325.The Laplace correction was computed from DEFLEC09 derived deflections.

KS0325

KS0325.The ellipsoidal height was determined by GPS observations

KS0325.and is referenced to NAD 83.

KS0325

KS0325. The following values were computed from the NAD 83(2011) position.

KS0325

KS0325;                    North         East     Units Scale Factor Converg.

KS0325;SPC CA 2     -   676,311.431 2,169,832.348   MT  0.99991826   +1 14 25.5

KS0325;SPC CA 2     - 2,218,865.09  7,118,858.30   sFT  0.99991826   +1 14 25.5

KS0325;UTM  10      - 4,347,431.529   756,115.072   MT  1.00040774   +1 52 41.1

KS0325;UTM  11      - 4,347,617.838   238,264.866   MT  1.00044358   -1 55 09.6

KS0325

KS0325!             -  Elev Factor  x  Scale Factor =   Combined Factor

KS0325!SPC CA 2     -   0.99970506  x   0.99991826  =   0.99962334

KS0325!UTM  10      -   0.99970506  x   1.00040774  =   1.00011268

KS0325!UTM  11      -   0.99970506  x   1.00044358  =   1.00014851

KS0325

KS0325                          SUPERSEDED SURVEY CONTROL

KS0325

KS0325  NAD 83(2007)-  39 14 18.28962(N)    120 01 57.18742(W) AD(2007.00) 0

KS0325  ELLIP H (02/10/07) 1880.421  (m)                       GP(2007.00)

KS0325  NAD 83(1998)-  39 14 18.28911(N)    120 01 57.18581(W) AD(2004.69) B

KS0325  ELLIP H (09/28/05) 1880.448  (m)                       GP(2004.69) 4 1

KS0325  NAD 83(1992)-  39 14 18.28539(N)    120 01 57.18025(W) AD(1991.35) 1

KS0325  ELLIP H (05/26/98) 1880.493  (m)                       GP(1991.35) 4 2

KS0325

KS0325.Superseded values are not recommended for survey control.

KS0325

KS0325.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

KS0325.See file dsdata.txt to determine how the superseded data were derived.

KS0325

KS0325_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SGJ5611547431(NAD 83)

KS0325

KS0325_MARKER: DB = BENCH MARK DISK

KS0325_SETTING: 80 = SET IN A BOULDER

KS0325_STAMPING: H 181 1932

KS0325_MARK LOGO: USGS

KS0325_MAGNETIC: N = NO MAGNETIC MATERIAL

KS0325_STABILITY: C = MAY HOLD, BUT OF TYPE COMMONLY SUBJECT TO

KS0325+STABILITY: SURFACE MOTION

KS0325_SATELLITE: THE SITE LOCATION WAS REPORTED AS SUITABLE FOR

KS0325+SATELLITE: SATELLITE OBSERVATIONS - October 05, 2004

KS0325

KS0325  HISTORY     - Date     Condition        Report By

KS0325  HISTORY     - 1932     MONUMENTED       USGS

KS0325  HISTORY     - 19960804 GOOD             CADT

KS0325  HISTORY     - 20040916 GOOD             INDIV

KS0325  HISTORY     - 20041005 GOOD             CADT

KS0325

KS0325                          STATION DESCRIPTION

KS0325

KS0325'DESCRIBED BY US GEOLOGICAL SURVEY 1932

KS0325'9.1 MI NE FROM TAHOE.

KS0325'9.1 MILES NORTHEAST ALONG STATE HIGHWAY 89 FROM THE POST OFFICE

KS0325'AT TAHOE, PLACER COUNTY, AT THE BROCKWAY GOLF COURSE, 222 FEET

KS0325'NORTH OF THE CENTERLINE OF THE HIGHWAY, 177 FEET SOUTH OF THE

KS0325'CENTER OF A CONCRETE TENNIS COURT, AND IN THE TOP OF A GRANITE

KS0325'BOULDER.  A UNITED STATES GEOLOGICAL SURVEY STANDARD DISK,

KS0325'STAMPED H 181 1932.

KS0325

KS0325                          STATION RECOVERY (1996)

KS0325

KS0325'RECOVERY NOTE BY CALTRANS 1996 (PTD)

KS0325'THE STATION WAS RECOVERED.  A COMPLETE NEW DESCRIPTION FOLLOWS.  THE

KS0325'STATION IS LOCATED ON THE GROUNDS OF THE OLD BROCKWAY GOLF COURSE IN

KS0325'KINGS BEACH, ABOUT 10 MI (16.1 KM) SOUTHEAST OF TRUCKEE, 8 MI (12.9

KS0325'KM) NORTHEAST OF TAHOE CITY AND 1.5 MI (2.4 KM) WEST OF THE

KS0325'CALIFORNIA/NEVADA STATE LINE.  TO REACH THE STATION FROM THE JUNCTION

KS0325'OF STATE HIGHWAYS 28 AND 267 IN KINGS BEACH, GO WEST ON HIGHWAY 28 FOR

KS0325'0.1 MI (0.2 KM) TO THE OLD BROCKWAY GOLF COURSE AND THE STATION ON THE

KS0325'RIGHT AT POST MILE 9.15.  THE STATION IS SET FLUSH IN THE TOP OF A

KS0325'PARTIALLY EXPOSED GRANITE BOULDER THAT PROJECTS 0.5 FT (15.2 CM) ABOVE

KS0325'GROUND, 133 FT (40.5 M) NORTH OF THE CENTERLINE OF HIGHWAY 28, 89 FT

KS0325'(27.1 M) WEST OF THE CENTERLINE OF BASSIE AVENUE, 77 FT (23.5 M) NORTH

KS0325'OF A WOOD FENCE, 63.5 FT (19.4 M) WEST-NORTHWEST OF A 3 FT (0.9 M)

KS0325'DIAMETER PINE TREE, 61.5 FT (18.7 M) SOUTHEAST OF A 4 FT (1.2 M)

KS0325'DIAMETER PINE TREE, 8 FT (2.4 M) WEST OF THE CENTER OF A GOLF CART

KS0325'PATH AND ABOUT 2 FT (0.6 M) HIGHER THAN HIGHWAY 28.  THE STATION WAS

KS0325'OCCUPIED AS PART OF A CALIFORNIA HPGN DENSIFICATION SURVEY.

KS0325

KS0325                          STATION RECOVERY (2004)

KS0325

KS0325'RECOVERY NOTE BY INDIVIDUAL CONTRIBUTORS 2004 (HSI)

KS0325'RECOVERED IN GOOD CONDITION.

KS0325

KS0325                          STATION RECOVERY (2004)

KS0325

KS0325'RECOVERY NOTE BY CALTRANS 2004 (DWM)

KS0325'THE STATION WAS RECOVERED AS DESCRIBED. THIS STATION WAS OCCUPIED AS

KS0325'PART OF A  CALTRANS NORTH REGION OFFICE OF SURVEYORS GPS HEIGHT

KS0325'MODERNIZATION PROJECT.

1        National Geodetic Survey,   Retrieval Date = JULY  8, 2012

KS0282 ***********************************************************************

KS0282  DESIGNATION -  G 125

KS0282  PID         -  KS0282

KS0282  STATE/COUNTY-  CA/PLACER

KS0282  COUNTRY     -  US

KS0282  USGS QUAD   -  TAHOE CITY (1992)

KS0282

KS0282                         *CURRENT SURVEY CONTROL

KS0282  ______________________________________________________________________

KS0282* NAD 83(1986) POSITION- 39 10 00.     (N) 120 08 40.     (W)   SCALED

KS0282* NAVD 88 ORTHO HEIGHT -  1900.84   (+/-2cm)    6236.3   (feet) VERTCON

KS0282  ______________________________________________________________________

KS0282  GEOID HEIGHT    -        -23.81  (meters)                     GEOID12

KS0282  VERT ORDER      -  SECOND    CLASS 0 (See Below)

KS0282

KS0282.The horizontal coordinates were scaled from a topographic map and have

KS0282.an estimated accuracy of +/- 6 seconds.

KS0282.

KS0282.The NAVD 88 height was computed by applying the VERTCON shift value to

KS0282.the NGVD 29 height (displayed under SUPERSEDED SURVEY CONTROL.)

KS0282

KS0282.The vertical order pertains to the NGVD 29 superseded value.

KS0282

KS0282;                    North         East    Units  Estimated Accuracy

KS0282;SPC CA 2     -   668,150.    2,160,340.      MT  (+/- 180 meters Scaled)

KS0282

KS0282                          SUPERSEDED SURVEY CONTROL

KS0282

KS0282.No superseded survey control is available for this station.

KS0282

KS0282_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SGJ467391(NAD 83)

KS0282

KS0282_MARKER: DB = BENCH MARK DISK

KS0282_SETTING: 36 = SET IN A MASSIVE STRUCTURE

KS0282_SP_SET: BRIDGE

KS0282_STAMPING: G 125 1932

KS0282_STABILITY: B = PROBABLY HOLD POSITION/ELEVATION WELL

KS0282_SATELLITE: THE SITE LOCATION WAS REPORTED AS NOT SUITABLE FOR

KS0282+SATELLITE: SATELLITE OBSERVATIONS - June 01, 2001

KS0282

KS0282  HISTORY     - Date     Condition        Report By

KS0282  HISTORY     - 1932     MONUMENTED       CGS

KS0282  HISTORY     - 1957     GOOD             CGS

KS0282  HISTORY     - 20010601 GOOD             CADT

KS0282  HISTORY     - 20060828 GOOD             GEOCAC

KS0282

KS0282                          STATION DESCRIPTION

KS0282

KS0282'DESCRIBED BY COAST AND GEODETIC SURVEY 1957

KS0282'0.2 MI SW FROM TAHOE CITY.

KS0282'0.2 MILE SOUTHWEST ALONG STATE HIGHWAY 28 FROM THE POST OFFICE

KS0282'AT TAHOE CITY, AT THE Y JUNCTION OF STATE HIGHWAY 89 LEADING

KS0282'NORTHWEST, AT BRIDGE 19-33 OVER TRUCKEE RIVER, IN THE TOP OF THE

KS0282'WEST CONCRETE CURB, 19 FEET WEST OF THE CENTER OF THE NORTH END

KS0282'OF THE BRIDGE, 12.2 FEET SOUTH OF THE NORTH END OF THE CURB,

KS0282'AND ABOUT 1 FOOT HIGHER THAN THE BRIDGE DECK.

KS0282

KS0282                          STATION RECOVERY (2001)

KS0282

KS0282'RECOVERY NOTE BY CALTRANS 2001 (FTC)

KS0282'FOUND AS DESCRIBED. THE BRIDGE IS KNOWN LOCALLY AS FANNY BRIDGE.

KS0282

KS0282                          STATION RECOVERY (2006)

KS0282

KS0282'RECOVERY NOTE BY GEOCACHING 2006 (HAN)

KS0282'RECOVERED IN FAIR TO GOOD CONDITION AT N 39  10.018 W 120  08.671, BY

KS0282'HANSOHN. THE DISK HAS BEEN SCRATCHED BY SNOW CLEARING EQUIPMENT.

1        National Geodetic Survey,   Retrieval Date = JULY  8, 2012

KS0285 ***********************************************************************

KS0285  DESIGNATION -  L 837

KS0285  PID         -  KS0285

KS0285  STATE/COUNTY-  CA/PLACER

KS0285  COUNTRY     -  US

KS0285  USGS QUAD   -  TAHOE CITY (1992)

KS0285

KS0285                         *CURRENT SURVEY CONTROL

KS0285  ______________________________________________________________________

KS0285* NAD 83(1986) POSITION- 39 09 59.22   (N) 120 08 40.50   (W)   HD_HELD1

KS0285* NAVD 88 ORTHO HEIGHT -  1900.85   (+/-2cm)    6236.4   (feet) VERTCON

KS0285  ______________________________________________________________________

KS0285  GEOID HEIGHT    -        -23.82  (meters)                     GEOID12

KS0285  VERT ORDER      -  SECOND    CLASS 0 (See Below)

KS0285

KS0285.The horizontal coordinates were established by differentially corrected

KS0285.hand held GPS obs and have an estimated accuracy of +/- 3 meters.

KS0285.

KS0285.The NAVD 88 height was computed by applying the VERTCON shift value to

KS0285.the NGVD 29 height (displayed under SUPERSEDED SURVEY CONTROL.)

KS0285

KS0285.The vertical order pertains to the NGVD 29 superseded value.

KS0285

KS0285.Photographs are available for this station.

KS0285

KS0285;                    North         East    Units  Estimated Accuracy

KS0285;SPC CA 2     -   668,121.0   2,160,326.2     MT  (+/- 3 meters HH1 GPS)

KS0285

KS0285                          SUPERSEDED SURVEY CONTROL

KS0285

KS0285.No superseded survey control is available for this station.

KS0285

KS0285_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SGJ4669639132(NAD 83)

KS0285

KS0285_MARKER: DB = BENCH MARK DISK

KS0285_SETTING: 17 = SET INTO TOP OF METAL PIPE DRIVEN INTO GROUND

KS0285_SP_SET: METAL PIPE DRIVEN INTO GROUND

KS0285_STAMPING: L 837

KS0285_MARK LOGO: BOR

KS0285_STABILITY: D = MARK OF QUESTIONABLE OR UNKNOWN STABILITY

KS0285

KS0285  HISTORY     - Date     Condition        Report By

KS0285  HISTORY     - UNK      MONUMENTED       BPR

KS0285  HISTORY     - 1957     GOOD             CGS

KS0285  HISTORY     - 20060828 GOOD             GEOCAC

KS0285

KS0285                          STATION DESCRIPTION

KS0285

KS0285'DESCRIBED BY COAST AND GEODETIC SURVEY 1957

KS0285'0.2 MI SW FROM TAHOE CITY.

KS0285'0.2 MILE SOUTHWEST ALONG STATE HIGHWAY 28 FROM THE POST OFFICE

KS0285'AT TAHOE CITY, ON THE SOUTH BANK OF THE TRUCKEE RIVER, 96.4

KS0285'FEET WEST OF THE SOUTHWEST CORNER OF BRIDGE 19-33 OVER TRUCKEE

KS0285'RIVER, 25.3 FEET SOUTHEAST OF A WATER GAGE, 22 FEET SOUTH OF

KS0285'WATERS EDGE OF THE RIVER, 21.8 FEET EAST OF THE EAST SIDE OF

KS0285'A 48-FOOT CORRUGATED METAL BUILDING, 4 FEET NORTHWEST OF A 12-INCH

KS0285'PINE TREE, 2.1 FEET SOUTH OF A WITNESS POST, AND WELDED ON THE TOP

KS0285'OF A 3-INCH IRON PIPE FLUSH WITH THE GROUND.

KS0285

KS0285                          STATION RECOVERY (2006)

KS0285

KS0285'RECOVERY NOTE BY GEOCACHING 2006 (HAN)

KS0285'RECOVERED IN GOOD CONDITION AT N 39  09.988 W 120  08.671, BY HANSOHN.

KS0285'