May 2012

Placer County California West Area NE of Sacramento LIDAR QC Survey Control Report 2012

The scope of this project included control recovery and GPS surveying to establish x, y, & z positions of 30 plus locations divided into 3 unique ground cover classifications to be used as LIDAR imagery ground truthing quality control checking throughout the new project image area.

Locations were planned from office project limits layouts with some field adjustments. Control points classification points were located then measured by gps surveys for horizontal and vertical locations.  Recovered NGS high Order horizontal and vertical monuments were used to establish the horizontal and vertical datum used for this survey. Six existing federal government geodetic control stations were incorporated to our primary control network.  Surveyor positioned one secondary base station to supplement the NGS control stations and to provide shorter vectors and a more dense overall network.  Control was planned to be at least Second Order horizontal and Third Order vertical.  The datum for this project was in NAD83 horizontal and NAVD88 vertical in meter units and the final adjusted data was reported in UTM North Zone 10 datum with orthometric elevations.

.

This project area is comprised of both populated and more remote areas north and east of the towns of Lincoln and Rocklin California in Placer County.  The town of Auburn is in the east central project area.  An area map is included within this report.

gps measurements commenced on July 03, 2012 and were completed on July 08, 2012 which is Julian days 185 thru 189 in year 2012. All measurements were made in a static mode. Each site was occupied for several minutes and the base stations ran for several hours. Control point sites were located with one dual frequency receiver running as a base station in addition to the local CORS base stations and a second and third and fourth(sometimes)dual frequency receiver as rovers to the various new locations.

The equipment configuration for this project consists of industry standard gps and conventional surveying equipment.  The gps equipment used was a combination of Topcon dual frequency(L1/L2) receivers.  The Topcon receivers are the Hiper GD and Hiper Plus type. Topcon Tools gps processing software was used to post process all observed data.

Each observation was logged for site id, receiver type, height of antenna, start time and date.  Length of vector, time of day, SV configuration and site obstructions determined the length of observation at each site. Data was downloaded to the PC after each day’s sessions.  Initial processing was performed to verify we had good vector solutions between sites.

The horizontal and vertical datum for this survey was based on recovered high order NGS monuments NGS PID JS0750, JS0786, JS0801, and CORS stations LNC1, LNC2 and SACR.

The Topcon Tools processing software reports the horizontal and vertical precision of every vector measured and summarizes the standard deviation in x, y and z position for each individual control point.

The final adjusted coordinate values are as listed herein.  gps software adjustment summaries are included for your future reference.  Photo references are attached in separate documents.

Steven A. Wood, L.S., C.P.,

Project Area Map

Land Cover Classifications

| NUMBER OF POINTS | LAND COVER CLASS | LAND COVER DESCRIPTION |
| --- | --- | --- |
| 10 | Class 1 | Bare Earth / Open Terrain |
| 10 | Class 3 | Tall Weeds and Crops |
| 10 | Class 5 | Forested and Fully Grown |

gps Observation  Survey Adjustments

Project Summary

Project name: PlacerWest07032012.ttp 
Surveyor: 
Comment: 
Linear unit: Meters 
Projection: UTMNorth-Zone_10 : 126W to 120W 
Geoid: g2009u05

Adjustment Summary

Adjustment type: Plane + Height, Constraint 
Confidence level: 95 % 
Number of adjusted points: 71 
Number of plane control points: 2 
Number of used GPS vectors: 172 
Number of rejected GPS vectors by plane: 1 
A posteriori plane UWE: 0.8135548 , Bounds: ( 0.9029723 , 1.096902 ) 
Number of height control points: 3 
Number of rejected GPS vectors by height: 3 
A posteriori height UWE: 1.217632 , Bounds: ( 0.8621718 , 1.137581 )

| Used GPS Observations |
| --- |
| Name | dN (m) | dE (m) | dHt (m) | Horz RMS (m) | Vert RMS (m) |
| 401−401A_PID | 18.284 | 7.094 | 0.298 | 0.001 | 0.002 |
| 401−LNC2 | 6169.073 | -14437.998 | -91.269 | 0.006 | 0.011 |
| 401−SACR | -15090.041 | -14375.589 | -90.112 | 0.008 | 0.015 |
| 401A_PID−LNC2 | 6150.798 | -14445.085 | -91.554 | 0.006 | 0.011 |
| 401A_PID−SACR | -15108.317 | -14382.675 | -90.393 | 0.008 | 0.015 |
| 402−402A | -30.161 | 28.893 | 0.262 | 0.004 | 0.006 |
| 402−LNC2 | -2034.849 | -21974.174 | -307.934 | 0.010 | 0.021 |
| 403−403A | -48.859 | -14.079 | -3.097 | 0.001 | 0.002 |
| 403−LNC2 | -3125.687 | -14850.293 | -237.868 | 0.006 | 0.012 |
| 403−SACR | -24384.801 | -14787.883 | -236.727 | 0.012 | 0.020 |
| 403A−LNC2 | -3076.836 | -14836.214 | -234.757 | 0.007 | 0.012 |
| 403A−SACR | -24335.951 | -14773.803 | -233.613 | 0.014 | 0.024 |
| 404−404A | 9.569 | -18.848 | -1.016 | 0.002 | 0.005 |
| 404−411Base | -1889.571 | -4144.568 | -111.204 | 0.002 | 0.004 |
| 404A−411Base | -1899.139 | -4125.721 | -110.184 | 0.003 | 0.008 |
| 405−405A_PID | -15.635 | 8.693 | 0.390 | 0.003 | 0.005 |
| 405−405B_PID | -14.558 | -10.151 | 0.667 | 0.004 | 0.005 |
| 405−411Base | -9642.460 | -5411.046 | -224.262 | 0.005 | 0.008 |
| 405A_PID−405B_PID | 1.077 | -18.845 | 0.274 | 0.003 | 0.004 |
| 405A_PID−411Base | -9626.835 | -5419.740 | -224.624 | 0.005 | 0.010 |
| 405B_PID−411Base | -9627.904 | -5400.898 | -224.897 | 0.006 | 0.009 |
| 406−406A | -5.127 | 64.818 | 3.649 | 0.010 | 0.017 |
| 406−411Base | -2236.264 | 3277.076 | 23.941 | 0.008 | 0.014 |
| 406−LNC2 | -9900.758 | -17301.540 | -304.953 | 0.021 | 0.035 |
| 406A−411Base | -2231.132 | 3212.252 | 20.282 | 0.003 | 0.004 |
| 406A−LNC2 | -9895.633 | -17366.361 | -308.621 | 0.009 | 0.015 |
| 407−407A_PID | 6.549 | -1.628 | -0.254 | 0.002 | 0.004 |
| 407−411Base | -7667.980 | 9435.696 | 247.523 | 0.006 | 0.010 |
| 407−LNC2 | -15332.458 | -11142.926 | -81.349 | 0.009 | 0.015 |
| 407A_PID−411Base | -7674.523 | 9437.319 | 247.779 | 0.007 | 0.012 |
| 407A_PID−LNC2 | -15339.004 | -11141.299 | -81.087 | 0.009 | 0.015 |
| 408−408A_PID | -51.128 | -0.683 | 0.208 | 0.005 | 0.009 |
| 408−411Base | -12710.806 | 15893.132 | 256.893 | 0.009 | 0.018 |
| 408−LNC2 | -20375.283 | -4685.472 | -71.942 | 0.008 | 0.016 |
| 408A_PID−411Base | -12659.693 | 15893.812 | 256.701 | 0.010 | 0.017 |
| 408A_PID−LNC2 | -20324.168 | -4684.794 | -72.142 | 0.010 | 0.018 |
| 409−409A | -16.998 | 1.449 | -0.356 | 0.004 | 0.011 |
| 409−411Base | -10682.673 | 17999.190 | 303.443 | 0.006 | 0.015 |
| 409−LNC1 | -18346.318 | -2552.107 | -25.331 | 0.005 | 0.014 |
| 409−LNC2 | -18347.163 | -2579.415 | -25.393 | 0.005 | 0.014 |
| 409A−411Base | -10665.680 | 17997.738 | 303.810 | 0.008 | 0.024 |
| 409A−LNC1 | -18329.326 | -2553.559 | -24.970 | 0.008 | 0.022 |
| 409A−LNC2 | -18330.172 | -2580.867 | -25.031 | 0.008 | 0.022 |
| 410−410A | -8.132 | 5.161 | 0.141 | 0.004 | 0.008 |
| 410−411Base | -6205.469 | 13981.891 | 290.392 | 0.014 | 0.026 |
| 410−LNC1 | -13869.120 | -6569.396 | -38.367 | 0.011 | 0.023 |
| 410−LNC2 | -13869.965 | -6596.705 | -38.429 | 0.010 | 0.021 |
| 410A−411Base | -6197.354 | 13976.735 | 290.299 | 0.008 | 0.016 |
| 410A−LNC1 | -13860.984 | -6574.565 | -38.519 | 0.007 | 0.012 |
| 410A−LNC2 | -13861.829 | -6601.874 | -38.577 | 0.007 | 0.013 |
| 411Base−412 | 4433.292 | -8221.174 | -194.323 | 0.004 | 0.006 |
| 411Base−412A | 4438.004 | -8216.863 | -194.046 | 0.004 | 0.006 |
| 411Base−505 | 7800.211 | 7437.371 | 213.144 | 0.006 | 0.010 |
| 411Base−505A | 7788.101 | 7458.875 | 214.515 | 0.005 | 0.010 |
| 411Base−506 | 9135.864 | -140.518 | 45.697 | 0.008 | 0.017 |
| 411Base−506A | 9090.575 | -145.987 | 45.461 | 0.007 | 0.015 |
| 411Base−507 | 5600.851 | -3350.574 | 15.798 | 0.004 | 0.008 |
| 411Base−507A | 5595.551 | -3330.099 | 15.558 | 0.004 | 0.007 |
| 411Base−508 | 10324.002 | -15169.233 | -254.175 | 0.007 | 0.013 |
| 411Base−508A | 10358.880 | -15157.184 | -249.317 | 0.008 | 0.015 |
| 411Base−509 | 7678.434 | -22347.040 | -328.485 | 0.010 | 0.023 |
| 411Base−509A | 7701.461 | -22326.539 | -328.200 | 0.011 | 0.024 |
| 411Base−509B_PID | 7656.296 | -22342.242 | -328.374 | 0.015 | 0.035 |
| 411Base−510 | 7791.753 | -17915.625 | -308.303 | 0.009 | 0.015 |
| 411Base−510A | 7776.631 | -17912.545 | -308.694 | 0.009 | 0.016 |
| 411Base−704 | 2580.291 | 861.746 | 73.315 | 0.004 | 0.007 |
| 411Base−704A | 2584.824 | 803.327 | 72.203 | 0.005 | 0.009 |
| 411Base−705 | 6067.705 | 3429.499 | 64.797 | 0.005 | 0.010 |
| 411Base−705A | 6077.717 | 3460.882 | 62.620 | 0.005 | 0.008 |
| 411Base−706 | 12441.596 | -2349.881 | 55.013 | 0.007 | 0.013 |
| 411Base−706A | 12450.964 | -2332.042 | 54.049 | 0.007 | 0.014 |
| 411Base−707 | -645.807 | -6431.408 | -244.413 | 0.007 | 0.012 |
| 411Base−707A | -634.242 | -6483.993 | -244.496 | 0.009 | 0.017 |
| 411Base−708 | 8669.887 | -3540.134 | 18.312 | 0.005 | 0.010 |
| 411Base−708A | 8664.346 | -3570.626 | 14.970 | 0.004 | 0.007 |
| 411Base−709 | 9171.934 | -12185.519 | -252.624 | 0.019 | 0.035 |
| 411Base−709A | 9171.170 | -12201.906 | -253.872 | 0.016 | 0.034 |
| 411Base−710 | 14485.275 | -17628.558 | -263.476 | 0.012 | 0.019 |
| 411Base−710A | 14423.196 | -17567.315 | -262.509 | 0.013 | 0.021 |
| 411Base−LNC1 | -7663.647 | -20551.299 | -328.807 | 0.008 | 0.013 |
| 411Base−LNC2 | -7664.492 | -20578.604 | -328.923 | 0.008 | 0.013 |
| 411Base−LNC2 | -7664.493 | -20578.608 | -328.868 | 0.008 | 0.013 |
| 411Base−LNC2 | -7664.489 | -20578.609 | -328.862 | 0.008 | 0.013 |
| 411Base−SACR | -28923.604 | -20516.194 | -327.745 | 0.012 | 0.021 |
| 411Base−SACR | -28923.601 | -20516.201 | -327.677 | 0.012 | 0.021 |
| 411Base−SACR | -28923.603 | -20516.190 | -327.657 | 0.012 | 0.021 |
| 412−412A | 4.711 | 4.310 | 0.274 | 0.002 | 0.003 |
| 412−LNC1 | -12096.950 | -12330.119 | -134.476 | 0.007 | 0.013 |
| 412−LNC2 | -12097.796 | -12357.428 | -134.537 | 0.007 | 0.013 |
| 412A−LNC1 | -12101.660 | -12334.428 | -134.749 | 0.008 | 0.013 |
| 412A−LNC2 | -12102.507 | -12361.738 | -134.809 | 0.008 | 0.013 |
| 501−501A | 16.920 | 11.301 | 0.996 | 0.001 | 0.003 |
| 501−LNC2 | 5073.050 | -16254.848 | -113.675 | 0.008 | 0.016 |
| 501−SACR | -16186.054 | -16192.446 | -112.526 | 0.010 | 0.021 |
| 501A−LNC2 | 5056.136 | -16266.155 | -114.682 | 0.007 | 0.016 |
| 501A−SACR | -16202.968 | -16203.754 | -113.531 | 0.010 | 0.021 |
| 502−502A | -8.363 | 16.409 | 0.571 | 0.002 | 0.003 |
| 502−LNC2 | 1492.937 | -19684.105 | -167.955 | 0.011 | 0.013 |
| 502−SACR | -19766.178 | -19621.696 | -166.773 | 0.016 | 0.017 |
| 502A−LNC2 | 1501.291 | -19700.510 | -168.522 | 0.010 | 0.014 |
| 502A−SACR | -19757.816 | -19638.096 | -167.340 | 0.015 | 0.018 |
| 503−503A | 18.443 | -51.373 | 0.437 | 0.001 | 0.001 |
| 503−LNC2 | -581.084 | -8829.685 | -85.702 | 0.004 | 0.007 |
| 503−SACR | -21840.196 | -8767.280 | -84.548 | 0.009 | 0.023 |
| 503A−LNC2 | -599.528 | -8778.312 | -86.144 | 0.004 | 0.008 |
| 503A−SACR | -21858.639 | -8715.912 | -84.987 | 0.009 | 0.023 |
| 504−504A | -21.296 | -7.237 | 0.037 | 0.002 | 0.003 |
| 504−LNC2 | -7579.835 | -20625.478 | -316.513 | 0.010 | 0.014 |
| 504A−LNC2 | -7558.533 | -20618.245 | -316.522 | 0.008 | 0.013 |
| 505−505A | -12.108 | 21.499 | 1.370 | 0.002 | 0.003 |
| 506−506A | -45.291 | -5.463 | -0.214 | 0.002 | 0.005 |
| 507−507A | -5.300 | 20.476 | -0.244 | 0.002 | 0.003 |
| 507−LNC2 | -13265.335 | -17228.035 | -344.720 | 0.009 | 0.015 |
| 508−508A | 34.880 | 12.051 | 4.865 | 0.001 | 0.002 |
| 508−LNC2 | -17988.495 | -5409.374 | -74.686 | 0.008 | 0.014 |
| 508−SACR | -39247.604 | -5346.964 | -73.523 | 0.015 | 0.025 |
| 508A−LNC2 | -18023.372 | -5421.422 | -79.545 | 0.009 | 0.015 |
| 508A−SACR | -39282.478 | -5359.011 | -78.390 | 0.017 | 0.028 |
| 509−509A | 23.029 | 20.499 | 0.290 | 0.001 | 0.001 |
| 509−509B_PID | -22.141 | 4.803 | 0.126 | 0.002 | 0.004 |
| 509−LNC2 | -15342.934 | 1768.422 | -0.399 | 0.005 | 0.011 |
| 509−SACR | -36602.048 | 1830.834 | 0.809 | 0.011 | 0.023 |
| 509A−509B_PID | -45.171 | -15.697 | -0.164 | 0.001 | 0.003 |
| 509A−LNC2 | -15365.961 | 1747.923 | -0.677 | 0.005 | 0.012 |
| 509A−SACR | -36625.075 | 1810.336 | 0.525 | 0.011 | 0.025 |
| 509B_PID−LNC2 | -15320.789 | 1763.619 | -0.516 | 0.010 | 0.024 |
| 510−510A | -15.129 | 3.075 | -0.381 | 0.002 | 0.003 |
| 510−LNC1 | -15455.401 | -2635.683 | -20.481 | 0.010 | 0.019 |
| 510−LNC2 | -15456.245 | -2662.984 | -20.544 | 0.020 | 0.037 |
| 510−LNC2 | -15456.247 | -2662.992 | -20.543 | 0.010 | 0.019 |
| 510A−LNC1 | -15440.278 | -2638.759 | -20.090 | 0.009 | 0.019 |
| 510A−LNC2 | -15441.124 | -2666.069 | -20.150 | 0.009 | 0.019 |
| 510A−LNC2 | -15441.130 | -2666.069 | -20.134 | 0.044 | 0.091 |
| 701−701A | -47.716 | -17.980 | -1.640 | 0.011 | 0.021 |
| 701A−LNC2 | 4275.503 | -19084.688 | -122.906 | 0.010 | 0.016 |
| 701A−SACR | -16983.605 | -19022.288 | -121.742 | 0.013 | 0.021 |
| 702−702A | 12.785 | 20.969 | 0.227 | 0.006 | 0.007 |
| 702−LNC2 | -3409.562 | -17785.917 | -232.287 | 0.013 | 0.017 |
| 702A−LNC2 | -3422.340 | -17806.884 | -232.518 | 0.013 | 0.016 |
| 703−703A | 28.206 | -5.585 | 0.552 | 0.003 | 0.006 |
| 703−LNC2 | -3926.858 | -24586.615 | -361.988 | 0.011 | 0.021 |
| 703A−LNC2 | -3955.064 | -24581.034 | -362.550 | 0.012 | 0.022 |
| 704−704A | 4.531 | -58.415 | -1.103 | 0.004 | 0.007 |
| 705−705A | 10.015 | 31.378 | -2.175 | 0.006 | 0.010 |
| 706−706A | 9.362 | 17.839 | -0.950 | 0.002 | 0.004 |
| 706−LNC2 | -20106.086 | -18228.714 | -383.938 | 0.012 | 0.022 |
| 706A−LNC2 | -20115.458 | -18246.557 | -382.964 | 0.010 | 0.021 |
| 707−707A | 11.565 | -52.589 | -0.106 | 0.009 | 0.019 |
| 707−LNC2 | -7018.671 | -14147.202 | -84.491 | 0.015 | 0.029 |
| 707A−LNC2 | -7030.247 | -14094.604 | -84.383 | 0.009 | 0.018 |
| 708−708A | -5.537 | -30.490 | -3.344 | 0.005 | 0.008 |
| 708−LNC2 | -16334.385 | -17038.476 | -347.167 | 0.009 | 0.017 |
| 708A−LNC2 | -16328.846 | -17007.984 | -343.814 | 0.008 | 0.017 |
| 709−709A | -0.758 | -16.377 | -1.303 | 0.008 | 0.016 |
| 709−LNC2 | -16836.409 | -8393.083 | -76.270 | 0.019 | 0.033 |
| 709A−LNC2 | -16835.658 | -8376.704 | -74.973 | 0.012 | 0.025 |
| 710−710A | -62.057 | 61.225 | 0.895 | 0.005 | 0.006 |
| 710−LNC2 | -22149.735 | -2950.039 | -65.430 | 0.012 | 0.017 |
| 710A−LNC2 | -22087.687 | -3011.267 | -66.326 | 0.012 | 0.017 |
| JS0750−LNC1 | 8458.995 | -8442.676 | -26.185 | 0.004 | 0.008 |
| JS0750−LNC2 | 8458.149 | -8469.984 | -26.244 | 0.004 | 0.008 |
| JS0750−SACR | -12800.967 | -8407.575 | -25.103 | 0.005 | 0.011 |
| JS0786os−LNC1 | -6641.016 | -24537.225 | -376.787 | 0.011 | 0.017 |
| JS0786os−LNC2 | -6641.861 | -24564.534 | -376.848 | 0.011 | 0.017 |
| JS0786os−SACR | -27900.911 | -24502.167 | -375.805 | 0.031 | 0.030 |
| JS0801os−LNC2 | -6412.702 | -24309.940 | -361.124 | 0.014 | 0.019 |
| LNC1−LNC2 | -0.849 | -27.308 | -0.062 | 0.001 | 0.001 |
| LNC1−SACR | -21259.948 | 35.106 | 1.137 | 0.010 | 0.016 |
| LNC2−SACR | -21259.111 | 62.411 | 1.147 | 0.009 | 0.015 |
| LNC2−SACR | -21259.114 | 62.408 | 1.166 | 0.008 | 0.012 |
| LNC2−SACR | -21259.098 | 62.413 | 1.194 | 0.009 | 0.015 |
| LNC2−SACR | -21259.111 | 62.409 | 1.181 | 0.008 | 0.013 |
| GPS Observation Residuals |
| Name | dN (m) | dE (m) | dHt (m) | Horz RMS (m) | Vert RMS (m) |
| 401−401A_PID | 18.284 | 7.094 | 0.298 | 0.001 | 0.002 |
| 401−LNC2 | 6169.073 | -14437.998 | -91.269 | 0.006 | 0.011 |
| 401−SACR | -15090.041 | -14375.589 | -90.112 | 0.008 | 0.015 |
| 401A_PID−LNC2 | 6150.798 | -14445.085 | -91.554 | 0.006 | 0.011 |
| 401A_PID−SACR | -15108.317 | -14382.675 | -90.393 | 0.008 | 0.015 |
| 402−402A | -30.161 | 28.893 | 0.262 | 0.004 | 0.006 |
| 402−LNC2 | -2034.849 | -21974.174 | -307.934 | 0.010 | 0.021 |
| 402A−LNC2 | -2004.680 | -22002.970 | -308.175 | 0.012 | 0.022 |
| 403−403A | -48.859 | -14.079 | -3.097 | 0.001 | 0.002 |
| 403−LNC2 | -3125.687 | -14850.293 | -237.868 | 0.006 | 0.012 |
| 403−SACR | -24384.801 | -14787.883 | -236.727 | 0.012 | 0.020 |
| 403A−LNC2 | -3076.836 | -14836.214 | -234.757 | 0.007 | 0.012 |
| 403A−SACR | -24335.951 | -14773.803 | -233.613 | 0.014 | 0.024 |
| 404−404A | 9.569 | -18.848 | -1.016 | 0.002 | 0.005 |
| 404−411Base | -1889.571 | -4144.568 | -111.204 | 0.002 | 0.004 |
| 404−LNC2 | -9554.046 | -24723.182 | -440.206 | 0.009 | 0.019 |
| 404A−411Base | -1899.139 | -4125.721 | -110.184 | 0.003 | 0.008 |
| 404A−LNC2 | -9563.611 | -24704.339 | -439.170 | 0.009 | 0.020 |
| 405−405A_PID | -15.635 | 8.693 | 0.390 | 0.003 | 0.005 |
| 405−405B_PID | -14.558 | -10.151 | 0.667 | 0.004 | 0.005 |
| 405−411Base | -9642.460 | -5411.046 | -224.262 | 0.005 | 0.008 |
| 405−LNC2 | -17306.919 | -25989.664 | -553.237 | 0.023 | 0.031 |
| 405A_PID−405B_PID | 1.077 | -18.845 | 0.274 | 0.003 | 0.004 |
| 405A_PID−411Base | -9626.835 | -5419.740 | -224.624 | 0.005 | 0.010 |
| 405B_PID−411Base | -9627.904 | -5400.898 | -224.897 | 0.006 | 0.009 |
| 406−406A | -5.127 | 64.818 | 3.649 | 0.010 | 0.017 |
| 406−411Base | -2236.264 | 3277.076 | 23.941 | 0.008 | 0.014 |
| 406−LNC2 | -9900.758 | -17301.540 | -304.953 | 0.021 | 0.035 |
| 406−SACR | -31159.959 | -17239.310 | -303.906 | 0.148 | 0.058 |
| 406A−411Base | -2231.132 | 3212.252 | 20.282 | 0.003 | 0.004 |
| 406A−LNC2 | -9895.633 | -17366.361 | -308.621 | 0.009 | 0.015 |
| 406A−SACR | -31154.815 | -17303.948 | -307.515 | 0.102 | 0.033 |
| 407−407A_PID | 6.549 | -1.628 | -0.254 | 0.002 | 0.004 |
| 407−411Base | -7667.980 | 9435.696 | 247.523 | 0.006 | 0.010 |
| 407−LNC2 | -15332.458 | -11142.926 | -81.349 | 0.009 | 0.015 |
| 407−SACR | -36591.565 | -11080.539 | -80.165 | 0.062 | 0.069 |
| 407A_PID−411Base | -7674.523 | 9437.319 | 247.779 | 0.007 | 0.012 |
| 407A_PID−LNC2 | -15339.004 | -11141.299 | -81.087 | 0.009 | 0.015 |
| 407A_PID−SACR | -36598.207 | -11078.922 | -79.821 | 0.067 | 0.080 |
| 408−408A_PID | -51.128 | -0.683 | 0.208 | 0.005 | 0.009 |
| 408−411Base | -12710.806 | 15893.132 | 256.893 | 0.009 | 0.018 |
| 408−LNC2 | -20375.283 | -4685.472 | -71.942 | 0.008 | 0.016 |
| 408−SACR | -41634.406 | -4622.986 | -70.703 | 0.056 | 0.046 |
| 408A_PID−411Base | -12659.693 | 15893.812 | 256.701 | 0.010 | 0.017 |
| 408A_PID−LNC2 | -20324.168 | -4684.794 | -72.142 | 0.010 | 0.018 |
| 408A_PID−SACR | -41583.134 | -4622.492 | -71.218 | 0.072 | 0.088 |
| 409−409A | -16.998 | 1.449 | -0.356 | 0.004 | 0.011 |
| 409−411Base | -10682.673 | 17999.190 | 303.443 | 0.006 | 0.015 |
| 409−LNC1 | -18346.318 | -2552.107 | -25.331 | 0.005 | 0.014 |
| 409−LNC2 | -18347.163 | -2579.415 | -25.393 | 0.005 | 0.014 |
| 409−SACR | -39606.286 | -2516.881 | -24.245 | 0.057 | 0.030 |
| 409A−411Base | -10665.680 | 17997.738 | 303.810 | 0.008 | 0.024 |
| 409A−LNC1 | -18329.326 | -2553.559 | -24.970 | 0.008 | 0.022 |
| 409A−LNC2 | -18330.172 | -2580.867 | -25.031 | 0.008 | 0.022 |
| 409A−SACR | -39589.317 | -2518.334 | -23.864 | 0.109 | 0.058 |
| 410−410A | -8.132 | 5.161 | 0.141 | 0.004 | 0.008 |
| 410−411Base | -6205.469 | 13981.891 | 290.392 | 0.014 | 0.026 |
| 410−LNC1 | -13869.120 | -6569.396 | -38.367 | 0.011 | 0.023 |
| 410−LNC2 | -13869.965 | -6596.705 | -38.429 | 0.010 | 0.021 |
| 410−SACR | -35129.040 | -6534.030 | -37.270 | 0.168 | 0.071 |
| 410A−411Base | -6197.354 | 13976.735 | 290.299 | 0.008 | 0.016 |
| 410A−LNC1 | -13860.984 | -6574.565 | -38.519 | 0.007 | 0.012 |
| 410A−LNC2 | -13861.829 | -6601.874 | -38.577 | 0.007 | 0.013 |
| 410A−SACR | -35120.890 | -6539.454 | -37.359 | 0.139 | 0.047 |
| 411Base−412 | 4433.292 | -8221.174 | -194.323 | 0.004 | 0.006 |
| 411Base−412A | 4438.004 | -8216.863 | -194.046 | 0.004 | 0.006 |
| 411Base−505 | 7800.211 | 7437.371 | 213.144 | 0.006 | 0.010 |
| 411Base−505A | 7788.101 | 7458.875 | 214.515 | 0.005 | 0.010 |
| 411Base−506 | 9135.864 | -140.518 | 45.697 | 0.008 | 0.017 |
| 411Base−506A | 9090.575 | -145.987 | 45.461 | 0.007 | 0.015 |
| 411Base−507 | 5600.851 | -3350.574 | 15.798 | 0.004 | 0.008 |
| 411Base−507A | 5595.551 | -3330.099 | 15.558 | 0.004 | 0.007 |
| 411Base−508 | 10324.002 | -15169.233 | -254.175 | 0.007 | 0.013 |
| 411Base−508A | 10358.880 | -15157.184 | -249.317 | 0.008 | 0.015 |
| 411Base−509 | 7678.434 | -22347.040 | -328.485 | 0.010 | 0.023 |
| 411Base−509A | 7701.461 | -22326.539 | -328.200 | 0.011 | 0.024 |
| 411Base−509B_PID | 7656.296 | -22342.242 | -328.374 | 0.015 | 0.035 |
| 411Base−510 | 7791.753 | -17915.625 | -308.303 | 0.009 | 0.015 |
| 411Base−510A | 7776.631 | -17912.545 | -308.694 | 0.009 | 0.016 |
| 411Base−704 | 2580.291 | 861.746 | 73.315 | 0.004 | 0.007 |
| 411Base−704A | 2584.824 | 803.327 | 72.203 | 0.005 | 0.009 |
| 411Base−705 | 6067.705 | 3429.499 | 64.797 | 0.005 | 0.010 |
| 411Base−705A | 6077.717 | 3460.882 | 62.620 | 0.005 | 0.008 |
| 411Base−706 | 12441.596 | -2349.881 | 55.013 | 0.007 | 0.013 |
| 411Base−706A | 12450.964 | -2332.042 | 54.049 | 0.007 | 0.014 |
| 411Base−707 | -645.807 | -6431.408 | -244.413 | 0.007 | 0.012 |
| 411Base−707A | -634.242 | -6483.993 | -244.496 | 0.009 | 0.017 |
| 411Base−708 | 8669.887 | -3540.134 | 18.312 | 0.005 | 0.010 |
| 411Base−708A | 8664.346 | -3570.626 | 14.970 | 0.004 | 0.007 |
| 411Base−709 | 9171.934 | -12185.519 | -252.624 | 0.019 | 0.035 |
| 411Base−709A | 9171.170 | -12201.906 | -253.872 | 0.016 | 0.034 |
| 411Base−710 | 14485.275 | -17628.558 | -263.476 | 0.012 | 0.019 |
| 411Base−710A | 14423.196 | -17567.315 | -262.509 | 0.013 | 0.021 |
| 411Base−LNC1 | -7663.647 | -20551.299 | -328.807 | 0.008 | 0.013 |
| 411Base−LNC2 | -7664.486 | -20578.610 | -328.974 | 0.008 | 0.013 |
| 411Base−LNC2 | -7664.492 | -20578.604 | -328.923 | 0.008 | 0.013 |
| 411Base−LNC2 | -7664.493 | -20578.608 | -328.868 | 0.008 | 0.013 |
| 411Base−LNC2 | -7664.489 | -20578.609 | -328.862 | 0.008 | 0.013 |
| 411Base−SACR | -28923.604 | -20516.194 | -327.745 | 0.012 | 0.021 |
| 411Base−SACR | -28923.601 | -20516.201 | -327.677 | 0.012 | 0.021 |
| 411Base−SACR | -28923.603 | -20516.190 | -327.657 | 0.012 | 0.021 |
| 412−412A | 4.711 | 4.310 | 0.274 | 0.002 | 0.003 |
| 412−LNC1 | -12096.950 | -12330.119 | -134.476 | 0.007 | 0.013 |
| 412−LNC2 | -12097.796 | -12357.428 | -134.537 | 0.007 | 0.013 |
| 412−SACR | -33356.904 | -12295.014 | -133.316 | 0.014 | 0.024 |
| 412A−LNC1 | -12101.660 | -12334.428 | -134.749 | 0.008 | 0.013 |
| 412A−LNC2 | -12102.507 | -12361.738 | -134.809 | 0.008 | 0.013 |
| 412A−SACR | -33361.617 | -12299.326 | -133.579 | 0.015 | 0.025 |
| 501−501A | 16.920 | 11.301 | 0.996 | 0.001 | 0.003 |
| 501−LNC2 | 5073.050 | -16254.848 | -113.675 | 0.008 | 0.016 |
| 501−SACR | -16186.054 | -16192.446 | -112.526 | 0.010 | 0.021 |
| 501A−LNC2 | 5056.136 | -16266.155 | -114.682 | 0.007 | 0.016 |
| 501A−SACR | -16202.968 | -16203.754 | -113.531 | 0.010 | 0.021 |
| 502−502A | -8.363 | 16.409 | 0.571 | 0.002 | 0.003 |
| 502−LNC2 | 1492.937 | -19684.105 | -167.955 | 0.011 | 0.013 |
| 502−SACR | -19766.178 | -19621.696 | -166.773 | 0.016 | 0.017 |
| 502A−LNC2 | 1501.291 | -19700.510 | -168.522 | 0.010 | 0.014 |
| 502A−SACR | -19757.816 | -19638.096 | -167.340 | 0.015 | 0.018 |
| 503−503A | 18.443 | -51.373 | 0.437 | 0.001 | 0.001 |
| 503−LNC2 | -581.084 | -8829.685 | -85.702 | 0.004 | 0.007 |
| 503−SACR | -21840.196 | -8767.280 | -84.548 | 0.009 | 0.023 |
| 503A−LNC2 | -599.528 | -8778.312 | -86.144 | 0.004 | 0.008 |
| 503A−SACR | -21858.639 | -8715.912 | -84.987 | 0.009 | 0.023 |
| 504−504A | -21.296 | -7.237 | 0.037 | 0.002 | 0.003 |
| 504−LNC2 | -7579.835 | -20625.478 | -316.513 | 0.010 | 0.014 |
| 504A−LNC2 | -7558.533 | -20618.245 | -316.522 | 0.008 | 0.013 |
| 505−505A | -12.108 | 21.499 | 1.370 | 0.002 | 0.003 |
| 506−506A | -45.291 | -5.463 | -0.214 | 0.002 | 0.005 |
| 506−LNC2 | -16800.352 | -20438.089 | -374.661 | 0.011 | 0.024 |
| 506A−LNC2 | -16755.069 | -20432.627 | -374.443 | 0.021 | 0.044 |
| 507−507A | -5.300 | 20.476 | -0.244 | 0.002 | 0.003 |
| 507−LNC2 | -13265.335 | -17228.035 | -344.720 | 0.009 | 0.015 |
| 507−SACR | -34524.456 | -17165.495 | -343.551 | 0.069 | 0.028 |
| 507A−LNC2 | -13260.037 | -17248.500 | -344.494 | 0.009 | 0.016 |
| 507A−SACR | -34519.164 | -17185.979 | -343.332 | 0.110 | 0.042 |
| 508−508A | 34.880 | 12.051 | 4.865 | 0.001 | 0.002 |
| 508−LNC2 | -17988.495 | -5409.374 | -74.686 | 0.008 | 0.014 |
| 508−SACR | -39247.604 | -5346.964 | -73.523 | 0.015 | 0.025 |
| 508A−LNC2 | -18023.372 | -5421.422 | -79.545 | 0.009 | 0.015 |
| 508A−SACR | -39282.478 | -5359.011 | -78.390 | 0.017 | 0.028 |
| 509−509A | 23.029 | 20.499 | 0.290 | 0.001 | 0.001 |
| 509−509B_PID | -22.141 | 4.803 | 0.126 | 0.002 | 0.004 |
| 509−LNC2 | -15342.934 | 1768.422 | -0.399 | 0.005 | 0.011 |
| 509−SACR | -36602.048 | 1830.834 | 0.809 | 0.011 | 0.023 |
| 509A−509B_PID | -45.171 | -15.697 | -0.164 | 0.001 | 0.003 |
| 509A−LNC2 | -15365.961 | 1747.923 | -0.677 | 0.005 | 0.012 |
| 509A−SACR | -36625.075 | 1810.336 | 0.525 | 0.011 | 0.025 |
| 509B_PID−LNC2 | -15320.789 | 1763.619 | -0.516 | 0.010 | 0.024 |
| 509B_PID−SACR | -36579.879 | 1825.835 | 0.647 | 0.139 | 0.047 |
| 510−510A | -15.129 | 3.075 | -0.381 | 0.002 | 0.003 |
| 510−LNC1 | -15455.401 | -2635.683 | -20.481 | 0.010 | 0.019 |
| 510−LNC2 | -15456.245 | -2662.984 | -20.544 | 0.020 | 0.037 |
| 510−LNC2 | -15456.247 | -2662.992 | -20.543 | 0.010 | 0.019 |
| 510−SACR | -36715.323 | -2600.454 | -19.390 | 0.056 | 0.028 |
| 510−SACR | -36715.342 | -2602.282 | -19.640 | 0.714 | 0.237 |
| 510A−LNC1 | -15440.278 | -2638.759 | -20.090 | 0.009 | 0.019 |
| 510A−LNC2 | -15441.124 | -2666.069 | -20.150 | 0.009 | 0.019 |
| 510A−LNC2 | -15441.130 | -2666.069 | -20.134 | 0.044 | 0.091 |
| 510A−SACR | -36700.217 | -2603.642 | -18.929 | 0.045 | 0.024 |
| 510A−SACR | -36700.312 | -2602.617 | -18.624 | 0.446 | 0.158 |
| 701−701A | -47.716 | -17.980 | -1.640 | 0.011 | 0.021 |
| 701−LNC2 | 4227.790 | -19102.633 | -124.482 | 0.027 | 0.052 |
| 701−SACR | -17031.305 | -19040.301 | -123.419 | 0.041 | 0.055 |
| 701A−LNC2 | 4275.503 | -19084.688 | -122.906 | 0.010 | 0.016 |
| 701A−SACR | -16983.605 | -19022.288 | -121.742 | 0.013 | 0.021 |
| 702−702A | 12.785 | 20.969 | 0.227 | 0.006 | 0.007 |
| 702−LNC2 | -3409.562 | -17785.917 | -232.287 | 0.013 | 0.017 |
| 702A−LNC2 | -3422.340 | -17806.884 | -232.518 | 0.013 | 0.016 |
| 703−703A | 28.206 | -5.585 | 0.552 | 0.003 | 0.006 |
| 703−LNC2 | -3926.858 | -24586.615 | -361.988 | 0.011 | 0.021 |
| 703A−LNC2 | -3955.064 | -24581.034 | -362.550 | 0.012 | 0.022 |
| 704−704A | 4.531 | -58.415 | -1.103 | 0.004 | 0.007 |
| 704−LNC2 | -10244.781 | -21440.361 | -402.302 | 0.011 | 0.019 |
| 705−705A | 10.015 | 31.378 | -2.175 | 0.006 | 0.010 |
| 706−706A | 9.362 | 17.839 | -0.950 | 0.002 | 0.004 |
| 706−LNC2 | -20106.086 | -18228.714 | -383.938 | 0.012 | 0.022 |
| 706−SACR | -41365.210 | -18166.366 | -382.741 | 0.089 | 0.045 |
| 706A−LNC2 | -20115.458 | -18246.557 | -382.964 | 0.010 | 0.021 |
| 706A−SACR | -41374.544 | -18184.173 | -381.794 | 0.069 | 0.034 |
| 707−707A | 11.565 | -52.589 | -0.106 | 0.009 | 0.019 |
| 707−LNC2 | -7018.671 | -14147.202 | -84.491 | 0.015 | 0.029 |
| 707−SACR | -28277.813 | -14084.847 | -83.247 | 0.194 | 0.106 |
| 707A−LNC2 | -7030.247 | -14094.604 | -84.383 | 0.009 | 0.018 |
| 707A−SACR | -28289.381 | -14032.461 | -83.303 | 0.088 | 0.055 |
| 708−708A | -5.537 | -30.490 | -3.344 | 0.005 | 0.008 |
| 708−LNC2 | -16334.385 | -17038.476 | -347.167 | 0.009 | 0.017 |
| 708−SACR | -37593.510 | -16975.993 | -346.036 | 0.063 | 0.033 |
| 708A−LNC2 | -16328.846 | -17007.984 | -343.814 | 0.008 | 0.017 |
| 708A−SACR | -37587.958 | -16945.521 | -342.673 | 0.066 | 0.037 |
| 709−709A | -0.758 | -16.377 | -1.303 | 0.008 | 0.016 |
| 709−LNC2 | -16836.409 | -8393.083 | -76.270 | 0.019 | 0.033 |
| 709−SACR | -38095.319 | -8330.499 | -75.369 | 0.431 | 0.439 |
| 709A−LNC2 | -16835.658 | -8376.704 | -74.973 | 0.012 | 0.025 |
| 709A−SACR | -38094.715 | -8314.329 | -73.851 | 0.121 | 0.122 |
| 710−710A | -62.057 | 61.225 | 0.895 | 0.005 | 0.006 |
| 710−LNC2 | -22149.735 | -2950.039 | -65.430 | 0.012 | 0.017 |
| 710−SACR | -43408.889 | -2887.608 | -64.190 | 0.056 | 0.045 |
| 710A−LNC2 | -22087.687 | -3011.267 | -66.326 | 0.012 | 0.017 |
| 710A−SACR | -43346.846 | -2948.740 | -65.026 | 0.068 | 0.057 |
| JS0750−LNC1 | 8458.995 | -8442.676 | -26.185 | 0.004 | 0.008 |
| JS0750−LNC2 | 8458.149 | -8469.984 | -26.244 | 0.004 | 0.008 |
| JS0750−SACR | -12800.967 | -8407.575 | -25.103 | 0.005 | 0.011 |
| JS0786os−LNC1 | -6641.016 | -24537.225 | -376.787 | 0.011 | 0.017 |
| JS0786os−LNC2 | -6641.861 | -24564.534 | -376.848 | 0.011 | 0.017 |
| JS0786os−SACR | -27900.911 | -24502.167 | -375.805 | 0.031 | 0.030 |
| JS0801os−LNC2 | -6412.702 | -24309.940 | -361.124 | 0.014 | 0.019 |
| LNC1−LNC2 | -0.849 | -27.308 | -0.062 | 0.001 | 0.001 |
| LNC1−SACR | -21259.948 | 35.106 | 1.137 | 0.010 | 0.016 |
| LNC2−SACR | -21259.111 | 62.411 | 1.147 | 0.009 | 0.015 |
| LNC2−SACR | -21259.114 | 62.408 | 1.166 | 0.008 | 0.012 |
| LNC2−SACR | -21259.098 | 62.413 | 1.194 | 0.009 | 0.015 |
| LNC2−SACR | -21259.111 | 62.409 | 1.181 | 0.008 | 0.013 |

| Control Points |
| --- |
| Name | Grid Northing (m) | Grid Easting (m) | Elevation (m) | Code |
| JS0750 | 4292577.665 | 651612.378 | 62.661 |  |
| JS0786os | 4307677.676 | 667706.927 | 411.344 |  |
| LNC2 | 4301035.814 | 643142.393 | 36.374 |  |
| SACR | 4279776.701 | 643204.805 | 37.978 |  |
| Adjusted Points |
| Name | Grid Northing (m) | Grid Easting (m) | Elevation (m) | Code |
| 401 | 4294866.738 | 657580.389 | 127.275 |  |
| 401A_PID | 4294885.021 | 657587.483 | 127.570 |  |
| 402 | 4303070.663 | 665116.567 | 342.933 |  |
| 402A | 4303040.502 | 665145.460 | 343.195 |  |
| 403 | 4304161.504 | 657992.687 | 273.369 |  |
| 403A | 4304112.645 | 657978.607 | 270.275 |  |
| 404 | 4310589.877 | 667865.568 | 474.387 |  |
| 404A | 4310599.445 | 667846.721 | 473.371 |  |
| 405 | 4318342.769 | 669132.047 | 586.876 |  |
| 405A_PID | 4318327.136 | 669140.741 | 587.264 |  |
| 405B_PID | 4318328.212 | 669121.896 | 587.539 |  |
| 406 | 4310936.568 | 660443.927 | 339.765 |  |
| 406A | 4310931.438 | 660508.748 | 343.414 |  |
| 407 | 4316368.278 | 654285.311 | 116.246 |  |
| 407A_PID | 4316374.827 | 654283.684 | 115.992 |  |
| 408 | 4321411.109 | 647827.868 | 106.951 |  |
| 408A_PID | 4321359.984 | 647827.186 | 107.161 |  |
| 409 | 4319382.979 | 645721.810 | 60.669 |  |
| 409A | 4319365.983 | 645723.260 | 60.312 |  |
| 410 | 4314905.779 | 649739.103 | 73.760 |  |
| 410A | 4314897.647 | 649744.266 | 73.900 |  |
| 411Base | 4308700.306 | 663721.000 | 363.602 |  |
| 412 | 4313133.602 | 655499.824 | 169.598 |  |
| 412A | 4313138.313 | 655504.135 | 169.872 |  |
| 501 | 4295962.757 | 659397.248 | 149.526 |  |
| 501A | 4295979.677 | 659408.549 | 150.521 |  |
| 502 | 4299542.880 | 662826.497 | 203.342 |  |
| 502A | 4299534.517 | 662842.905 | 203.912 |  |
| 503 | 4301616.898 | 651972.080 | 121.739 |  |
| 503A | 4301635.340 | 651920.707 | 122.179 |  |
| 504 | 4308615.645 | 663767.874 | 351.235 |  |
| 504A | 4308594.349 | 663760.637 | 351.272 |  |
| 505 | 4316500.515 | 671158.374 | 575.794 |  |
| 505A | 4316488.407 | 671179.874 | 577.163 |  |
| 506 | 4317836.171 | 663580.479 | 408.658 |  |
| 506A | 4317790.880 | 663575.016 | 408.446 |  |
| 507 | 4314301.156 | 660370.427 | 379.259 |  |
| 507A | 4314295.856 | 660390.902 | 379.013 |  |
| 508 | 4319024.306 | 648551.766 | 109.796 |  |
| 508A | 4319059.187 | 648563.817 | 114.657 |  |
| 509 | 4316378.745 | 641373.969 | 36.052 |  |
| 509A | 4316401.774 | 641394.468 | 36.340 |  |
| 509B_PID | 4316356.603 | 641378.771 | 36.179 |  |
| 510 | 4316492.064 | 645805.383 | 55.994 |  |
| 510A | 4316476.935 | 645808.458 | 55.613 |  |
| 701 | 4296808.024 | 662245.066 | 160.131 |  |
| 701A | 4296760.309 | 662227.085 | 158.494 |  |
| 702 | 4304445.373 | 660928.309 | 267.543 |  |
| 702A | 4304458.157 | 660949.278 | 267.768 |  |
| 703 | 4304962.671 | 667729.010 | 396.672 |  |
| 703A | 4304990.877 | 667723.425 | 397.223 |  |
| 704 | 4311280.597 | 664582.745 | 436.669 |  |
| 704A | 4311285.128 | 664524.330 | 435.566 |  |
| 705 | 4314768.010 | 667150.501 | 427.754 |  |
| 705A | 4314778.024 | 667181.881 | 425.576 |  |
| 706 | 4321141.905 | 661371.117 | 417.910 |  |
| 706A | 4321151.268 | 661388.956 | 416.957 |  |
| 707 | 4308054.496 | 657289.593 | 119.759 |  |
| 707A | 4308066.062 | 657237.002 | 119.669 |  |
| 708 | 4317370.193 | 660180.866 | 381.547 |  |
| 708A | 4317364.654 | 660150.376 | 378.206 |  |
| 709 | 4317872.231 | 651535.476 | 111.257 |  |
| 709A | 4317871.473 | 651519.097 | 109.961 |  |
| 710 | 4323185.563 | 646092.441 | 100.428 |  |
| 710A | 4323123.504 | 646153.667 | 101.326 |  |
| JS0750 | 4292577.665 | 651612.378 | 62.661 |  |
| JS0786os | 4307677.676 | 667706.927 | 411.344 |  |
| JS0801os | 4307448.516 | 667452.333 | 395.669 |  |
| LNC1 | 4301036.661 | 643169.702 | 36.436 |  |
| LNC2 | 4301035.814 | 643142.393 | 36.374 |  |

Final Control Summary

| Placer County West Sacramento CA |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Swood | Jul-12 |  |  |  |  |  |
| UTM North Zone 10 |  |  |  |  |  |  |
| NAD83, NAVD88, Meters |  |  |  |  |  |
|  | LIDAR QC Classification Codes |  |  |  |  |
|  | Bare Earth/Open Terrain | 400s |  | OT |  |
|  | Tall Weeds and Crops | 500s |  | TW |  |
|  | Forested and Fuly Grown | 700s |  | F |  |
| Name | Grid Northing (m) | Grid Easting (m) | Elevation (m) |  | Control | Note |
| 401 | 4294866.738 | 657580.389 | 127.275 |  | None | OT |
| 402 | 4303070.663 | 665116.567 | 342.933 |  | None | OT |
| 403 | 4304161.504 | 657992.687 | 273.369 |  | None | OT |
| 404 | 4310589.877 | 667865.568 | 474.387 |  | None | OT |
| 405 | 4318342.769 | 669132.047 | 586.876 |  | None | OT |
| 406 | 4310936.568 | 660443.927 | 339.765 |  | None | OT |
| 407 | 4316368.278 | 654285.311 | 116.246 |  | None | OT |
| 408 | 4321411.109 | 647827.868 | 106.951 |  | None | OT |
| 409 | 4319382.979 | 645721.810 | 60.669 |  | None | OT |
| 410 | 4314905.779 | 649739.103 | 73.760 |  | None | OT |
| 412 | 4313133.602 | 655499.824 | 169.598 |  | None | OT |
| 501 | 4295962.757 | 659397.248 | 149.526 |  | None | TW |
| 502 | 4299542.880 | 662826.497 | 203.342 |  | None | TW |
| 503 | 4301616.898 | 651972.080 | 121.739 |  | None | TW |
| 504 | 4308615.645 | 663767.874 | 351.235 |  | None | TW |
| 505 | 4316500.515 | 671158.374 | 575.794 |  | None | TW |
| 506 | 4317836.171 | 663580.479 | 408.658 |  | None | TW |
| 507 | 4314301.156 | 660370.427 | 379.259 |  | None | TW |
| 508 | 4319024.306 | 648551.766 | 109.796 |  | None | TW |
| 509 | 4316378.745 | 641373.969 | 36.052 |  | None | TW |
| 510 | 4316492.064 | 645805.383 | 55.994 |  | None | TW |
| 701 | 4296808.024 | 662245.066 | 160.131 |  | None | F |
| 702 | 4304445.373 | 660928.309 | 267.543 |  | None | F |
| 703 | 4304962.671 | 667729.010 | 396.672 |  | None | F |
| 704 | 4311280.597 | 664582.745 | 436.669 |  | None | F |
| 705 | 4314768.010 | 667150.501 | 427.754 |  | None | F |
| 706 | 4321141.905 | 661371.117 | 417.910 |  | None | F |
| 707 | 4308054.496 | 657289.593 | 119.759 |  | None | F |
| 708 | 4317370.193 | 660180.866 | 381.547 |  | None | F |
| 709 | 4317872.231 | 651535.476 | 111.257 |  | None | F |
| 710 | 4323185.563 | 646092.441 | 100.428 |  | None | F |
| 401A_PID | 4294885.021 | 657587.483 | 127.570 |  | None | OT |
| 402A | 4303040.502 | 665145.460 | 343.195 |  | None | OT |
| 403A | 4304112.645 | 657978.607 | 270.275 |  | None | OT |
| 404A | 4310599.445 | 667846.721 | 473.371 |  | None | OT |
| 405A_PID | 4318327.136 | 669140.741 | 587.264 |  | None | OT |
| 405B_PID | 4318328.212 | 669121.896 | 587.539 |  | None | OT |
| 406A | 4310931.438 | 660508.748 | 343.414 |  | None | OT |
| 407A_PID | 4316374.827 | 654283.684 | 115.992 |  | None | OT |
| 408A_PID | 4321359.984 | 647827.186 | 107.161 |  | None | OT |
| 409A | 4319365.983 | 645723.260 | 60.312 |  | None | OT |
| 410A | 4314897.647 | 649744.266 | 73.900 |  | None | OT |
| 411Base | 4308700.306 | 663721.000 | 363.602 |  | None | OT |
| 412A | 4313138.313 | 655504.135 | 169.872 |  | None | OT |
| 501A | 4295979.677 | 659408.549 | 150.521 |  | None | TW |
| 502A | 4299534.517 | 662842.905 | 203.912 |  | None | TW |
| 503A | 4301635.340 | 651920.707 | 122.179 |  | None | TW |
| 504A | 4308594.349 | 663760.637 | 351.272 |  | None | TW |
| 505A | 4316488.407 | 671179.874 | 577.163 |  | None | TW |
| 506A | 4317790.880 | 663575.016 | 408.446 |  | None | TW |
| 507A | 4314295.856 | 660390.902 | 379.013 |  | None | TW |
| 508A | 4319059.187 | 648563.817 | 114.657 |  | None | TW |
| 509A | 4316401.774 | 641394.468 | 36.340 |  | None | TW |
| 509B_PID | 4316356.603 | 641378.771 | 36.179 |  | None | TW |
| 510A | 4316476.935 | 645808.458 | 55.613 |  | None | TW |
| 701A | 4296760.309 | 662227.085 | 158.494 |  | None | F |
| 702A | 4304458.157 | 660949.278 | 267.768 |  | None | F |
| 703A | 4304990.877 | 667723.425 | 397.223 |  | None | F |
| 704A | 4311285.128 | 664524.330 | 435.566 |  | None | F |
| 705A | 4314778.024 | 667181.881 | 425.576 |  | None | F |
| 706A | 4321151.268 | 661388.956 | 416.957 |  | None | F |
| 707A | 4308066.062 | 657237.002 | 119.669 |  | None | F |
| 708A | 4317364.654 | 660150.376 | 378.206 |  | None | F |
| 709A | 4317871.473 | 651519.097 | 109.961 |  | None | F |
| 710A | 4323123.504 | 646153.667 | 101.326 |  | None | F |
| JS0750 | 4292577.665 | 651612.378 | 62.661 |  | Vertical | NGS PID |
| JS0786os | 4307677.676 | 667706.927 | 411.344 |  | Vertical | NGS PID |
| JS0801os | 4307448.516 | 667452.333 | 395.669 |  | None | NGS PID |
| LNC1 | 4301036.661 | 643169.702 | 36.436 |  | None | CORS |
| LNC2 | 4301035.814 | 643142.393 | 36.374 |  | Horizontal | CORS |
| SACR | 4279776.701 | 643204.805 | 37.978 |  | Both | CORS |

| Name | Std Dev n (m) | Std Dev e (m) | Std Dev u (m) | Std Dev Hz (m) | Geoid Separation (m) |
| --- | --- | --- | --- | --- | --- |
| 401 | 0.003 | 0.002 | 0.008 | 0.004 |  | -29.660 |  |
| 402 | 0.008 | 0.006 | 0.026 | 0.010 |  | -28.646 |  |
| 403 | 0.003 | 0.003 | 0.010 | 0.004 |  | -29.152 |  |
| 404 | 0.002 | 0.002 | 0.007 | 0.003 |  | -27.963 |  |
| 405 | 0.003 | 0.002 | 0.009 | 0.004 |  | -27.410 |  |
| 406 | 0.005 | 0.004 | 0.014 | 0.007 |  | -28.478 |  |
| 407 | 0.003 | 0.002 | 0.009 | 0.004 |  | -28.549 |  |
| 408 | 0.004 | 0.003 | 0.012 | 0.005 |  | -28.645 |  |
| 409 | 0.002 | 0.002 | 0.010 | 0.003 |  | -28.915 |  |
| 410 | 0.003 | 0.003 | 0.011 | 0.005 |  | -28.968 |  |
| 412 | 0.002 | 0.002 | 0.007 | 0.003 |  | -28.702 |  |
| 501 | 0.004 | 0.003 | 0.012 | 0.004 |  | -29.491 |  |
| 502 | 0.005 | 0.003 | 0.010 | 0.006 |  | -29.046 |  |
| 503 | 0.002 | 0.002 | 0.007 | 0.003 |  | -29.683 |  |
| 504 | 0.005 | 0.004 | 0.013 | 0.007 |  | -28.384 |  |
| 505 | 0.004 | 0.003 | 0.011 | 0.005 |  | -27.429 |  |
| 506 | 0.005 | 0.004 | 0.015 | 0.006 |  | -27.752 |  |
| 507 | 0.003 | 0.002 | 0.008 | 0.003 |  | -28.232 |  |
| 508 | 0.003 | 0.003 | 0.009 | 0.004 |  | -28.758 |  |
| 509 | 0.003 | 0.002 | 0.009 | 0.003 |  | -29.316 |  |
| 510 | 0.003 | 0.003 | 0.010 | 0.004 |  | -29.094 |  |
| 701 | 0.010 | 0.010 | 0.030 | 0.014 |  | -29.235 |  |
| 702 | 0.009 | 0.004 | 0.015 | 0.009 |  | -28.901 |  |
| 703 | 0.006 | 0.005 | 0.019 | 0.008 |  | -28.327 |  |
| 704 | 0.003 | 0.002 | 0.009 | 0.004 |  | -28.136 |  |
| 705 | 0.003 | 0.003 | 0.011 | 0.005 |  | -27.737 |  |
| 706 | 0.003 | 0.003 | 0.011 | 0.004 |  | -27.668 |  |
| 707 | 0.004 | 0.004 | 0.013 | 0.006 |  | -28.941 |  |
| 708 | 0.003 | 0.003 | 0.010 | 0.004 |  | -28.017 |  |
| 709 | 0.007 | 0.006 | 0.022 | 0.009 |  | -28.635 |  |
| 710 | 0.005 | 0.004 | 0.013 | 0.007 |  | -28.648 |  |
| 401A_PID | 0.003 | 0.002 | 0.008 | 0.004 |  | -29.659 |  |
| 402A | 0.008 | 0.007 | 0.027 | 0.011 |  | -28.646 |  |
| 403A | 0.003 | 0.003 | 0.010 | 0.004 |  | -29.156 |  |
| 404A | 0.002 | 0.002 | 0.008 | 0.003 |  | -27.964 |  |
| 405A_PID | 0.003 | 0.002 | 0.009 | 0.004 |  | -27.411 |  |
| 405B_PID | 0.003 | 0.002 | 0.009 | 0.004 |  | -27.411 |  |
| 406A | 0.002 | 0.002 | 0.007 | 0.003 |  | -28.473 |  |
| 407A_PID | 0.003 | 0.002 | 0.009 | 0.004 |  | -28.549 |  |
| 408A_PID | 0.005 | 0.003 | 0.013 | 0.005 |  | -28.648 |  |
| 409A | 0.003 | 0.002 | 0.012 | 0.004 |  | -28.916 |  |
| 410A | 0.003 | 0.003 | 0.009 | 0.004 |  | -28.969 |  |
| 411Base | 0.001 | 0.001 | 0.005 | 0.002 |  | -28.382 |  |
| 412A | 0.002 | 0.002 | 0.007 | 0.003 |  | -28.702 |  |
| 501A | 0.004 | 0.003 | 0.012 | 0.004 |  | -29.489 |  |
| 502A | 0.005 | 0.003 | 0.010 | 0.006 |  | -29.045 |  |
| 503A | 0.002 | 0.002 | 0.008 | 0.003 |  | -29.684 |  |
| 504A | 0.005 | 0.004 | 0.013 | 0.006 |  | -28.386 |  |
| 505A | 0.003 | 0.003 | 0.010 | 0.005 |  | -27.429 |  |
| 506A | 0.005 | 0.004 | 0.015 | 0.006 |  | -27.755 |  |
| 507A | 0.003 | 0.002 | 0.008 | 0.003 |  | -28.231 |  |
| 508A | 0.003 | 0.003 | 0.009 | 0.004 |  | -28.754 |  |
| 509A | 0.003 | 0.002 | 0.009 | 0.003 |  | -29.314 |  |
| 509B_PID | 0.003 | 0.002 | 0.009 | 0.003 |  | -29.317 |  |
| 510A | 0.003 | 0.003 | 0.010 | 0.004 |  | -29.094 |  |
| 701A | 0.006 | 0.006 | 0.016 | 0.008 |  | -29.239 |  |
| 702A | 0.009 | 0.004 | 0.015 | 0.009 |  | -28.899 |  |
| 703A | 0.006 | 0.005 | 0.019 | 0.008 |  | -28.325 |  |
| 704A | 0.004 | 0.003 | 0.010 | 0.004 |  | -28.140 |  |
| 705A | 0.003 | 0.003 | 0.010 | 0.005 |  | -27.735 |  |
| 706A | 0.003 | 0.003 | 0.011 | 0.004 |  | -27.666 |  |
| 707A | 0.005 | 0.003 | 0.014 | 0.006 |  | -28.945 |  |
| 708A | 0.002 | 0.002 | 0.009 | 0.003 |  | -28.020 |  |
| 709A | 0.006 | 0.005 | 0.021 | 0.008 |  | -28.636 |  |
| 710A | 0.005 | 0.004 | 0.013 | 0.007 |  | -28.648 |  |
| JS0750 | 0.002 | 0.002 | 0.000 | 0.003 |  | -30.026 |  |
| JS0786os | 0.007 | 0.004 | 0.000 | 0.008 |  | -28.159 |  |
| JS0801os | 0.010 | 0.009 | 0.023 | 0.014 |  | -28.191 |  |
| LNC1 | 0.001 | 0.001 | 0.004 | 0.001 |  | -30.020 |  |
| LNC2 | 0.000 | 0.000 | 0.004 | 0.000 |  | -30.021 |  |
| SACR | 0.000 | 0.000 | 0.000 | 0.000 |  | -30.473 |  |

Gps Observations Summary Part One

| Point Name | Original Name | Antenna Type | Antenna Height (USft) | Ant Height Method | Start Time |
| --- | --- | --- | --- | --- | --- |
| 501A | B2850703a_1728 | HiPer GD/GGD | 4.41 | Vertical | 7/3/2012 19:09 |
| 401 | B2850703b_1728 | HiPer GD/GGD | 4.41 | Vertical | 7/3/2012 19:51 |
| 701 | B2850703c_1728 | HiPer GD/GGD | 4.41 | Vertical | 7/3/2012 20:45 |
| 502 | B2850703e_1728 | HiPer GD/GGD | 4.41 | Vertical | 7/3/2012 21:36 |
| 402 | B2850703f_1728 | HiPer GD/GGD | 4.41 | Vertical | 7/3/2012 22:25 |
| 501 | R0600703t_1LHC | HiPer+ | 4.35 | Vertical | 7/3/2012 19:08 |
| 401A_PID | R0600703ta_1LHC | HiPer+ | 4.41 | Vertical | 7/3/2012 19:52 |
| 701A | R0600703u_1LHC | HiPer+ | 4.41 | Vertical | 7/3/2012 20:48 |
| 502A | R0600703v_1LHC | HiPer+ | 4.41 | Vertical | 7/3/2012 21:38 |
| 402A | R0600703w_1LHC | HiPer+ | 4.41 | Vertical | 7/3/2012 22:26 |
| SACR | SACR |  | 0.00 | Vertical | 7/3/2012 0:00 |
| 503A | B38730704p_DO1S | HiPer+ | 4.41 | Vertical | 7/4/2012 15:57 |
| 403A | B38730704q_DO1S | HiPer+ | 4.41 | Vertical | 7/4/2012 16:47 |
| 702 | B38730704r_DO1S | HiPer+ | 4.41 | Vertical | 7/4/2012 17:41 |
| 703A | B38730704t_DO1S | HiPer+ | 4.41 | Vertical | 7/4/2012 19:00 |
| 503 | R0600704p_1LHC | HiPer+ | 4.41 | Vertical | 7/4/2012 15:55 |
| 403 | R0600704q_1LHC | HiPer+ | 4.41 | Vertical | 7/4/2012 16:46 |
| 702A | R0600704r_1LHC | HiPer+ | 4.41 | Vertical | 7/4/2012 17:43 |
| 703 | R0600704s_1LHC | HiPer+ | 4.41 | Vertical | 7/4/2012 18:58 |
| SACR | SACR |  | 0.00 | Vertical | 7/4/2012 0:00 |
| LNC2 | LNC2 | ASH701945E_M SCIT | 0.00 | Vertical | 7/4/2012 0:00 |
| LNC2 | LNC2 | ASH701945E_M SCIT | 0.00 | Vertical | 7/3/2012 0:00 |
| 405B_PID | R0600705v_1LHC | HiPer+ | 4.47 | Vertical | 7/5/2012 21:50 |
| 504 | B0560705a_81KW | HiPer+ | 4.41 | Vertical | 7/5/2012 16:31 |
| 704 | B0560705b_81KW | HiPer+ | 4.31 | Vertical | 7/5/2012 18:05 |
| 404A | B0560705c_81KW | HiPer+ | 4.41 | Vertical | 7/5/2012 18:55 |
| 705A | B0560705d_81KW | HiPer+ | 4.41 | Vertical | 7/5/2012 19:55 |
| 505 | B0560705e_81KW | HiPer+ | 4.41 | Vertical | 7/5/2012 20:51 |
| 405A_PID | B0560705f_81KW | HiPer+ | 4.41 | Vertical | 7/5/2012 21:45 |
| 506 | B0560705g_81KW | HiPer+ | 4.41 | Vertical | 7/5/2012 23:02 |
| 706 | B0560706a_81KW | HiPer+ | 4.41 | Vertical | 7/6/2012 0:08 |
| 507 | B0560706b_81KW | HiPer+ | 4.25 | Vertical | 7/6/2012 1:19 |
| 406A | B0560706c_81KW | HiPer+ | 4.41 | Vertical | 7/6/2012 2:14 |
| 707 | B0560706d_81KW | HiPer+ | 4.41 | Vertical | 7/6/2012 2:59 |
| JS0801os | B3610705a_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/5/2012 14:57 |
| 504A | B3610705b_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/5/2012 16:32 |
| 411Base | B3610705d_ESQO | HiPer GD/GGD | 4.41 | Vertical | 7/5/2012 17:40 |
| 704A | B38730705s_DO1S | HiPer+ | 4.25 | Vertical | 7/5/2012 18:07 |
| 404 | B38730705sa_DO1S | HiPer+ | 4.34 | Vertical | 7/5/2012 18:53 |
| 705 | B38730705t_DO1S | HiPer+ | 4.41 | Vertical | 7/5/2012 19:53 |
| 505A | B38730705u_DO1S | HiPer+ | 4.41 | Vertical | 7/5/2012 20:52 |
| 405 | B38730705v_DO1S | HiPer+ | 4.41 | Vertical | 7/5/2012 21:44 |
| 506A | B38730705x_DO1S | HiPer+ | 4.41 | Vertical | 7/5/2012 23:03 |
| 706A | B38730706a_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 0:10 |
| 507A | B38730706b_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 1:20 |
| 406 | B38730706c_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 2:10 |
| 707A | B38730706d_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 3:00 |
| LNC2 | LNC2 | ASH701945E_M SCIT | 0.00 | Vertical | 7/5/2012 0:00 |
| 509B_PID | B0560706e_81KW | HiPer+ | 4.70 | Vertical | 7/6/2012 23:16 |
| 412 | R0600707c_1LHC | HiPer+ | 4.41 | Vertical | 7/7/2012 2:22 |
| 708 | B38730706q_DO1S | HiPer+ | 4.30 | Vertical | 7/6/2012 16:00 |
| 407 | B38730706s_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 18:00 |
| 709A | B38730706t_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 19:12 |
| 508 | B38730706ta_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 19:56 |
| 408 | B38730706v_DO1S | HiPer+ | 4.41 | Vertical | 7/6/2012 21:53 |
| 710 | B38730706u_DO1S | HiPer+ | 4.30 | Vertical | 7/6/2012 20:43 |
| 509 | B38730706w_DO1S | HiPer+ | 4.30 | Vertical | 7/6/2012 22:59 |
| 510A | B38730706x_DO1S | HiPer+ | 4.30 | Vertical | 7/6/2012 23:50 |
| 409A | B38730707a_DO1S | HiPer+ | 4.41 | Vertical | 7/7/2012 0:32 |
| 410A | B38730707b_DO1S | HiPer+ | 4.41 | Vertical | 7/7/2012 1:24 |
| 412A | B38730707c_DO1S | HiPer+ | 4.41 | Vertical | 7/7/2012 2:24 |
| 411Base | R0590706o_UN0G | HiPer+ | 4.50 | Vertical | 7/6/2012 14:59 |
| 708A | R0600706q_1LHC | HiPer+ | 4.30 | Vertical | 7/6/2012 16:03 |
| 407A_PID | R0600706s_1LHC | HiPer+ | 4.41 | Vertical | 7/6/2012 18:02 |
| 709 | R0600706t_1LHC | HiPer+ | 4.41 | Vertical | 7/6/2012 19:10 |
| 508A | R0600706ta_1LHC | HiPer+ | 4.30 | Vertical | 7/6/2012 19:59 |
| 710A | R0600706u_1LHC | HiPer+ | 4.30 | Vertical | 7/6/2012 20:46 |
| 408A_PID | R0600706v_1LHC | HiPer+ | 4.41 | Vertical | 7/6/2012 21:56 |
| LNC2 | LNC2 | ASH701945E_M SCIT | 0.00 | Vertical | 7/6/2012 0:00 |
| 509A | R0600706x_1LHC | HiPer+ | 4.30 | Vertical | 7/6/2012 23:01 |
| 510 | R0600706xa_1LHC | HiPer+ | 4.30 | Vertical | 7/6/2012 23:49 |
| 409 | R0600707a_1LHC | HiPer+ | 4.41 | Vertical | 7/7/2012 0:31 |
| 410 | R0600707b_1LHC | HiPer+ | 4.41 | Vertical | 7/7/2012 1:23 |
| JS0750 | R0600707q_1LHC | HiPer+ | 4.30 | Vertical | 7/7/2012 16:02 |
| JS0786os | B38730707v_DO1S | HiPer+ | 4.41 | Vertical | 7/7/2012 21:23 |
| LNC2 | LNC2 | ASH701945E_M SCIT | 0.00 | Vertical | 7/7/2012 0:00 |
| LNC1 | LNC1 | ASH701945E_M SCIT | 0.00 | Vertical | 7/7/2012 0:00 |
| SACR | SACR |  | 0.00 | Vertical | 7/7/2012 0:00 |
| SACR | SACR |  | 0.00 | Vertical | 7/6/2012 0:00 |

Gps Observations Summary Part Two

| Point Name | Original Name | Stop Time | Duration | Method | Receiver |
| --- | --- | --- | --- | --- | --- |
| 501A | B2850703a_1728 | 7/3/2012 19:36 | 0:27:30 | Static | 8R0PSO61728 |
| 401 | B2850703b_1728 | 7/3/2012 20:27 | 0:35:50 | Static | 8R0PSO61728 |
| 701 | B2850703c_1728 | 7/3/2012 21:20 | 0:35:10 | Static | 8R0PSO61728 |
| 502 | B2850703e_1728 | 7/3/2012 22:09 | 0:33:10 | Static | 8R0PSO61728 |
| 402 | B2850703f_1728 | 7/3/2012 23:01 | 0:36:30 | Static | 8R0PSO61728 |
| 501 | R0600703t_1LHC | 7/3/2012 19:36 | 0:27:20 | Static | 8RJYCOT1LHC |
| 401A_PID | R0600703ta_1LHC | 7/3/2012 20:27 | 0:35:10 | Static | 8RJYCOT1LHC |
| 701A | R0600703u_1LHC | 7/3/2012 21:21 | 0:33:40 | Static | 8RJYCOT1LHC |
| 502A | R0600703v_1LHC | 7/3/2012 22:10 | 0:31:55 | Static | 8RJYCOT1LHC |
| 402A | R0600703w_1LHC | 7/3/2012 23:00 | 0:33:55 | Static | 8RJYCOT1LHC |
| SACR | SACR | 7/4/2012 0:00 | 0:00:00 | Static | 4624K01578 |
| 503A | B38730704p_DO1S | 7/4/2012 16:24 | 0:26:40 | Static | 8RHDWKLDO1S |
| 403A | B38730704q_DO1S | 7/4/2012 17:18 | 0:30:45 | Static | 8RHDWKLDO1S |
| 702 | B38730704r_DO1S | 7/4/2012 18:15 | 0:34:15 | Static | 8RHDWKLDO1S |
| 703A | B38730704t_DO1S | 7/4/2012 19:30 | 0:30:05 | Static | 8RHDWKLDO1S |
| 503 | R0600704p_1LHC | 7/4/2012 16:22 | 0:26:55 | Static | 8RJYCOT1LHC |
| 403 | R0600704q_1LHC | 7/4/2012 17:19 | 0:33:10 | Static | 8RJYCOT1LHC |
| 702A | R0600704r_1LHC | 7/4/2012 18:17 | 0:34:50 | Static | 8RJYCOT1LHC |
| 703 | R0600704s_1LHC | 7/4/2012 19:30 | 0:31:35 | Static | 8RJYCOT1LHC |
| SACR | SACR | 7/4/2012 23:00 | 23:00:00 | Static | 4624K01578 |
| LNC2 | LNC2 | 7/5/2012 0:00 | 0:00:00 | Static | 4751143269 |
| LNC2 | LNC2 | 7/4/2012 0:00 | 0:00:00 | Static | 4751143269 |
| 405B_PID | R0600705v_1LHC | 7/5/2012 22:30 | 0:39:45 | Static | 8RJYCOT1LHC |
| 504 | B0560705a_81KW | 7/5/2012 17:35 | 1:04:40 | Static | 8PZFI4M81KW |
| 704 | B0560705b_81KW | 7/5/2012 18:40 | 0:35:05 | Static | 8PZFI4M81KW |
| 404A | B0560705c_81KW | 7/5/2012 19:29 | 0:33:55 | Static | 8PZFI4M81KW |
| 705A | B0560705d_81KW | 7/5/2012 20:32 | 0:36:45 | Static | 8PZFI4M81KW |
| 505 | B0560705e_81KW | 7/5/2012 21:31 | 0:39:45 | Static | 8PZFI4M81KW |
| 405A_PID | B0560705f_81KW | 7/5/2012 22:29 | 0:44:20 | Static | 8PZFI4M81KW |
| 506 | B0560705g_81KW | 7/5/2012 23:46 | 0:44:05 | Static | 8PZFI4M81KW |
| 706 | B0560706a_81KW | 7/6/2012 0:50 | 0:41:55 | Static | 8PZFI4M81KW |
| 507 | B0560706b_81KW | 7/6/2012 1:56 | 0:37:00 | Static | 8PZFI4M81KW |
| 406A | B0560706c_81KW | 7/6/2012 2:46 | 0:31:45 | Static | 8PZFI4M81KW |
| 707 | B0560706d_81KW | 7/6/2012 3:28 | 0:29:00 | Static | 8PZFI4M81KW |
| JS0801os | B3610705a_ESQO | 7/5/2012 15:27 | 0:29:50 | Static | 8PJPJX3ESQO |
| 504A | B3610705b_ESQO | 7/5/2012 17:36 | 1:03:45 | Static | 8PJPJX3ESQO |
| 411Base | B3610705d_ESQO | 7/6/2012 3:48 | 10:07:50 | Static | 8PJPJX3ESQO |
| 704A | B38730705s_DO1S | 7/5/2012 18:41 | 0:34:50 | Static | 8RHDWKLDO1S |
| 404 | B38730705sa_DO1S | 7/5/2012 19:28 | 0:34:40 | Static | 8RHDWKLDO1S |
| 705 | B38730705t_DO1S | 7/5/2012 20:31 | 0:37:45 | Static | 8RHDWKLDO1S |
| 505A | B38730705u_DO1S | 7/5/2012 21:32 | 0:39:25 | Static | 8RHDWKLDO1S |
| 405 | B38730705v_DO1S | 7/5/2012 22:32 | 0:48:30 | Static | 8RHDWKLDO1S |
| 506A | B38730705x_DO1S | 7/5/2012 23:45 | 0:41:30 | Static | 8RHDWKLDO1S |
| 706A | B38730706a_DO1S | 7/6/2012 0:51 | 0:41:05 | Static | 8RHDWKLDO1S |
| 507A | B38730706b_DO1S | 7/6/2012 1:56 | 0:35:25 | Static | 8RHDWKLDO1S |
| 406 | B38730706c_DO1S | 7/6/2012 2:47 | 0:36:50 | Static | 8RHDWKLDO1S |
| 707A | B38730706d_DO1S | 7/6/2012 3:29 | 0:28:35 | Static | 8RHDWKLDO1S |
| LNC2 | LNC2 | 7/6/2012 0:00 | 0:00:00 | Static | 4751143269 |
| 509B_PID | B0560706e_81KW | 7/6/2012 23:33 | 0:17:15 | Static | 8PZFI4M81KW |
| 412 | R0600707c_1LHC | 7/7/2012 2:55 | 0:33:20 | Static | 8RJYCOT1LHC |
| 708 | B38730706q_DO1S | 7/6/2012 16:43 | 0:43:10 | Static | 8RHDWKLDO1S |
| 407 | B38730706s_DO1S | 7/6/2012 18:32 | 0:32:30 | Static | 8RHDWKLDO1S |
| 709A | B38730706t_DO1S | 7/6/2012 19:43 | 0:31:40 | Static | 8RHDWKLDO1S |
| 508 | B38730706ta_DO1S | 7/6/2012 20:30 | 0:34:10 | Static | 8RHDWKLDO1S |
| 408 | B38730706v_DO1S | 7/6/2012 22:32 | 0:38:50 | Static | 8RHDWKLDO1S |
| 710 | B38730706u_DO1S | 7/6/2012 21:29 | 0:46:35 | Static | 8RHDWKLDO1S |
| 509 | B38730706w_DO1S | 7/6/2012 23:36 | 0:36:50 | Static | 8RHDWKLDO1S |
| 510A | B38730706x_DO1S | 7/7/2012 0:21 | 0:30:35 | Static | 8RHDWKLDO1S |
| 409A | B38730707a_DO1S | 7/7/2012 1:06 | 0:34:10 | Static | 8RHDWKLDO1S |
| 410A | B38730707b_DO1S | 7/7/2012 1:56 | 0:32:05 | Static | 8RHDWKLDO1S |
| 412A | B38730707c_DO1S | 7/7/2012 2:56 | 0:32:00 | Static | 8RHDWKLDO1S |
| 411Base | R0590706o_UN0G | 7/7/2012 3:20 | 12:21:10 | Static | 8QCP5IOUN0G |
| 708A | R0600706q_1LHC | 7/6/2012 16:44 | 0:41:05 | Static | 8RJYCOT1LHC |
| 407A_PID | R0600706s_1LHC | 7/6/2012 18:33 | 0:31:50 | Static | 8RJYCOT1LHC |
| 709 | R0600706t_1LHC | 7/6/2012 19:42 | 0:31:50 | Static | 8RJYCOT1LHC |
| 508A | R0600706ta_1LHC | 7/6/2012 20:29 | 0:30:05 | Static | 8RJYCOT1LHC |
| 710A | R0600706u_1LHC | 7/6/2012 21:31 | 0:44:55 | Static | 8RJYCOT1LHC |
| 408A_PID | R0600706v_1LHC | 7/6/2012 22:29 | 0:32:30 | Static | 8RJYCOT1LHC |
| LNC2 | LNC2 | 7/7/2012 0:00 | 0:00:00 | Static | 4751143269 |
| 509A | R0600706x_1LHC | 7/6/2012 23:35 | 0:33:55 | Static | 8RJYCOT1LHC |
| 510 | R0600706xa_1LHC | 7/7/2012 0:20 | 0:31:30 | Static | 8RJYCOT1LHC |
| 409 | R0600707a_1LHC | 7/7/2012 1:07 | 0:36:05 | Static | 8RJYCOT1LHC |
| 410 | R0600707b_1LHC | 7/7/2012 1:56 | 0:32:35 | Static | 8RJYCOT1LHC |
| JS0750 | R0600707q_1LHC | 7/7/2012 16:51 | 0:49:30 | Static | 8RJYCOT1LHC |
| JS0786os | B38730707v_DO1S | 7/7/2012 22:23 | 1:00:15 | Static | 8RHDWKLDO1S |
| LNC2 | LNC2 | 7/8/2012 0:00 | 0:00:00 | Static | 4751143269 |
| LNC1 | LNC1 | 7/8/2012 0:00 | 0:00:00 | Static | 4751143257 |
| SACR | SACR | 7/8/2012 0:00 | 0:00:00 | Static | 4624K01578 |
| SACR | SACR | 7/7/2012 0:00 | 0:00:00 | Static | 4624K01578 |

Placer County West Area CP Sketch

NGS DataSheets

## The NGS Data Sheet

##### See file dsdata.txt for more information about the datasheet.

DATABASE = NGSIDB , PROGRAM = datasheet95, VERSION = 7.89

1        National Geodetic Survey,   Retrieval Date = JULY  5, 2012

DF7467 ***********************************************************************

DF7467  CORS        -  This is a GPS Continuously Operating Reference Station.

DF7467  DESIGNATION -  LINCOLN 2 CORS ARP

DF7467  CORS_ID     -  LNC2

DF7467  PID         -  DF7467

DF7467  STATE/COUNTY-  CA/PLACER

DF7467  COUNTRY     -  US

DF7467  USGS QUAD   -  ROSEVILLE (1992)

DF7467

DF7467                         *CURRENT SURVEY CONTROL

DF7467  ______________________________________________________________________

DF7467* NAD 83(2011) POSITION- 38 50 47.41588(N) 121 21 01.92687(W)   ADJUSTED

DF7467* NAD 83(2011) ELLIP HT-     6.381 (meters)        (08/??/11)   ADJUSTED

DF7467* NAD 83(2011) EPOCH   -  2010.00

DF7467* NAVD 88 ORTHO HEIGHT -          **(meters)           **(feet)

DF7467  ______________________________________________________________________

DF7467  NAD 83(2011) X  - -2,587,855.568 (meters)                     COMP

DF7467  NAD 83(2011) Y  - -4,247,830.076 (meters)                     COMP

DF7467  NAD 83(2011) Z  -  3,979,063.983 (meters)                     COMP

DF7467  GEOID HEIGHT    -        -30.01  (meters)                     GEOID12

DF7467  HORZ ORDER      -  SPECIAL (CORS)

DF7467  ELLP ORDER      -  SPECIAL (CORS)

DF7467

DF7467.The coordinates were established by GPS observations

DF7467.and adjusted by the National Geodetic Survey in August 2011.

DF7467

DF7467.NAD 83(2011) refers to NAD 83 coordinates where the reference

DF7467.frame has been affixed to the stable North American Tectonic Plate.

DF7467

DF7467.The coordinates are valid at the epoch date displayed above

DF7467.which is a decimal equivalence of Year/Month/Day.

DF7467

DF7467.The PID for the CORS L1 Phase Center is DG6998.

DF7467

DF7467.The XYZ, and position/ellipsoidal ht. are equivalent.

DF7467

DF7467.The ellipsoidal height was determined by GPS observations

DF7467.and is referenced to NAD 83.

DF7467

DF7467. The following values were computed from the NAD 83(2011) position.

DF7467

DF7467;                    North         East     Units Scale Factor Converg.

DF7467;SPC CA 2     -   631,169.704 2,056,377.346   MT  0.99992327   +0 24 34.1

DF7467;SPC CA 2     - 2,070,762.60  6,746,631.34   sFT  0.99992327   +0 24 34.1

DF7467

DF7467!             -  Elev Factor  x  Scale Factor =   Combined Factor

DF7467!SPC CA 2     -   0.99999900  x   0.99992327  =   0.99992227

DF7467

DF7467                          SUPERSEDED SURVEY CONTROL

DF7467

DF7467  NAD 83(CORS)-  38 50 47.41366(N)    121 21 01.92412(W) AD(2002.00) c

DF7467  ELLIP H (03/??/08)    6.381  (m)                       GP(2002.00) c c

DF7467  NAD 83(CORS)-  38 50 47.41360(N)    121 21 01.92404(W) AD(2002.00) c

DF7467  ELLIP H (10/??/04)    6.389  (m)                       GP(2002.00) c c

DF7467  NAD 83(CORS)-  38 50 47.41355(N)    121 21 01.92408(W) AD(2002.00) c

DF7467  ELLIP H (08/??/03)    6.277  (m)                       GP(2002.00) c c

DF7467

DF7467.Superseded values are not recommended for survey control.

DF7467

DF7467.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DF7467.See file dsdata.txt to determine how the superseded data were derived.

DF7467

DF7467_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SFJ4314201035(NAD 83)

DF7467

DF7467_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DF7467

DF7467                          STATION DESCRIPTION

DF7467

DF7467'DESCRIBED BY NATIONAL GEODETIC SURVEY 2011

DF7467'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DF7467'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DF7467'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DF7467'   ftp://cors.ngs.noaa.gov/cors/README.txt

DF7467'   ftp://cors.ngs.noaa.gov/cors/coord/coord_08

DF7467'   ftp://cors.ngs.noaa.gov/cors/station_log

DF7467'   http://geodesy.noaa.gov/CORS

1        National Geodetic Survey,   Retrieval Date = JULY  5, 2012

DH8725 ***********************************************************************

DH8725  HT_MOD      -  This is a Height Modernization Survey Station.

DH8725  CORS        -  This is a GPS Continuously Operating Reference Station.

DH8725  DESIGNATION -  SACRAMENTO COOP CORS ARP

DH8725  CORS_ID     -  SACR

DH8725  PID         -  DH8725

DH8725  STATE/COUNTY-  CA/SACRAMENTO

DH8725  COUNTRY     -  US

DH8725  USGS QUAD   -  CITRUS HEIGHTS (1992)

DH8725

DH8725                         *CURRENT SURVEY CONTROL

DH8725  ______________________________________________________________________

DH8725* NAD 83(2011) POSITION- 38 39 17.97131(N) 121 21 15.19332(W)   ADJUSTED

DH8725* NAD 83(2011) ELLIP HT-     7.475 (meters)        (08/??/11)   ADJUSTED

DH8725* NAD 83(2011) EPOCH   -  2010.00

DH8725* NAVD 88 ORTHO HEIGHT -    37.97   (meters)     124.6   (feet) GPS OBS

DH8725  ______________________________________________________________________

DH8725  NAVD 88 orthometric height was determined with geoid model    GEOID09

DH8725  GEOID HEIGHT    -        -30.47  (meters)                     GEOID09

DH8725  GEOID HEIGHT    -        -30.47  (meters)                     GEOID12

DH8725  NAD 83(2011) X  - -2,595,053.378 (meters)                     COMP

DH8725  NAD 83(2011) Y  - -4,259,028.356 (meters)                     COMP

DH8725  NAD 83(2011) Z  -  3,962,484.543 (meters)                     COMP

DH8725  HORZ ORDER      -  SPECIAL (CORS)

DH8725  ELLP ORDER      -  SPECIAL (CORS)

DH8725

DH8725.The coordinates were established by GPS observations

DH8725.and adjusted by the National Geodetic Survey in August 2011.

DH8725

DH8725.NAD 83(2011) refers to NAD 83 coordinates where the reference

DH8725.frame has been affixed to the stable North American Tectonic Plate.

DH8725

DH8725.The coordinates are valid at the epoch date displayed above

DH8725.which is a decimal equivalence of Year/Month/Day.

DH8725

DH8725.The orthometric height was determined by GPS observations and a

DH8725.high-resolution geoid model using precise GPS observation and

DH8725.processing techniques.

DH8725

DH8725.The PID for the CORS L1 Phase Center is DI1709.

DH8725

DH8725.The XYZ, and position/ellipsoidal ht. are equivalent.

DH8725

DH8725.The ellipsoidal height was determined by GPS observations

DH8725.and is referenced to NAD 83.

DH8725

DH8725. The following values were computed from the NAD 83(2011) position.

DH8725

DH8725;                    North         East     Units Scale Factor Converg.

DH8725;SPC CA 2     -   609,909.477 2,056,208.522   MT  0.99994262   +0 24 25.7

DH8725;SPC CA 2     - 2,001,011.34  6,746,077.46   sFT  0.99994262   +0 24 25.7

DH8725

DH8725!             -  Elev Factor  x  Scale Factor =   Combined Factor

DH8725!SPC CA 2     -   0.99999883  x   0.99994262  =   0.99994145

DH8725

DH8725                          SUPERSEDED SURVEY CONTROL

DH8725

DH8725  NAD 83(CORS)-  38 39 17.96927(N)    121 21 15.19007(W) AD(2002.00) c

DH8725  ELLIP H (03/??/06)    7.482  (m)                       GP(2002.00) c c

DH8725

DH8725.Superseded values are not recommended for survey control.

DH8725

DH8725.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DH8725.See file dsdata.txt to determine how the superseded data were derived.

DH8725

DH8725_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SFH4320479776(NAD 83)

DH8725

DH8725_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DH8725

DH8725                          STATION DESCRIPTION

DH8725

DH8725'DESCRIBED BY NATIONAL GEODETIC SURVEY 2011

DH8725'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DH8725'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DH8725'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DH8725'   ftp://cors.ngs.noaa.gov/cors/README.txt

DH8725'   ftp://cors.ngs.noaa.gov/cors/coord/coord_08

DH8725'   ftp://cors.ngs.noaa.gov/cors/station_log

DH8725'   http://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:02

64a94033-1196-4c22-bcdb-14018c710166

Y2:64a94033-1196-4c22-bcdb-14018c710166

JS0801 ***********************************************************************

JS0801  DESIGNATION -  P 201

JS0801  PID         -  JS0801

JS0801  STATE/COUNTY-  CA/PLACER

JS0801  COUNTRY     -  US

JS0801  USGS QUAD   -  AUBURN (1981)

JS0801

JS0801                         *CURRENT SURVEY CONTROL

JS0801  ______________________________________________________________________

JS0801* NAD 83(1986) POSITION- 38 53 59.     (N) 121 04 10.     (W)   SCALED

JS0801* NAVD 88 ORTHO HEIGHT -   396.160  (meters)    1299.73  (feet) ADJUSTED

JS0801  ______________________________________________________________________

JS0801  GEOID HEIGHT    -        -28.23  (meters)                     GEOID12

JS0801  DYNAMIC HEIGHT  -        395.890 (meters)     1298.85  (feet) COMP

JS0801  MODELED GRAVITY -    979,934.1   (mgal)                       NAVD 88

JS0801

JS0801  VERT ORDER      -  FIRST     CLASS II

JS0801

JS0801.The horizontal coordinates were scaled from a topographic map and have

JS0801.an estimated accuracy of +/- 6 seconds.

JS0801.

JS0801.The orthometric height was determined by differential leveling and

JS0801.adjusted in June 1991.

JS0801

JS0801.The dynamic height is computed by dividing the NAVD 88

JS0801.geopotential number by the normal gravity value computed on the

JS0801.Geodetic Reference System of 1980 (GRS 80) ellipsoid at 45

JS0801.degrees latitude (g = 980.6199 gals.).

JS0801

JS0801.The modeled gravity was interpolated from observed gravity values.

JS0801

JS0801;                    North         East    Units  Estimated Accuracy

JS0801;SPC CA 2     -   637,290.    2,080,720.      MT  (+/- 180 meters Scaled)

JS0801

JS0801                          SUPERSEDED SURVEY CONTROL

JS0801

JS0801.No superseded survey control is available for this station.

JS0801

JS0801_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SFJ674074(NAD 83)

JS0801

JS0801_MARKER: DB = BENCH MARK DISK

JS0801_SETTING: 36 = SET IN A MASSIVE STRUCTURE

JS0801_SP_SET: BALUSTRADE

JS0801_STAMPING: P 201 1935

JS0801_STABILITY: B = PROBABLY HOLD POSITION/ELEVATION WELL

JS0801_SATELLITE: THE SITE LOCATION WAS REPORTED AS NOT SUITABLE FOR

JS0801+SATELLITE: SATELLITE OBSERVATIONS - March 13, 2004

JS0801

JS0801  HISTORY     - Date     Condition        Report By

JS0801  HISTORY     - 1935     MONUMENTED       CGS

JS0801  HISTORY     - 1935     GOOD             CGS

JS0801  HISTORY     - 20040313 GOOD             CADT

JS0801  HISTORY     - 20070322 GOOD             GEOCAC

JS0801

JS0801                          STATION DESCRIPTION

JS0801

JS0801'DESCRIBED BY COAST AND GEODETIC SURVEY 1935

JS0801'AT AUBURN.

JS0801'AT AUBURN, PLACER COUNTY, AT THE PLACER COUNTY SAVINGS BANK, AT

JS0801'THE FRONT ENTRANCE, IN THE TOP OF THE WEST CONCRETE BALUSTRADE,

JS0801'0.5 FOOT NORTH OF THE SOUTH END OF THE BALUSTRACE, 0.5 FOOT

JS0801'WEST OF THE EAST EDGE, AND 14.5 FEET NORTH OF THE NORTH CURB

JS0801'LINE OF LINCOLN WAY.  A STANDARD DISK, STAMPED P 201 1935.

JS0801

JS0801                          STATION RECOVERY (2004)

JS0801

JS0801'RECOVERY NOTE BY CALTRANS 2004 (DWM)

JS0801'RECOVERED IN GOOD CONDITION.

JS0801

JS0801                          STATION RECOVERY (2007)

JS0801

JS0801'RECOVERY NOTE BY GEOCACHING 2007 (TFW)

JS0801'RECOVERED AS DESCRIBED

1        National Geodetic Survey,   Retrieval Date = JULY  4, 2012

JS0786 ***********************************************************************

JS0786  DESIGNATION -  T 1200

JS0786  PID         -  JS0786

JS0786  STATE/COUNTY-  CA/PLACER

JS0786  COUNTRY     -  US

JS0786  USGS QUAD   -  AUBURN (1981)

JS0786

JS0786                         *CURRENT SURVEY CONTROL

JS0786  ______________________________________________________________________

JS0786* NAD 83(1986) POSITION- 38 54 06.4    (N) 121 03 56.7    (W)   HD_HELD2

JS0786* NAVD 88 ORTHO HEIGHT -   412.973  (meters)    1354.90  (feet) ADJUSTED

JS0786  ______________________________________________________________________

JS0786  GEOID HEIGHT    -        -28.20  (meters)                     GEOID12

JS0786  DYNAMIC HEIGHT  -        412.692 (meters)     1353.97  (feet) COMP

JS0786  MODELED GRAVITY -    979,934.6   (mgal)                       NAVD 88

JS0786

JS0786  VERT ORDER      -  FIRST     CLASS I

JS0786

JS0786.The horizontal coordinates were established by autonomous hand held GPS

JS0786.observations and have an estimated accuracy of +/- 10 meters.

JS0786.

JS0786.The orthometric height was determined by differential leveling and

JS0786.adjusted in June 1991.

JS0786

JS0786.Photographs are available for this station.

JS0786

JS0786.The dynamic height is computed by dividing the NAVD 88

JS0786.geopotential number by the normal gravity value computed on the

JS0786.Geodetic Reference System of 1980 (GRS 80) ellipsoid at 45

JS0786.degrees latitude (g = 980.6199 gals.).

JS0786

JS0786.The modeled gravity was interpolated from observed gravity values.

JS0786

JS0786;                    North         East    Units  Estimated Accuracy

JS0786;SPC CA 2     -   637,520.    2,081,035.      MT  (+/- 10 meters HH2 GPS)

JS0786

JS0786                          SUPERSEDED SURVEY CONTROL

JS0786

JS0786.No superseded survey control is available for this station.

JS0786

JS0786_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SFJ6772807655(NAD 83)

JS0786

JS0786_MARKER: DB = BENCH MARK DISK

JS0786_SETTING: 30 = SET IN A LIGHT STRUCTURE

JS0786_SP_SET: FOUNDATION

JS0786_STAMPING: T 1200 1969

JS0786_STABILITY: D = MARK OF QUESTIONABLE OR UNKNOWN STABILITY

JS0786_SATELLITE: THE SITE LOCATION WAS REPORTED AS NOT SUITABLE FOR

JS0786+SATELLITE: SATELLITE OBSERVATIONS - March 14, 2004

JS0786

JS0786  HISTORY     - Date     Condition        Report By

JS0786  HISTORY     - 1969     MONUMENTED       CGS

JS0786  HISTORY     - 20040314 GOOD             CADT

JS0786  HISTORY     - 20070322 GOOD             GEOCAC

JS0786

JS0786                          STATION DESCRIPTION

JS0786

JS0786'DESCRIBED BY COAST AND GEODETIC SURVEY 1969

JS0786'AT AUBURN.

JS0786'AT AUBURN, 124.6 FEET SOUTH OF THE SOUTHWEST CORNER OF THE

JS0786'SOUTHERN PACIFIC COMPANY RAILROAD STATION, IN THE TOP AND ALONG

JS0786'THE EAST SIDE OF A 3- BY 3-FOOT CONCRETE FOUNDATION OF THE

JS0786'NORTHEAST LEG OF CITY SIREN STEEL TOWER, 50.0 FEET WEST OF THE

JS0786'WEST RAIL OF THE WESTBOUND MAIN TRACK, 58 FEET EAST OF THE CENTER

JS0786'LINE OF LINCOLN WAY NORTH, 5 FEET SOUTHEAST OF THE EXTENDED

JS0786'CENTER LINE OF LINCOLN WAY SOUTHWEST, 9 FEET EAST OF THE CITY

JS0786'FLAGPOLE, 1.0 FOOT EAST OF THE NORTHEAST STEEL LEG OF THE TOWER,

JS0786'AND ABOUT 2 1/2 FEET LOWER THAN THE TRACK.

JS0786

JS0786                          STATION RECOVERY (2004)

JS0786

JS0786'RECOVERY NOTE BY CALTRANS 2004 (DWM)

JS0786'RECOVERED IN GOOD CONDITION.

JS0786

JS0786                          STATION RECOVERY (2007)

JS0786

JS0786'RECOVERY NOTE BY GEOCACHING 2007 (TFW)

JS0786'RECOVERED AS DESCRIBED

1        National Geodetic Survey,   Retrieval Date = JULY  7, 2012

JS0750 ***********************************************************************

JS0750  DESIGNATION -  D 566

JS0750  PID         -  JS0750

JS0750  STATE/COUNTY-  CA/PLACER

JS0750  COUNTRY     -  US

JS0750  USGS QUAD   -  ROSEVILLE (1992)

JS0750

JS0750                         *CURRENT SURVEY CONTROL

JS0750  ______________________________________________________________________

JS0750* NAD 83(1986) POSITION- 38 46 08.     (N) 121 15 17.     (W)   SCALED

JS0750* NAVD 88 ORTHO HEIGHT -    62.661  (meters)     205.58  (feet) ADJUSTED

JS0750  ______________________________________________________________________

JS0750  GEOID HEIGHT    -        -30.01  (meters)                     GEOID12

JS0750  DYNAMIC HEIGHT  -         62.619 (meters)      205.44  (feet) COMP

JS0750  MODELED GRAVITY -    979,959.5   (mgal)                       NAVD 88

JS0750

JS0750  VERT ORDER      -  FIRST     CLASS I

JS0750

JS0750.The horizontal coordinates were scaled from a topographic map and have

JS0750.an estimated accuracy of +/- 6 seconds.

JS0750.

JS0750.The orthometric height was determined by differential leveling and

JS0750.adjusted in June 1991.

JS0750

JS0750.The dynamic height is computed by dividing the NAVD 88

JS0750.geopotential number by the normal gravity value computed on the

JS0750.Geodetic Reference System of 1980 (GRS 80) ellipsoid at 45

JS0750.degrees latitude (g = 980.6199 gals.).

JS0750

JS0750.The modeled gravity was interpolated from observed gravity values.

JS0750

JS0750;                    North         East    Units  Estimated Accuracy

JS0750;SPC CA 2     -   622,620.    2,064,770.      MT  (+/- 180 meters Scaled)

JS0750

JS0750                          SUPERSEDED SURVEY CONTROL

JS0750

JS0750.No superseded survey control is available for this station.

JS0750

JS0750_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SFH516925(NAD 83)

JS0750

JS0750_MARKER: DB = BENCH MARK DISK

JS0750_SETTING: 32 = SET IN A RETAINING WALL OR CONCRETE LEDGE

JS0750_SP_SET: HEADWALL

JS0750_STAMPING: D 566 1938

JS0750_MARK LOGO: CGS

JS0750_STABILITY: C = MAY HOLD, BUT OF TYPE COMMONLY SUBJECT TO

JS0750+STABILITY: SURFACE MOTION

JS0750_SATELLITE: THE SITE LOCATION WAS REPORTED AS SUITABLE FOR

JS0750+SATELLITE: SATELLITE OBSERVATIONS - March 13, 2004

JS0750

JS0750  HISTORY     - Date     Condition        Report By

JS0750  HISTORY     - 1938     MONUMENTED       CGS

JS0750  HISTORY     - 1969     GOOD             CGS

JS0750  HISTORY     - 19881111 GOOD             USPSQD

JS0750  HISTORY     - 19890202 GOOD             NGS

JS0750  HISTORY     - 20040313 GOOD             CADT

JS0750

JS0750                          STATION DESCRIPTION

JS0750

JS0750'DESCRIBED BY COAST AND GEODETIC SURVEY 1969

JS0750'2.2 MI NE FROM ROSEVILLE.

JS0750'2.15 MILES NORTHEAST ALONG THE SOUTHERN PACIFIC COMPANY RAILROAD

JS0750'FROM THE STATION AT ROSEVILLE, 9 1/2 POLES SOUTHWEST OF MILEPOLE

JS0750'109, 7 RAILS SOUTHWEST OF A PRIVATE ROAD CROSSING, 6 RAILS

JS0750'NORTHEAST OF SEMAPHORE 1087, IN THE TOP AND 1.0 FOOT NORTHEAST

JS0750'OF THE SOUTHWEST END OF THE SOUTHEAST CONCRETE HEAD WALL OF PIPE

JS0750'CULVERT 108.75, 9.8 FEET SOUTHEAST OF THE SOUTHEAST RAIL OF THE

JS0750'SOUTHEAST TRACK, 55 FEET NORTHWEST OF THE CENTER LINE OF TAYLOR

JS0750'ROAD, AND ABOUT 2 1/2 FEET LOWER THAN THE TRACK.

JS0750

JS0750                          STATION RECOVERY (1988)

JS0750

JS0750'RECOVERY NOTE BY US POWER SQUADRON 1988 (EH)

JS0750'RECOVERED IN GOOD CONDITION.

JS0750

JS0750                          STATION RECOVERY (1989)

JS0750

JS0750'RECOVERY NOTE BY NATIONAL GEODETIC SURVEY 1989

JS0750'RECOVERED IN GOOD CONDITION.

JS0750

JS0750                          STATION RECOVERY (2004)

JS0750

JS0750'RECOVERY NOTE BY CALTRANS 2004 (DWM)

JS0750'RECOVERED IN GOOD CONDITION.

## The NGS Data Sheet

##### See file dsdata.txt for more information about the datasheet.

PROGRAM = datasheet95, VERSION = 7.89.2

1        National Geodetic Survey,   Retrieval Date = AUGUST  8, 2012

DF7465 ***********************************************************************

DF7465  HT_MOD      -  This is a Height Modernization Survey Station.

DF7465  CORS        -  This is a GPS Continuously Operating Reference Station.

DF7465  DESIGNATION -  LINCOLN 1 CORS ARP

DF7465  CORS_ID     -  LNC1

DF7465  PID         -  DF7465

DF7465  STATE/COUNTY-  CA/PLACER

DF7465  COUNTRY     -  US

DF7465  USGS QUAD   -  ROSEVILLE (1992)

DF7465

DF7465                         *CURRENT SURVEY CONTROL

DF7465  ______________________________________________________________________

DF7465* NAD 83(2011) POSITION- 38 50 47.42727(N) 121 21 00.79386(W)   ADJUSTED

DF7465* NAD 83(2011) ELLIP HT-     6.443 (meters)        (08/??/11)   ADJUSTED

DF7465* NAD 83(2011) EPOCH   -  2010.00

DF7465* NAVD 88 ORTHO HEIGHT -    36.46   (meters)     119.6   (feet) GPS OBS

DF7465  ______________________________________________________________________

DF7465  NAVD 88 orthometric height was determined with geoid model    GEOID09

DF7465  GEOID HEIGHT    -        -30.02  (meters)                     GEOID09

DF7465  GEOID HEIGHT    -        -30.01  (meters)                     GEOID12

DF7465  NAD 83(2011) X  - -2,587,832.145 (meters)                     COMP

DF7465  NAD 83(2011) Y  - -4,247,844.144 (meters)                     COMP

DF7465  NAD 83(2011) Z  -  3,979,064.296 (meters)                     COMP

DF7465  HORZ ORDER      -  SPECIAL (CORS)

DF7465  ELLP ORDER      -  SPECIAL (CORS)

DF7465

DF7465.The coordinates were established by GPS observations

DF7465.and adjusted by the National Geodetic Survey in August 2011.

DF7465

DF7465.NAD 83(2011) refers to NAD 83 coordinates where the reference

DF7465.frame has been affixed to the stable North American Tectonic Plate.

DF7465

DF7465.The coordinates are valid at the epoch date displayed above

DF7465.which is a decimal equivalence of Year/Month/Day.

DF7465

DF7465.The orthometric height was determined by GPS observations and a

DF7465.high-resolution geoid model using precise GPS observation and

DF7465.processing techniques.

DF7465

DF7465.The PID for the CORS L1 Phase Center is DG6997.

DF7465

DF7465.The XYZ, and position/ellipsoidal ht. are equivalent.

DF7465

DF7465.The ellipsoidal height was determined by GPS observations

DF7465.and is referenced to NAD 83.

DF7465

DF7465. The following values were computed from the NAD 83(2011) position.

DF7465

DF7465;                    North         East     Units Scale Factor Converg.

DF7465;SPC CA 2     -   631,170.251 2,056,404.663   MT  0.99992327   +0 24 34.8

DF7465;SPC CA 2     - 2,070,764.40  6,746,720.97   sFT  0.99992327   +0 24 34.8

DF7465

DF7465!             -  Elev Factor  x  Scale Factor =   Combined Factor

DF7465!SPC CA 2     -   0.99999899  x   0.99992327  =   0.99992226

DF7465

DF7465                          SUPERSEDED SURVEY CONTROL

DF7465

DF7465  NAD 83(CORS)-  38 50 47.42507(N)    121 21 00.79111(W) AD(2002.00) c

DF7465  ELLIP H (03/??/08)    6.443  (m)                       GP(2002.00) c c

DF7465  NAD 83(CORS)-  38 50 47.42500(N)    121 21 00.79097(W) AD(2002.00) c

DF7465  ELLIP H (10/??/04)    6.450  (m)                       GP(2002.00) c c

DF7465  NAD 83(CORS)-  38 50 47.42500(N)    121 21 00.79110(W) AD(2002.00) c

DF7465  ELLIP H (08/??/03)    6.338  (m)                       GP(2002.00) c c

DF7465  NAVD 88 (02/03/05)   36.47   (m)  GEOID03 model used   GPS OBS

DF7465

DF7465.Superseded values are not recommended for survey control.

DF7465

DF7465.NGS no longer adjusts projects to the NAD 27 or NGVD 29 datums.

DF7465.See file dsdata.txt to determine how the superseded data were derived.

DF7465

DF7465_U.S. NATIONAL GRID SPATIAL ADDRESS: 10SFJ4316901036(NAD 83)

DF7465

DF7465_MARKER: STATION IS THE ANTENNA REFERENCE POINT OF THE GPS ANTENNA

DF7465

DF7465                          STATION DESCRIPTION

DF7465

DF7465'DESCRIBED BY NATIONAL GEODETIC SURVEY 2011

DF7465'STATION IS A GPS CORS.  LATEST INFORMATION INCLUDING POSITIONS AND

DF7465'VELOCITIES ARE AVAILABLE IN THE COORDINATE AND LOG FILES ACCESSIBLE

DF7465'BY ANONYMOUS FTP OR THE WORLDWIDE WEB.

DF7465'   ftp://cors.ngs.noaa.gov/cors/README.txt

DF7465'   ftp://cors.ngs.noaa.gov/cors/coord/coord_08

DF7465'   ftp://cors.ngs.noaa.gov/cors/station_log

DF7465'   http://geodesy.noaa.gov/CORS

*** retrieval complete.

Elapsed Time = 00:00:05