Horizontal and Vertical Accuracy Reports for the

2006 Aerial Photography and LIDAR Project

for Fulton County and the City of Atlanta.

Reports Compiled by Fulton County

March 2007

Definition of 2006 Aerial Photography and LIDAR Project.   ……………..

Horizontal Accuracy

*Tested 0.90539 (feet) horizontal accuracy at 95% confidence level*

Vertical Accuracy

*Tested 1.44 (feet) vertical accuracy at 95% confidence level*

Horizontal and Vertical accuracy tests were performed using the methodologies defined in “Geospatial Positioning Accuracy Standards, Part 3: National Standard for Spatial Data Accuracy” (FGDC-STD-007.3-1998)

Horizontal Accuracy Testing

Fulton County provided 20 manhole sample locations that were easily identifiable in the Aerial Photography images.  These manholes had been located using GPS-RTK (Real Time Kinetic) equipment at better than 2 centimeter accuracy.  The Fulton County data is evenly distributed  over a 10 square mile area in Northern Fulton County

The City of Atlanta provided 50 random manhole sample locations.  21 of these locations were identifiable on the Aerial Photography.  These manholes had been located using “Engineering Grade” survey methods.  The City of Atlanta data is clustered in small groups spread out over the entirety of the City’s limits.

Each sample manhole was located in the Aerial Photography imagery and the difference between the two locations was measured as the error.

| Fulton County / City of Atlanta 2006 Aerial Imagery / LIDAR project |  |  |
| --- | --- | --- |
| NSSDA worksheet |  |  |  |  |  |
| ID TAG | Easting | Northing | Error (feet) | Err Sqr | Comment |
| 13940102601 | 2246807.4994605 | 1364283.9905912 | 0.8 | 0.64 |  |
| 23170302501 | 2191159.0777767 | 1346377.6323025 | 0.76 | 0.5776 |  |
| 23150305301 | 2238901.927 | 1330190.558 | 0.68 | 0.4624 |  |
| 23390327301 | 2245761.9995556 | 1363239.9908462 | 0.6 | 0.36 |  |
| 13970322301 | 2226309.5062254 | 1350485.2605944 | 0.59 | 0.3481 |  |
| 23460420201 | 2246391.9996841 | 1364696.7496316 | 0.58 | 0.3364 |  |
| 23150325301 | 2211051.37 | 1371683.84 | 0.57 | 0.3249 |  |
| 13970312601 | 2226946.86 | 1351758.83 | 0.56 | 0.3136 |  |
| 23070415501 | 2244316.8795542 | 1365373.1208322 | 0.5 | 0.25 |  |
| 23330404501 | 2225463.0030567 | 1409508.7504413 | 0.46 | 0.2116 |  |
| 23460420001 | 2191373.1588009 | 1347036.5112792 | 0.44 | 0.1936 |  |
| 23390324601 | 2243993.0728339 | 1363242.8997742 | 0.39 | 0.1521 |  |
| 23330404601 | 2224020.7489753 | 1408348.7519763 | 0.33 | 0.1089 |  |
| 13940101801 | 2210334.817 | 1372297.432 | 0.32 | 0.1024 |  |
| 23250400901 | 2209760.578 | 1371518.003 | 0.32 | 0.1024 |  |
| 23390303701 | 2209370.699 | 1370951.111 | 0.32 | 0.1024 |  |
| 23190412601 | 2225667.0025448 | 1351333.5027712 | 0.29 | 0.0841 |  |
| 23070416601 | 2191862.3563694 | 1347795.9967199 | 0.28 | 0.0784 |  |
| 13970314701 | 2194544.7448519 | 1372596.102983 | 0.21 | 0.0441 |  |
| 13970316401 | 2193151.0155706 | 1372728.8185031 | 0.16 | 0.0256 |  |
| 13970317601 | 2193315.5193787 | 1373466.6399438 | 0.16 | 0.0256 |  |
| BC6619690 | 2257974.248 | 1482632.884 | 1.12 | 1.2544 |  |
| BC5911090 | 2255160 | 1446605.482 | 0.8 | 0.64 |  |
| BC5017240 | 2277483.893 | 1485885.06 | 0.59 | 0.3481 |  |
| BC5012510 | 2279434.566 | 1490413.093 | 0.85 | 0.7225 |  |
| BC5012060 | 2282547.363 | 1488736.203 | 0.34 | 0.1156 |  |
| BC5009790 | 2283530.971 | 1487474.133 | 0.59 | 0.3481 |  |
| BC4906150 | 2269240.152 | 1486602.271 | 0.96 | 0.9216 |  |
| BC4709300 | 2277240.099 | 1477840.698 | 0.76 | 0.5776 |  |
| BC4612430 | 2272047.61 | 1478548.45 | 0.7 | 0.49 |  |
| BC4521130 | 2264399.607 | 1486266.334 | 0.83 | 0.6889 |  |
| BC4426370 | 2269259.452 | 1474060.709 | 0.56 | 0.3136 |  |
| BC4422700 | 2266578.288 | 1477333.38 | 0.43 | 0.1849 |  |
| BC4017800 | 2269558.865 | 1471711.052 | 0.52 | 0.2704 |  |
| BC3406900 | 2265611.711 | 1464225.145 | 0.6 | 0.36 |  |
| BC3319080 | 2256375.127 | 1467746.781 | 0.56 | 0.3136 |  |
| BC2106010 | 2247533.395 | 1479093.676 | 0.36 | 0.1296 |  |
| BC1420090 | 2244087.87 | 1470722.65 | 0.77 | 0.5929 |  |
| BC0813030 | 2230890.698 | 1462902.692 | 1.54 | 2.3716 |  |
| BC0812770 | 2233798.767 | 1460149.452 | 0.76 | 0.5776 |  |
| BC0207930 | 2226617.35 | 1462834.91 | 0.86 | 0.7396 |  |
|  |  |  | E95 = | 0.90539 |  |

Vertical Accuracy Testing

Fulton County provided 16872 manhole sample locations.  16668 of these locations were modelable using the methods described below.  These manholes had been field located using GPS-RTK (RTK) and Total Station (TS) survey equipment at better than 2 centimeter horizontal accuracy and better than a 6 centimeter vertical accuracy.  The Fulton County data is evenly distributed  over a 10 square mile area in Northern Fulton County

The City of Atlanta provided 282  random manhole sample locations.  274 of these locations were modelable using the methods described below.  These manholes had been located using “Engineering Grade” (ES) survey methods.  The City of Atlanta data is evenly distributed over the entirety of the City’s limits.

Each elevation for each sample manhole was computed from a model and the difference between the measured and computed elevations was measured as the error.

Because of suspicions of the quality vertical measurements in the manhole samples, a cross validation between the DEM model, the elevation Contour Model, the raw LIDAR samples, and the manhole sample locations was performed.

Sampling from the Elevation Contour Model

One of two methods was used; a bilinear resampling of the elevation contours above and below the XY location of the manhole sample.  This method constructed two shortest beams from the manhole to elevation contours with different elevations, the beams not touching or crossing any other elevation contour.  When it was not possible to produce beams to two contours of different elevations, the nearest elevation contour was used as a elevation sample.

create index rtk_beam__rgid__ind on aerial_analysis.rtk_beam (rgid,distance);

insert into aerial_analysis.rtk_beam

(elevation,distance,rgid,cgid,cseg,pct_along)

( select c.elevation, distance(c.shape, m.shape),

m.name as rgid, c.geo_oid as cgid, c.segment_num as cseg,

line_locate_point(c.shape,m.shape) as pct_along

from aerial.contour_05seg c,  aerial.nssda_z m

where

c.shape && expand(m.shape,100) and

not exists (select 1 from aerial_analysis.rtk_beam rb

where rb.rgid = m.name and

rb.cgid = c.geo_oid and

rb.cseg = c.segment_num

)

)

update aerial_analysis.rtk_beam set beam = makeline(m.shape,line_interpolate_point(c.shape,pct_along))

from aerial.contour_05seg c,  aerial.nssda_z m

where rtk_beam.beam is null and

c.geo_oid = rtk_beam.cgid and

c.segment_num = rtk_beam.cseg and

m.name = rtk_beam.rgid and

rtk_beam.pct_along is not null;

-- flag any line that does not crosses(), SQL-MM 3: 5.1.29, any other elevation contour.

update aerial_analysis.rtk_beam set xing = boolean_int(exists ( select 1

from  aerial.contour_05seg c

where

c.shape && rtk_beam.beam and

crosses(c.shape,rtk_beam.beam)))

where

xing is null and

-- only check the some beams during testing

rtk_beam.rgid in ( select rgid from aerial_analysis.rtk_beam where xing is null limit 100000 );

update aerial.nssda_z set contour_z= (be.elevation + (2.0 * (be.distance / (be.distance + he.distance)))), contour_model = 'linear-bivalued'

from

aerial_analysis.rtk_beam be,

aerial_analysis.rtk_beam he

where

contour_z is null and

be.rgid = nssda_z.name and

he.rgid = nssda_z.name and

be.xing = 0 and

he.xing = 0 and

be.elevation < he.elevation and

(he.elevation - be.elevation) = 2.0

Sampling from the DEM model

The XY location of each manhole was used to locate the three nearest DEM cell centers.  A plane was constructed from of the three DEM cell centers and the elevation on that plane of the manhole’s XY coordinate was computed.  This method proved to form a baseline in accuracy, which while routinely was not as accurate as the other elevation contour model sampling method, was more accurate when either of those methods were not able to produce a clean sample.

create table aerial_analysis.rtk_dem_beam as ( select z(dem.shape) as elevation,

distance(setsrid(dem.shape,2240), m.shape),

m.name as rgid, dem.dem_id as demid,

makeline(m.shape,setsrid(dem.shape,2240)) as beam,

null::integer as status

from aerial.dem,  aerial.nssda_z m

where

dem.shape && setsrid(expand(m.shape,20),-1)

);

create index rtk_dem_beam__rgid__ind on aerial_analysis.rtk_dem_beam(rgid);

-- first nearest three points

update aerial_analysis.rtk_dem_beam set status = 1

where

status is null and

distance <= ( select max(distance) from

(select distance

from aerial_analysis.rtk_dem_beam rb

where

status is null and

--                   same manhole

rb.rgid = rtk_dem_beam.rgid and

--                   beam to a dem sample with the same elevation

rb.elevation = rtk_dem_beam.elevation

limit 3

) as x

)

;

update aerial.nssda_z set dem_z = planar_resample(endpoint(be.beam), endpoint(me.beam), endpoint(he.beam), nssda_z.shape),

dem_model = 'planar-resample'

from

aerial_analysis.rtk_dem_beam be,

aerial_analysis.rtk_dem_beam me,

aerial_analysis.rtk_dem_beam he

where

be.rgid = nssda_z.name and

me.rgid = nssda_z.name and

he.rgid = nssda_z.name and

be.status = 1 and

me.status = 1 and

he.status = 1 and

be.demid != me.demid and

be.demid != he.demid and

me.demid != he.demid  ;

Sampling from the raw LIDAR samples

As a further check, the nearest LIDAR sample with an ASPRS class of 2 (Bare Earth) was sampled for each manhole sample.  Actual SQL code is optimized to handle the 1.13 billion LIDAR samples more efficiently.

insert into aerial_analysis.rtk_las_beam

(elevation, distance, trgid, demid

( select z(dem.shape) as elevation,

distance(dem.shape, m.shape),

m.name as rgid, dem.las_id as demid,

from

aerial.nssda_z as m,

aerial.las_data as dem

where

expand(m.shape,30) && dem.shape and

dem.asprsclass = 2

);

update aerial_analysis.rtk_las_beam set status = 1

where

status is null and

distance <= ( select max(distance)

from aerial_analysis.rtk_las_beam rb

where

rb.rgid = rtk_las_beam.rgid and

);

update aerial.nssda_z set las_z = l.elevation

las_model = 'nearest_sample'

from

aerial_analysis.rtk_las_beam l

where

l.rgid = nssda_z.name and

l.status = 1

;

Comparison of Field Collection Methods

Using the Contour modeling methods to evaluate the 95% percentile for each of the field collection methods.  RTK is GPS Real-Time Kinetic,  TS is Total Station (theodolite), ES is generic “Engineering Grade” survey methods.

| ERROR | ES Samples | ES percentile | RTK Samples | RTK Percentile | TS Samples | TS Percentile |
| --- | --- | --- | --- | --- | --- | --- |
| > 12.0 | 1 | 100.00% | 3 | 100.00% | 3 | 100.00% |
| 11.5 – 12.0 | 1 | 99.64% | 0 | 99.96% | 0 | 99.96% |
| 11.0 – 11.5 | 0 | 99.27% | 0 | 99.96% | 0 | 99.96% |
| 10.5 – 11.0 | 1 | 99.27% | 2 | 99.96% | 0 | 99.96% |
| 10.0 – 10.5 | 1 | 98.91% | 0 | 99.94% | 2 | 99.96% |
| 9.5 – 10.0 | 1 | 98.54% | 0 | 99.94% | 0 | 99.94% |
| 9.0 – 9.5 | 1 | 98.18% | 0 | 99.94% | 2 | 99.94% |
| 8.5 – 9.0 | 0 | 97.81% | 2 | 99.94% | 4 | 99.92% |
| 8.0 – 8.5 | 0 | 97.81% | 1 | 99.91% | 5 | 99.87% |
| 7.5 – 8.0 | 3 | 97.81% | 0 | 99.90% | 5 | 99.81% |
| 7.0 – 7.5 | 2 | 96.72% | 1 | 99.90% | 2 | 99.75% |
| 6.5 – 7.0 | 2 | 95.99% | 1 | 99.89% | 2 | 99.73% |
| 6.0 – 6.5 | 0 | 95.26% | 1 | 99.88% | 6 | 99.70% |
| 5.5 – 6.0 | 1 | 95.26% | 3 | 99.87% | 5 | 99.63% |
| 5.0 – 5.5 | 0 | 94.89% | 5 | 99.83% | 14 | 99.57% |
| 4.5 – 5.0 | 1 | 94.89% | 7 | 99.77% | 12 | 99.41% |
| 4.0 – 4.5 | 2 | 94.53% | 6 | 99.68% | 18 | 99.27% |
| 3.5 – 4.0 | 1 | 93.80% | 6 | 99.61% | 26 | 99.05% |
| 3.0 – 3.5 | 1 | 93.43% | 18 | 99.54% | 59 | 98.75% |
| 2.5 – 3.0 | 1 | 93.07% | 24 | 99.32% | 98 | 98.05% |
| 2.0 – 2.5 | 6 | 92.70% | 60 | 99.03% | 201 | 96.89% |
| 1.5 – 2.0 | 17 | 90.51% | 169 | 98.30% | 426 | 94.51% |
| 1.0 – 1.5 | 38 | 84.31% | 448 | 96.24% | 874 | 89.47% |
| 0.5 – 1.0 | 85 | 70.44% | 2117 | 90.79% | 2205 | 79.13% |
| 0 – 0.5 | 108 | 39.42% | 5343 | 65.02% | 4482 | 53.04% |
| Total Samples | 274 |  | 8217 |  | 8451 |  |
| 95th Percentile |  | 5.4 foot error |  | 1.2 foot error |  | 1.8 foot error |

Limiting the NSSDA Vertical Accuracy tests to those samples with less than a 2.0 foot error the NSSDA Accuracy would be:

contour_model     |        nssdaz_contour         |          nssdaz_dem           | count

----------------------+-------------------------------+-------------------------------+-------

linear-bivalued      | 0.976626511054772362419406520 | 1.331260992938981194797666960 | 14343

nearest-singlevalued |     1.34577690474281975235560 | 1.286149515416319844580923920 |  2057

coll_meth |    contour_model     |        nssdaz_contour         |          nssdaz_dem           | count

-----------+----------------------+-------------------------------+-------------------------------+-------

ES        | linear-bivalued      | 1.669383412637786666795222360 | 1.211161330426971765795004520 |   232

ES        | nearest-singlevalued |     1.14132321965923979590040 | 1.355264624083845809644744000 |    25

RTK       | linear-bivalued      | 0.757355652406039571534237560 | 1.062874182721703197541933720 |  7027

RTK       | nearest-singlevalued |     1.09993120585561710551880 | 1.001451427999325888726495200 |  1080

TS        | linear-bivalued      | 1.105262245298992593477399840 | 1.509535660269011952237518760 |  7084

TS        | nearest-singlevalued |     1.54442285155769292507280 | 1.491118769394401348387932480 |   952

Being conservative, the vertical NSSDA tests were limited to samples with less than a 3.0 foot error.

The average of the 95th percentiles for the three field sampling methods is 2.8 feet, and samples with larger errors can be considered erroneous.

That means that the NSSDA accuracy of the Models is certainly less than reported but at the moment cannot be confidently expressed.  Further evaluation of the manhole data for errors will be necessary to produce a more accurate number.