# VERTICAL ACCURACY ASSESSMENT

# REPORT

FOR

U.S. ARMY CORPS OF ENGINEERS

ST. LOUIS DISTRICT

CHAMPAIGN COUNTY, IL

## December 23, 2008

AERO-METRIC PROJECT NO. 1-080208

U.S. Army Corps of Engineers

St Louis District

Champaign County, Illinois

#### Vertical Accuracy Assessment Report

AERO-METRIC, INC.

4020 Technology Parkway

Sheboygan, WI 53083

AERO-METRIC Project No. 1-080208

# Background

The National Standard for Spatial Data Accuracy (NSSDA) defines guidelines for testing and reporting the accuracy of digital geospatial data.  The NSSDA makes the assumption that all errors follow a normal error distribution where Root-Mean-Square-Error (RMSE) procedures apply.  The Federal Emergency Management Agency (FEMA) guidelines implement the NSSDA standards and recommend the survey of a minimum of 20 checkpoints per ground cover category representative of the area being tested.  A minimum of three categories (60 checkpoints) is required.  The National Digital Elevation Program (NDEP) and the American Society for Photogrammetry and Remote Sensing (ASPRS) provide an alternative method for reporting the vertical accuracy whereby errors in vegetation categories are not assumed to follow a normal error distribution.  Even though the ASPRS guidelines are directly referenced to the assessment of LiDAR digital data, the same ideals can be applied to the digital elevation data collected for this project.  A minimum of 60 checkpoints is again recommended, with up to 100 points preferred.  For the Champaign County project, five major ground cover categories were defined by AERO-METRIC (AME) as representative of the project area.  The county met the checkpoint requirements of five separate major ground cover categories containing at least 20 points per category.  For one of the categories (brush), only 4 checkpoints were surveyed due to limited accessibility.  For the remaining four categories (hard surface, tall grass, brush, and woods), 20 or more checkpoints were surveyed in each of these areas.  An additional 37 temporary base station and cross section points were included making a total of 166 checkpoints over the entire project area.

AME’s vertical accuracy assessment for the Champaign County project was carried out in accordance with the two methods mentioned above.  The first method (defined by NSSDA and FEMA) assumes all errors follow a normal error distribution and the newer second method (defined by NDEP and ASPRS) assumes that errors in some land cover categories may not follow a normal error distribution.  Comparing the two methods helps determine the amount of systematic errors that may exist in the five ground cover categories: hard surface, short grass, tall grass, brush, and woods.  The following table summarizes the criteria used to evaluate the vertical data.  Criteria highlighted in yellow refer to the NSSDA and FEMA guidelines and those highlighted in orange refer to the NDEP and ASPRS guidelines.

Table 1 -- DTM Acceptance Criteria

| Criteria | Acceptable Value |
| --- | --- |
| RMSEz= NSSDA vertical accuracy statistic at 68% confidence level (1.0 x RMSEz) | 0.60 ft for all ground cover categories combined |
| Accuracyz= NSSDA vertical accuracy statistic at the 95% confidence level (1.96 x RMSEz) | 1.19 ft (RMSEz x 1.9600) for all ground cover categories combined |
| Fundamental Vertical Accuracy (FVA) in open terrain only = 95% confidence level | 1.19 ft (RMSEz x 1.9600) for open terrain only |
| Supplemental Vertical Accuracy (SVA) in individual ground cover categories = 95% confidence level | 1.19 ft (based on 95th percentile per category; this is a target value only, not mandatory) |
| Consolidated Vertical Accuracy (CVA) in all ground cover categories combined = 95% confidence level | 1.19 ft (based on combined 95th percentile) |

AME tested the digital vertical data using the following steps:

- AME ground survey personnel collected and processed GPS data for each of the ground cover checkpoints.  These points were distributed throughout ground cover category areas within the Champaign County project limits.

- The checkpoints were compared to the digital vertical data using the TerraSolid, LTD program TerraScan.  The program creates a TIN surface from the digital vertical data and computes vertical differences between the surface and the surveyed checkpoints.  An output file records the vertical differences and associated statistics.  Files were created for each of the ground cover categories separately and one file for all categories combined.

- The results were analyzed by AME to assess the quality of the data.  Various accuracy parameters as defined by the NDEP and ASPRS guidelines were used in the review process.  Also, the overall descriptive statistics of each dataset were computed to assess any tendencies or inconsistencies.  The following tables, graphs, and figures illustrate the data quality.

Using the NDEP and ASPRS Guidelines for Vertical Accuracy Testing

The required Fundamental Vertical Accuracy (FVA) and the optional Supplemental Vertical Accuracy (SVA) and Consolidated Vertical Accuracy (CVA) are specified by the NDEP and ASPRS guidelines.  FVA determines how well the digital data was collected in open terrain type ground cover where all errors are presumed to be random.  The SVA determines how well the digital data represents the actual ground in each of the ground cover categories, tested separately.  The CVA determines the overall accuracy of all the ground categories combined as one test.

FVA for this project is calculated using only the checkpoints in the Hard Surface ground cover category.  The digital data in this category is most likely to represent the actual ground surface and the random errors will follow a normal error distribution.  The FVA shows how well the Photogrammetric process used to produce the digital vertical data represents the actual ground.  With a normal error distribution, the vertical accuracy at the 95% confidence level is computed as the vertical root mean square error (RMSEz) of the checkpoints x 1.9600, as specified in Appendix 3-A of the NSSDA guidelines.  As shown in Table 1, the maximum allowable FVA for this project (2 ft contours) is 1.19 ft.

CVA is calculated with all the checkpoints in all the ground cover categories combined plus the 19 cross section points.  There is a possibility that the digital vertical data may yield errors that do not follow a normal distribution.  CVA at the 95% confidence level equals the 95th percentile error for all checkpoints in all ground cover categories combined.  The CVA produces a listing of the 5% outliers that are larger than the 95th percentile and that may not follow the normal error distribution.

SVA is computed for each ground cover category separately.  There again is a possibility that the digital vertical data may yield errors that do not follow a normal error distribution.  Systematic errors per ground cover category are identified.  For each category, the SVA at the 95% confidence level equals the 95th percentile error for all checkpoints in each individual ground cover category.  The individual SVA statistics are used to analyze the data based on each of the ground cover categories.

Table 2 summarizes the vertical accuracy by Fundament, Consolidated, and Supplemental methods:

Table 2 – FVA, CVA, and SVA Vertical Accuracy at 95% Confidence Level

| Ground Cover Category | # of Points | FVA Fundamental Vertical Accuracy Spec = 1.19 ft | CVA Consolidated Vertical Accuracy Spec = 1.19 ft | SVA Supplemental Vertical Accuracy Target = 1.19 ft |
| --- | --- | --- | --- | --- |
| Total Combined | 166 |  | 0.67 ft |  |
| Hard Surface | 35 | 0.63 ft |  | 0.71 ft |
| Short Grass | 38 |  |  | 0.63 ft |
| Tall Grass | 30 |  |  | 0.63 ft |
| Brush | 4 |  |  | 0.56 ft |
| Woods | 22 |  |  | 0.62 ft |

The digital vertical data for the Champaign County project meets all mandatory and target specifications as per the following vertical accuracy tests:

Compared with the 1.19 ft FVA specification, FVA tested 0.63 ft at the 95% confidence level on the hard surfaces ground cover category, based on RMSEz x 1.9600.  The NSSDA specifies that vertical accuracy at the 95% confidence level equals RMSEz x 1.9600; the NDEP and ASPRS state that this method is valid only when random errors follow a normal error distribution, as in the hard surface category.

Compared with the 1.19 ft CVA specification, CVA tested 0.67 ft at the 95% confidence level on the hard surfaces, short grass, tall grass, brush, and woods ground cover categories combined, based on the 95th Percentile.  NDEP and ASPRS guidelines specify that vertical accuracy at the 95% confidence level equals the 95th percentile when random errors may not follow a normal error distribution, as in vegetated or obstructed areas.  Table 3 lists the 5% outliers larger than the 95th percentile (0.67ft).

Table 3 – 5% Outliers Larger than 95th Percentile

| Ground Cover Category | Elev. Diff (ft) | None of the errors were larger than the CVA standard (1.19ft) which permits up to 5% of the checkpoints, 8 out of 166, to be larger than 1.19 ft. |
| --- | --- | --- |
| Hard Surface | 0.83 |  |
| Hard Surface | 0.74 |  |
| Hard Surface | 0.69 |  |
| Short Grass | 0.68 |  |
| Short Grass | 0.68 |  |
| Tall Grass | 0.70 |  |
| Tall Grass | 0.73 |  |

Compared with the 1.19 ft SVA target values, SVA tested 0.71 ft at the 95% confidence level on hard surfaces; 0.63 ft in short grass; 0.63 ft in tall grass; 0.56 ft in brush; and 0.62 ft in woods ground cover categories, based on the 95th Percentile.  These values exceed all of their target values (1.19 ft).

Figure 1 illustrates the SVA by specific ground cover category.  Figure 2 illustrates the magnitude of the differences between the checkpoints and the digital vertical data by specific ground cover category and sorted from lowest to highest.  All of the checkpoints are within the 1.19 ft criteria shown in figure 2.  This exceeds the 95% requirement, where up to five checkpoints could be outside the 1.19 ft criteria.

Figure 1 -- Graph of SVA Values by Ground Cover Category

Figure 2 – Magnitude of Elevation Discrepancies, Sorted from Largest Negative to Largest Positive

Vertical Accuracy Testing in Accordance with NSSDA and FEMA Procedures

The NSSDA and FEMA guidelines were both published before it was recognized that digital data errors do not always follow a normal error distribution.  Future changes to these guidelines are expected to follow those of the NDEP and ASPRS.  In order to comply with FEMA’s current requirements, RMSEz and other statistics were computed in all five ground cover categories, individually and combined.  These statistics are shown in Figures 3 and 4 and Table 4 below.

Figure 3 shows the RMSEz values as calculated for each ground cover category separately.

Figure 3 – RMSEz statistics by Ground Cover Category

Table 4 – Overall Descriptive Statistics by Ground Cover Category

| Land Cover Category | RMSEz (ft) | Mean (ft) | Median (ft) | Skew | Std Dev (ft) | # of Points | Min (ft) | Max (ft) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Consolidated | 0.33 | 0.10 | 0.09 | -0.36 | 0.31 | 166 | -0.83 | 1.03 |
| Hard Surface | 0.32 | -0.01 | 0.03 | -0.53 | 0.33 | 35 | -0.83 | 0.74 |
| Short Grass | 0.32 | 0.11 | 0.11 | -0.28 | 0.30 | 38 | -0.68 | 0.68 |
| Tall Grass | 0.31 | 0.08 | 0.10 | -0.81 | 0.31 | 30 | -0.73 | 0.70 |
| Brush | 0.35 | -0.04 | 0.06 | -1.21 | 0.41 | 4 | -0.61 | 0.33 |
| Woods | 0.35 | 0.17 | 0.24 | -0.77 | 0.32 | 22 | -0.59 | 0.63 |

Figure 4 shows a histogram of the elevation differences between the field surveyed checkpoints and the TIN surface computed from the digital vertical data.  The histogram shows the number of occurrences (frequency) along the vertical axis that fell within the 0.20 ft ranges shown along the horizontal axis.

Figure 4 – Histogram of Elevation Discrepancies within 0.2 ft bands

Summary and Conclusions

The vertical accuracy testing methods derived from the NSSDA/FEMA and NDEP/ASPRS guidelines, when applied to the Champaign County project, verify that the digital vertical data provided by AME is well suited for the production of 2 ft contours.

Per NSSDA/FEMA guidelines:  RMSEz x 1.9600 = 95% confidence level

0.33 x 1.9600 = 0.65 ft

Per NDEP/ASPRS guidelines:  95th percentile (CVA) = 95% confidence level

= 0.67 ft

Both of the 95% confidence level test results exceed the required 1.19 ft accuracy level to support the generation of 2 ft contours.

# Endnotes

Part 3: National Standards for Spatial Data Accuracy (NSSDA), “Geospatial Positioning Accuracy Standards,” published by the Federal Geographic Data Committee (FGDC), 1998

Appendix A, Guidance for Aerial Mapping and Surveying, “Guidelines and Specifications for Flood Hazard Mapping Partners,” published by the Federal Emergency Management Agency (FEMA), April 2003

Guidelines for Digital Elevation Data, Version 1.0, published by the National Digital Elevation Program (NDEP), May 2004

ASPRS Guidelines, Vertical Accuracy Reporting for Lidar Data, published by the American Society for Photogrammetry and Remote Sensing (ASPRS), May 2004

APPENDIX

Quality Control Report (All Check Points)

O:\1080208\Lidar\QC\Champaign\Champaign_All.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

100              1013914.987  1322141.221   732.800   733.020    +0.220

106              1023197.596  1319022.378   757.518   757.800    +0.282

111              1028496.975  1322238.202   754.310   755.050    +0.740

116              1023141.034  1327783.690   728.762   729.100    +0.338

118              1047813.643  1186363.060   672.479   672.160    -0.319

121              1048626.266  1180892.067   680.248   679.580    -0.668

123              1053881.091  1186148.494   665.730   665.040    -0.690

127              1053873.716  1188248.250   668.571   668.090    -0.481

128              1048586.810  1190658.452   664.851   664.020    -0.831

133              1043634.671  1186267.742   680.097   679.950    -0.147

136              1043211.552  1186118.625   680.415   680.490    +0.075

141              1000758.281  1181028.146   715.291   714.980    -0.311

146               992562.273  1175211.659   686.065   686.470    +0.405

149               997740.380  1175194.011   696.964   697.060    +0.096

152              1000255.995  1175179.533   707.056   706.850    -0.206

153               995648.507  1175729.355   691.075   691.220    +0.145

160               995374.161  1182930.239   694.926   694.810    -0.116

163               995575.181  1179859.553   697.190   697.050    -0.140

164               991062.221  1332526.144   722.522   722.750    +0.228

168               988153.962  1332518.555   706.892   706.720    -0.172

172               985699.666  1337813.509   722.184   722.450    +0.266

175               979679.356  1332447.552   721.052   721.230    +0.178

180              1080357.633  1338704.691   725.268   725.380    +0.112

183              1080142.124  1347232.594   732.643   732.490    -0.153

184              1080239.647  1343839.891   728.027   728.060    +0.033

187              1079056.648  1338725.676   731.888   731.890    +0.002

191              1073588.890  1338692.782   759.132   758.980    -0.152

195              1085777.966  1338692.241   722.594   722.690    +0.096

199              1080481.369  1334489.687   731.783   731.870    +0.087

203              1083025.911  1293465.573   714.976   715.350    +0.374

204              1083043.949  1293451.327   714.730   715.050    +0.320

207              1078871.838  1292092.511   685.445   685.420    -0.025

209              1074601.693  1292645.528   676.436   676.380    -0.056

213              1076863.588  1298488.138   705.960   705.930    -0.030

214              1077843.628  1301388.424   769.943   770.020    +0.077

101              1013990.915  1322117.169   731.055   731.130    +0.075

105              1023142.537  1319099.859   757.968   758.590    +0.622

110              1028531.030  1321936.838   750.884   751.110    +0.226

112              1028551.283  1322241.532   752.285   752.820    +0.535

113              1023093.886  1327720.271   727.308   727.840    +0.532

122              1053811.862  1186163.835   665.481   665.070    -0.411

126              1053858.558  1188304.530   667.420   667.730    +0.310

131              1048598.037  1190817.845   665.596   664.920    -0.676

135              1043627.791  1186297.250   680.763   680.420    -0.343

137              1043187.759  1186128.359   680.022   679.860    -0.162

140              1000698.343  1181068.901   711.262   711.010    -0.252

147               992598.310  1175193.227   685.556   685.950    +0.394

150               997836.810  1175215.399   696.114   696.350    +0.236

157               995509.761  1175783.626   687.764   687.610    -0.154

158               995447.297  1182895.902   693.253   693.070    -0.183

167               991079.796  1332375.731   722.761   722.890    +0.129

171               988149.887  1332492.663   706.534   706.460    -0.074

174               985840.915  1337787.974   721.340   721.610    +0.270

178               979733.615  1332385.432   718.758   718.930    +0.172

181              1080315.454  1338740.302   726.104   726.270    +0.166

182              1080406.606  1338679.727   722.728   722.820    +0.092

186              1080221.127  1343791.518   726.127   726.220    +0.093

190              1078860.930  1338702.877   728.791   728.760    -0.031

192              1073634.736  1338718.871   758.808   758.860    +0.052

198              1085755.620  1338724.199   721.931   722.190    +0.259

202              1080462.406  1334426.383   729.546   729.620    +0.074

206              1081800.425  1292149.597   692.059   692.090    +0.031

210              1074658.031  1292600.761   676.816   676.830    +0.014

1                1027045.679  1217947.308   687.246   687.790    +0.544

2                1047828.370  1186336.033   672.384   672.120    -0.264

3                 983075.993  1332541.718   716.150   716.150    +0.000

4                1080653.288  1338625.768   723.319   723.470    +0.151

5                1027019.055  1325592.769   760.943   761.620    +0.677

6                1078865.264  1296008.448   704.880   704.690    -0.190

231               977954.812  1297658.143   705.891   706.370    +0.479

232              1028612.008  1314487.719   735.852   736.010    +0.158

240               980518.334  1318506.139   705.783   706.170    +0.387

241               980588.875  1300960.167   710.776   711.170    +0.394

103              1013910.498  1322162.625   732.968   733.040    +0.072

107              1023175.221  1319039.147   758.266   758.660    +0.394

109              1028471.788  1321820.040   750.704   750.990    +0.286

114              1023178.817  1327739.169   726.291   726.990    +0.699

117              1023181.297  1327863.516   727.397   727.730    +0.333

119              1048657.155  1180860.988   679.057   678.560    -0.497

124              1053918.040  1186116.332   663.785   663.250    -0.535

125              1053848.342  1188419.962   664.169   664.310    +0.141

129              1048607.985  1190640.719   663.870   663.140    -0.730

132              1043715.317  1186303.753   679.723   679.410    -0.313

139              1043215.381  1185949.104   678.184   678.030    -0.154

142              1000800.367  1181033.750   711.373   711.190    -0.183

144               992472.562  1175188.020   684.910   685.270    +0.360

148               997774.881  1175218.493   696.324   696.700    +0.376

154               995603.173  1175789.518   688.499   688.550    +0.051

161               995327.563  1182996.578   691.895   691.810    -0.085

162               995523.396  1179831.853   693.102   693.160    +0.058

166               991090.387  1332553.608   720.310   720.730    +0.420

170               988188.736  1332549.113   705.655   705.760    +0.105

173               985587.051  1337831.376   720.008   720.280    +0.272

177               979663.592  1332480.435   719.877   720.230    +0.353

185              1080206.353  1343872.932   726.619   726.800    +0.181

188              1079156.011  1338746.656   732.462   732.490    +0.028

193              1073845.566  1338669.514   750.730   750.820    +0.090

197              1085684.643  1338722.027   722.600   722.700    +0.100

201              1080504.883  1334568.171   731.603   731.630    +0.027

205              1081712.289  1292114.263   691.685   691.810    +0.125

208              1078937.432  1292121.044   685.681   685.730    +0.049

211              1074521.834  1292624.701   674.969   675.050    +0.081

218              1077627.753  1301353.782   767.262   767.610    +0.348

102              1013923.248  1322117.654   732.892   732.980    +0.088

104              1023199.676  1319107.916   758.519   759.140    +0.621

108              1028473.599  1321750.719   750.694   751.010    +0.316

115              1023036.054  1327797.341   729.270   729.660    +0.390

130              1048602.424  1190753.088   664.746   664.160    -0.586

134              1043728.254  1186238.326   680.054   679.750    -0.304

138              1043200.079  1186152.437   680.494   680.090    -0.404

143              1000803.678  1181007.776   711.249   711.200    -0.049

145               992522.782  1175189.677   685.012   685.490    +0.478

151               998188.535  1175199.936   698.037   698.200    +0.163

159               995431.651  1182913.661   692.823   692.750    -0.073

165               991083.192  1332487.863   722.079   722.320    +0.241

169               988086.305  1332466.446   705.980   705.900    -0.080

176               979650.501  1332413.762   719.707   719.950    +0.243

189              1078889.378  1338684.009   728.381   728.620    +0.239

194              1073905.575  1338677.559   749.592   749.680    +0.088

196              1085751.040  1338740.508   722.236   722.620    +0.384

200              1080468.515  1334510.313   731.498   732.130    +0.632

212              1076884.103  1298452.849   704.264   704.500    +0.236

215              1077804.344  1301417.053   767.771   767.940    +0.169

216              1077713.970  1301411.623   766.098   766.500    +0.402

217              1077606.979  1301420.865   764.552   765.030    +0.478

120              1048592.430  1180866.490   679.175   678.570    -0.605

155               995567.700  1175706.231   687.751   687.910    +0.159

156               995560.824  1175605.247   687.453   687.410    -0.043

179              1080638.183  1338591.601   723.650   723.980    +0.330

300              1023581.424  1322238.924   765.277   765.650    +0.373

301              1023581.627  1322231.329   765.205   765.180    -0.025

302              1023581.693  1322226.558   763.883   764.390    +0.507

303              1023581.539  1322220.722   764.483   764.970    +0.487

304              1023581.381  1322211.529   764.897   765.540    +0.643

305              1023581.040  1322202.474   764.332   764.820    +0.488

306              1023581.030  1322193.737   763.155   764.180    +1.025

307              1023581.339  1322187.523   764.933   765.040    +0.107

400               995486.474  1179798.546   693.663   693.590    -0.073

401               995507.517  1179792.276   693.053   693.090    +0.037

402               995522.254  1179786.735   693.102   693.100    -0.002

403               995538.695  1179780.885   696.537   696.420    -0.117

404               995546.441  1179778.316   696.646   696.630    -0.016

405               995569.922  1179770.862   694.772   694.620    -0.152

406               995576.421  1179768.684   694.592   694.620    +0.028

407               995585.706  1179766.079   692.171   692.650    +0.479

408               995599.275  1179762.588   692.610   692.670    +0.060

500              1080323.082  1339136.853   730.458   730.770    +0.312

501              1080327.419  1339136.620   729.270   729.740    +0.470

502              1080329.444  1339136.774   729.070   729.740    +0.670

503              1080334.529  1339137.033   729.985   730.220    +0.235

504              1080339.867  1339137.148   730.579   730.810    +0.231

505              1080346.947  1339137.345   730.845   730.910    +0.065

506              1080354.430  1339137.174   730.320   730.380    +0.060

507              1080362.147  1339137.154   728.942   729.390    +0.448

508              1080367.524  1339137.013   729.424   729.340    -0.084

509              1080373.200  1339137.263   729.290   729.420    +0.130

600              1078837.750  1294576.620   700.855   700.810    -0.045

601              1078842.055  1294576.597   700.008   699.940    -0.068

602              1078844.991  1294576.751   699.408   699.700    +0.292

603              1078850.375  1294577.240   699.841   700.210    +0.369

604              1078852.485  1294577.434   700.415   700.390    -0.025

605              1078862.107  1294577.408   701.055   701.010    -0.045

606              1078871.661  1294577.099   700.619   700.650    +0.031

607              1078875.733  1294576.728   700.159   700.110    -0.049

608              1078882.035  1294576.922   699.293   699.510    +0.217

609              1078888.571  1294576.935   700.533   700.480    -0.053

Average dz           +0.105

Minimum dz           -0.831

Maximum dz           +1.025

Average magnitude     0.253

Root mean square      0.326

Std deviation         0.309

Quality Control Report ( Hard-Surface Check Points )

O:\1080208\Lidar\QC\Champaign\Champaign_Hard_Surface.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

100              1013914.987  1322141.221   732.800   733.020    +0.220

106              1023197.596  1319022.378   757.518   757.800    +0.282

111              1028496.975  1322238.202   754.310   755.050    +0.740

116              1023141.034  1327783.690   728.762   729.100    +0.338

118              1047813.643  1186363.060   672.479   672.160    -0.319

121              1048626.266  1180892.067   680.248   679.580    -0.668

123              1053881.091  1186148.494   665.730   665.040    -0.690

127              1053873.716  1188248.250   668.571   668.090    -0.481

128              1048586.810  1190658.452   664.851   664.020    -0.831

133              1043634.671  1186267.742   680.097   679.950    -0.147

136              1043211.552  1186118.625   680.415   680.490    +0.075

141              1000758.281  1181028.146   715.291   714.980    -0.311

146               992562.273  1175211.659   686.065   686.470    +0.405

149               997740.380  1175194.011   696.964   697.060    +0.096

152              1000255.995  1175179.533   707.056   706.850    -0.206

153               995648.507  1175729.355   691.075   691.220    +0.145

160               995374.161  1182930.239   694.926   694.810    -0.116

163               995575.181  1179859.553   697.190   697.050    -0.140

164               991062.221  1332526.144   722.522   722.750    +0.228

168               988153.962  1332518.555   706.892   706.720    -0.172

172               985699.666  1337813.509   722.184   722.450    +0.266

175               979679.356  1332447.552   721.052   721.230    +0.178

180              1080357.633  1338704.691   725.268   725.380    +0.112

183              1080142.124  1347232.594   732.643   732.490    -0.153

184              1080239.647  1343839.891   728.027   728.060    +0.033

187              1079056.648  1338725.676   731.888   731.890    +0.002

191              1073588.890  1338692.782   759.132   758.980    -0.152

195              1085777.966  1338692.241   722.594   722.690    +0.096

199              1080481.369  1334489.687   731.783   731.870    +0.087

203              1083025.911  1293465.573   714.976   715.350    +0.374

204              1083043.949  1293451.327   714.730   715.050    +0.320

207              1078871.838  1292092.511   685.445   685.420    -0.025

209              1074601.693  1292645.528   676.436   676.380    -0.056

213              1076863.588  1298488.138   705.960   705.930    -0.030

214              1077843.628  1301388.424   769.943   770.020    +0.077

Average dz           -0.001

Minimum dz           -0.831

Maximum dz           +0.740

Average magnitude     0.243

Root mean square      0.321

Std deviation         0.326

Quality Control Report ( Short Grass Check Points )

O:\1080208\Lidar\QC\Champaign\Champaign_Short_Grass.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

101              1013990.915  1322117.169   731.055   731.130    +0.075

105              1023142.537  1319099.859   757.968   758.590    +0.622

110              1028531.030  1321936.838   750.884   751.110    +0.226

112              1028551.283  1322241.532   752.285   752.820    +0.535

113              1023093.886  1327720.271   727.308   727.840    +0.532

122              1053811.862  1186163.835   665.481   665.070    -0.411

126              1053858.558  1188304.530   667.420   667.730    +0.310

131              1048598.037  1190817.845   665.596   664.920    -0.676

135              1043627.791  1186297.250   680.763   680.420    -0.343

137              1043187.759  1186128.359   680.022   679.860    -0.162

140              1000698.343  1181068.901   711.262   711.010    -0.252

147               992598.310  1175193.227   685.556   685.950    +0.394

150               997836.810  1175215.399   696.114   696.350    +0.236

157               995509.761  1175783.626   687.764   687.610    -0.154

158               995447.297  1182895.902   693.253   693.070    -0.183

167               991079.796  1332375.731   722.761   722.890    +0.129

171               988149.887  1332492.663   706.534   706.460    -0.074

174               985840.915  1337787.974   721.340   721.610    +0.270

178               979733.615  1332385.432   718.758   718.930    +0.172

181              1080315.454  1338740.302   726.104   726.270    +0.166

182              1080406.606  1338679.727   722.728   722.820    +0.092

186              1080221.127  1343791.518   726.127   726.220    +0.093

190              1078860.930  1338702.877   728.791   728.760    -0.031

192              1073634.736  1338718.871   758.808   758.860    +0.052

198              1085755.620  1338724.199   721.931   722.190    +0.259

202              1080462.406  1334426.383   729.546   729.620    +0.074

206              1081800.425  1292149.597   692.059   692.090    +0.031

210              1074658.031  1292600.761   676.816   676.830    +0.014

1                1027045.679  1217947.308   687.246   687.790    +0.544

2                1047828.370  1186336.033   672.384   672.120    -0.264

3                 983075.993  1332541.718   716.150   716.150    +0.000

4                1080653.288  1338625.768   723.319   723.470    +0.151

5                1027019.055  1325592.769   760.943   761.620    +0.677

6                1078865.264  1296008.448   704.880   704.690    -0.190

231               977954.812  1297658.143   705.891   706.370    +0.479

232              1028612.008  1314487.719   735.852   736.010    +0.158

240               980518.334  1318506.139   705.783   706.170    +0.387

241               980588.875  1300960.167   710.776   711.170    +0.394

Average dz           +0.114

Minimum dz           -0.676

Maximum dz           +0.677

Average magnitude     0.258

Root mean square      0.320

Std deviation         0.303

Quality Control Report ( Tall Grass Check Points )

O:\1080208\Lidar\QC\Champaign\Champaign_Tall_Grass.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

103              1013910.498  1322162.625   732.968   733.040    +0.072

107              1023175.221  1319039.147   758.266   758.660    +0.394

109              1028471.788  1321820.040   750.704   750.990    +0.286

114              1023178.817  1327739.169   726.291   726.990    +0.699

117              1023181.297  1327863.516   727.397   727.730    +0.333

119              1048657.155  1180860.988   679.057   678.560    -0.497

124              1053918.040  1186116.332   663.785   663.250    -0.535

125              1053848.342  1188419.962   664.169   664.310    +0.141

129              1048607.985  1190640.719   663.870   663.140    -0.730

132              1043715.317  1186303.753   679.723   679.410    -0.313

139              1043215.381  1185949.104   678.184   678.030    -0.154

142              1000800.367  1181033.750   711.373   711.190    -0.183

144               992472.562  1175188.020   684.910   685.270    +0.360

148               997774.881  1175218.493   696.324   696.700    +0.376

154               995603.173  1175789.518   688.499   688.550    +0.051

161               995327.563  1182996.578   691.895   691.810    -0.085

162               995523.396  1179831.853   693.102   693.160    +0.058

166               991090.387  1332553.608   720.310   720.730    +0.420

170               988188.736  1332549.113   705.655   705.760    +0.105

173               985587.051  1337831.376   720.008   720.280    +0.272

177               979663.592  1332480.435   719.877   720.230    +0.353

185              1080206.353  1343872.932   726.619   726.800    +0.181

188              1079156.011  1338746.656   732.462   732.490    +0.028

193              1073845.566  1338669.514   750.730   750.820    +0.090

197              1085684.643  1338722.027   722.600   722.700    +0.100

201              1080504.883  1334568.171   731.603   731.630    +0.027

205              1081712.289  1292114.263   691.685   691.810    +0.125

208              1078937.432  1292121.044   685.681   685.730    +0.049

211              1074521.834  1292624.701   674.969   675.050    +0.081

218              1077627.753  1301353.782   767.262   767.610    +0.348

Average dz           +0.082

Minimum dz           -0.730

Maximum dz           +0.699

Average magnitude     0.248

Root mean square      0.314

Std deviation         0.308

Quality Control Report ( Brush Check Points )

O:\1080208\Lidar\QC\Champaign\Champaign_Brush.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

120              1048592.430  1180866.490   679.175   678.570    -0.605

155               995567.700  1175706.231   687.751   687.910    +0.159

156               995560.824  1175605.247   687.453   687.410    -0.043

179              1080638.183  1338591.601   723.650   723.980    +0.330

Average dz           -0.040

Minimum dz           -0.605

Maximum dz           +0.330

Average magnitude     0.284

Root mean square      0.354

Std deviation         0.407

Quality Control Report ( Trees Check Points )

O:\1080208\Lidar\QC\Champaign\Champaign_Trees_Forest.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

102              1013923.248  1322117.654   732.892   732.980    +0.088

104              1023199.676  1319107.916   758.519   759.140    +0.621

108              1028473.599  1321750.719   750.694   751.010    +0.316

115              1023036.054  1327797.341   729.270   729.660    +0.390

130              1048602.424  1190753.088   664.746   664.160    -0.586

134              1043728.254  1186238.326   680.054   679.750    -0.304

138              1043200.079  1186152.437   680.494   680.090    -0.404

143              1000803.678  1181007.776   711.249   711.200    -0.049

145               992522.782  1175189.677   685.012   685.490    +0.478

151               998188.535  1175199.936   698.037   698.200    +0.163

159               995431.651  1182913.661   692.823   692.750    -0.073

165               991083.192  1332487.863   722.079   722.320    +0.241

169               988086.305  1332466.446   705.980   705.900    -0.080

176               979650.501  1332413.762   719.707   719.950    +0.243

189              1078889.378  1338684.009   728.381   728.620    +0.239

194              1073905.575  1338677.559   749.592   749.680    +0.088

196              1085751.040  1338740.508   722.236   722.620    +0.384

200              1080468.515  1334510.313   731.498   732.130    +0.632

212              1076884.103  1298452.849   704.264   704.500    +0.236

215              1077804.344  1301417.053   767.771   767.940    +0.169

216              1077713.970  1301411.623   766.098   766.500    +0.402

217              1077606.979  1301420.865   764.552   765.030    +0.478

Average dz           +0.167

Minimum dz           -0.586

Maximum dz           +0.632

Average magnitude     0.303

Root mean square      0.351

Std deviation         0.317