# VERTICAL ACCURACY ASSESSMENT

# REPORT

FOR

U.S. ARMY CORPS OF ENGINEERS

ST. LOUIS DISTRICT

McHENRY COUNTY, IL

## December 12, 2008

AERO-METRIC PROJECT NO. 1-080208

U.S. Army Corps of Engineers

St Louis District

McHenry County, Illinois

#### Vertical Accuracy Assessment Report

AERO-METRIC, INC.

4020 Technology Parkway

Sheboygan, WI 53083

AERO-METRIC Project No. 1-080208

# Background

The National Standard for Spatial Data Accuracy (NSSDA) defines guidelines for testing and reporting the accuracy of digital geospatial data.  The NSSDA makes the assumption that all errors follow a normal error distribution where Root-Mean-Square-Error (RMSE) procedures apply.  The Federal Emergency Management Agency (FEMA) guidelines implement the NSSDA standards and recommend the survey of a minimum of 20 checkpoints per ground cover category representative of the area being tested.  A minimum of three categories (60 checkpoints) is required.  The National Digital Elevation Program (NDEP) and the American Society for Photogrammetry and Remote Sensing (ASPRS) provide an alternative method for reporting the vertical accuracy whereby errors in vegetation categories are not assumed to follow a normal error distribution.  Even though the ASPRS guidelines are directly referenced to the assessment of LiDAR digital data, the same ideals can be applied to the digital elevation data collected for this project.  A minimum of 60 checkpoints is again recommended, with up to 100 points preferred.  For the McHenry County project, five major ground cover categories were defined by AERO-METRIC (AME) as representative of the project area.  Each county met the checkpoint requirements of five separate major ground cover categories containing at least 20 points per category.  For one of the categories (short grass), only 16 checkpoints were surveyed due to limited accessibility.  For the remaining four categories (hard surface, tall grass, brush, and woods), 20 or more checkpoints were surveyed in each of these areas.  An additional 19 cross section points were included making a total of 126 checkpoints over the entire project area.

AME’s vertical accuracy assessment for the McHenry County project was carried out in accordance with the two methods mentioned above.  The first method (defined by NSSDA and FEMA) assumes all errors follow a normal error distribution and the newer second method (defined by NDEP and ASPRS) assumes that errors in some land cover categories may not follow a normal error distribution.  Comparing the two methods helps determine the amount of systematic errors that may exist in the five ground cover categories: hard surface, short grass, tall grass, brush, and woods.  The following table summarizes the criteria used to evaluate the vertical data.  Criteria highlighted in yellow refer to the NSSDA and FEMA guidelines and those highlighted in orange refer to the NDEP and ASPRS guidelines.

Table 1 -- DTM Acceptance Criteria

| Criteria | Acceptable Value |
| --- | --- |
| RMSEz= NSSDA vertical accuracy statistic at 68% confidence level (1.0 x RMSEz) | 0.60 ft for all ground cover categories combined |
| Accuracyz= NSSDA vertical accuracy statistic at the 95% confidence level (1.96 x RMSEz) | 1.19 ft (RMSEz x 1.9600) for all ground cover categories combined |
| Fundamental Vertical Accuracy (FVA) in open terrain only = 95% confidence level | 1.19 ft (RMSEz x 1.9600) for open terrain only |
| Supplemental Vertical Accuracy (SVA) in individual ground cover categories = 95% confidence level | 1.19 ft (based on 95th percentile per category; this is a target value only, not mandatory) |
| Consolidated Vertical Accuracy (CVA) in all ground cover categories combined = 95% confidence level | 1.19 ft (based on combined 95th percentile) |

AME tested the digital vertical data using the following steps:

- AME ground survey personnel collected and processed GPS data for each of the ground cover checkpoints.  These points were distributed throughout ground cover category areas within the McHenry County project limits.

- The checkpoints were compared to the digital vertical data using the TerraSolid, LTD program TerraScan.  The program creates a TIN surface from the digital vertical data and computes vertical differences between the surface and the surveyed checkpoints.  An output file records the vertical differences and associated statistics.  Files were created for each of the ground cover categories separately and one file for all categories combined.

- The results were analyzed by AME to assess the quality of the data.  Various accuracy parameters as defined by the NDEP and ASPRS guidelines were used in the review process.  Also, the overall descriptive statistics of each dataset were computed to assess any tendencies or inconsistencies.  The following tables, graphs, and figures illustrate the data quality.

Using the NDEP and ASPRS Guidelines for Vertical Accuracy Testing

The required Fundamental Vertical Accuracy (FVA) and the optional Supplemental Vertical Accuracy (SVA) and Consolidated Vertical Accuracy (CVA) are specified by the NDEP and ASPRS guidelines.  FVA determines how well the digital data was collected in open terrain type ground cover where all errors are presumed to be random.  The SVA determines how well the digital data represents the actual ground in each of the ground cover categories, tested separately.  The CVA determines the overall accuracy of all the ground categories combined as one test.

FVA for this project is calculated using only the checkpoints in the Hard Surface ground cover category.  The digital data in this category is most likely to represent the actual ground surface and the random errors will follow a normal error distribution.  The FVA shows how well the Photogrammetric process used to produce the digital vertical data represents the actual ground.  With a normal error distribution, the vertical accuracy at the 95% confidence level is computed as the vertical root mean square error (RMSEz) of the checkpoints x 1.9600, as specified in Appendix 3-A of the NSSDA guidelines.  As shown in Table 1, the maximum allowable FVA for this project (2 ft contours) is 1.19 ft.

CVA is calculated with all the checkpoints in all the ground cover categories combined plus the 19 cross section points.  There is a possibility that the digital vertical data may yield errors that do not follow a normal distribution.  CVA at the 95% confidence level equals the 95th percentile error for all checkpoints in all ground cover categories combined.  The CVA produces a listing of the 5% outliers that are larger than the 95th percentile and that may not follow the normal error distribution.

SVA is computed for each ground cover category separately.  There again is a possibility that the digital vertical data may yield errors that do not follow a normal error distribution.  Systematic errors per ground cover category are identified.  For each category, the SVA at the 95% confidence level equals the 95th percentile error for all checkpoints in each individual ground cover category.  The individual SVA statistics are used to analyze the data based on each of the ground cover categories.

Table 2 summarizes the vertical accuracy by Fundament, Consolidated, and Supplemental methods:

Table 2 – FVA, CVA, and SVA Vertical Accuracy at 95% Confidence Level

| Ground Cover Category | # of Points | FVA Fundamental Vertical Accuracy Spec = 1.19 ft | CVA Consolidated Vertical Accuracy Spec = 1.19 ft | SVA Supplemental Vertical Accuracy Target = 1.19 ft |
| --- | --- | --- | --- | --- |
| Total Combined | 126 |  | 0.45 ft |  |
| Hard Surface | 26 | 0.27 ft |  | 0.24 ft |
| Short Grass | 16 |  |  | 0.33 ft |
| Tall Grass | 22 |  |  | 0.28 ft |
| Brush | 23 |  |  | 0.62 ft |
| Woods | 20 |  |  | 0.45 ft |

The digital vertical data for the McHenry County project meets all mandatory and target specifications as per the following vertical accuracy tests:

Compared with the 1.19 ft FVA specification, FVA tested 0.27 ft at the 95% confidence level on the hard surfaces ground cover category, based on RMSEz x 1.9600.  The NSSDA specifies that vertical accuracy at the 95% confidence level equals RMSEz x 1.9600; the NDEP and ASPRS state that this method is valid only when random errors follow a normal error distribution, as in the hard surface category.

Compared with the 1.19 ft CVA specification, CVA tested 0.45 ft at the 95% confidence level on the hard surfaces, short grass, tall grass, brush, and woods ground cover categories combined, based on the 95th Percentile.  NDEP and ASPRS guidelines specify that vertical accuracy at the 95% confidence level equals the 95th percentile when random errors may not follow a normal error distribution, as in vegetated or obstructed areas.  Table 3 lists the 5% outliers larger than the 95th percentile (0.45ft).

Table 3 – 5% Outliers Larger than 95th Percentile

| Ground Cover Category | Elev. Diff (ft) | None of the errors were larger than the CVA standard (1.19ft) which permits up to 5% of the checkpoints, 6 out of 126, to be larger than 1.19 ft. |
| --- | --- | --- |
| Tall Grass | 0.55 |  |
| Brush | 0.52 |  |
| Brush | 0.56 |  |
| Brush | 0.62 |  |
| Brush | 1.07 |  |
| Woods | 0.46 |  |

Compared with the 1.19 ft SVA target values, SVA tested 0.24 ft at the 95% confidence level on hard surfaces; 0.33 ft in short grass; 0.28 ft in tall grass; 0.62 ft in brush; and 0.45 ft in woods ground cover categories, based on the 95th Percentile.  These values exceed all of their target values (1.19 ft).

Figure 1 illustrates the SVA by specific ground cover category.  Figure 2 illustrates the magnitude of the differences between the checkpoints and the digital vertical data by specific ground cover category and sorted from lowest to highest.  All of the checkpoints are within the 1.19 ft criteria shown in figure 2.  This exceeds the 95% requirement, where up to five checkpoints could be outside the 1.19 ft criteria.

Figure 1 -- Graph of SVA Values by Ground Cover Category

Figure 2 – Magnitude of Elevation Discrepancies, Sorted from Largest Negative to Largest Positive

Vertical Accuracy Testing in Accordance with NSSDA and FEMA Procedures

The NSSDA and FEMA guidelines were both published before it was recognized that digital data errors do not always follow a normal error distribution.  Future changes to these guidelines are expected to follow those of the NDEP and ASPRS.  In order to comply with FEMA’s current requirements, RMSEz and other statistics were computed in all five ground cover categories, individually and combined.  These statistics are shown in Figures 3 and 4 and Table 4 below.

Figure 3 shows the RMSEz values as calculated for each ground cover category separately.

Figure 3 – RMSEz statistics by Ground Cover Category

Table 4 – Overall Descriptive Statistics by Ground Cover Category

| Land Cover Category | RMSEz (ft) | Mean (ft) | Median (ft) | Skew | Std Dev (ft) | # of Points | Min (ft) | Max (ft) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Consolidated | 0.25 | 0.06 | 0.02 | 0.97 | 0.25 | 126 | -0.43 | 1.07 |
| Hard Surface | 0.14 | -0.05 | -0.07 | 0.38 | 0.13 | 26 | -0.27 | 0.23 |
| Short Grass | 0.19 | 0.04 | 0.08 | 0.38 | 0.19 | 16 | -0.23 | 0.44 |
| Tall Grass | 0.19 | 0.08 | 0.09 | 0.63 | 0.17 | 22 | -0.20 | 0.55 |
| Brush | 0.37 | 0.24 | 0.18 | 1.02 | 0.29 | 23 | -0.15 | 1.07 |
| Woods | 0.25 | 0.12 | 0.12 | 0.01 | 0.23 | 20 | -0.25 | 0.46 |

Figure 4 shows a histogram of the elevation differences between the field surveyed checkpoints and the TIN surface computed from the digital vertical data.  The histogram shows the number of occurrences (frequency) along the vertical axis that fell within the 0.20 ft ranges shown along the horizontal axis.

Figure 4 – Histogram of Elevation Discrepancies within 0.2 ft bands

Summary and Conclusions

The vertical accuracy testing methods derived from the NSSDA/FEMA and NDEP/ASPRS guidelines, when applied to the McHenry County project, verify that the digital vertical data provided by AME is well suited for the production of 2 ft contours.

Per NSSDA/FEMA guidelines:  RMSEz x 1.9600 = 95% confidence level

0.25 x 1.9600 = 0.49 ft

Per NDEP/ASPRS guidelines:  95th percentile (CVA) = 95% confidence level

= 0.45 ft

Both of the 95% confidence level test results exceed the required 1.19 ft accuracy level to support the generation of 2 ft contours.

# Endnotes

Part 3: National Standards for Spatial Data Accuracy (NSSDA), “Geospatial Positioning Accuracy Standards,” published by the Federal Geographic Data Committee (FGDC), 1998

Appendix A, Guidance for Aerial Mapping and Surveying, “Guidelines and Specifications for Flood Hazard Mapping Partners,” published by the Federal Emergency Management Agency (FEMA), April 2003

Guidelines for Digital Elevation Data, Version 1.0, published by the National Digital Elevation Program (NDEP), May 2004

ASPRS Guidelines, Vertical Accuracy Reporting for Lidar Data, published by the American Society for Photogrammetry and Remote Sensing (ASPRS), May 2004

APPENDIX

Quality Control Report (All Check Points)

O:\1080208\Lidar\QC\McHenry\McHenry_all.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

100               896601.274  2026374.271   790.461   790.580    +0.119

101               896617.544  2019690.521   809.405   809.510    +0.105

102               896595.523  2019785.514   807.853   808.000    +0.147

103               896640.986  2019790.291   808.086   808.210    +0.124

104               896649.946  2019638.746   807.741   808.020    +0.279

105               898090.454  2029241.174   796.747   796.660    -0.087

106               898114.063  2029179.035   797.344   797.790    +0.446

107               898136.530  2029238.996   797.325   797.450    +0.125

108               898035.704  2029252.933   796.258   796.430    +0.172

109               963921.734  2032991.246   931.081   931.020    -0.061

110               963981.104  2032886.794   928.413   928.870    +0.457

111               964137.576  2032885.350   930.274   931.340    +1.066

112               964196.592  2033019.303   932.518   932.590    +0.072

113               964133.420  2033010.911   931.957   932.070    +0.113

114               960287.866  2032175.381   920.644   920.810    +0.166

115               960405.297  2032196.382   918.751   919.180    +0.429

116               960472.669  2032225.502   914.929   915.450    +0.521

117               960628.305  2032245.374   917.285   917.350    +0.065

118               960642.383  2032266.844   917.964   918.000    +0.036

119               960062.237  2032213.718   919.004   919.140    +0.136

120               964478.668  2028990.683   894.516   894.750    +0.234

121               964845.866  2028968.951   893.351   893.730    +0.379

122               964477.021  2029015.118   893.929   894.370    +0.441

123               964511.657  2028963.823   892.357   892.700    +0.343

124               964467.251  2028956.424   892.406   892.960    +0.554

125               965233.713  2035878.008   905.884   905.830    -0.054

126               965190.009  2035907.460   911.156   911.000    -0.156

127               965163.309  2036053.369   911.396   911.310    -0.086

128               965225.829  2036140.901   913.696   913.610    -0.086

129               965229.694  2036210.954   914.207   914.130    -0.077

130               982499.623  2021747.482   886.317   886.150    -0.167

131               982555.676  2021689.087   884.500   884.370    -0.130

132               982440.525  2021547.492   891.412   891.160    -0.252

133               982417.917  2021516.879   892.479   892.250    -0.229

134               982512.254  2021594.536   889.788   889.800    +0.012

135               982904.045  2016492.368   902.462   902.190    -0.272

136               982954.051  2016649.238   907.019   906.900    -0.119

137               982857.988  2016728.270   906.475   906.500    +0.025

138               982881.125  2016311.742   899.309   899.070    -0.239

139               983003.234  2016037.658   893.217   893.170    -0.047

140               986644.388  2019569.734   889.477   889.510    +0.033

141               986716.045  2019419.436   866.845   867.140    +0.295

142               986647.968  2019414.514   866.475   866.730    +0.255

143               986589.985  2019449.170   866.202   866.540    +0.338

144               988833.619  2017446.857   885.156   885.270    +0.114

145               988771.595  2017524.856   885.152   885.450    +0.298

146               903356.481  2105031.607   908.158   908.020    -0.138

147               903572.566  2105137.112   906.432   906.440    +0.008

148               903557.724  2105203.591   906.166   906.460    +0.294

149               903648.134  2105189.182   905.973   906.160    +0.187

150               903471.208  2105148.198   906.209   906.300    +0.091

151               912433.936  2113249.707   955.959   956.520    +0.561

152               912347.844  2113128.024   955.930   955.860    -0.070

153               916329.086  2110069.274  1023.748  1023.650    -0.098

154               916361.478  2110038.129  1021.461  1021.500    +0.039

155               916538.324  2110130.488  1028.380  1028.570    +0.190

156               911971.188  2109780.203   946.786   946.640    -0.146

157               912055.440  2109793.996   948.351   948.160    -0.191

158               912244.593  2109712.090   948.177   948.110    -0.067

159               912361.354  2109707.014   947.200   947.510    +0.310

160               912470.554  2109703.648   948.062   948.210    +0.148

161               911897.595  2104328.288   975.802   975.820    +0.018

162               911753.518  2104344.800   969.145   969.460    +0.315

163               911938.780  2104352.573   975.074   975.080    +0.006

164               912005.712  2104367.589   976.409   976.330    -0.079

165               912172.057  2104368.295   977.252   977.090    -0.162

166               911475.713  2108407.322   945.405   945.710    +0.305

167               911605.342  2108303.798   948.328   948.950    +0.622

168               911568.662  2108074.035   949.795   949.820    +0.025

169               911506.878  2108069.360   950.917   950.930    +0.013

170               938815.485  2075087.822   923.249   923.280    +0.031

171               938819.796  2075036.985   923.919   924.020    +0.101

172               938784.143  2075159.842   921.576   921.760    +0.184

173               938852.368  2075142.280   918.587   918.780    +0.193

174               938726.472  2075044.741   925.694   925.880    +0.186

175               936164.765  2072989.643   908.220   908.100    -0.120

176               936128.938  2072926.628   905.799   905.960    +0.161

177               936192.544  2072944.634   906.993   906.960    -0.033

178               936126.185  2073061.707   908.633   908.480    -0.153

179               936129.798  2073033.400   907.921   908.060    +0.139

180               930601.462  2074387.377   922.810   922.820    +0.010

181               930654.418  2074415.559   919.158   919.290    +0.132

182               930600.084  2074313.046   918.036   918.460    +0.424

183               930479.783  2074067.916   916.409   916.480    +0.071

184               930410.239  2074085.245   915.700   915.860    +0.160

185               932222.378  2075927.833   948.787   948.650    -0.137

186               932185.901  2076015.956   947.967   947.890    -0.077

187               933672.467  2075276.525   911.527   911.400    -0.127

188               933649.288  2075323.189   911.012   910.890    -0.122

189               933571.758  2075214.380   905.320   905.720    +0.400

190               933725.964  2075220.918   905.845   905.840    -0.005

191               934774.981  2075091.782   913.922   913.860    -0.062

192               993678.344  2096367.428   834.027   834.010    -0.017

193               993676.031  2096312.195   835.156   835.410    +0.254

194               993833.629  2096395.640   826.225   826.140    -0.085

195               993816.487  2096332.520   829.729   829.840    +0.111

196               992979.694  2093780.150   834.523   834.450    -0.073

197               992918.634  2093794.165   830.185   830.320    +0.135

198               992556.827  2099632.126   778.411   778.170    -0.241

199               992637.185  2099623.484   777.147   776.950    -0.197

200               992622.503  2099574.938   776.101   776.410    +0.309

201               992739.212  2099569.685   776.367   776.350    -0.017

202               987338.928  2095240.823   813.630   813.420    -0.210

203               987110.191  2095187.755   812.974   812.880    -0.094

204               987168.984  2095122.371   800.645   800.440    -0.205

205               987365.309  2095344.382   808.496   808.680    +0.184

206               987412.579  2095423.513   803.653   803.500    -0.153

300               965222.262  2036125.357   913.728   913.480    -0.248

301               965210.025  2036124.294   912.656   912.530    -0.126

302               965205.970  2036124.409   912.567   912.690    +0.123

303               965200.937  2036124.209   913.302   913.210    -0.092

304               965190.586  2036123.333   913.683   913.370    -0.313

305               965179.553  2036122.840   913.433   913.150    -0.283

306               965174.087  2036122.614   912.623   913.490    +0.867

307               965168.972  2036122.598   915.372   915.070    -0.302

400               934758.829  2075180.958   913.092   912.900    -0.192

401               934759.456  2075174.642   913.476   913.680    +0.204

402               934760.411  2075165.358   917.006   916.710    -0.296

403               934761.077  2075159.528   917.872   917.640    -0.232

404               934761.858  2075148.468   918.328   918.060    -0.268

405               934762.501  2075137.267   918.194   917.850    -0.344

406               934762.740  2075132.313   917.531   917.100    -0.431

407               934763.905  2075117.995   912.003   912.270    +0.267

408               934763.764  2075116.355   912.147   912.090    -0.057

409               934764.305  2075114.180   912.757   912.500    -0.257

410               934764.938  2075100.906   913.450   913.470    +0.020

Average dz           +0.056

Minimum dz           -0.431

Maximum dz           +1.066

Average magnitude     0.193

Root mean square      0.253

Std deviation         0.248

Quality Control Report (Hard-Surface Check Points)

O:\1080208\Lidar\QC\McHenry\McHenry_hard-surface.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

100               896601.274  2026374.271   790.461   790.580    +0.119

101               896617.544  2019690.521   809.405   809.510    +0.105

105               898090.454  2029241.174   796.747   796.660    -0.087

109               963921.734  2032991.246   931.081   931.020    -0.061

114               960287.866  2032175.381   920.644   920.810    +0.166

120               964478.668  2028990.683   894.516   894.750    +0.234

126               965190.009  2035907.460   911.156   911.000    -0.156

130               982499.623  2021747.482   886.317   886.150    -0.167

135               982904.045  2016492.368   902.462   902.190    -0.272

140               986644.388  2019569.734   889.477   889.510    +0.033

144               988833.619  2017446.857   885.156   885.270    +0.114

146               903356.481  2105031.607   908.158   908.020    -0.138

152               912347.844  2113128.024   955.930   955.860    -0.070

153               916329.086  2110069.274  1023.748  1023.650    -0.098

157               912055.440  2109793.996   948.351   948.160    -0.191

161               911897.595  2104328.288   975.802   975.820    +0.018

169               911506.878  2108069.360   950.917   950.930    +0.013

170               938815.485  2075087.822   923.249   923.280    +0.031

175               936164.765  2072989.643   908.220   908.100    -0.120

180               930601.462  2074387.377   922.810   922.820    +0.010

185               932222.378  2075927.833   948.787   948.650    -0.137

187               933672.467  2075276.525   911.527   911.400    -0.127

192               993678.344  2096367.428   834.027   834.010    -0.017

196               992979.694  2093780.150   834.523   834.450    -0.073

198               992556.827  2099632.126   778.411   778.170    -0.241

202               987338.928  2095240.823   813.630   813.420    -0.210

Average dz           -0.051

Minimum dz           -0.272

Maximum dz           +0.234

Average magnitude     0.116

Root mean square      0.137

Std deviation         0.130

Quality Control Report (Short Grass Check Points)

O:\1080208\Lidar\QC\McHenry\McHenry_short-grass.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

103               896640.986  2019790.291   808.086   808.210    +0.124

113               964133.420  2033010.911   931.957   932.070    +0.113

119               960062.237  2032213.718   919.004   919.140    +0.136

122               964477.021  2029015.118   893.929   894.370    +0.441

128               965225.829  2036140.901   913.696   913.610    -0.086

133               982417.917  2021516.879   892.479   892.250    -0.229

139               983003.234  2016037.658   893.217   893.170    -0.047

145               988771.595  2017524.856   885.152   885.450    +0.298

150               903471.208  2105148.198   906.209   906.300    +0.091

156               911971.188  2109780.203   946.786   946.640    -0.146

165               912172.057  2104368.295   977.252   977.090    -0.162

174               938726.472  2075044.741   925.694   925.880    +0.186

179               936129.798  2073033.400   907.921   908.060    +0.139

183               930479.783  2074067.916   916.409   916.480    +0.071

191               934774.981  2075091.782   913.922   913.860    -0.062

204               987168.984  2095122.371   800.645   800.440    -0.205

Average dz           +0.041

Minimum dz           -0.229

Maximum dz           +0.441

Average magnitude     0.159

Root mean square      0.186

Std deviation         0.187

Quality Control Report (Tall Grass Check Points)

O:\1080208\Lidar\QC\McHenry\McHenry_tall-grass.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

104               896649.946  2019638.746   807.741   808.020    +0.279

108               898035.704  2029252.933   796.258   796.430    +0.172

112               964196.592  2033019.303   932.518   932.590    +0.072

117               960628.305  2032245.374   917.285   917.350    +0.065

124               964467.251  2028956.424   892.406   892.960    +0.554

127               965163.309  2036053.369   911.396   911.310    -0.086

134               982512.254  2021594.536   889.788   889.800    +0.012

136               982954.051  2016649.238   907.019   906.900    -0.119

142               986647.968  2019414.514   866.475   866.730    +0.255

149               903648.134  2105189.182   905.973   906.160    +0.187

155               916538.324  2110130.488  1028.380  1028.570    +0.190

160               912470.554  2109703.648   948.062   948.210    +0.148

164               912005.712  2104367.589   976.409   976.330    -0.079

168               911568.662  2108074.035   949.795   949.820    +0.025

173               938852.368  2075142.280   918.587   918.780    +0.193

176               936128.938  2072926.628   905.799   905.960    +0.161

184               930410.239  2074085.245   915.700   915.860    +0.160

186               932185.901  2076015.956   947.967   947.890    -0.077

190               933725.964  2075220.918   905.845   905.840    -0.005

195               993816.487  2096332.520   829.729   829.840    +0.111

199               992637.185  2099623.484   777.147   776.950    -0.197

206               987412.579  2095423.513   803.653   803.500    -0.153

Average dz           +0.085

Minimum dz           -0.197

Maximum dz           +0.554

Average magnitude     0.150

Root mean square      0.188

Std deviation         0.172

Quality Control Report (Brush Check Points)

O:\1080208\Lidar\QC\McHenry\McHenry_brush.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

107               898136.530  2029238.996   797.325   797.450    +0.125

111               964137.576  2032885.350   930.274   931.340    +1.066

116               960472.669  2032225.502   914.929   915.450    +0.521

118               960642.383  2032266.844   917.964   918.000    +0.036

123               964511.657  2028963.823   892.357   892.700    +0.343

125               965233.713  2035878.008   905.884   905.830    -0.054

131               982555.676  2021689.087   884.500   884.370    -0.130

137               982857.988  2016728.270   906.475   906.500    +0.025

143               986589.985  2019449.170   866.202   866.540    +0.338

148               903557.724  2105203.591   906.166   906.460    +0.294

151               912433.936  2113249.707   955.959   956.520    +0.561

154               916361.478  2110038.129  1021.461  1021.500    +0.039

159               912361.354  2109707.014   947.200   947.510    +0.310

163               911938.780  2104352.573   975.074   975.080    +0.006

167               911605.342  2108303.798   948.328   948.950    +0.622

172               938784.143  2075159.842   921.576   921.760    +0.184

178               936126.185  2073061.707   908.633   908.480    -0.153

182               930600.084  2074313.046   918.036   918.460    +0.424

189               933571.758  2075214.380   905.320   905.720    +0.400

194               993833.629  2096395.640   826.225   826.140    -0.085

197               992918.634  2093794.165   830.185   830.320    +0.135

200               992622.503  2099574.938   776.101   776.410    +0.309

205               987365.309  2095344.382   808.496   808.680    +0.184

Average dz           +0.239

Minimum dz           -0.153

Maximum dz           +1.066

Average magnitude     0.276

Root mean square      0.368

Std deviation         0.286

Quality Control Report (Trees Check Points)

O:\1080208\Lidar\QC\McHenry\McHenry_trees.txt

Number               Easting     Northing   Known Z   Laser Z        Dz

-----------------------------------------------------------------------

102               896595.523  2019785.514   807.853   808.000    +0.147

106               898114.063  2029179.035   797.344   797.790    +0.446

110               963981.104  2032886.794   928.413   928.870    +0.457

115               960405.297  2032196.382   918.751   919.180    +0.429

121               964845.866  2028968.951   893.351   893.730    +0.379

129               965229.694  2036210.954   914.207   914.130    -0.077

132               982440.525  2021547.492   891.412   891.160    -0.252

138               982881.125  2016311.742   899.309   899.070    -0.239

141               986716.045  2019419.436   866.845   867.140    +0.295

147               903572.566  2105137.112   906.432   906.440    +0.008

158               912244.593  2109712.090   948.177   948.110    -0.067

162               911753.518  2104344.800   969.145   969.460    +0.315

166               911475.713  2108407.322   945.405   945.710    +0.305

171               938819.796  2075036.985   923.919   924.020    +0.101

177               936192.544  2072944.634   906.993   906.960    -0.033

181               930654.418  2074415.559   919.158   919.290    +0.132

188               933649.288  2075323.189   911.012   910.890    -0.122

193               993676.031  2096312.195   835.156   835.410    +0.254

201               992739.212  2099569.685   776.367   776.350    -0.017

203               987110.191  2095187.755   812.974   812.880    -0.094

Average dz           +0.118

Minimum dz           -0.252

Maximum dz           +0.457

Average magnitude     0.208

Root mean square      0.253

Std deviation         0.230