Required Subcontractor Information:  Peoria, Illinois Project

CONTROL REPORTS: run a control report against your dataset once all of the ground filtering has been completed. Fill in the information below:

*note: the RMS needs to be below 18.5 cm or .6 ft

| Control Point | Easting | Northing | Known Z | Laser Z | DZ |
| --- | --- | --- | --- | --- | --- |
| PIA_A | 2430781.969 | 1456245.269 | 654.623 | removed | * |
| TOPCON_AP_POINT | 2430545.710 | 1456851.086 | 651.055 | 651.667 | +0.612 |
| LC2076 | 2449871.300 | 1504023.462 | 766.634 | 767.167 | +0.533 |
| TRM60D | 2430525.780 | 1456820.057 | 651.866 | 652.333 | +0.467 |
| 68 | 2427742.886 | 1426290.144 | 462.028 | 462.250 | +0.222 |
| 67 | 2481986.593 | 1565947.889 | 635.028 | 635.167 | +0.139 |
| 45 | 2345937.678 | 1441922.781 | 699.810 | 699.750 | -0.060 |
| LC1405 | 2373361.579 | 1515555.114 | 677.335 | 677.250 | -0.085 |
| 27 | 2410241.522 | 1505052.688 | 656.187 | 656.083 | -0.104 |
| BONTZ | 2423461.373 | 1496810.325 | 705.353 | 705.167 | -0.186 |
| 59 | 2352347.949 | 1568972.863 | 689.724 | 689.333 | -0.391 |
| 95_3458_ST | 2363041.473 | 1614928.528 | 761.896 | outside | * |
| ILSA | 2452952.371 | 1133717.514 | 611.551 | outside | * |

| RMS Value | Std. Deviation | Minimum DZ | Maximum DZ | Average DZ |
| --- | --- | --- | --- | --- |
| .340 | .337 | -.391 | +.612 | +.115 |

- Data results in IL State Plane Zone West NAD83 US Survey Feet, NAVD88 US Survey Feet

ACQUISITION PARAMETERS: fill in the appropriate sensor information below and which sensor(s) you are using for Peoria, IL.

LEICA ALS50 Phase 2 MPIA

| Average Altitude | 2500 Meters AGL |
| --- | --- |
| Airspeed | ~120 Knots |
| Scan Frequency | 32.9 Hertz |
| Scan Width Half Angle | 19.5 Degrees |
| Pulse Rate | 90,000 Hertz |

COLLECTION INFORMATION: fill in the highlighted areas in this spread sheet below with mission specific information:

| Mission | Date | Start Time | End Time | Altitude (m agl) | Airspeed (Knots) | Scan Angle | Scan Rate | Pulse Rate | PDOP |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Day085 | March 25 | 13:22 | 16:57 | 2500 | 120 | 39 | 32.9 | 90000 | 1.9 |
| Day086 | March 26 | 14:23 | 17:35 | 2500 | 120 | 39 | 32.9 | 90000 | 1.8 |
| Day088 | March 28 | 14:08 | 17:21 | 2500 | 120 | 39 | 32.9 | 90000 | 2.0 |
| Day089 | March 29 | 08:20 | 11:35 | 2500 | 120 | 39 | 32.9 | 90000 | 2.5 |
| Day089 | March 29 | 13:08 | 16:30 | 2500 | 120 | 39 | 32.9 | 90000 | 1.7 |
| Day 089 | March 29 | 16:50 | 18:05 | 2500 | 120 | 39 | 32.9 | 90000 | 1.9 |

List the programs you use to develop your data.

Airborne GPS is differentially processed using the GrafNAV V7.50 software by Waypoint Consulting of Calgary, Alberta, Canada.

IMU data is processed using the IPAS Pro V1.22 software by Leica Geosystems of St. Gallen, Switzerland.

The reflective surface is derived using the ALS Post Processor software by Leica Geosystems GIS & Mapping Division of Atlanta, Georgia.

The classification of LiDAR data is carried out using TerraScan software by Terrasolid Limited of Helsinki, Finland.

The quality control (QC) and calibration is completed using VG4D software by Virtual Geomatics, Inc of Austin, Texas.