Elevation QA Report

Project:       Contractor:

Data Delivery Date:   Date Data Reviewed:

Reviewer:    Total Square Miles Reviewed:

Elevation Type:     Format:       Grid Spacing:    Tile size:

Projection:       Zone:       Datum:         Units:

Licensing:           Metadata:

Materials Received:

Vertical Accuracy Test Performed:       Test Point Source:            RMSE:

Vertical Accuracy Test Notes:

QA Review Summary:

07-08-2010

LiDAR Quality Control (QA) Review Process

Preparation:

-Metadata reviewed to determine data projection, datum, format, etc.

-If ARRA contract, check for raw .LAS files, classified .LAS files, breaklines, blind control points,

and DEM in Image or Grid format

-Open data in Global Mapper

Vertical accuracy testing:

-If ARRA contract, use Vertical Accuracy Test Worksheet to perform RMSE on 20 blind point

positions provided by contractor

Inspection and Correction of data:

-Minimum and maximum elevations in dataset; correct if in error

-Appropriate hydro flattening as specified in V12 Lidar Specification (For ARRA/GPSC Data)

-Data void areas

-Data spikes

-Tile edge seam lines

-Non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Elevation errors - raised/lowered areas/tiles

-Other surface treatment anomalies

-Check DRGs for correct elevations and horizontal positioning (if test points not available)

-Create footprint (project boundary) shape file and establish square miles

During Inspection, identify data errors and create “error” file folder:

-Capture geo-referenced JPG or TIFF image(s) of identified errors

-Copy to Error file

During Inspection, level elevations and remove artifacts (these two steps not done for ARRA data):

-Level smoothing to remove non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Level data spikes where possible

Export image files and create project Elevation QA Review Report:

-Export ERDAS Imagine image files in native projection and resolution

-If ARRA, Copy Vertical Accuracy Test Worksheet into QA Report

-Place QA Review Process and Project Area Extent into QA Report

-If rejected, attach sample geo-referenced JPG or TIFF error images with an explanation of reason

-If rejected, restart QA process when replacement data is received

-Provide completed Elevation QA Review Report to Elevation Supervisor for final viewing

-Add QA Report, footprint, Imagine image(s), and Error file to original data file for final shipment to EROS

Area Extent

Errors

Breaklines do not represent ground conditions at 48° 52' 22.8161" N, 98° 17' 31.5439" W

Breaklines do not represent ground conditions at 48° 51' 29.2645" N, 98° 47' 46.5490" W

Breaklines do not represent ground conditions at 48° 44' 5.7538" N, 98° 23' 8.9180" W

Breaklines do not represent ground conditions at 48° 39' 54.4377" N, 98° 18' 22.4086" W

Breaklines do not represent ground conditions at 48° 22' 16.7509" N, 98° 47' 48.3174" W

Culvert removal at 48° 56' 6.0760" N, 98° 30' 53.9138" W

Culvert removal at 48° 29' 32.6894" N, 97° 54' 43.0760" W

Differing water elevations, no dam or spillway at 48° 56' 14.0451" N, 98° 21' 54.1269" W

Hydro-flattening needed at 48° 58' 26.4505" N, 98° 41' 48.2665" W

Hydro-flattening needed at 48° 54' 26.1742" N, 97° 53' 8.8311" W

Hydro-flattening needed at 48° 51' 36.1497" N, 98° 48' 1.7707" W

Pits in road at 48° 59' 32.3995" N, 97° 46' 13.8956" W