Elevation QC Report

Project:       Contractor:

Data Delivery Date:   Date Data Reviewed:

Reviewer:    Total Square Miles Reviewed:

Elevation Type:     Format:       Grid Spacing:    Tile size:

Projection:       Zone:       Datum:         Units:

Licensing:           Metadata:

Materials Received:

Vertical Accuracy Test Performed:       Test Point Source:            RMSE:

Vertical Accuracy Test Notes:

QC Review Summary:

LiDAR Quality Control (QC) Review Process                                                                      6-7-2010

Preparation:

-Metadata reviewed to determine data projection, datum, format, etc.

-If ARRA contract, check for raw .LAS files, classified .LAS files, breaklines, blind control points, and other

V12 Lidar Specification requirements

-Open data in Global Mapper

-Create footprint (project boundary) shape file and establish square miles

Inspection of data for:

-Appropriate hydro flattening as specified in V12 Lidar Specification (For ARRA/GPSC Data)

-Data void areas

-Data spikes

-Tile edge seam lines

-Non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Elevation errors - raised/lowered areas/tiles

-Other surface treatment anomalies

-Check DRGs for correct elevations and horizontal positioning (if test points not available)

Identify data errors/create “error” file folder:

-Capture geo-referenced JPG or TIFF image(s) of identified errors

-Copy to Error file

Elevation leveling/artifact removal (these two steps not done for ARRA data):

-Level smoothing to remove non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Level data spikes wherever possible

Vertical accuracy testing:

-If ARRA contract, use Vertical Accuracy Test Worksheet to perform RMSE on 20 blind point positions

provided by contractor

Export image files and create project Elevation QC Review Report:

-Export 1/9th arc-second ERDAS Imagine image files

-Obtain copy of MS Word format Elevation QC Review Report

-Select proper metadata pull-down box items and fill in descriptive text boxes

-Copy Vertical Accuracy Test Worksheet into QC Report

-Place Review Process information into QC Report

-If rejected, attach sample geo-referenced JPG or TIFF error images with an explanation of reason

-If rejected, restart QC process when replacement data is received

-Provide completed Elevation QC Review Report to Elevation Supervisor for final viewing

-Add QC Report, footprint, Imagine image(s), and Error file to original data file for final shipment

Cole-Callaway-Osage Cos.  Area Extent