LiDAR Remote Sensing Data Collection

DEPARTMENT OF GEOLOGY AND MINERAL INDUSTRIES

South Coast, oregon

May 8, 2009

Submitted to:

Department of Geology and Mineral Industries

800 NE Oregon Street, Suite 965

Portland, OR 97232

Submitted by:

Watershed Sciences

529 SW 3rd Avenue, Suite 300

Portland, OR 97204

LiDAR Remote Sensing Data Collection:

DOGAMI, South Coast study area

TABLE OF CONTENTS

1. Overview	1

1.1 Study Area (South Coast)	1

1.2 Area Delivered to Date	2

1.3 Acquisition and Ground Survey	4

2. Accuracy	13

2.1 Relative Accuracy	13

2.2 Absolute Accuracy	13

3. Data Density/Resolution	15

3.1 Density Statistics	15

3.2 Data Density/Resolution per Delivery	19

3.2.1 Delivery 1	19

3.2.2 Delivery 2	20

3.2.3 Delivery 3	22

3.2.4 Delivery 4	23

4. Selected Imagery	25

# 1. Overview

## 1.1 Study Area (South Coast)

Watershed Sciences, Inc. has collected Light Detection and Ranging (LiDAR) data of the South Coast study area for the Oregon Department of Geology and Mineral Industries (DOGAMI).  The Area of Interest (AOI) covers portions of four counties in southwest Oregon.  The requested LiDAR area totals ~1,610,136 acres; the map below shows the Total Area to be Flown (TAF), covering ~1,632,390 acres.  The TAF acreage is greater than the original AOI acreage due to buffering and flight planning optimization.  This report will be amended to reflect new data and cumulative statistics for the overall LiDAR survey.  DOGAMI data are delivered in OGIC(HARN):  Projection: Oregon Statewide Lambert Conformal Conic; horizontal and vertical datums:  NAD83 (HARN)/NAVD88(Geoid03); Units:  International Feet.

Figure 1.1.  DOGAMI South Coast study area.

## 1.2 Area Delivered to Date

Table 1.1. Total delivered acreage to date.

|  | DOGAMI Southern Oregon Coast |
| --- | --- |
|  | Delivery Date | Acquisition Date | AOI Acres | TAF Acres |
| Delivery 1 | September 3, 2008 | May 3 – June 26, 2008 | 46,568 | 47,798 |
| Delivery 2 | October 2, 2008 | May 3 – June 26, 2008 | 86,505 | 88,789 |
| Delivery 3 | October 16, 2008 | May 3 – June 26, 2008 | 68,913 | 71,791 |
| Delivery 4 | November 21, 2008 | June 12 – June 29, 2008 | 111,851 | 113,638 |
| Delivery 5 | January 19, 2009 | June 12 – June 29, 2008 | 113,350 | 113,794 |
| Delivery 6 | April 15, 2009 | June 15 – August 9, 2008 | 221,939 | 222,692 |
| Delivery 7 | April 15, 2009 | June 15 – August 9, 2008 | 133,226 | 134,276 |
| Delivery 8a | April 15, 2009 | June 15 – August 9, 2008 | 91,453 | 93,631 |
| Delivery 8b | May 8, 2009 | June 8 - Oct. 19, 2008 | 47,388 | 48,275 |
| Delivery 9 | May 8, 2009 | June 15 – Oct. 19, 2008 | 139,023 | 139,024 |
| Delivery 10 | May 8, 2009 | June 29 – Sept. 28, 2008 | 143,891 | 145,854 |
|  |  | Total | 1,204,107 | 1,219,562 |

Figure 1.2.  DOGAMI southern Oregon coast study area, illustrating the delivered portion of the TAF.

Figure 1.3.  South Coast study area, illustrating the delivered 7.5 and 0.75-minute USGS quads.

## 1.3 Acquisition and Ground Survey

LiDAR acquisition for all data occurred from April 27, 2008 to April 5, 2009 for the South Coast study area.

Figure 1.4. Actual flightlines for the South Coast study area illustrating the dates flown (based on GPS week).

Figure 1.5. Base stations for the South Coast study area for data delivered to date.

Table 1.2 (Continued on next page).  Base Station Surveyed Coordinates, (NAD83/NAVD88, OPUS corrected) used for kinematic post-processing of the aircraft GPS data for the South Coast study area.

|  | Datum NAD83(HARN) | GRS80 |
| --- | --- | --- |
| Base Station ID | Latitude (North) | Longitude (West) | Ellipsoid Height (m) |
| OLC5CD1 | 43 15 20.76929 | 123 53 22.87770 | 217.600 |
| OLC5CD2 | 43 20 23.11132 | 124 11 55.76971 | -20.988 |
| OLC5CD3 | 43 20 56.06002 | 123 54 36.20001 | 217.506 |
| OLC5PGW1 | 43 21 2.60751 | 124 20 13.64907 | -2.435 |
| OLC5PW | 43 21 2.60751 | 124 20 13.64907 | -2.435 |
| OLC6MSD2 | 43 39 20.26276 | 123 54 46.89022 | -18.419 |
| OLC6MSD3 | 43 29 50.26635 | 124 13 08.39367 | -12.939 |
| OLCCF1 | 42 58 00.42449 | 124 06 55.61889 | 28.559 |

Table 1.2 (Continued from previous page). Base Station Surveyed Coordinates, (NAD83/NAVD88, OPUS corrected) used for kinematic post-processing of the aircraft GPS data for the South Coast study area.

|  | Datum NAD83(HARN) | GRS80 |
| --- | --- | --- |
| Base Station ID | Latitude (North) | Longitude (West) | Ellipsoid Height (m) |
| OLCCF2 | 42 57 55.66164 | 124 07 06.22758 | 102.674 |
| OLCCF3 | 43 01 54.71258 | 124 06 43.96709 | -7.289 |
| OLCJN1 | 42 08 30.08496 | 124 12 49.11911 | 428.475 |
| OLCJN2 | 42 08 27.95822 | 124 12 49.29884 | 427.870 |
| OLCJN3 | 42 03 04.54697 | 124 17 30.17996 | 1.811 |
| OLCJN4 | 42 03 50.25255 | 124 12 46.39603 | 31.933 |
| OLCJN5 | 42 28 05.44507 | 124 20 46.24558 | -21.890 |
| OLCJN6 | 42 25 33.04097 | 124 25 35.72884 | -19.346 |
| OLCJN7 | 42 48 31.65550 | 124 29 21.62711 | 33.225 |
| OLCJN8 | 43 09 26.13789 | 124 22 44.20041 | -19.734 |
| OLCJN9 | 42 47 10.43094 | 124 28 52.40738 | -13.568 |
| OLCJN10 | 43 00 44.63261 | 123 41 38.18942 | 307.728 |
| OLCJN11 | 42 57 16.07660 | 123 46 38.70609 | 543.201 |
| OLCPWH1 | 42 19 43.74040 | 124 25 33.76978 | 177.778 |
| OLCPWH2 | 42 32 11.15305 | 124 23 59.59628 | -13.175 |
| OLCPWH3 | 42 27 48.10893 | 124 21 45.53382 | -15.340 |
| OLCPWH4 | 42 16 31.44293 | 124 24 15.39346 | -21.678 |
| OLCPWH5 | 42 48 26.82761 | 124 20 09.43708 | 68.264 |
| OLCPWH6 | 43 07 56.53594 | 124 21 10.15905 | -22.854 |
| OLCPWH7 | 43 15 44.29178 | 123 49 12.34815 | 32.003 |
| OLCPWH8 | 43 10 23.32427 | 124 12 00.96021 | -19.743 |
| OLCPWH9 | 42 59 01.23604 | 123 48 06.84695 | 733.518 |
| OLCPWH10 | 43 15 44.25471 | 123 49 12.35897 | 285.251 |
| OLCPWH11 | 43 09 54.31855 | 124 02 56.98822 | 62.611 |
| OLCPWH12 | 43 15 44.29178 | 123 49 12.34815 | 285.248 |
| OLCPWH13 | 43 00 21.54079 | 123 53 20.67738 | 50.495 |
| OLCPWH14 | 42 59 29.68950 | 123 50 23.50621 | 328.574 |
| OLCPWH15 | 42 56 37.78974 | 124 05 51.77012 | 43.503 |
| OLCPWH16 | 42 54 02.56554 | 124 07 27.51313 | 117.941 |
| OLCPWH17 | 43 21 47.87472 | 124 04 51.53211 | -19.865 |
| OLCBTK1 | 42 07 32.49487 | 124 18 37.00074 | 295.173 |
| OLCBTK2 | 42 04 08.31008 | 124 18 52.63704 | -16.064 |
| OLCBTK3 | 42 08 39.24373 | 124 21 22.62505 | -6.578 |
| OLCBTK4 | 42 02 44.62353 | 124 16 04.64324 | -21.946 |
| AA5136 | 42 52 23.01388 | 124 03 42.88679 | 64.842 |
| NGS_PID_OA07 | 43 5 54.88105 | 124 24 55.03463 | -0.860 |
| DH7020 | 43 5 11.08316 | 124 24 26.18403 | 7.977 |
| 6NCM2 | 43 42 14.56952 | 124 06 17.75696 | -19.441 |

For data delivered to date, 20,024 RTK points were collected in the study area.  Figures 1.6-1.11 show detailed views of RTK point locations.

Figure 1.6.  RTK point locations in the study area; images are NAIP Orthoimages.

Figure 1.7.  RTK point locations in the study area; images are NAIP Orthoimages.

Figure 1.8.  RTK point locations in the study area; images are NAIP Orthoimages.

Figure 1.9.  RTK point locations in the study area; images are NAIP Orthoimages.

Figure 1.10.  RTK point locations in the study area; images are NAIP Orthoimages.

Figure 1.11.  RTK point locations in the study area; images are NAIP Orthoimages.

2. Accuracy

## 2.1 Relative Accuracy

Relative accuracy statistics evaluate internal consistency (line to line reproducibility) for a LiDAR dataset, and are measured as the divergence between points from distinct, overlapping flightlines.  The final report will include relative accuracy statistics for the entire South Coast study area.  To date, reported project averages are well within contracted specifications.

## 2.2 Absolute Accuracy

Absolute accuracy compares known Real Time Kinematic (RTK) ground survey points to the closest laser point.  For the South Coast study area, 20,024 RTK points were collected for data delivered to date.  Accuracy statistics are reported in Table 2.1 and shown in Figures 2.3-2.3.

Table 2.1.  Absolute Accuracy – Deviation between laser points and RTK survey points.

| Sample Size (n): 20,024 |
| --- |
| Root Mean Square Error (RMSE): 0.14 feet (0.04 meters) |
| Standard Deviations | Deviations |
| 1 sigma (σ): 0.14 feet (0.04 meters) | Minimum ∆z: -0.66 feet (-0.20 meters) |
| 2 sigma (σ): 0.10 feet (0.32 meters) | Maximum ∆z: 0.67 feet (0.20 meters) |
|  | Average ∆z: 0.12 feet (0.04 meters) |

Figure 2.1.  Portion of the study area for which absolute accuracy statistics are reported.

Figure 2.2.  South Coast Study area histogram statistics

Figure 2.3.  South Coast study area point absolute deviation statistics.

# 3. Data Density/Resolution

## 3.1 Density Statistics

Some types of surfaces (i.e., dense vegetation or water) may return fewer pulses than the laser originally emitted.  Therefore, the delivered density can be less than the native density and vary according to distributions of terrain, land cover and water bodies.  Density histograms and maps (Figures 3.1 – 3.4) have been calculated based on first return laser point density and ground-classified laser point density.

Table 3.1. Average density statistics for South Coast data delivered to date.

| Average Pulse Density (per square ft) | Average Pulse Density (per square m) | Average Ground Density (per square ft) | Average Ground Density (per square m) |
| --- | --- | --- | --- |
| 0.77 | 8.28 | 0.06 | 0.69 |

Figure 3.1.  Histogram of first return laser point density for data delivered to date.

Figure 3.2.  Image shows first return laser point per 0.75’ USGS Quad for data delivered to date.

Ground classifications were derived from ground surface modeling.  Supervised classifications were performed by reseeding of the ground model where it was determined that the ground model failed, usually under dense vegetation and/or at breaks in terrain, steep slopes and at bin boundaries.

Figure 3.3.  Histogram of ground-classified laser point density for data delivered to date.

Figure 3.4.  Ground-classified laser point density per 0.75’ USGS Quad for data delivered to date.

## 3.2 Data Density/Resolution per Delivery

### 3.2.1 Delivery 1

Figure 3.5.  Quadrants containing few ground classified points include coastal areas and areas of dense vegetation.

### 3.2.2 Delivery 2

Figure 3.6.  This quadrant illustrates a high number of ground classified points due to flightline overlap and areas of little or no ground cover.

Figure 3.7.  Quadrants displaying fewer first return points correlate directly with flightline density.

### 3.2.3 Delivery 3

Figure 3.8.  Quadrants containing few ground classified points include coastal areas and areas of dense vegetation.

### 3.2.4 Delivery 4

Figure 3.9.  Quadrants with exposed ground or little vegetation result in higher ground-classified point density.

Figure 3.10.  Quadrants with higher flightline density result in greater numbers of first return points.

# 4. Selected Imagery

Example areas are presented to show sample imagery (see Figures 4.1-4.13).

Figure 4.1.  View to Northwest at oceanside near Harris Beach State Park, Oregon (quad 42124-A3).  Top image derived from highest hit LiDAR, lower image derived from bare earth LiDAR.

Figure 4.2.  View to Southeast and upstream along Chetco River at its confluence with Jack Creek (quad 42124-A2).  Top image is derived from highest hit LiDAR, lower image derived from bare earth LiDAR.

Figure 4.3.  View upstream and to Northeast of Chetco River at confluence with North Fork Chetco River (quad 42124-a2).  Top image derived from highest hit LiDAR, lower image derived from bare earth LiDAR.

Figure 4.4.  Oblique view of coastline at confluence of Whalehead Creek and ocean (quad 42124-b3).  Upper image derived from highest hit LiDAR, lower image derived from bare earth LiDAR.

Figure 4.5.  Oblique view to North over Chetco River and North Fork Chetco River (quad 42124-a2).  Top image derived from LiDAR highest hits, bottom from bare earth LiDAR.

Figure 4.6.  Cape Arago State Park, South Cove (Quad 43124C4).  Top image derived from LiDAR highest hits, bottom from bare earth LiDAR.

Figure 4.7.  Chetco River upstream of confluence with Elk Creek (quad 42124-b2).  Upper image derived from highest hit LiDAR, center image derived from bare earth LiDAR, lower image derived from NAIP orthophoto.

Figure 4.8.  Whalehead and Coon Creek at terminus in ocean near Highway 101 (quad42124-b3).  Top image derived from highest hit LiDAR, center image from bare earth LiDAR, lower image derived from NAIP orthophotos.

Figure 4.9. View of the Sixes River and Bea Creek confluence in delivery tile 42124g3.  Top image derived from bare earth LiDAR, center image from highest hit LiDAR, and lower image derived from NAIP orthophotos.

Figure 4.10.  View of the confluence of Sixes River and Edson Creek in delivery tile 42124g4.  Top image derived from bare earth LiDAR, center image from highest hit LiDAR, and lower image derived from NAIP orthophotos.

Figure 4.11.  Stream confluence entering South Slough just north of Cox Canyon in delivery tile 43124C3.  Upper image derived from highest hit LiDAR, center image derived from bare earth LiDAR, lower image derived from NAIP orthophoto.

Figure 4.12.  Coast beach north of Cape Arago State Park in delivery tile 43124C4.  Upper image derived from highest hit LiDAR, center image derived from bare earth LiDAR, lower image derived from NAIP orthophoto.

Figure 4.13.  Upper Pony Creek Reservoir in delivery tile 43124C3.  Upper image derived from highest hit LiDAR, center image derived from bare earth LiDAR, lower image derived from NAIP orthophoto.

# Text boxes

LiDAR Bare Earth

NAIP Orthophoto

NAIP Orthophoto

LiDAR Highest Hit

LiDAR Bare Earth

LiDAR Highest Hit

LiDAR Bare Earth

LiDAR Highest Hit

LiDAR Bare Earth

NAIP Orthophoto

LiDAR Highest Hit

NAIP Orthophoto