Submitted to:

Department of Geology and Mineral Industries

800 NE Oregon Street, Suite 965

Portland, OR 97232

Submitted by:

Watershed Sciences

529 SW 3rd Avenue, Suite 300

Portland, OR 97204

LiDAR Remote Sensing Data Collection:

DOGAMI, Yambo Study Area

TABLE OF CONTENTS

1. Overview	1

1.1 Study Area	1

1.2 Area Delivered to Date	2

2. Acquisition	4

2.1 Airborne Survey Overview – Instrumentation and Methods	4

2.2 Ground Survey – Instrumentation and Methods	6

3. Accuracy	13

3.1 Relative Accuracy	13

3.2 Absolute Accuracy	15

4. Data Density/Resolution	17

4.1 Density Statistics	17

5. Selected Imagery	22

Front Cover:  Image of where Cedar Creek meets the Siletz River; along the Siletz Highway in Delivery Area 1. View is from the North, looking South.

Back Cover:  Parts of the Evergreen Aviation Museum and McMinnville Municipal Airport, with E Salmon River Highway running through the middle.  View is from the North, looking South. Image is from Delivery Area 5.

# 1. Overview

## 1.1 Study Area

Watershed Sciences, Inc. has collected Light Detection and Ranging (LiDAR) data of the Yambo Study Area for the Oregon Department of Geology and Mineral Industries (DOGAMI).  The area of interest (AOI) totals 1,063 square miles (680,432 acres) and the total area flown (TAF) covers 1,083 square miles (692,852 acres).  The TAF acreage is greater than the original AOI acreage due to buffering and flight planning optimization (Figure 1.1 below).  This report will be amended to reflect new data and cumulative statistics for the overall LiDAR survey with every delivery.  DOGAMI data are delivered in OGIC (HARN):  Projection: Oregon Statewide Lambert Conformal Conic; horizontal and vertical datum:  NAD83 (HARN)/NAVD88 (Geoid03); units:  International Feet.

Figure 1.1.  DOGAMI Yambo Study Area.

## 1.2 Area Delivered to Date

Total delivered acreage to date is detailed below.

| DOGAMI Yambo Study Area |
| --- |
|  | Delivery Date | Acquisition Dates | AOI Acres | TAF Acres |
| Delivery Area 1 | October 30, 2010 | April 14, 2010 | 10,041 | 10,760 |
| Delivery Area 2 | September 30, 2010 | March 1, 2010 – June 5, 2010 | 60,810 | 62,451 |
| Delivery Area 3 | September 30, 2010 | May 7, 2010 – July 14, 2010 | 120,812 | 122,938 |
| Delivery Area 4 | October 30, 2010 | January 3, 2010 – May 27, 2010 | 95,919 | 97,317 |
| Delivery Area 5 | October 30, 2010 | January 3, 2010 – May 27, 2010 | 145,633 | 147,839 |
| Delivery Area 6 | October 30, 2010 | March 5, 2010 – May 15, 2010 | 82,766 | 84,277 |
| Delivery Area 7 | October 30, 2010 | March 17, 2010 – July 14, 2010 | 164,451 | 167,271 |

Figure 1.2.  Yambo Study Area, illustrating the delivered portions of the TAF.

Figure 1.3.  Yambo Study Area, illustrating the delivered 7.5 minute USGS quads.

# 2. Acquisition

## 2.1 Airborne Survey Overview – Instrumentation and Methods

The LiDAR survey utilized Leica ALS60 and Leica ALS50 Phase II sensors mounted in multiple Cessna Caravans 208B.  The Leica systems were set to acquire ≥105,000 laser pulses per second (i.e. 105 kHz pulse rate) and flown at 900 and 1300 meters above ground level (AGL), capturing a scan angle of ±14o from nadir.  These settings are developed to yield points with an average native density of (8 points per square meter over terrestrial surfaces.  The native pulse density is the number of pulses emitted by the LiDAR system.  Some types of surfaces (i.e. dense vegetation or water) may return fewer pulses than the laser originally emitted.  Therefore, the delivered density can be less than the native density and lightly variable according to distributions of terrain, land cover and water bodies.

The Cessna Caravan is a powerful, stable platform, which is ideal for the often remote and mountainous terrain found in the Pacific Northwest.  The Leica ALS60 sensor head installed in the Caravan is shown on the right.

Table 2.1 LiDAR Survey Specifications

| Sensor | Leica ALS60, Leica ALS50 Phase II |
| --- | --- |
| Survey Altitude (AGL) | 900 m and 1300 m |
| Pulse Rate | >105 kHz |
| Pulse Mode | Single |
| Mirror Scan Rate | 52 Hz |
| Field of View | 28o (±14o from nadir) |
| Roll Compensated | Up to 15o |
| Overlap | 100% (50% Side-lap) |

The study area was surveyed with opposing flight line side-lap of ≥50% (≥100% overlap) to reduce laser shadowing and increase surface laser painting.  The system allows up to four range measurements per pulse, and all discernable laser returns were processed for the output dataset.

To solve for laser point position, it is vital to have an accurate description of aircraft position and attitude.  Aircraft position is described as x, y and z and measured twice per second (2 Hz) by an onboard differential GPS unit.  Aircraft attitude is measured 200 times per second (200 Hz) as pitch, roll and yaw (heading) from an onboard inertial measurement unit (IMU).  Figure 2.1 shows the flight lines completed for deliveries to date.

Figure 2.1. Actual flightlines for the Yambo Study Area illustrating the dates flown for deliveries to date.

## 2.2 Ground Survey – Instrumentation and Methods

During the LiDAR survey, static (1 Hz recording frequency) ground surveys were conducted over either known or set monuments.  Monument coordinates are provided in Table 2.2 and shown in Figure 2.2 for the AOI.  After the airborne survey, the static GPS data are processed using triangulation with continuous operation stations (CORS) and checked using the Online Positioning User Service (OPUS) to quantify daily variance.  Multiple sessions are processed over the same monument to confirm antenna height measurements and reported position accuracy.

#### 2.2.1 Instrumentation

For this study area all Global Navigation Satellite System (GNSS) survey work used a Trimble GPS receiver model R7 with a Zephyr Geodetic antenna and ground plane for static control points.  A Trimble GPS R8 unit is used primarily for RTK work but when needed, it can be used as a static receiver as well. For RTK data, the collector begins recording after remaining stationary for 5 seconds then calculating the pseudo range position from at least three epochs with the relative error under 1.5cm horizontal and 2cm vertical. All GPS measurements are made with dual frequency L1-L2 receivers with carrier-phase correction.

#### 2.2.2 Monumentation

Whenever possible, existing and established survey benchmarks shall serve as control points during LiDAR acquisition including those previously set by Watershed Sciences. In addition to NGS, the county surveyor’s offices and ODOT often establish their own benchmarks. NGS benchmarks are preferred for control points. In the absence of NGS benchmarks, county surveys, or ODOT monumentation, Watershed Sciences produces our own monuments.  These monuments are spaced at a minimum of one mile and every effort is made to keep these monuments within the public right of way.  If monuments are required on private property, consent from the owner is required. All monumentation is done with 5/8” x 24” or 30” rebar topped with an aluminum cap.

#### 2.2.3 Methodology

Each aircraft is assigned a ground crew member with two R7 receivers and an R8 receiver. The ground crew vehicles are equipped with standard field survey supplies and equipment including safety materials. All data points are observed for a minimum of two survey sessions lasting no fewer than 6 hours.  At the beginning of every session the tripod and antenna are reset, resulting in two independent instrument heights and data files.  Data are collected at a rate of 1Hz using a 10 degree mask on the antenna.

The ground crew uploads the GPS data to our FTP site on a daily basis to be collected by the office for PLS oversight, QA/QC review and post-processing.  OPUS processing triangulates the monument position using 3 CORS stations resulting in a fully adjusted position. CORPSCON 6.0.1 software is used to convert the geodetic positions from the OPUS reports. After multiple days of data have been collected at each monument, accuracy and error ellipses are calculated. This information leads to a rating of the monument based on FGDC-STD-007.2-1998 Part 2 table 2.1 at the 95% confidence level.

All GPS measurements are made during periods with PDOP less than or equal to 3.0 and with at least 6 satellites in view of both a stationary reference receiver and the roving receiver. RTK positions are collected on 20% of the flight lines and on bare earth locations such as paved, gravel or stable dirt roads, and other locations where the ground is clearly visible (and is likely to remain visible) from the sky during the data acquisition and RTK measurement period(s). In order to facilitate comparisons with LiDAR measurements, RTK measurements are not taken on highly reflective surfaces such as center line stripes or lane markings on roads.  In addition, it is desirable to include locations that can be readily identified and occupied during subsequent field visits in support of other quality control procedures described later.  Examples of identifiable locations would include manhole and other flat utility structures that have clearly indicated center points or other measurement locations. In the absence of utility structures, a PK nail can be driven into asphalt or concrete and marked with paint.

Table 2.2.  Base Station Surveyed Coordinates, (NAD83/NAVD88, OPUS corrected) used for kinematic post-processing of the aircraft GPS data for the Yambo Study Area.

|  | Datum NAD83 (HARN) | GRS80 (Geoid 03) |
| --- | --- | --- |
| PID | Lat | Long | Ellips |
| Yambo_002 | 45 10 04.02192 | 123 08 27.18124 | 27.979 |
| Yambo_001 | 45 14 40.80509 | 123 07 47.39043 | 26.920 |
| YB_ALR1 | 45 09 11.87802 | 123 10 04.42373 | 27.153 |
| YB_ALR2 | 45 09 10.55025 | 123 04 40.87143 | 26.931 |
| YB_ALR3 | 45 09 01.18776 | 123 13 02.50809 | 27.021 |
| YB_RI1 | 45 16 38.07885 | 123 12 39.76092 | 32.605 |
| YB_RI2 | 45 13 29.37686 | 123 13 57.64191 | 27.662 |
| WB9_AR2 | 44 57 08.25321 | 123 16 10.74392 | 47.350 |
| YB2_PWH1 | 45 01 32.88251 | 123 19 12.71976 | 32.621 |
| YB2_LW1 | 45 02 32.67450 | 123 16 00.10390 | 35.623 |
| WV11_EG3 | 45 17 56.90315 | 123 19 22.02617 | 117.408 |
| YB_RI3 | 45 03 41.76302 | 123 38 38.51435 | 107.284 |
| YB_RI4 | 45 04 44.78105 | 123 36 43.31042 | 92.539 |
| YB_RI5 | 44 50 24.05343 | 123 39 33.66278 | 319.384 |
| YB_LW3 | 45 02 03.52089 | 123 51 50.38801 | 109.729 |
| YB_LW5 | 44 46 16.73625 | 123 49 29.32957 | 57.052 |
| YB_LW4 | 44 46 40.77293 | 123 54 32.04912 | -1.573 |
| YB_RI6 | 45 09 52.41733 | 123 37 13.50468 | 421.961 |
| YBRI6 | 45 01 32.04708 | 123 57 52.15663 | -18.835 |
| YB_LW7 | 45 10 08.66426 | 123 37 28.28248 | 453.991 |
| YB5_PWH2 | 45 09 55.09298 | 123 40 15.05132 | 421.849 |
| YB5_PWH1 | 45 08 49.66036 | 123 39 13.72549 | 273.112 |
| YB5_DB2 | 45 13 37.49404 | 123 44 06.71446 | 908.309 |
| YB_DB1 | 45 10 34.38212 | 123 34 08.69834 | 384.902 |
| YB5_DB4 | 45 16 34.05079 | 123 48 52.74602 | 12.002 |
| YB5_DB3 | 45 17 25.47599 | 123 42 07.33694 | 83.695 |
| YB8_PWH1 | 45 17 27.89020 | 123 14 54.07926 | 45.501 |
| YB8_PWH2 | 45 19 48.06449 | 123 13 57.11501 | 46.432 |
| YB8_PWH3 | 45 15 53.64665 | 123 19 13.85714 | 419.795 |
| YB5_EG1 | 45 12 46.32075 | 123 45 21.85479 | 936.554 |
| YB8_DB1 | 45 07 51.72000 | 123 17 05.03728 | 25.910 |
| YB6_PWH1 | 45 18 13.25004 | 123 52 35.04928 | 246.589 |
| YB_LW2 | 45 01 49.45785 | 123 55 56.01333 | 9.440 |
| NC2_DB4 | 44 57 41.05701 | 123 54 25.27865 | 224.796 |
| YB4_PWH1 | 45 01 49.74323 | 123 57 14.76443 | -17.033 |

Figure 2.2. Base stations for the Yambo Study Area.

For data delivered to date, 12,171 RTK (Real-time kinematic) points were collected in the study area.  Figures 2.3 shows detailed views of selected RTK locations for the area delivered to date.

Figure 2.3.  Selected RTK point locations in the study area for delivery areas 2 and 3; images are NAIP orthophotos.

Figure 2.4.  Selected RTK point locations in the study area for delivery areas 4 and 5; images are NAIP orthophotos.  The town featured from delivery area 4 is Lafayette, OR.

Figure 2.5.  Selected RTK point locations in the study area for delivery areas 1, 6 and 7; images are NAIP orthophotos.

3. Accuracy

## 3.1 Relative Accuracy

Relative Accuracy Calibration Results

Relative accuracy refers to the internal consistency of the data set and is measured as the divergence between points from different flightlines within an overlapping area.  Divergence is most apparent when flightlines are opposing.  When the LiDAR system is well calibrated the line to line divergence is low (<10 cm).  Internal consistency is affected by system attitude offsets (pitch, roll and heading), mirror flex (scale), and GPS/IMU drift.  Flightline offsets may be visible in flat sections of the dataset due to changes in the ground surface over time (e.g. the plowing of a field during the three month period that the data were collected).

Relative accuracy statistics are based on the comparison of 320 flightlines and over one billion points.  Relative accuracy is reported for the portion of the study area shown in Figure 3.1 below.

- Project Average = 0.23 ft (0.07 m)

- Median Relative Accuracy = 0.23 ft (0.07 m)

- 1( Relative Accuracy = 0.28 ft (0.08 m)

- 2( Relative Accuracy = 0.37 ft (0.11 m)

Figure 3.1.  Relative Accuracy Covered Area.

Figure 3.2.  Statistical relative accuracies, non slope-adjusted.

Figure 3.3.  Percentage distribution of relative accuracies, non slope-adjusted.

## 3.2 Absolute Accuracy

Absolute accuracy compares known RTK ground survey points to the closest laser point.  For the Yambo Study Area, 12,171 RTK points were collected for data delivered to date.  Absolute accuracy is reported for the portion of the study area shown in Figure 3.4 and reported in Table 3.1 below.  Histogram and absolute deviation statistics are reported in Figures 3.5 and 3.6.

Table 3.1.  Absolute Accuracy – Deviation between laser points and RTK survey points.

| Sample Size (n): 12,171 |
| --- |
| Root Mean Square Error (RMSE): 0.12 ft (0.04m) |
| Standard Deviations | Deviations |
| 1 sigma (σ): 0.11 ft (0.03 m) | Minimum ∆z: -0.60 ft (-0.18 m) |
| 2 sigma (σ): 0.25 ft (0.08 m) | Maximum ∆z: 0.41 ft (0.13 m) |
|  | Average ∆z: 0.09 ft (0.03 m) |

Figure 3.4.  Absolute Accuracy Covered Area.

Figure 3.5.  Yambo Study Area histogram statistics

Figure 3.6.  Yambo Study Area point absolute deviation statistics.

# 4. Data Density/Resolution

## 4.1 Density Statistics

Some types of surfaces (i.e. dense vegetation or water) may return fewer pulses than the laser originally emitted.  Therefore, the delivered density can be less than the native density and vary according to terrain, land cover and water bodies.  Density histograms and maps (Figures 4.1 – 4.4) have been calculated based on first return laser point density and ground-classified laser point density.

Table 4.1. Average density statistics for Yambo Study Area data delivered to date.

| Average Pulse Density (per square ft) | Average Pulse Density (per square m) | Average Ground Density (per square ft) | Average Ground Density (per square m) |
| --- | --- | --- | --- |
| 0.85 | 9.17 | 0.10 | 1.06 |

Figure 4.1.  Histogram of first return laser point density for data delivered to date.

Figure 4.2. First return laser point densities per 0.75' USGS Quad for data delivered to date.

Ground classifications were derived from ground surface modeling.  In areas where the ground model failed, classifications were manually performed by reseeding the ground model, usually under dense vegetation and/or at breaks in terrain, steep slopes and at bin boundaries.

Figure 4.3. Histogram of ground-classified laser point density for data delivered to date.

Figure 4.4. Ground-classified laser point density per 0.75’ USGS Quad for data delivered to date.

Figure 4.5. Ground point density data tends to be lower in heavily forested areas, and higher in areas with less dense vegetation.

# 5. Selected Imagery

Figure 5.1. View of Nestucca River, one mile north east of McGuire Reservoir. First image derived from highest hit LiDAR, second image derived from bare earth LiDAR, third image derived from NAIP orthophoto draped over highest hit LiDAR.

Figure 5.2. Section of Upper Nestucca River in Siuslaw National Forest, viewed from the south. Top image derived from highest hit LiDAR, bottom image derived from bare earth LiDAR.

Figure 5.3.  Siuslaw National Forest near Blaine Road, East of Beaver, Oregon. Image is a three dimensional LiDAR point cloud with RGB values extracted from a NAIP orthophoto.

Figure 5.4.  Summit of Mount Hebo.  Image is a three dimensional LiDAR point cloud with RGB values extracted from a NAIP orthophoto.

Figure 5.5.  Ridge and clear cut located approximately 2.5 miles, southeast of Grand Ronde Mountain.

Figure 5.6.  Town  of Sheridan, Oregon. View from the North.

Figure 5.7.  Forested area 6 miles south of Grand Ronde.  Top: LiDAR derived highest hit face colored by 2009 NAIP imagery. Middle: LiDAR derived highest hit surface colored by vegetation height. Bottom: LiDAR bare earth surface colored by elevation.

Figure 5.8.  View of Siuslaw National Forrest from the North West.  Top image derived from highest hit LiDAR and NAIP image overlay, lower image derived from bare earth LiDAR.

Figure 5.9. Agricultural land 3 miles north of Siletz, OR.  Top image derived from highest hit LiDAR with a NAIP Orthophoto overlay, middle image derived from highest hit LiDAR, lower image derived from bare earth LiDAR.

Figure 5.10.  Forested area 8.5 miles south west of Grande Ronde. Top: LiDAR derived highest hit surface colored by 2009 NAIP imagery. Middle: LiDAR derived highest hit surface colored by vegetation height. Bottom: LiDAR bare earth surface colored by elevation.

# Footnotes

Nadir refers to the perpendicular vector to the ground directly below the aircraft. Nadir is commonly used to measure the angle from the vector and is referred to a “degrees from nadir”.

Online Positioning User Service (OPUS) is run by the National Geodetic Survey to process corrected monument positions.

GNSS: Global Navigation Satellite System consisting of the U.S. GPS constellation and Soviet GLONASS constellation

U.S. Army Corps of Engineers , Engineer Research and Development Center Topographic Engineering Center software

Federal Geographic Data Committee Draft Geospatial Positioning Accuracy Standards

# Text boxes

Base Station with RTK Radio

Base Station in the Yambo Study Area

LiDAR Remote Sensing Data Collection

Department of Geology and Mineral Industries

Yambo Study Area

October 30, 2010