Identification_Information:

Citation:

Citation_Information:

Originator: JALBTCX

Publication_Date: 20060501

Publication_Time: 06410525Z

Title: ASCII XYZ (First Return)

Edition: 2006

Series_Information:

Series_Name: 2006_NCMP_SC_001g_TF

Issue_Identification: 2006

Publication_Information:

Publication_Place: San Diego, CA

Publisher: Fugro Pelagos, Inc.

Larger_Work_Citation:

Citation_Information:

Series_Information:

Publication_Information:

Description:

Abstract:

The U.S. Army Corps of Engineers collects (by themselves and contractors)

and maintains LiDAR data including orthophotos in coastal areas of the

United States and its territories.  The Corps acquires this data in the

course of performing its mission of Flood Control, Navigation,

Environmental Engineering, and support for the Army and others.

These data were collected using a SHOALS-1000T hydrographic and topographic

LIDAR sensor.

Topographic: Altitude 500m, Spot Spacing 1.3m x 1.4m

Purpose:

The purpose of this survey was to obtain the existing conditions of the

beach and near shore in support of the Joint Airborne LIDAR Bathymetric

Technical Center of Expertise National Coastal mapping Program.

Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Range_of_Dates/Times:

Beginning_Date: 20051211

Ending_Date: 20060113

Multiple_Dates/Times:

Currentness_Reference: Ground Condition

Status:

Progress: Complete

Maintenance_and_Update_Frequency: As needed

Spatial_Domain:

Bounding_Coordinates:

West_Bounding_Coordinate: -078.603767

East_Bounding_Coordinate: -078.551036

North_Bounding_Coordinate: 33.855262

South_Bounding_Coordinate: 33.840685

Keywords:

Theme:

Theme_Keyword_Thesaurus: None

Theme_Keyword: LiDAR

Theme_Keyword: Bathymetry

Theme_Keyword: Topography

Theme_Keyword: ASCII XYZ (First Return)

Theme_Keyword: Survey

Place:

Place_Keyword_Thesaurus: Geographic Names Information System

Place_Keyword: South Carolina

Place_Keyword: Atlantic

Place_Keyword: United States

Stratum:

Stratum_Keyword_Thesaurus: None

Stratum_Keyword: Surface

Temporal:

Temporal_Keyword_Thesaurus: None

Temporal_Keyword: 2006

Access_Constraints: None

Use_Constraints:

These data depict the heights at the time of the survey and  are only accurate for

that time. Acknowledgement of the Joint  Airborne LIDAR Bathymetry Center of

Expertise (JALBTCX) would  be appreciated in any publications or derived products.

Point_of_Contact:

Contact_Information:

Contact_Person_Primary:

Contact_Organization_Primary:

Contact_Organization: JALBTCX

Contact_Address:

Address_Type: mailing and physical address

Address: 7225 Stennis Airport Road, STE100

City: Kiln

State_or_Province: MS

Postal_Code: 39556

Country: USA

Contact_Voice_Telephone: (228) 252-1103

Hours_of_Service: 8 am to 5 pm Monday through Friday

Data_Set_Credit: Fugro Pelagos, Inc.

Security_Information:

Native_Data_Set_Environment:

ASCII XYZ

Cross_Reference:

Citation_Information:

Series_Information:

Publication_Information:

Data_Quality_Information:

Attribute_Accuracy:

Attribute_Accuracy_Report: N/A

Logical_Consistency_Report: See Process Step

Completeness_Report: See Process Step

Positional_Accuracy:

Horizontal_Positional_Accuracy:

Horizontal_Positional_Accuracy_Report:

The data has been collected and compiled to meet the  3m (2

sigma) accuracy specification.

Vertical_Positional_Accuracy:

Vertical_Positional_Accuracy_Report:

The data has been collected and compiled to meet the  30cm (2

sigma) accuracy specification.

Lineage:

Source_Information:

Source_Citation:

Citation_Information:

Originator:

Publication_Date: 20060501

Publication_Time: 06410525Z

Title: ASCII XYZ (First Return)

Edition: 2006

Series_Information:

Series_Name: 2006_NCMP_SC_001g_TF

Issue_Identification: 2006

Publication_Information:

Publication_Place: San Diego, CA

Publisher: Fugro Pelagos, Inc.

Larger_Work_Citation:

Citation_Information:

Series_Information:

Publication_Information:

Source_Scale_Denominator: N/A

Type_of_Source_Media: Digital Data

Source_Time_Period_of_Content:

Time_Period_Information:

Single_Date/Time:

Range_of_Dates/Times:

Beginning_Date:

Ending_Date:

Multiple_Dates/Times:

Source_Currentness_Reference: Ground Condition

Source_Citation_Abbreviation: JALBTCX

Source_Contribution: Fugro Pelagos, Inc.

Process_Step:

Process_Description:

Acquisition

Data were acquired using a SHOALS-1000T.  Sensor  orientation was

measured using a POS AV 410, while  images were acquired at 1Hz

using a Duncantech  DT4000 digital camera.  Prior to survey PDOP

was  checked and missions planned to avoid PDOP greater  than 3.5.

During survey the plane was always within  30km of a GPS ground

control point, to provide a good  quality position solution.  Final

positions were determined  using a post-processed inertially aided

Kinematic GPS  (KGPS) solution.  GPS ground control data were

acquired  at 1Hz.

Data received by the airborne system were continually  monitored

for data quality during acquisition operations.   Display windows

showed coverage and information about  the system status.  In

addition, center waveforms at 5Hz  were shown.  All of this

information allowed the airborne  operator to assess the quality of

data being collected.

Data were processed in the field to very coverage and  data quality.

Processing

Data were processed using the SHOALS Ground Control  System (GCS).

The GCS includes links to Applanix  POSPac software for GPS and

inertial processing, and  IVS Fledermaus software for data

visualization, 3D editing  and tie-line analysis.  Data were

processed in NAD83  horizontal and vertical datum.  Data were later

converted  to the NAVD88 vertical datum using the GEOID03 model.

Fugro in-house utilities were used to extract XYZ data from  the

native LIDAR files and split the data in to pre-defined  boxes,

each covering approximately 5km of shoreline.   ASCII files include

Longitude Latitude Elevation Date Time  Intensity (Topo) or Depth

Confidence (Hydro).

Process_Date: 20060501

Process_Contact:

Contact_Information:

Contact_Person_Primary:

Contact_Organization_Primary:

Contact_Organization: Fugro Pelagos, Inc.

Contact_Person: Carol Lockhart

Contact_Position: Hydrographic LIDAR Technical Manager

Contact_Address:

Address_Type: mailing and physical address

Address: 3738 Ruffin Road

City: San Diego

State_or_Province: CA

Postal_Code: 92123

Country: USA

Contact_Voice_Telephone: (858) 292-8922

Hours_of_Service: 8 am to 5 pm Monday through Friday

Spatial_Data_Organization_Information:

Spatial_Reference_Information:

Horizontal_Coordinate_System_Definition:

Geographic:

Latitude_Resolution: 0.00000001

Longitude_Resolution: 0.00000001

Geographic_Coordinate_Units: Degree

Geodetic_Model:

Horizontal_Datum_Name: GCS_North_American_1983

Ellipsoid_Name: GRS_1980

Semi-major_Axis: 6378137.000

Denominator_of_Flattening_Ratio: 0.003352811

Vertical_Coordinate_System_Definition:

Altitude_System_Definition:

Altitude_Datum_Name: NAVD88

Altitude_Resolution: 0.01

Altitude_Distance_Units: Meters

Altitude_Encoding_Method: Explicit elevation coordinate included

with horizontal coordinates

Depth_System_Definition:

Depth_Datum_Name: NAVD88

Depth_Resolution: 0.01

Depth_Distance_Units: Meters

Depth_Encoding_Method: Explicit depth coordinate included with

horizontal coordinates

Entity_and_Attribute_Information:

Detailed_Description:

Entity_Type:

Attribute:

Attribute_Domain_Values:

Attribute_Value_Accuracy_Information:

Overview_Description:

Distribution_Information:

Distributor:

Contact_Information:

Contact_Person_Primary:

Contact_Organization_Primary:

Contact_Organization: JALBTCX

Contact_Address:

Address_Type: mailing and physical address

Address: 7225 Stennis Airport Road, STE100

City: Kiln

State_or_Province: MS

Postal_Code: 39556

Country: USA

Contact_Voice_Telephone: (228) 252-1103

Hours_of_Service: 8 am to 5 pm Monday through Friday

Standard_Order_Process:

Digital_Form:

Digital_Transfer_Information:

Digital_Transfer_Option:

Online_Option:

Computer_Contact_Information:

Network_Address:

Dialup_Instructions:

OffLine_Option:

Recording_Capacity:

Available_Time_Period:

Time_Period_Information:

Single_Date/Time:

Range_of_Dates/Times:

Multiple_Dates/Times:

Metadata_Reference_Information:

Metadata_Date: 20060501

Metadata_Contact:

Contact_Information:

Contact_Person_Primary:

Contact_Organization_Primary:

Contact_Organization: Fugro Pelagos, Inc.

Contact_Person: Carol Lockhart

Contact_Position: Hydrographic LIDAR Technical Manager

Contact_Address:

Address_Type: mailing and physical address

Address: 3738 Ruffin Road

City: San Diego

State_or_Province: CA

Postal_Code: 92123

Country: USA

Contact_Voice_Telephone: (858) 292-8922

Hours_of_Service: 8 am to 5 pm Monday through Friday

Metadata_Standard_Name: FGDC Content Standards for Digital Geospatial Metadata

Metadata_Standard_Version: FGDC-STD-001-1998

Metadata_Time_Convention: Universal time

Metadata_Security_Information: