Elevation QA Report

Project:       Contractor:

Data Delivery Date:   Date Data Reviewed:

Reviewer:    Total Square Miles Reviewed:

Elevation Type:     Format:       Grid Spacing:    Tile size:

Projection:       Zone:       Datum:         Units:

Licensing:           Metadata:

Materials Received:

Vertical Accuracy Test Performed:       Test Point Source:            RMSE:

Vertical Accuracy Test Notes:

QA Review Summary:

11-2-2010

LiDAR Quality Control (QC) Review Process

Preparation:

-Metadata reviewed to determine data projection, datum, format, etc.

-If ARRA contract, check for raw .LAS files, classified .LAS files, breaklines, blind control points,

and DEM in Image or Grid format

-Open data in Global Mapper

Vertical accuracy testing:

-If ARRA contract, use Vertical Accuracy Test Worksheet to perform RMSE on 20 blind point

positions provided by contractor

Inspection and Correction of data:

-Minimum and maximum elevations in dataset; correct if in error

-Appropriate hydro flattening as specified in V13 Lidar Specification (For ARRA/GPSC Data)

-Data void areas

-Data spikes

-Tile edge seam lines

-Non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Elevation errors - raised/lowered areas/tiles

-Other surface treatment anomalies

-Check DRGs for correct elevations and horizontal positioning (if test points not available)

-Create footprint (project boundary) shape file and establish square miles

During Inspection, identify data errors and create “error” file folder:

-Capture geo-referenced JPG or TIFF image(s) of identified errors

-Copy to Error file

During Inspection, level elevations and remove artifacts (these two steps not done for ARRA data):

-Level smoothing to remove non-bare earth surface artifacts (structures, bridges, vegetation, etc.)

-Level data spikes where possible

Export image files and create project Elevation QC Review Report:

-Export ERDAS Imagine image files in native projection and resolution

-If ARRA, Copy Vertical Accuracy Test Worksheet into QC Report

-Place QC Review Process and Project Area Extent into QC Report

-If rejected, attach sample geo-referenced JPG or TIFF error images with an explanation of reason

-If rejected, restart QC process when replacement data is received

-Provide completed Elevation QC Review Report to Elevation Supervisor for final viewing

-Add QC Report, footprint, Imagine image(s), and Error file to original data file for final shipment to EROS

TN_OSMRE_2011 Area Extent

| Vertical Accuracy Statistic Worksheet |  |  |  |
| --- | --- | --- | --- |
| elevations units in feet |  |  |  |
| A | D | E | F | G | H |  |
| Point | Point | z | z |  |  | TN OSMRE LiDAR |
| number | description | Vendor | NGTOC | diff in z | (diff in z)2 |  |
| 1 | 201 | 1515.600 | 1515.402 | 0.198 | 0.039 |  |
| 2 | 202 | 1277.490 | 1277.51 | -0.020 | 0.000 |  |
| 3 | 203 | 2660.430 | 2660.238 | 0.192 | 0.037 |  |
| 4 | 204 | 2879.870 | 2879.45 | 0.420 | 0.176 |  |
| 5 | 205 | 2817.330 | 2816.936 | 0.394 | 0.155 |  |
| 6 | 206 | 1448.280 | 1448.62 | -0.340 | 0.116 |  |
| 7 | 207 | 1355.660 | 1355.563 | 0.097 | 0.009 |  |
| 8 | 208 | 1370.590 | 1370.407 | 0.183 | 0.033 |  |
| 9 | 209 | 1338.330 | 1338.033 | 0.297 | 0.088 |  |
| 10 | 210 | 1763.770 | 1763.69 | 0.080 | 0.006 |  |
| 11 | 211 | 1336.550 | 1336.865 | -0.315 | 0.099 |  |
| 12 | 212 | 1085.460 | 1085.056 | 0.404 | 0.163 |  |
| 13 | 213 | 1064.110 | 1064.014 | 0.096 | 0.009 |  |
| 14 | 214 | 2558.090 | 2557.85 | 0.240 | 0.058 |  |
| 15 | 215 | 1706.030 | 1705.89 | 0.140 | 0.020 |  |
| 16 | 216 | 1367.740 | 1367.569 | 0.171 | 0.029 |  |
| 17 | 217 | 1484.030 | 1483.908 | 0.122 | 0.015 |  |
| 18 | 218 | 1363.480 | 1363.24 | 0.240 | 0.058 |  |
| 19 | 219 | 1499.610 | 1499.435 | 0.175 | 0.031 |  |
| 20 | 220 | 1314.920 | 1314.685 | 0.235 | 0.055 |  |
|  |  |  |  | sum | 1.198 |  |
| Outlier: a control point located in an area that does not reflect the true ground elevation, i.e. bridges, etc. | average | 0.060 |  |
|  | RMSE | 0.245 | 0.245 ft RMSEz = 7.47 cm |
|  | NSSDA | 0.480 |  |

Errors…

*Note – This error, being the only one, was subsequently fixed in the DEM by NGTOC LiDAR staff; this

error still exists in the LAS.