Horizon’s, Inc.

# LiDAR Acquisition/Processing/Quality Control

13582 Utah 1.4 Meter Area

#### LiDAR Acquisition

LiDAR Acquisition.  LiDAR acquisition for this project was performed by  in a  equipped with an LH System  LiDAR system including an inertial measuring unit (IMU) and a dual frequency GPS receiver.  Acquisition was accomplished between 10/29/2006 and 5/15/2007. Maps identifying the flight lines and LiDAR collection log sheets containing information regarding flights, times, conditions, etc are included in the Appendix.  The LiDAR flight specifications follow:

| Field of View | 29 Degrees |
| --- | --- |
| Altitude | 4000 feet AMT |
| Scan Rate | 45 Hz |
| Pulse Rate | 66000 kHz |
| Airspeed | 140 knots |
| Average Post Spacing | 1.4 meters |
| Average Swath Width | 2265 feet |
| Intensity Mode | 4+3 |
| Total Flight Lines: | 375 |
| Number of Lifts | 13 |

# GPS Data Collection

GPS Data Collection.  A GPS receiver was in constant operation over a  control point during flight acquisition.  The base station identification and location are listed in the following table. Base station information is also included in the Appendix.

| Station | Location |
| --- | --- |
| LO0622 | 40 37 05.78236 111 59 47.19312 |

# GPS base station

# GPS Data Processing

GPS Data Processing. All GPS phase data was post processed with continuous kinematic survey techniques using “On the Fly” (OTF) integer ambiguity resolution.  The GPS data was processed with forward and reverse processing algorithms.  The results from each process, using the data collected at the airport, were combined to yield a single fixed integer phase differential solution of the aircraft trajectory.  Plots of altitude and the forward and reverse GPS solution residuals are included in the Appendix. The differences between the forward to reverse solution within the project area were within project specifications (<10cm) in both the horizontal and vertical components, indicating a valid and accurate solution.

# IMU Data Processing

IMU Data Processing. An IMU was used to record precise changes in position and orientation of the LIDAR scanner at a rate of 200 Hz.  All IMU data was processed post flight with a filter to integrate inertial measurements and precise phase differential GPS positions.  The resulting solution contains geodetic position, omega, phi, kappa, and time for subsequent merging with the laser ranging information.LiDAR Data Processing

LIDAR Data Preprocess

Flight Line Data Acquisition/Quality Control Check.  LiDAR data and the IMU files were processed together using LIDAR processing software.  The data set for each flight line was checked for project area coverage, data gaps between overlapping flight lines, and tension/compression areas (areas where data points are more or less dense than the average project specified post spacing). Based on this check it appears the entire project area is covered without gaps. LiDAR Coverage Check and Line Overlap Check Diagrams are included in Appendix.

Boresighting Process.  Pre-processing of LiDAR corrects for rotational, atmospheric, and elevation differences that are inherent to LiDAR data sets. This process is called boresighting. LiDAR data was collected for bi- and cross-directional flight lines over the project area. Using an iterative process that involves analyzing raster difference calculations the Omega, Phi, Kappa angle corrections of the LiDAR instrument were determined. The corrections were applied to the LiDAR data set for the project area.

Vertical Accuracy Check. Extensive comparisons were made of vertical and horizontal positional differences between points common to two or more LiDAR flight lines. This was done for the airport bore-sight testing area and the project area. All flight lines (airport and project) were within project specifications for vertical accuracy.

LiDAR Intensity Check.  An intensity raster for each flight line was generated.  The raster was checked and verified that intensity was recorded for each LiDAR point.

Project Coordinate System.  LiDAR preprocessing software outputs data to its corresponding UTM zone in meters and a GRS80 ellipsoidal height.  LiDAR data was transformed to a project coordinate system of   NAD83 NAVD88 Meters UTM zone 12 Geoid 03 .

Vertical Bias Correction.  LiDAR has a consistent vertical offset.  LiDAR ground points were compared to independently surveyed and positioned ground control points in the project area.  Based on the results of these comparisons, the LiDAR data was vertically biased down to the ground.

Project Ground Control Check. Comparisons between on-site ground survey control points and LiDAR data yielded the following results:

1 Meter Area

| Vertical Accuracy (RMSE) | 0.073 |
| --- | --- |
| Standard Deviation | 0.073 |
| Mean Difference | 0.013 |
| Number of Points | 39 |

LiDAR Data Surfacing Process.

Raw LiDAR Data Set.  LiDAR data in overlap areas of project flight lines was removed and data from all swaths was merged into a single data set.  The data set was trimmed to the digital project boundary including an additional buffer zone (buffer zone assures adequate contour generation from the DEM).  Resulting data set is the Raw LiDAR data. The Raw LiDAR data set was processed through a minimum block mean algorithm and points were classified as either bare earth or non-bare earth.  User developed “macros” that factor mean terrain angle and height from the ground, were used to determine bare earth point classification.

LiDAR Surfacing Process.  The surfacing process is a 2D-edit procedure that ensures the accuracy of the automated feature classification. Editors used a combination of imagery, intensity of the LiDAR reflection and tin-editing software to assess points.  The resulting data set is 2D Surfaced Bare Earth. The LiDAR data is filtered using a quadric error metric to remove redundant points. This method leaves points where there is a change in the slope of surfaces (road ditches) and eliminates points from evenly sloped terrain (flat field) where the points do not affect the TIN LiDAR data. The resulting data set is 2D Surfaced/Filtered Bare Earth

Appendix Items.

Flight Map 1.4 Meter Area

LiDAR Collection Logsheet

Lift 6 Page 1

Lift6 Page2

Diagram – GPS Solution Residuals

F and R Lift 6

F and R RMS Lift 6

Height Lift 6

PDOP Lift 6

Diagram – Aircraft Trajectory Plot

Trajectory Lift 6

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 6

LiDAR Collection Logsheet

Lift 7 Page 1

Lift 7 Page 2

Diagram – GPS Solution Residuals

F and R combined Lift 7

F and R RMS Lift 7

Height Lift 7

PDOP Lift 7

Diagram – Aircraft Trajectory Plot

Trajectory Lift 7

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 7

LiDAR Collection Logsheet

Lift 12 Page 1

lift 12 Page 2

Diagram – GPS Solution Residuals

F and R combined Lift 12

F and R RMS Lift 12

Height Lift 12

PDOP Lift 12

Trajectory Lift 12

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 12

LiDAR Collection Logsheet

Lift 13 Page 1

Lift13 Page 2

Lift13 Page 3

Diagram – GPS Solution Residuals

F and R combined Lift 13

F and R RMS Lift 13

Height Lift 13

PDOP Lift 13

Diagram – Aircraft Trajectory Plot

Trajectory Lift 13

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 13

LiDAR Collection Logsheet

Lift 17 Page 1

Diagram – GPS Solution Residuals

F and R combined Lift 17

F and R RMS Lift 17

Height Lift 17

PDOP Lift 17

Trajectory Lift 17

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 17

LiDAR Collection Logsheet

Lift 19 Page 1

Lift 19 Page 2

Diagram – GPS Solution Residuals

F and R combined Lift 19

F and R RMS Lift 19

Height Lift 19

PDOP Lift 19

Trajectory Lift 19

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 19

LiDAR Collection Logsheet

Lift 22 Page 1

Lift 22 Page 2

Diagram – GPS Solution Residuals

F and R combined Lift 22

F and R RMS Lift 22

Height Lift 22

PDOP Lift 22

Trajectory Lift 22

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 22

LiDAR Collection Logsheet

Lift 23 Page 1

Lift 23 Page 2

Diagram – GPS Solution Residuals

F and R combined Lift 23

F and R RMS Lift 23

Height Lift 23

PDOP Lift 23

Trajectory Lift 23

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 23

LiDAR Collection Logsheet

Lift 24 Page 1

Lift24 Page 2

Lift 24 Page 3

Diagram – GPS Solution Residuals

F and R combined Lift 24

F and R RMS Lift 24

Height Lift 24

PDOP Lift 24

Trajectory Lift 24

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 24

LiDAR Collection Logsheet

Lift 25 Page 1

Diagram – GPS Solution Residuals

F and R combined Lift 25

F and R RMS Lift 25

Height Lift 25

PDOP Lift 25

Trajectory Lift 25

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 25

LiDAR Collection Logsheet

Lift 26 Page 1

Diagram – GPS Solution Residuals

F and R combined Lift 26

F and R RMS Lift 26

Height Lift 26

PDOP Lift 26

Trajectory Lift 26

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 26

LiDAR Collection Logsheet

Lift 27 Page 1

Lift 27 Page 2

Diagram – GPS Solution Residuals

F and R combined Lift 27

F and R RMS Lift 27

Height Lift 27

PDOP Lift 27

Trajectory Lift 27

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 27

LiDAR Collection Logsheet

Lift 28 Page 1

Diagram – GPS Solution Residuals

F and R combined Lift 28

F and R RMS Lift 28

Height Lift 28

PDOP Lift 28

Trajectory Lift 28

Diagram – LiDAR Coverage Check for Project Lines

LiDAR Coverage Check Lift 28