TASK ORDER DETAIL

USGS CONTRACT:	 G10PC00057

CONTRACTOR: Woolpert

TASK ORDER NUMBER: G15PD00937

TASK NAME:	 Mesa County Lidar

The Contractor shall furnish all facilities, labor, materials, and equipment, unless specifically identified otherwise, to provide the mapping services and products in accordance with the specifications, terms, and conditions contained in Contract No. G10PC00057

, and the following requirements specific to this Task Order, and in accordance with Contractor’s proposal dated September 10th, 2015 and in the amount of:

Task Order Fixed Price

- DESCRIPTION/SPECIFICATIONS/WORK STATEMENT.

The following Section C additional requirements are applicable to this Task Order:

  - Statement of Work (SOW): Reference C.1 of the Contract. This task order is for Planning, Acquisition, processing, and derivative products of lidar data to be collected at two points per square meter and nominal pulse spacing (NPS) of 0.7 meters. Lidar data, and derivative products produced in compliance with this task order are based on the “U.S. Geological Survey National Geospatial Program Lidar Base Specification Version 1.2”, which is incorporated by reference into this task order.  This specification may be viewed at http://pubs.usgs.gov/tm/11b4/. These lidar specifications are required baseline specifications. In addition to the Specification Requirements, this task order shall meet NEEA QL2. For any item which is not specifically addressed, the referenced Specification Version 1.2 will be the required specification authority.

This task order requests lidar surveys be collected for Mesa County, Colorado. The data is to be acquired and processed under the requirements identified in this task order. The total area of the Mesa County AOI is approximately 3,341 square miles. This project will require hydro-flattening.

An area of about 5.6 square miles within the main AOI will be collected at QL1. The nominal pulse spacing (NPS) will be .35 meters with a point density of 8 points per meter2.

    - KICK-OFF MEETING: A kick-off meeting shall be held to outline communication procedures that shall be followed for data acquisition with respect to verification of local ground conditions and vegetation requirements. This meeting shall be used as a forum to clarify and resolve collection condition issues. Local contact(s) shall be established to provide ground condition updates. The kick-off meeting shall be held no later than two (2) weeks after contract award and prior to data acquisition.

    - DATA ACQUISITION (COLLECTION): The contractor shall be responsible for acquisition of lidar data of sufficient density and quality to meet the requirements specified in the referenced Version 1.2 specification.

      - Collection area: The collection area shall be defined as the Defined Project Area, buffered by no less than 100-meters. The Project Area is defined in “Attachment A – Project Description and Diagram” and further delineated by the ESRI ArcShape file included as “Attachment B – Shape File(s)”

      - Nominal Pulse Spacing: Nominal Pulse Spacing (NPS) shall be no greater than 0.70 meters (QL2); assessment to be made against single swath, first return data located within the geometrically usable center portion (typically ~90%) of each swath.

      - Signal Returns The laser system shall be configured to collect multiple echoes per pulse, with a minimum of a first return and a last return and at least one additional intermediate return. All returns captured during acquisition shall be delivered. Return number shall be recorded.

      - GPS Times: shall be recorded as Adjusted GPS Time, at a precision sufficient to allow unique timestamps for each return. Adjusted GPS Time is defined to be Standard (or satellite) GPS time minus 1*109. See the LAS Specification for more detail.

      - Signal Strength: The signal strength (intensity) of each return pulse shall be recorded.

      - Clustering: The spatial distribution of geometrically usable points is expected to be uniform and free from clustering. In order to ensure uniform densities throughout the data set:

        - A regular grid, with cell size equal to the design 2*NPS will be laid over the data.

        - At least 90% of the cells in the grid shall contain at least 1 lidar point.

        - Clustering will be tested against the 1st return only data

        - Acceptable data voids identified elsewhere in this specification are excluded.

      - Control: Lidar shall be acquired using the following control specifications.

        - Supplemental Ground Control: Differentially corrected GPS Ground Control used to supplement the Airborne GPS positional accuracy.

        - Quality Check points:  The Contractor shall collect additional Ground Control Check Points in each project area which shall be delivered in ESRI Arc Shape format and will be used by the Government for validation.

          - Positional Accuracy Standards for Digital Geospatial Data (American Society for Photogrammetry and Remote Sensing, 2014) http://www.asprs.org/a/society/committees/standards/ASPRS_Positional_Accuracy_Standards_Edition1_Version100_November2014.pdf should be consulted to determine the minimum number of checkpoints required.  The quantity of checkpoints is linked to the size of the project’s AOI.  Adherence to the ASPRS recommendations is required, but in no case shall an NVA be based on less than 20 check points.

          - The ASPRS-recommended distribution of total number of check points between NVA and VVA assessments shall be met and checkpoints within each type shall be well-distributed across the entire project.  Within each assessment type, check points will be distributed among all constituent land cover types in approximate proportion to the areas of those land cover types.

          - Checkpoints for NVA assessments shall be located only in clear, open terrain, where there is a high probability that the sensor will have detected the ground surface without influence from surrounding vegetation (single return only, away from objects of low reflectivity).  Ground that has been plowed or disturbed is not acceptable.

          - The same check points may be used for NVA assessment of the point cloud and DEM.

          - VVA points should have survey areas sized with a minimum homogeneous area of (NPSx5)^2, with less than one-third of the required RMSEz deviation from a low-slope (less than 10 degrees) plane.

          - The checkpoint accuracy shall be 3 times the targeted accuracy of the lidar data.

          - NVA amd VVA are typically comprised of the following land cover categories (but not limited to):

            - NVA: Bare Earth/Open Terrain and Urban

            - VVA: Tall Weeds/Crops, Brush lands and Trees, and Forested and Fully

Grown

        - Check points shall not be incorporated into the contractor’s vertical solution.

      - Vertical Accuracy Requirements: Lidar collected under this task order shall meet or exceed these vertical accuracies. Assessment procedures shall comply with NDEP guidelines. See C.1.b.(i)(a) below for complete vertical accuracy reporting requirements.

RMSEZ = 10 cm

NVA = 19.6 cm 95% Confidence Level (Required Accuracy)

VVA = 29.4 cm 95th Percentile (Required Accuracy)

      - Positional Accuracy Validation: The absolute and relative accuracy of the data, both horizontal and vertical, relative to known control, shall be verified prior to classification and subsequent product development. A detailed report of this validation is a required deliverable

      - Relative Accuracy Requirements: Relative accuracy shall be <= 6-cm RMSEZ within swaths and <=8-cm RMSEZ between adjacent swaths with a maximum difference of ±16 cm.

      - Acquisition Window: Acquisition window shall the fall-winter 2015 leaf off window running through December 15th, 2015.

      - Swath Length: Refer to USGS Lidar Base Specification v 1.2, page 7 - section on Swath Size and Segmentation

      - Full Swath data shall be delivered Edge data from each swath shall not be trimmed from the delivered data.

      - Overlap: Flight line overlap is at the contractor’s discursion, but is cautioned to be vigorous to ensure there are no data gaps between the usable portions of the swaths and to ensure the nominal pulse density (NPD) can be achieved. Collections in high relief terrain are expected to require greater overlap. Any data with gaps between the geometrically usable portions of the swaths will be rejected.

      - Data Voids: Data Voids [areas => (4*NPS2), measured using 1st-returns only]  within a single swath are not acceptable, except:

        - where caused by water bodies

        - where caused by areas of low near infra-red (NIR) reflectivity such as asphalt or composition roofing; or

        - where appropriately filled-in by another swath

      - Data Acquisition Conditions:

        - Atmospheric: Cloud and fog-free between the aircraft and ground

        - Ground:

          - Snow free; very light, undrifted snow may be acceptable in special cases, with prior approval.

          - No unusual flooding or inundation, except in cases where the goal of the collection is to map the inundation.

        - Vegetation: Leaf-off is preferred, however:

          - As numerous factors will affect vegetative condition at the time of any collection, the USGS National Geospatial Program (NGP) only requires that penetration to the ground must be adequate to produce an accurate and reliable bare-earth surface suitable for incorporation into the 1/9 (3-meter) NED.

          - Collections for specific scientific research projects may be exempted from this requirement, with prior approval.

      - Time of Day:  Time of day is not of concern.

    - DATA PROCESSING AND HANDLING: The contractor shall be responsible for post processing of lidar data of sufficient density and quality to meet the requirements specified in the National Geospatial Program Lidar Base Specification Version 1.2. All processing should be carried out with the understanding that all point deliverables are required to be in fully compliant LAS format, v 1.4. Data producers are encouraged to review the LAS specification in detail. Specifications of the LAS datasets will be verified.

      - ACCURACY REPORTING

        - Data Accuracy: Data collected under this Task Order shall meet the National Standard for Spatial Database Accuracy (NSSDA) accuracy standards.  The NSSDA standards specify that vertical accuracy be reported at the 95 percent confidence level for data tested by an independent source of higher accuracy.  For example the metadata statement shall read, “Tested __ (meters, feet) vertical accuracy at 95 percent confidence level.”

          - Accuracy of the Lidar Point Cloud Data: The Absolute Accuracy is assessed by Nonvegetated Vertical Accuracy (NVA) of the Lidar Point Cloud data. This shall be calculated against TINs derived from the final calibrated and controlled swath data. The required accuracy (ACCZ) is: 19.6 cm at a 95% confidence level, derived according to NSSDA, i.e., based on RMSE of 10 cm in the “open terrain” or “urban areas” land cover category. This is a required accuracy.

          - Accuracy of the Derived DEM: The accuracy (ACCZ) of the derived DEM shall be calculated and reported in three (3) ways:

- RMSEz (Non-Vegetated): The required RMSEz is: ≤10 cm.

- Non-Vegetated Vertical Accuracy (NVA) The required NVA is: ≤19.6 cm at a 95% confidence level, derived according to NSSDA, i.e., based on RMSEz of 10 cm in the “open terrain” and/or “Urban” land cover categories. This is a required accuracy.

- Vegetated Vertical Accuracy (VVA): The required VVA is: ≤29.4 cm at a 95th percentile level, derived according to ASPRS Guidelines, Vertical Accuracy Reporting for lidar Data, i.e., based on the 95th percentile error in Vegetated land cover categories combined (Tall Grass, Brush, Forested Areas). This is a required accuracy.

      - Hydro Flattening Requirements:

        - Inland Ponds and Lakes:

          - ~2-acre or greater surface area (~350’ diameter for a round pond)

          - Flat and level water bodies (single elevation for every bank vertex defining a given water body).

          - The entire water surface edge must be at or just below the immediately surrounding terrain.

          - Long impoundments such as reservoirs, inlets, and fjords, whose water surface elevations drop when moving downstream, should be treated as rivers.

        - Inland Streams and Rivers:

          - 100’ nominal width: This should not unnecessarily break a stream or river into multiple segments. At times it may squeeze slightly below 100’ for short segments. Data producers should use their best professional judgment.

          - Flat and level bank-to-bank (perpendicular to the apparent flow centerline); gradient to follow the immediately surrounding terrain.

          - The entire water surface edge must be at or just below the immediately surrounding terrain.

          - Streams should break at road crossings (culvert locations). These road fills should not be removed from DEM. However, streams and rivers should not break at bridges. Bridges (as defined in the USGS Lidar Base Specification v1.1) shall be removed from the DEM. Instructions in the first two paragraphs of the ‘Digital Elevation Model Hydro-Flattening’ section of the v1.1 Base Specification regarding the use of breaklines applies also to non-hydrographic terrain generation below bridges. Any breaklines used to enforce a logical terrain surface below a bridge shall be considered a required deliverable of this task order.

● The bare earth surface below the bridge shall be a continuous logical interpolation of the apparent terrain lateral to the bridge deck.

● Where abutments are clearly visible, the bare earth interpolation shall begin at the junction of the bridge deck and approach structure. Where this junction is not clear the contractor shall use their best judgment to delineate the separation of below-bridge terrain from elevated bridge surface.

● Streams, rivers, and water bodies meeting the criteria for hydro-flattening in the Lidar Base Specification v1.1 shall be monotonically continuous where bridge decks have been removed.

        - Non-Tidal Boundary Waters:

          - Represented only as an edge or edges within the project area; collection does not include the opposing shore.

          - The entire water surface edge must be at or below the immediately surrounding terrain.

          - The elevation along the edge or edges should behave consistently throughout the project. May be a single elevation (i.e., lake) or gradient (i.e., river), as appropriate.

        - Tidal Waters:

          - Water bodies such as oceans, seas, gulfs, bays, inlets, salt marshes, very large lakes, etc. Includes any significant water body that is affected by tidal variations.

          - Tidal variations over the course of a collection, and between different collections, will result in discontinuities along shorelines. This is considered normal and these “anomalies” should be retained. The final DEM should represent as much ground as the collected data permits.

          - Variations in water surface elevation resulting in tidal variations during a collection should NOT be removed or adjusted, as this requires either the removal of ground points or the introduction of unmeasured ground into the DEM. The USGS NGP priority is on the ground surface, and accepts the unavoidable irregularities in water surface.

          - Scientific research projects in coastal areas often have very specific requirements with regard to how tidal land-water boundaries are to be handled. For such projects, the requirements of the research will take precedence.

    - DELIVERABLE PRODUCTS: The following deliverable products shall be produced from the lidar produced in C.1.b above.

      - Raw Point Cloud Data:

        - Fully compliant LAS v1.4, Point Record Format 6, 7, 8, 9, or 10. Proper use of the Overlap and Withheld bit flags is required.

        - LAS v1.4 deliverables with waveform data are to use external “auxiliary” files with the extension “.wdp” for the storage of waveform packet data. See the LAS v1.4 Specification for additional information.

        - Georeference information included in all LAS file headers (OGC WKT).

        - GPS times are to be recorded as Adjusted GPS Time, at a precision sufficient to allow unique timestamps for each return.

        - Intensity values, 16 bit linear rescaling. See the LAS v1.4 Specification for additional information.

        - Full swaths, all collected points to be delivered.

        - Swaths may be segmented, as described in the NGP Lidar Base Specification, at the contractor’s discursion if needed.

        - A report of the assessed relative vertical accuracy of the point cloud (smooth surface repeatability and overlap consistency).  Raw swath point cloud data shall meet the required accuracy levels before point cloud classification and derivative product generation.

        - A report of the assessed absolute vertical accuracy (NVA only) of the unclassified lidar point data in accordance with the guidelines set forth in the Positional Accuracy Standards for Digital Geospatial Data (American Society for Photogrammetry and Remote Sensing, 2014).  Raw swath point cloud data shall meet the required accuracy levels before point cloud classification and derivative product generation.

        - 1 file per swath, 1 swath per file.

      - Classified Point Cloud:

        - Fully compliant LAS v1.4, Point Record Format 6, 7, 8, 9, or 10 including “File Source ID.” Proper use of the Overlap and Withheld bit flags is required.

        - LAS v1.4 deliverables with waveform data are to use external “auxiliary” files with the extension “.wdp” for the storage of waveform packet data. See the LAS v1.4 Specification for additional information.

        - Georeference information included in LAS header (OGC WKT).

        - GPS times are to be recorded as Adjusted GPS Time, at a precision sufficient to allow unique timestamps for each return.

        - Intensity values, 16 bit linear rescaling. See the LAS v1.4 Specification for additional information.

        - Tiled delivery, without overlap

        - Classification Scheme (minimum):

          - Code 1 – Processed, but unclassified

          - Code 2 – Bare-earth ground

          - Code 7 – Noise (low or high, manually identified, if needed

          - Code 9 – Water

          - Code 10 – Ignored Ground (Breakline Proximity)

          - Code 17 – Bridge Decks

          - Code 18 – High Noise

        - Note: Classes 7 and 18 are included as a convenience for the data producer. It is not required that all “noise” be assigned to those Classes.

        - Note: Class 10, Ignored Ground, is for points previously classified as bare-earth but whose proximity to a subsequently added breakline requires that it be excluded during Digital Elevation Model (DEM) generation.

      - Bare Earth Surface (Raster DEM):

        - Cell Size shall be one (1.0) meter, and no less than the design Nominal Pulse Spacing (NPS).

        - Delivery in an industry-standard, GIS-compatible, 32-bit floating point raster format (ERDAS .IMG preferred)

        - Georeference information shall be included in raster file

        - Tiled delivery, without overlap

        - Mosaicked bare-earth DEM

        - DEM tiles will show no edge artifacts or mismatch

        - Void areas (i.e., areas outside the project boundary but within the tiling scheme) shall be coded using a unique “NODATA” value. This value shall be identified in the appropriate location within the file header.

        - A report on the assessed absolute vertical accuracy (NVA and VVA) of the bare-earth surface in accordance with the guidelines set forth in the “Positional Accuracy Standards for Digital Geospatial Data” (American Society for Photogrammetry and Remote Sensing, 2014). Absolute vertical accuracy requirements using the ASPRS methodology for the bare-earth DEM are listed in “Absolute vertical accuracy for digital elevation models, Quality Level 0–Quality Level 3” (table 5).

        - Depressions (sinks), natural or man-made, are not to be filled (as in hydro-conditioning and hydro-enforcement).

        - Depressions (sinks), natural or man-made, are not to be filled (as in hydro-conditioning and hydro-enforcement).

        - Water Bodies (ponds and lakes), wide streams and rivers (“double-line”), and other non-tidal water bodies as defined in Section III are to be hydro-flattened within the DEM. Hydro-flattening shall be applied to all water impoundments, natural or man-made, that are larger than ~2 acre in area (equivalent to a round pond ~350’ in diameter), to all streams that are nominally wider than 100’, and to all non-tidal boundary waters bordering the project area regardless of size. The methodology used for hydro-flattening is at the discretion of the data producer.

        - Bridges removed from the surface.

        - Road or other travel ways over culverts intact in the surface.

      - Breaklilnes:

        - Breaklines for all hydro-flattened areas will be delivered, regardless of technique used for hydro-flattening the DEM.

        - Breaklines delivered in shapefile or file geodatabase formats, as PolylineZ and PolygonZ feature classes, as appropriate to the type of feature represented and the methodology used by the data producer.

        - Breaklines are to be developed to the limit of the project boundary area.

        - Breaklines in the same coordinate reference system and units (horizontal and vertical) as the lidar point delivery.

        - Breakline delivery may be in a single layer or in tiles, at the discretion of the data producer. In the case of tiled deliveries, all features shall edge-match exactly across tile boundaries in both the horizontal (x, y) and vertical (z) spatial dimensions. Delivered data shall be sufficient for the USGS to effectively re-create the delivered DEMs using the lidar points and breaklines without substantial editing.

      - Control: Control, as defined in C.1.a. above shall be delivered to the Government as specified in C.2. Digital Deliverables.

      - LiDAR Intensity Image in grayscale 8-bit GeoTiff format using the same tile structure as the other lidar deliverables.

      - Breaklines: Hydro Enforced/Flattened breaklines shall be delivered in mutually agreeable format, preferably ESRI Arc Shape format.

      - Contours: Delivered in 2 foot intervals as 6 mile X 6 mile blocks in both ESRI Shapefile format and as feature classes in a GDB.

      - Metadata: FGDC- compliant metadata shall pass the USGS Metadata Parser (MP) without errors. The following requirements for Metadata shall be met:

        - Collection Report detailing mission planning and flight logs.

        - Survey Report detailing the collection of control and check points used for calibration and QA/QC.

        - Processing Report detailing calibration, classification, and product generation procedures including methodology used for breakline collection and hydro-flattening.

        - QA/QC Reports (detailing the analysis, accuracy assessment and validation of:

          - The point data (absolute, [NVA], relative vertical accuracy)

          - The bare-earth surface (absolute vertical accuracy [NVA and VVA].

          - Other optional deliverables as appropriate

        - Control and Calibration points: All control and reference points used to calibrate, control, process, and validate the lidar point data or any derivative products are to be delivered.

        - An ESRI polygon shapefile or geodatabase is required. Geo-referenced, digital spatial representation of the precise extents of each delivered dataset. This should reflect the extents of the actual lidar source or derived product data, exclusive of Triangular Irregular Network (TIN) artifacts or raster NODATA areas. A union of tile boundaries or minimum bounding rectangle is not acceptable. For the point clouds, no line segment in the boundary will be further than four times the ANPS from the nearest lidar point.

        - Product metadata (FGDC compliant, XML format metadata). One file for each:

          - Project

          - Lift (note: this one per lift – not one per project)

          - Tiled deliverable product group (classified point data, bare-earth DEMs, breaklines, and any other datasets delivered etc.). Metadata files for individual tiles are not required

      - Project Report: The contractor shall deliver a production report which details:

        - A record of field work procedures.

        - Data derivation and adjustments.

        - Quality control procedures and results.

        - Any problems encountered and solutions used in resolving such problems.

        - Statistical report summarizing the results of the airborne GPS adjustment and the overall accuracy of the adjusted IMU data.

        - Production report shall be Microsoft Word, Adobe PDF format or other compatible digital format.

      - Acquisition Reports: Contractor shall provide regular progress updates to the technical point of contact throughout the data acquisition process.

        - Update frequency shall be based upon the collection period, but no less that once a week.

        - Reports shall be delivered as shapefiles which represent the geographic extent of the acquired data.

        - Updates shall commence at acquisition onset and shall continue until acquisition is complete.

      - Project Pilot: Contractor shall deliver a Project Pilot Delivery consisting of the NVA reporting of the UNCLASSIFIED point cloud data, a minimum of five (5) square miles of classified LAS data in each of the primary land cover categories (NVA categories), and corresponding Hydro Flattened Bare Earth DEM’s.

        - Note that the NGP version 1.2 of the Lidar Base Specification, has a modified XML metadata template to reflect other updates in the specification, careful review is advised.

    - TILING SCHEME AND DATA FORMAT:

      - Tile Coverage: Tiles which lie completely within the project area shall be complete to the tile edges. Tiles which lie partially outside the project boundary shall be complete to the project boundary with enough overlap beyond the project boundary to ensure that no parts of the project are omitted.

        - Tile Size:

          - Tiles shall be 5000 ft X 5000 ft

          - Tiled deliverables shall conform to the tiling scheme, without added overlap.

          - Tiling scheme will be used for all tiled deliverables.

          - Tiled deliverables shall edge-match seamlessly in both the horizontal and vertical.

        - Tile Naming:

          - Tiles shall be named according to the US National Grid conventions.

        - Spatial Reference System:

                - UTM Zone 13, Feet NAD-83(HARN) (horizontally), NAVD88 (Latest Geoid), Feet

                - All data shall be delivered in Orthometric Heights.

    - NOTIFICATION: The Government POC named below shall be notified within 24 hours of the start of acquisition of data. Notification can be made by e-mail and is for information purposes only, not permission to proceed.

    - PERMITS: The contractor shall be responsible for obtaining all permits which may be required in the performance of this task order, which shall include, but not be limited to any permits for acquisition of data in controlled or restricted airspace, and access to control points on the ground.

    - USE AND DISTRIBUTION RIGHTS: All deliverable data and documentation shall be free from restrictions regarding use and distribution. Data and documentation provided under this Task Order shall be freely distributable by government agencies.

      - NOTE: “National Geospatial Program Lidar Base Specification Version 1.2”, page 9 “Deliverables”, regarding data provider’s rights to resell data or derivative products as they see fit are specifically exempted from this task order.

    - CERTIFICATIONS: The contractor shall certify as part of its proposal that the work performed on this task order complies with Section 52.225-05 of the Federal Acquisition Regulations relating to Trade Agreements.

    - THE GOVERNMENT POINT-OF-CONTACT (POC) FOR THIS TASK ORDER: The Government Point of Contact for this task order and any modifications shall be the POC listed below.

# Address: USGS/NGTOC 		Telephone: (303) 202-4419

ATTN: Kathryn Yoder,	             		 FAX:(303)-202-4020
U.S. Geological Survey                                              e-mail: kyoder@usgs.gov
One Denver Federal Center
Building 810, Entrance E-11, MS 510
Denver, CO  80225-0046

  - Digital Deliverables: Reference C.1 of the Contract.

    - The Contractor shall deliver one copy of the lidar data products and documentation as specified in Section C.1 of this Task Order.

    - Format: Data shall be delivered in the formats specified in C.1.c above.

    - Delivery Medium: The digital data shall be delivered on external hard drive, i.e. (firewire, or USB2 – Less than USB2 is not acceptable). Files shall be stored into appropriate directories on the drive.

    - Deliverable Validation: Reference C.1 - 3.12 of the Contract. The Government may choose to contract with a separate contractor for validation on all submitted deliverables.

- - PACKAGING AND MARKING

  - No additional Section D requirements are applicable to this Task Order.

- - INSPECTION AND ACCEPTANCE - The following Section E additional requirements are applicable to this Task Order:

  - Inspection Period: Reference GS0720 of the Contract. The inspection period begins the day after the data has been delivered. All deliverables will be validated within a Sixty (60) calendar-day of the inspection period

  - Inspection and Acceptance Procedures: ReferenceE780 of the Contract. The Government will perform a full inspection of all deliverables in accordance with E780 (b) of the Contract.

  - Nonconforming deliverables: Nonconforming deliverables returned to contractor for rework shall be delivered in accordance with Contract clause E784 (b).

- - DELIVERIES OR PERFORMANCE - The following Section F additional requirements are applicable to this Task Order:

  - Place of Delivery: Reference GS0904 of the Contract. Contractor shall submit all requested deliverables to the address of the POC, as shown in Section C of this Task Order.

  - Delivery Schedule: Reference F981 of the Contract. The Government requires the following delivery schedule:

    - Lot One (1) Kick-off Meeting: A kick-off meeting (Virtual Webinar or WebEx anticipated) will be held to outline communication procedures that will be followed for data acquisition with respect to verification of local ground conditions and vegetation requirements. The kick-off meeting will be held no later than two (2) weeks after task order award and the onset of data acquisition. Contractor proposes that the kick-off meeting occur on or before September 30th, 2015

    - Lot Two (2) Acquisition & Survey Complete: Contractor shall submit the acquisition report and survey report via TOMIS no later than December 15th, 2015.

    - Lot Three (3) Delivery (Pilot Area): Includes full deliverables for a client approved area delivered no later than February 29th, 2016

    - Lot Four (4) Delivery (Full Area): Consisting of all required deliverables (including metadata) of the lidar data and its derived products as specified in the task order, shall be delivered no later than May 30th, 2016.

    - Lot Five (5) Final Delivery (Full Area):  One copy of final accepted lidar data production and documentation no later than June 30th, 2016.

  - Progress Reports: Contractor shall submit a monthly progress report for this task order in accordance with Contract clause GS0921 and GS0931.

- - CONTRACT ADMINISTRATION DATA

  - No additional Section G requirements are applicable to this Task Order

- - SPECIAL CONTRACT REQUIREMENTS -The following Section H additional requirements are applicable to this Task Order:

  - Applicable Regulations And Permits -- Aircraft Operations:  Reference H1344 of the contract.  The contractor shall be responsible for applying for and obtaining any required permits for access, over-flight, or intrusion into restricted or otherwise limited ground access and/or airspace, which may be included within the requirement of this task order.

  - Government Furnished Property: Reference H1480 (Conditions Regarding Use Of GFP) of the contract. No Government furnished property is being supplied with this Task Order.

- - CONTRACT CLAUSES

  - No additional detail is required for this Task Order.

- - LIST OF ATTACHMENTS TO THIS TASK ORDER

  - Attachment A - 	Project Area Description	1 Page

  - Attachment B - 	Shapefiles	1 Page

TASK ORDER Attachment A -

Mesa County QL2 – Project Description and Diagram

This project is for high resolution lidar covering Mesa County, Colorado which is approximately 3,341 square miles

END “ATTACHMENT A”

TASK ORDER Attachment B -

Mesa County QL 2– Project Shape Files

THIS SECTION CONSISTS OF THE FOLLOWING DATA SET(S)

MesaCountyQL2.zip

QL1.zip

END “ATTACHMENT B”