LIDAR Airborne GPS/IMU and Ground Checkpoint Survey Report

FOR

U.S. ARMY CORPS OF ENGINEERS

ST. LOUIS DISTRICT

Champaign, Grundy, Kane, and McHenry Counties, Illinois

LIDAR Digital Elevation Model for

Contour Generation

## December 24, 2008

AERO-METRIC PROJECT NO. 1-080208

PHOTOGRAMMETRY & GEOSPATIAL DATA SOLUTIONS		                      AERO-METRIC, INC.

LIDAR Airborne GPS/IMU Survey Report

FOR

U.S. ARMY CORPS OF ENGINEERS

ST. LOUIS DISTRICT

1222 SPRUCE STREET

ST. LOUIS, MO  63103-2833

314-331-8373

PREPARED BY

AERO-METRIC INC.

4020 TECHNOLOGY PARKWAY

P.O. BOX 449

SHEBOYGAN, WISCONSIN  53082-0449

920-457-3631

AERO-METRIC PROJECT NO. 1-080208

DECEMBER 2, 2008

Table of Contents

LIDAR Airborne GPS/IMU Survey Report

U.S. Army Corps of Engineers

St. Louis District

Champaign, Grundy, Kane, and McHenry Counties, Illinois

LIDAR Digital Elevation Model for

Contour Generation

AERO-METRIC Project No. 1-080208

TITLE                                                                                                                                              SECTION

NARRATIVE………….………………………………….………………………….………………………1

NGS DATASHEETS…………………………………………………………………………………………2

TRAJECTORY SEPARATION PLOTS………………………………………………………….………….3

NARRATIVE

U.S. Army Corps of Engineers

St Louis District

Champaign, Grundy, Kane, and McHenry Counties, Illinois

LIDAR Digital Elevation Model for

Contour Generation

Contract No. W912P9-08-D-0503

LIDAR Airborne GPS/IMU Survey Report

AERO-METRIC, INC.

4020 Technology Parkway

Sheboygan, WI 53083

AERO-METRIC Project No. 1-080208

Abstract

AERO-METRIC, INC. established accurate digital Airborne GPS and IMU trajectories for Champaign, Grundy, Kane, and McHenry Counties in the state of Illinois to support the acquisition of LIDAR data.  The entire area was flown at an altitude of 1700 meters above ground using an Optech 3100EA sensor.  The information allows photogrammetrists to position the photography with minimal ground control and maintain the standards published by the Federal Geographic Data Committee.  In conjunction with the AirBorne Global Positioning System (ABGPS) and Inertial Measuring Unit (IMU) that is utilized during the LiDAR acquisition, 501 surveyed ground control points (checkpoints) were established to validate the accuracy of the LiDAR data.

Airborne GPS/IMU control surveys were completed between November 18, 2008 and November 27, 2008 during the acquisition of the LiDAR data.

Ground GPS control surveys consisting of establishing 501 checkpoints throughout the project area were completed between April 14 and June 19, 2008.

Ground GPS measurements used Wild/Leica System 300 and 500 receivers.  In addition, various GPS receivers were utilized through the National Geodetic Survey (NGS) Continuously Operating Reference Station (CORS) network.  The all GPS systems were dual frequency, multi-channeled receivers.

Airborne positions were completed for the project area, under Contract No. W912P9-08-D-0503 entered into on February 14, 2008 between the St. Louis District Army Corps of Engineers and AERO-METRIC, INC.

Horizontal and Vertical Control

Base horizontal control consisted of 12 National Geodetic Survey (NGS) COOP Continuous Operating Reference Station (CORS) stations and temporary base stations determined using 12 NGS monumented ground control and the NGS COOP CORS stations.  The NGS COOP CORS stations consisted of the following:  DP3A, DP5A, KA11, KA14, KA15, KA17, KAR4, KAR6, TM05, TM06, TM07, and TM11.   The NGS monumented ground control consisted of the following:  NGS Order A station ZAU B; NGS Order B stations NUNDA RM1 and PESOTUM; NGS First Order stations BELLINGER, BLISSDALE, BRACE, DANISH, GARDNER, K 131, VEEN, and W 19; NGS Second Order station GRAY.

Horizontal control is referenced to the Illinois State Plane Coordinate System - East Zone, based on the North American Datum of 1983/1997 (NAD83/97).   Final coordinates are published in US Survey Feet.

Base vertical control consisted of the above mentioned 12 NGS COOP CORS stations using published ellipsoidal heights and the following 15 NGS benchmark stations: NGS First Order – Class I station K 131; NGS First Order – Class II stations C 173 RESET and H 301; NGS Second Order stations BELLINGER, BRACE, DANISH, E 17, GARDNER, GRAY, NUNDA RM 1, PESOTUM,

W 17, and W 19; NGS Second Order – Class I stations VEEN and ZAU B using their published NAVD88 elevations.  The NGS Geoid Model GEOID03 was then applied to the computed and published ellipsoid heights that approximate the North America Vertical Datum of 1988.

Vertical control is based on the North American Vertical Datum Of 1988 (NAVD88).

The above listed horizontal and vertical control stations were also used to constrain the ground check point surveys used to evaluate the vertical accuracy of the final LIDAR surface.

NGS recovery sheets are located in Section 2 of the Control Survey Report.

Ground Computations

GPS measurements were done in two stages.  Initial computations were done with LEICA Geo Office (LGO), version 4.0. LGO permits the conversion of raw satellite data collected by the receivers to a meaningful coordinate difference between points (baseline solutions).  Once the baseline solutions were determined, they were input into the GeoSurv - GeoLab2 series of programs (Geolab version 2.4d).  An adjustment was performed for analysis and quality closure.

Aero-Metric surveyed each county independently using existing control stations located within or nearby each county.  The unconstrained, control closure adjustment results for each county are shown below.

CHAMPAIGN COUNTY

The control closures shown below are from the adjustments holding the position and elevation of GRAY fixed.

HORIZONTAL CLOSURES (UNITS IN METERS)

STATION     NORTHING  EASTING  LINEAR   DISTANCE       PROPORTION

BELLINGER     0.099    0.029    0.103    16720.6      1:  162,000

PESOTUM       0.089    0.006    0.089    44228.8      1:  495,000

VERTICAL (UNITS IN METERS)

PUBLISHED      COMPUTED                 3rd Order

STATION        ELEVATION      ELEVATION     CLOSURE    ALLOWABLE

BELLINGER        260.581        260.609       0.028        0.049

C 173 RESET      226.731        226.676       0.055        0.056

H 301            210.217        210.195       0.022        0.066

PESOTUM          211.286        211.285       0.001        0.080

GRUNDY COUNTY

The control closures shown below are from the adjustments holding the position and elevation of KA17 fixed.

HORIZONTAL CLOSURES (UNITS IN METERS)

STATION     NORTHING  EASTING  LINEAR   DISTANCE       PROPORTION

BRACE         0.014    0.011    0.018    37824.6      1:2,101,000

DANISH        0.010    0.005    0.011    36420.2      1:3,257,000

GARDNER       0.010    0.019    0.021    36346.4      1:1,692,000

KA11          0.000    0.003    0.003    42436.0      1:14,145,000

KAR6          0.006    0.010    0.012    51503.2      1:4,416,000

VERTICAL (UNITS IN METERS)

PUBLISHED      COMPUTED                 3rd Order

STATION        ELEVATION      ELEVATION     CLOSURE    ALLOWABLE

BRACE            178.542        178.586       0.044        0.074

DANISH           181.976        181.938       0.038        0.072

GARDNER          178.928        178.886       0.042        0.072

KA11             199.954        199.948       0.006        0.078

KAR6             197.286        197.273       0.013        0.086

KANE COUNTY

The control closures shown below are from the adjustments holding the position and elevation of

K 131 fixed.

HORIZONTAL CLOSURES (UNITS IN METERS)

STATION     NORTHING  EASTING  LINEAR   DISTANCE       PROPORTION

KA11          0.001    0.012    0.012    48552.0      1:4,046,000

KA15          0.001    0.021    0.021    31766.1      1:1,513,000

W 19          0.000    0.006    0.006    32430.9      1:5,405,000

ZAU B         0.001    0.004    0.004    36316.4      1:9,079,000

VERTICAL (UNITS IN METERS)

PUBLISHED      COMPUTED                 3rd Order

STATION        ELEVATION      ELEVATION     CLOSURE    ALLOWABLE

KA11             199.954        199.979       0.025        0.084

KA15             247.300        247.214       0.086        0.068

W 17             221.339        221.330       0.009        0.054

W 19             218.764        218.764       0.000        0.068

ZAU B            211.213        211.217       0.004        0.072

McHENRY COUNTY

The control closures shown below are from the adjustments holding the position and elevation of

NUNDA RM 1 fixed.

HORIZONTAL CLOSURES (UNITS IN METERS)

STATION     NORTHING  EASTING  LINEAR   DISTANCE       PROPORTION

BLISSDALE     0.018    0.001    0.018    31198.6      1:1,730,000

VEEN          0.001    0.011    0.011    27038.3      1:2,458,000

VERTICAL (UNITS IN METERS)

PUBLISHED      COMPUTED                 3rd Order

STATION        ELEVATION      ELEVATION     CLOSURE    ALLOWABLE

E 17             245.969        245.932       0.037        0.047

VEEN             293.637        293.641       0.004        0.062

All published control was held in the final fully constrained scaled least squares base network adjustment that is used to support the LiDAR and Checkpoints.

LiDAR Control and Computations

Airborne GPS

The carrier phase ambiguity resolution on the fly, without initialization, process was used to determine the airborne positions.  This solution achieve a sub-decimeter kinematic position without the operational constraint of static initialization as used in semi-kinematic or stop-and-go positioning was utilized for the airborne GPS post-processing.

The processing technique used by Applanix, Inc. for achieving the desired accuracy is Kinematic Ambiguity Resolution (KAR).  KAR searches for ambiguities and uses a special method to evaluate the relative quality of each intersection (RMS).  The quality indicator is used to evaluate the accuracy of the solution for each processing computation.  In addition to the quality indicator, the software will compute separation plots between any two solutions, which will ultimately determine the acceptance of the airborne GPS post processing.

Inertial Data

The post-processing between the inertial measuring unit (IMU) and aiding sensor data (i.e. airborne GPS post processed data) computes an optimally blended navigation solution. A Kalman filter-based aided inertial navigation algorithm generates the optimally accurate (in the sense of least-square error) navigation solution that retains the best characteristics of the processed input data.  An example of inertial/GPS sensor blending is the following: inertial data is smooth in the short-term.  However, a free-inertial navigation solution has errors that grow without bound with time.  A GPS navigation solution exhibits short-term noise but has errors that are bounded.  This optimally blended navigation solution will retain the best features of both, i.e. the blended navigation solution has errors that are smooth and bounded.

The resultant processing generates the following data:

- Position:	latitude, longitude, altitude with respect to a user selectable datum

- Velocity:	North, East, and Down components

- 3-axis attitude:	roll, pitch, true heading

- Acceleration:	x, y, z components

- Angular rates:	x, y, z components

These procedures are utilized for both the airborne processing and the blending of inertial and GPS processing.  The software maker is Applanix, Inc.  Programs utilized are POSPac (Position and Orientation System post-processing PACkage), POSGPS (POS Global Positioning System), POSProc (POS post-PROCessing), and POSEO (POS Exterior Orientation), versions 4.31.

The ABGPS/IMU post processed data along with the LiDAR raw measurements were processed using Optech Incorporated’s DASHMap, version 3.0005 software.  This software was used to match the raw LiDAR measurements with the computed ABGPS/IMU positions and attitudes of the LiDAR sensor.  The result was a “point cloud” of LiDAR measured points referenced to the ground control system.

The LiDAR point cloud classification involves importing the point cloud data in TerraSolid’s TerraScan and TerraMatch suite of software that is integrated with Bentley’s MicroStation V8.  This software is initially used in an automatic mode to remove systematic errors found between flight lines and then classify the points to identify the ground (bare-earth surface).  The software computed the errors and classifications using algorithms, with customized parameters to best fit the project area.  Several areas of varying relief and planimetric features were inspected to verify the final ground surface before manual editing.  Once the automatic processing is completed, as a quality control measure, AERO-METRIC meticulously reviews the generated bare-earth surface data to insure that proper classification was achieved.

Statistics pertaining to the analysis and accuracy of the LiDAR points are as follows:

1)   1700 meters above mean terrain was the flying height.

2)   1.2 meter nominal ground point spacing as tested.

3)   Side to side scan width was a nominal 36 degrees

4)   501 total checkpoints spread throughout the area were used to validate the LiDAR elevation.

5)   Checkpoints were divided into 5 classes of surfaces.

6)   The vertical Root Mean Square (RMS) error found from the 5 surface classes:

Champaign County

Hard surface  	= 0.32 feet

Short grass     	= 0.32 feet

Tall grass	= 0.31 feet

Brush              	= 0.35 feet

Trees             	= 0.35 feet

Grundy County

Hard surface  	= 0.18 feet

Short grass     	= 0.24 feet

Tall grass	= 0.23 feet

Brush              	= 0.39 feet

Trees             	= 0.34 feet

Kane County

Hard surface  	= 0.17 feet

Short grass     	= 0.19 feet

Tall grass	= 0.26 feet

Brush              	= 0.36 feet

Trees             	= 0.44 feet

McHenry County

Hard surface  	= 0.14 feet

Short grass     	= 0.19 feet

Tall grass	= 0.19 feet

Brush              	= 0.37 feet

Trees             	= 0.25 feet

NGS DATASHEETS

TRAJECTORY SEPARATION PLOTS