TASK ORDER DETAIL

USGS CONTRACT:	 G10PC00057

CONTRACTOR:	Woolpert

TASK ORDER NUMBER: 	G15PD01145

TASK NAME:	FY15 WA Elwha River QL2 Topo and Topo-Bathy Lidar

The Contractor shall furnish all facilities, labor, materials, and equipment, unless specifically identified otherwise, to provide the mapping services and products in accordance with the specifications, terms, and conditions contained in Contract No. G10PC00057, and the following requirements specific to this Task Order, and in accordance with Contractor’s proposal dated September 17th, 2015 and in the amount of:

Task Order Fixed Price			$

- DESCRIPTION/SPECIFICATIONS/WORK STATEMENT.

The following Section C additional requirements are applicable to this Task Order:

  - Statement of Work (SOW): Reference C.1 of the Contract. This FY15 WA Elwha River QL2 Topo and Topo-Bathy Lidar Lidar task order is for Planning, Acquisition, processing, and derivative products of lidar data to be collected at 2 Points per Square Meter.  Specifications listed below are based on the “National Geospatial Program Lidar Base Specification Version 1.2”, which are incorporated by reference to this task order.  This specification may be viewed at http://pubs.usgs.gov/tm/11b4/. These lidar specifications are required baseline specifications. In addition to the requirements listed below, variations from the specifications will be shown and noted below. For any item which is not specifically addressed, the referenced Version 1.2 specifications will be the required specification authority. This task is for a high resolution data set of lidar of 17.34 square miles in along and at the mouth of the Elwha River in Washington.

Additionally, this FY15 WA Elwha River QL2 Topo and Topo-Bathy Lidar task order is for Planning, Acquisition, processing, and derivative products of topo-bathymetric lidar data to be collected at 1.2 points per m2 in shallow water (Shallow bathymetry Dmax = 2.2 / k (~1.5 Secchi depth).  The topographic lidar will be acquired at 11 points per square meter.

This task order requests bathymetric lidar surveys be collected for two areas along the lower mouth of the Elwha River and along the Eastern Coast from where the Elwha River opens into the Salish Sea; approximately 11.86 square miles, as shown by the shapefile included in Attachment A.  The contractor shall use the Leica Chiroptera II sensor or in combination with the Leica Hawkeye 3 sensor.  Imagery shall be acquired with an RCD30 (in the Chiroptera II sensor) during the bathy/topo lidar data acquisition.  The imagery shall be used to assist with the point cloud editing and classification and shall be provided as a mosaicked product.

    - KICK-OFF MEETING: A kick-off meeting shall be held to outline communication procedures that shall be followed for data acquisition with respect to verification of local ground conditions and vegetation requirements. This meeting shall be used as a forum to clarify and resolve collection condition issues. Local contact(s) shall be established, (if requested), to provide ground condition updates. The kick-off meeting shall be held no later than two (2) weeks after contract award and prior to data acquisition.

    - DATA ACQUISITION (COLLECTION): The contractor shall be responsible for acquisition of lidar data of sufficient density and quality to meet the requirements specified in the referenced Version 1.2 Lidar Base Specification, except where explicitly stipulated in this contract for the terrestrial lidar collections:

      - Collection area: The collection area shall be defined as the Defined Project Area, buffered by no less than 100-meters.  The Project Area is defined in “Attachment A – Project Description and Diagram” and further delineated by the ESRI ArcShape file included as “Attachment B – Shape File(s)” Note that the geometry of the Topo-Bathy polygon Shapefile is not exact as it is based on flight lines proposed by the contractor and may not fit this requirement exactly.

      - Nominal Pulse Spacing: Nominal Pulse Spacing (NPS) shall be no greater than 0.70 meters (QL2); assessment to be made against single swath, first return data located within the geometrically usable center portion (typically ~90%) of each swath.

      - Signal Returns The laser system shall be configured to collect multiple echoes per pulse, with a minimum of a first return and a last return and at least one additional intermediate return. All returns captured during acquisition shall be delivered. Return number shall be recorded.

      - GPS Times: shall be recorded as Adjusted GPS Time, at a precision sufficient to allow unique timestamps for each return. Adjusted GPS Time is defined to be Standard (or satellite) GPS time minus 1*109. See the LAS Specification for more detail.

      - Signal Strength: The signal strength (intensity) of each return pulse shall be recorded.

      - Clustering: The spatial distribution of geometrically usable points is expected to be uniform and free from clustering. In order to ensure uniform densities throughout the data set:

        - A regular grid, with cell size equal to the design 2*NPS will be laid over the data.

        - At least 90% of the cells in the grid shall contain at least 1 lidar point.

        - Clustering will be tested against the 1st return only data of points located in the geometrically usable center part (typically 95%) of each swath.

        - Acceptable data voids identified elsewhere in this task order are excluded.

      - Control: LIDAR shall be acquired using the following control specifications.

        - Supplemental Ground Control: Differentially corrected GPS Ground Control used to supplement the Airborne GPS positional accuracy shall be delivered in ESRI Arc Shape format and shall be delivered to the Government.

        - Quality Check points:  The Contractor shall collect additional Ground Control Check Points in each project area which shall be delivered in ESRI Arc Shape format and will be used by the Government for validation.

          - Positional Accuracy Standards for Digital Geospatial Data (American Society for Photogrammetry and Remote Sensing, 2014) http://www.asprs.org/a/society/divisions/pad/Accuracy/ASPRS_Positional_Accuracy_Standards_for_Digital_Geospatial_Data_Draft_Rev7_V1.pdf should be consulted to determine the minimum number of checkpoints required.  The quantity of checkpoints is linked to the size of the project’s AOI.  Adherence to the ASPRS recommendations is required, but in no case shall an NVA be based on less than 20 check points.

          - The ASPRS-recommended distribution of total number of check points between NVA and VVA assessments shall be met and checkpoints within each type shall be well-distributed across the entire project.  Within each assessment type, check points will be distributed among all constituent land cover types in approximate proportion to the areas of those land cover types.

          - Checkpoints for NVA assessments shall be located only in clear, open terrain, where there is a high probability that the sensor will have detected the ground surface without influence from surrounding vegetation (single return only, away from objects of low reflectivity).  Ground that has been plowed or disturbed is not acceptable.

          - The same check points may be used for NVA assessment of the point cloud and DEM.

          - VVA points should have survey areas sized with a minimum homogeneous area of (NPSx5)^2, with less than one-third of the required RMSEz deviation from a low-slope (less than 10 degrees) plane.

          - The checkpoint accuracy shall be 3 times the targeted accuracy of the lidar data.

          - NVA amd VVA are typically comprised of the following land cover categories (but not limited to):

            - NVA: Bare Earth/Open Terrain and Urban

            - VVA: Tall Weeds/Crops, Brush lands and Trees, and Forested and Fully Grown

        - Check points shall not be incorporated into the contractor’s vertical solution.

      - Vertical Accuracy Requirements: Lidar collected under this task order shall meet or exceed these vertical accuracies. Assessment procedures shall comply with NDEP guidelines. See C.1.c.(i)(a) below for complete vertical accuracy reporting requirements.

RMSEZ ≤ 10 cm (non-vegetated Swath, DEM, Topographic Data)

RMSEZ ≤ 18.5 cm for Topo-bathometric data

NVA ≤ 19.6 cm 95% Confidence Level (Swath, DEM, Topographic Data)

VVA ≤ 29.4 cm 95th Percentile (DEM, Topographic Data)

      - Positional Accuracy Validation: The absolute and relative accuracy of the data, both horizontal and vertical, relative to known control, shall be verified prior to classification and subsequent product development. A detailed report of this validation is a required deliverable.

      - Relative Accuracy Requirements: Relative accuracy of the topographic lidar data shall be ≤ 6cm within individual swaths (smooth surface repeatability) and ≤ 8 cm RMSD within swath overlap (between adjacent swaths) with a maximum difference of ±16 cm.

For bathymetric areas, the relative accuracy shall be ≤ 14.8 cm RMSEz between adjacent swaths with a maximum difference of ±29.6 cm.

      - Acquisition Window: The acquisition window shall be at a period of annual minimal water level in the Winter/Spring 2016 leaf off window running through March 30, 2016 for the Topographic Spring Acquisition.

The acquisition window shall be the fall/winter (September) 2015 season for the Topo-Bathymetric lidar acquisition.  Acquisition should be completed in clear and calm water with acceptable turbidity (within the river channel).

With USGS authorization and as mutually agreed, the contractor may extend these windows based on weather, ground and vegetation conditions.

      - Swath Length: Long swaths (those which result in a LAS file larger than 2GB) shall be split into segments, only if the vendor has a preference to do so for processing efficiency. In such case, each segment shall thenceforth be regarded as a unique swath. Other swath segmentation criteria may be acceptable, with prior approval.

        - Full Swath data shall be delivered.  Edge data from each swath shall not be trimmed from the delivered data.

      - Overlap: Flight line overlap is at the vendor’s discursion, but is cautioned to be vigorous to ensure there are no data gaps between the usable portions of the swaths and to ensure the nominal pulse density (ANPD) can be achieved. Collections in high relief terrain are expected to require greater overlap. Any data with gaps between the geometrically usable portions of the swaths will be rejected.

      - Data Voids:  Data Voids [areas => 4(ANPS2), measured using 1st-returns only]  within a single swath are not acceptable, except:

        - where caused by water bodies

        - where caused by areas of low near infra-red (NIR) reflectivity such as asphalt or composition roofing.

        - where appropriately filled-in by another swath

      - Data Acquisition Conditions:

        - Atmospheric: Cloud and fog-free between the aircraft and ground

        - Ground:

          - Snow free;

          - No unusual flooding or inundation, except in cases where the goal of the collection is to map the inundation.

        - Vegetation: Leaf-off is preferred, however:

          - As numerous factors will affect vegetative condition at the time of any collection, the USGS National Geospatial Program (NGP) only requires that penetration to the ground must be adequate to produce an accurate and reliable bare-earth surface suitable for incorporation into the 1/9 (3-meter) NED.

          - Collections for specific scientific research projects may be exempted from this requirement, with prior approval.

      - Time of Day:  Time of day is not of concern.

      - Tide Requirement:  Tidal water level must be no greater than 0.4m above MLLW at the NOAA Tidal gauge at Port Angeles, WA (Station 9444090) for both acquisitions.  Except where flight safety is a concern and in such case effort shall be made to fly at the lowest tide possible within acceptable safety conditions.

      - Water Clarity: The river portion of the bathymetry collection shall have a clarity requirement.  The water must be of acceptable clarity conditions in order to collect. Where data is not attainable due to poor water clarity (in river areas), the Contractor shall make 2 attempts to achieve data coverage, after the event causing poor water clarity issues has passed, and within the scheduled field deployment.  If an area of permanently poor water clarity is identified, this will be brought to the attention of USGS.  Gaging stations can be used to help determine optimal conditions: http://waterdata.usgs.gov/wa/nwis/uv?site_no=12046260

    - DATA PROCESSING AND HANDLING: The contractor shall be responsible for post processing of lidar data of sufficient density and quality to meet the requirements specified in the referenced “National Geospatial Program Lidar Base Specification Version 1.2, except where allowances are explicitly stipulated in this Task Order.  All processing should be carried out with the understanding that all point deliverables are required to be in fully compliant LAS format, v1.4 (PRF 6-10). Data producers are encouraged to review the LAS specification in detail. Specifications of the LAS data sets will be verified.

      - ACCURACY REPORTING

        - Data Accuracy: Data collected under this Task Order shall meet the National Standard for Spatial Database Accuracy (NSSDA) accuracy standards.  The NSSDA standards specify that vertical accuracy be reported at the 95 percent confidence level for data tested by an independent source of higher accuracy.  For example the metadata statement shall read, “Tested __ (meters, feet) vertical accuracy at 95 percent confidence level.”

          - Accuracy of the Lidar Point Cloud Data (Topographic): The Non-Vegetated Vertical Accuracy (NVA) of the Lidar Point Cloud data shall be calculated against TINs derived from the final calibrated and controlled swath data. The required accuracy (ACCZ) is: 19.6 cm at a 95% confidence level, derived according to NSSDA, i.e., based on RMSEz of 10 cm in the “open terrain” and/or “Urban” land cover categories. This is a required accuracy.

          - Accuracy of the Derived DEM (Topographic): The accuracy (ACCZ) of the derived DEM shall be calculated and reported in three (3) ways:

- RMSEz (Non-Vegetated): The required RMSEz is: ≤10 cm.

- Non-Vegetated Vertical Accuracy (NVA) The required NVA is: ≤19.6 cm at a 95% confidence level, derived according to NSSDA, i.e., based on RMSEz of 10 cm in the “open terrain” and/or “Urban” land cover categories. This is a required accuracy.

- Vegetated Vertical Accuracy (VVA): The required VVA is: ≤29.4 cm at a 95th percentile level, derived according to ASPRS Guidelines, Vertical Accuracy Reporting for LiDAR Data, i.e., based on the 95th percentile error in Vegetated land cover categories combined (Tall Grass, Brush, Forested Areas). This is a required accuracy.

      - Hydro Flattening Requirements:

        - Hydro Flattening is Not required for this Task Order.

          - Scientific research projects in coastal areas often have very specific requirements with regard to how tidal land-water boundaries are to be handled. For such projects, the requirements of the research will take precedence.

    - DELIVERABLE PRODUCTS: The following deliverable products shall be produced from the lidar produced in C.1.c above.

      - Raw Point Cloud Data:

        - Fully compliant LAS v1.4, Point Record Format 6, 7, 8, 9, or 10 as appropriate.

        - Proper use of the LAS withheld and overlap bits is required.  Use of the overlap bit is required for marking overlap points.

        - Georeference information included in all LAS file headers (OGC WKT).

        - GPS times are to be recorded as Adjusted GPS Time, at a precision sufficient to allow unique timestamps for each return. In compliance with LAS specification requirements, the encoding tag in the LAS header must be properly set.

        - Intensity values, 16 Bit, Linear Rescaling.

        - Full swaths, all collected points to be delivered.

        - Swaths may be segmented, as described in the NGP Lidar Base Specification, at the contractor’s discursion if needed.  Otherwise, 1file per swath, 1 swath per file.

        - A report of the assessed relative vertical accuracy of the point cloud (smooth surface repeatability and overlap consistency) shall be provided and dated.  Raw swath point cloud data shall meet the required accuracy levels before point cloud classification and derivative product generation.

        - A report of the assessed absolute vertical accuracy (NVA only) of the unclassified lidar point data in accordance with the guidelines set forth in the Positional Accuracy Standards for Digital Geospatial Data (American Society for Photogrammetry and Remote Sensing, 2014) shall be provided and dated.  Raw swath point cloud data shall meet the required accuracy levels before point cloud classification and derivative product generation.

      - Classified Point Cloud:

        - Fully compliant LAS v1.4, Point Record Format 6, 7, 8, 9, or 10 as appropriate, including “File Source ID.”

        - Proper use of the LAS withheld and overlap bits is required.  Use of the overlap bit is required for marking overlap points.

        - Georeference information included in LAS header (OGC WKT).

        - GPS times are to be recorded as Adjusted GPS Time, at a precision sufficient to allow unique timestamps for each return. In compliance with LAS specification requirements, the encoding tag in the LAS header must be properly set.

        - Intensity values, 16 Bit, Linear Rescaling.

        - Tiled delivery, without overlap

        - Classification Scheme (minimum):

Topographic-Bathymetric Point Cloud Data

          - Class 1 – Processed, but unclassified

          - Class 2 – Bare-earth ground

          - Class 7 – Low Noise (low, manually identified, if necessary)

          - Class 18 – High Noise (high, manually identified, if necessary)

          - Class 22 –Bathymetric Ground (Riverbed/Seabed)

Topographic Point Cloud

          - Class 1 – Processed, but unclassified

          - Class 2 – Bare-earth ground

          - Class 7 – Low Noise (low, manually identified, if necessary)

          - Class 18 – High Noise (high, manually identified, if necessary)

        - Note: Classes 7 and 18 are included as a convenience for the data producer. It is not required that all “noise” be assigned to those Classes.

      - Topo-Bathy Imagery

        - The 10cm pixel imagery will be rectified , auto-mosiaked, and clipped to the existing tile Scheme.

        - Processed and provided in a GIS compatible raster and mosaic format, i.e. GeoTiff.

      - Bare Earth Surface (Raster DEM):

        - Cell Size no greater than 1.0 meter, and no less than the design Nominal Pulse Spacing (NPS), 3 foot cells preferred.

        - Delivery in an industry-standard, GIS-compatible, 32-bit floating point raster format (Erdas Imagine (.img format)).

        - Georeference information shall be included in raster files.

        - Tiled delivery, without overlap or gaps.

        - DEM tiles will show no edge artifacts or mismatch

        - Void areas (i.e., areas outside the project boundary but within the tiling scheme) shall be coded using a unique “NODATA” value. This value shall be identified in the appropriate location within the file header.

        - A report on the assessed absolute vertical accuracy (NVA and VVA) of the bare-earth surface in accordance with the guidelines set forth in the “Positional Accuracy Standards for Digital Geospatial Data” (American Society for Photogrammetry and Remote Sensing, 2014). Absolute vertical accuracy requirements using the ASPRS methodology for the bare-earth DEM are listed in “Absolute vertical accuracy for digital elevation models, Quality Level 0–Quality Level 3” (table 5).

        - Depressions (sinks), natural or man-made, are not to be filled (as in hydro-conditioning or hydro-enforcement).

        - Tiles are to be delivered for areas of open water within the project boundary even if data was not collected for those areas.

        - Bridges shall be removed from the DEM surface and for other non-water features, i.e. overpasses.  In no case shall the removal of a bridge leave a saddling artifact in the DEM, use of breaklines may be used to mitigate such instances.  If breaklines are used they are to be considered a required deliverable.

        - Road or other travel ways over culverts intact in the surface.

      - Control: Control, as defined in C.1.a. above shall be delivered to the Government as specified in C.2. Digital Deliverables.

      - Metadata: The following requirements for Metadata shall be met:

        - Collection Report detailing mission planning and flight logs.

        - Survey Report detailing the collection of control and check points used for calibration and QA/QC.

        - Processing Report detailing calibration, classification, and product generation procedures including methodology used.

        - QA/QC Reports (detailing the analysis, accuracy assessment and validation of:

          - The point data (absolute, within swath, and between swath)

          - The bare-earth surface (absolute)

          - Other optional deliverables as appropriate

        - Calibration points and any validation points: All control and check points used to calibrate, control, process, and validate the lidar point data or any derivative products are to be delivered.

        - Geo-referenced, digital spatial representation (shapefile) of the precise extents of each delivered dataset. This should reflect the extents of the actual lidar source or derived product data, exclusive of Triangular Irregular Network (TIN) artifacts or raster NODATA areas. A union of tile boundaries or minimum bounding rectangle is not acceptable. ESRI Polygon shapefile is preferred.

        - Product metadata (FGDC compliant, XML format metadata). One file for each:

          - Project

          - Lift (note: this one per lift – not one per project)

          - Tiled deliverable product group (classified point data, bare-earth DEMs, etc.)  Product group metadata should contain contents unique and specific to that product group, a renamed copy of the project level metadata is not sufficient.  Metadata files for individual tiles are not required.

        - Note that the NGP version 1.2 of the Lidar Base Specification, has a modified XML metadata template to reflect other updates in the specification, careful review is advised.

      - Project Report: The contractor shall deliver a production report which details:

        - A record of field work procedures.

        - Data derivation and adjustments.

        - Quality control procedures and results.

        - Any problems encountered and solutions used in resolving such problems.

        - Statistical report summarizing the results of the airborne GPS adjustment and the overall accuracy of the adjusted IMU data.

        - Production report shall be Microsoft Word, Adobe PDF format or other compatible digital format.

      - Acquisition Reports: Contractor shall provide regular progress updates to the technical point of contact throughout the data acquisition process.

        - Update frequency shall be based upon the collection period, but no less that once a week.

        - Reports shall be delivered as shapefiles which represent the geographic extent of the acquired data.

        - Updates shall commence at acquisition onset and shall continue until acquisition is complete

      - Intensity Image: An Intensity Image shall be produced for each tile. Image shall be 8-bit, 256 color gray scale, GeoTIFF format, with world files. Images shall match the tiling scheme of the Classified LAS files and DEM.

      - All hydro flattened materials shall be delivered (chiefly, if other techniques than breaklines were used) and shall be delivered in mutually agreeable format, preferably ESRI Shapefile format.

    - TILING SCHEME AND DATA FORMAT:

      - Tile Coverage: Tiles which lie completely within the project area shall be complete to the tile edges. Tiles which lie partially outside the project boundary shall be complete to the project boundary with enough overlap beyond the project boundary to ensure that no parts of the project are omitted.

        - Tile Size:

          - Tiles shall be 1,500 meters x 1,500 meters.

          - Tiled deliverables shall conform to the tiling scheme, without added overlap.

          - Tiling scheme will be used for all tiled deliverables.

          - Tiled deliverables shall edge-match seamlessly in both the horizontal and vertical.

        - Tile Naming:

          - Tiles shall be named according to the US National Grid conventions.

        - Spatial Reference System:

          - The Spatial Reference System shall be: UTM Zone 10, NAD83, Meters (to 2 decimal places); NAVD88, GEOID12A, Meters (to 2 decimal places).

          - All data shall be delivered in Orthometric Heights.

    - NOTIFICATION: The Government POC named below shall be notified within 24 hours of the start of acquisition of data. Notification can be made by e-mail and is for information purposes only, not permission to proceed.

    - PERMITS: The contractor shall be responsible for obtaining all permits which may be required in the performance of this task order, which shall include, but not be limited to any permits for acquisition of data in controlled or restricted airspace, and access to control points on the ground.

    - USE AND DISTRIBUTION RIGHTS: All deliverable data and documentation shall be free from restrictions regarding use and distribution. Data and documentation provided under this Task Order shall be freely distributable by government agencies.

    - CERTIFICATIONS: The contractor shall certify as part of its proposal that the work performed on this task order complies with Section 52.225-05 of the Federal Acquisition Regulations relating to Trade Agreements.

    - THE GOVERNMENT POINT-OF-CONTACT (POC) FOR THIS TASK ORDER: The Government Point of Contact for this task order and any modifications shall be the POC listed below.

# Address: USGS/NGTOC 	Telephone:(573) 308-3654

# ATTN: Tim Saultz, 
             1400 Independence 670 Rolla MO 65401 US	e-mail: tsaultz@usgs.gov

  - Digital Deliverables: Reference C.1 of the Contract.

    - The Contractor shall deliver one copy of the Lidar data products and documentation as specified in Section C.1 of this Task Order.

    - Format: Data shall be delivered in the formats specified in C.1.c above.

    - Delivery Medium: The digital data shall be delivered on external hard drive, i.e. (eSATA, or USB2/3 – Less than USB2 is not acceptable). Files shall be stored into appropriate directories on the drive.

    - Deliverable Validation: Reference C.1 - 3.12 of the Contract. The Government may choose to contract with a separate contractor for validation on all submitted deliverables.

- - PACKAGING AND MARKING

  - No additional Section D requirements are applicable to this Task Order.

- - INSPECTION AND ACCEPTANCE - The following Section E additional requirements are applicable to this Task Order:

  - Inspection Period: Reference GS0720 of the Contract. The inspection period begins the day after the data has been delivered. All deliverables will be validated within a Sixty (60) calendar-day inspection period, with the exception of the Pilot Data which will be reviewed within seven (7) calendar days.

  - Inspection and Acceptance Procedures: ReferenceE780 of the Contract. The Government will perform a full inspection of all deliverables in accordance with E780 (b) of the Contract.

  - Nonconforming deliverables: Nonconforming deliverables returned to contractor for rework shall be delivered in accordance with Contract clause E784 (b).

- - DELIVERIES OR PERFORMANCE - The following Section F additional requirements are applicable to this Task Order:

  - Place of Delivery: Reference GS0904 of the Contract. Contractor shall submit all requested deliverables to the address of the POC, as shown in Section C of this Task Order.

  - Delivery Schedule: Reference F981 of the Contract. The Government requires the following delivery schedule:

    - Lot One (1) Kick-off Meeting: A kick-off meeting will be held to outline communication procedures that will be followed for lidar data acquisition with respect to verification of local ground conditions and vegetation requirements. The kick-off meeting will be held no later than two (2) weeks after task order award and prior to data acquisition. USGS proposes that the kick-off meeting occur on or before September 23rd, 2015.

    - Lot Two (2) Topographic-Bathymetric Lidar Data Acquisition Updates: During this time the contractor will submit regular lidar data acquisition updates in the form of shapefile(s) which represent the acquired geographic extent. Regular lidar data acquisition updates will commence upon the start of the lidar data acquisition but not later than October 15th, 2015 and will conclude upon lidar data acquisition completion. Multiple deliveries of this item will be submitted by contractor.  The Topographic-Bathymetric Lidar Data Acquisition will be completed by October 31, 2015.

    - Lot Three (3): Topographic-Bathymetric Lidar Data Deliverables: Consisting of all required deliverables (including metadata) of the topographic-bathymetric lidar data and the derived products as specified in the task order, no later than December 31, 2015.

    - Lot Four (4): Topographic Lidar Data Acquisition with Updates: During this time the contractor will submit regular lidar data acquisition updates in the form of shapefile(s) which represent the acquired geographic extent. Regular lidar data acquisition updates will commence upon the start of the lidar data acquisition but not later than March 1st, 2016 and will conclude upon lidar data acquisition completion. Multiple deliveries of this item will be submitted by contractor.  The Topographic Lidar Data Acquisition will be completed by March 31st, 2016.

    - Lot Five (5): Topographic-Bathymetric Lidar Data Deliverables: Consisting of all required deliverables (including metadata) of the topographic-bathymetric lidar data and the derived products as specified in the task order, no later than June 30th, 2016.

    - Lot Seven (7): One copy of all the final accepted lidar data products and documentation shall be delivered no later than 30 days following acceptance of Lot 6, but no later than August 31, 2016.

  - Progress Reports: Contractor shall submit a monthly progress report for this task order in accordance with Contract clause GS0921 and GS0931.

- - CONTRACT ADMINISTRATION DATA

  - No additional Section G requirements are applicable to this Task Order

- - SPECIAL CONTRACT REQUIREMENTS -The following Section H additional requirements are applicable to this Task Order:

  - Applicable Regulations And Permits -- Aircraft Operations:  Reference H1344 of the contract.  The contractor shall be responsible for applying for and obtaining any required permits for access, over-flight, or intrusion to restricted or otherwise limited ground access and/or airspace, which may be included within the requirement of this task order.

  - Government Furnished Property: Reference H1480 (Conditions Regarding Use Of GFP) of the contract. No Government furnished property is being supplied with this Task Order.

- - CONTRACT CLAUSES

  - No additional detail is required for this Task Order.

- - LIST OF ATTACHMENTS TO THIS TASK ORDER

  - Attachment A - 	Project Area Description	1 Page

  - Attachment B - 	Shape file	1 Page

TASK ORDER Attachment A -

Project Description and Diagram

END “ATTACHMENT A”

TASK ORDER Attachment B -

THIS SECTION CONSISTS OF THE FOLLOWING DATA SET(S)

FY15_WA_ElwhaRiver_QL2_Lidar_AOI_Topographic.zip

FY15_WA_ElwhaRiver_QL2_Lidar_AOI_2015Fall_TopoBathy.zip

END “ATTACHMENT B”